## Slide 1
Al-Najah National University
Engineering Faculty
Civil Engineering Department
Graduation Project 11
Sewer Network for Tyaseer town
Submitted to Prof: Abdul Fattah AL Mallah
Prepared By : Abdul Hamid Alahmad
Fathiyya Daraghmeh
Israa Daraghmeh
Monday , 21 December 2015

## Slide 2
Objectives
Background
Methodology and Analysis
Results and output
Conclusion
Recommendations
Outline

## Slide 3
Objectives
Growth in world population and urbanization presents a host of challenges to the Engineers and planners who design, maintain, and operate wastewater management systems.
Conducting a sewage network to overcome the problem of the waste water and ends discharging these wastes in the streams
2. Following the standers in the network design and following the environmental conditions

## Slide 4
3. Conducting a treatment planet to receive the whole waste water that come from the town and treat them to have a new water resource to be used in the agriculture
4. Reducing the use of the clean water by using the treated water for agriculture and the clean for drinking
5. Protecting the groundwater and stopping the leaking of the waste water beneath the ground by designing the network and the treatment planet
Objectives

## Slide 5
Wastewater is liquid waste discharged by domestic residences, commercial properties, industry, agriculture, which often contains some contaminants that result from the mixing of wastewater from different sources , Wastewater also could be considered as a serious vital problem that threatens environment , humans , vegetations and that's why wastewater treatment is an important issue that the world is focusing on to come over all these threats to ensure the safety for all humans , environment and vegetation as well.
Background

## Slide 6
Other countries treat the wastewater not to use them in agricultural or even in the toilets they just do that to protect themselves from being infected by a disease and to protect and keep their environment too , but in Palestine things are different we suffer mainly from water deficit so we can handle that by treating the wastewater and use it in such cases instead of the clean water .
Background

## Slide 7
Domestic
It is the waste water from houses, offices, other buildings, hotels and institutions.
Figure 1 Domestic waste water

## Slide 8
Industrial
It is the liquid waste from the industrial places from their different industrial processes like dying, paper matting, tanneries, chemical industries, etc.
Figure 2 Industrial waste water

## Slide 9
Types of Sewer Systems
Separate System.
It is the system in which storm water is carried separately from domestic and industrial waste water. This system is preferred when
There is an immediate need for collection of sanitary sewage but not for storm water
When sanitary sewage needs treatment but the storm water does not
Figure 3 Separate System.

## Slide 10
Combined System
Figure 4 Combined System
It is the type of system in which sewer carries both the sanitary and storm water. Combined system is favored when
Combined sewage can be disposed off without treatment
Both sanitary and storm water need treatment
Streets are narrow and two separate sewers can not be laid.
Types of Sewer Systems

## Slide 11
Study area
Tayasir is a Palestinian town in the Tubas Governorate in the northern West Bank. The town is located 22 km northeast of Nablus and 3 kilometers northeast of Tubas, at the elevation of 300m a.m.s.l . Nearby localities include al-Aqabah to the east, al-Bikai'a to the northeast, Salhab to the north, Aqqaba to the west and ath-Thaghra to the southwest

## Slide 12
2016 | 2015 | 2014 | 2013 | 2012 | 2011 | 2010 | 2009 | 2008 | 2007 | years
3311 | 3205 | 3101 | 3000 | 2901 | 2805 | 2712 | 2622 | 2535 | 2451 | pop
According to the Palestinian Central Bureau of Statistics, Tayasir had a population of 2,451 in 2007 . It was declared a municipality of 1998.
Table of Population Projections According to the Palestinian Central Bureau of Statistics (PCBS 2015)
Population
Table 1 Population Projections

## Slide 13
Economy and land use
Tayasir's total land area amounts to about 26,000 dunams, of which roughly 500 make up the village's "built-up" area. About 5,000 dunams are classified as arable land, of which 3,545 are cultivated, mostly with field crops and fruit trees. The Israeli authorities have confiscated 15,875 dunams for security reasons and military use.
Agriculture is the largest economic sector, accounting for 82% of the active labor force. The second largest sector is the Israeli labor market accounting for 10% of workers. Between 2002 and 2006, the average household income dropped by 60% largely due to measures implemented by Israel as a result of the second intefada which began in 2000. In 2007 the PCBS recorded that there were 49 business establishments in Tayasir. According to ARIJ,2010 these included 22 retail and grocery stores, two restaurants and one government-run health clinic. Most services are provided by nearby Tubas.

## Slide 14
Figure 5 Tayassir land use
Tayassir land use

## Slide 15
Methodology & Analysis
To achieve our goal of design Tayassir area for waste water network for 25 years a sewer cad program was used.
Data used in design:
*pop. Of Tayassir in 2040 was predicted by using many ways
Assume growth rate = 2% (pop. In 2007= 2451 taken from PCBS 2007)

## Slide 16
Constant annual compounding method
Methodology & Analysis

## Slide 17
Exponential method
Arithmetic method
= 4745
=3111
t
Assume
=5000

## Slide 18
Another data was used
* computer files as follow:-
Aerial photo for the village.

## Slide 19
Contour map with 2.5 m interval.
The town plan drawings. (road and building )

## Slide 20
calculation of the sewage flow:
Q(Separate System) = A ( B+C+D+E)
A= generation rate =85 %
B: Domestic water demands
According to PWA the Domestic water demands =227 l/c/d
C: Institutional demand (hospitals & schools) = 20% Qavg
D: Industrial demand = assumed to be zero
E: Inflow and leakage = 20% Qavg

## Slide 21
Q Separate system = .85 (227)+20%(227)+20%(227) =283.75 l/c/d
Sanitary load= 283.75*5000=1418750 l/d
Calculation of peak & min flow:
Q design = 5675 m3/day
= 354687.5 l/d
= 5675000l/d

## Slide 22
UPvc material was used in the design( manning coefficient =0.015 ) for many reasons:
. Don’t corrode ( Unaffected by the
Following fluid )
. Light in Weight
. Easy and quick to install
. Long lifetime
Sewer material:

## Slide 23
Design steps

## Slide 24
Selection of manholes location
.Manholes are normally located at the change in direction ,grade, pipe size , or at the intersection of collection sewers.

## Slide 25
Distance between manholes varies with the sewer diameter, for 8, 10-in sewers , manholes spaced no larger than 50 m to permit cleaning when necessary .
So, in our design the distance between manholes didn’t exceed 50m in high- population areas, and larger than 50m in low- population areas.

## Slide 26
Distribution of load on manholes by (Distribution by area ( scenario

## Slide 27
Load (m³/day) | Node Id
31.6 | MH-127
32.7 | MH-126
46.18 | MH-125
53.3 | MH-124
40.83 | MH-123
21.56 | MH-122
46.62 | MH-121
30.34 | MH-120
31.19 | MH-119
60.58 | MH-118
15.15 | MH-39
28.41 | MH-150
6.48 | MH-117
11.75 | MH-43
8.83 | MH-30
This table shows the value of load on some manholes

## Slide 28
Average velocity is computed as the arithmetic average between the entrance and exit velocities for conduits.
Min. velocity = 0.6 m/s necessary for self cleaning
Max. velocity = 3.5 m/s important to prevent erosion of the internal surface of the pipe.
Design constrains

## Slide 29
Slope constrain:
Slope of the sewer is the difference in sewer invert elevations per sewer length.
Min. slope =1%
Max. slope = 15%

## Slide 30
Cover constrain:
The cover is the distance between the elevations of the street surface & that of the sewer crown.
Min. cover =1 m
Max. cover =5m

## Slide 31
Result
Final Network

## Slide 32
The final design came out and consisted of several components:
1· Pipelines (conduits)
*the conduits were 8 and 10 inches diameter made of PVC with 0.013
Manning coefficient.
.*Total length for all pipes summed up to 5717.8 m
*All pipes met the specification of velocity (0.6 - 3.5) m/sec and
slops (0.5 -15) %.

## Slide 33
This table shows the results of some conduits .

## Slide 34
This table shows the results of some conduits .

## Slide 35
The following table summarize an average values for all the conduits in the network
35.5 | Average length (m)
5.996 | Average slope (%)
1.17 | Average velocity(m/s)

## Slide 36
Engineering profile for manholes with 8in conduits

## Slide 37
Engineering profile for manholes with 10in conduits

## Slide 38
Manholes
* 161manholes were used in our model, and all manholes met
.the specifications
* The depth of all manholes structural ranges between (1.2-3.7 ) m.
The diameters of all manholes is 1m and this value is suitable for the depth

## Slide 39
Flow (Total In) (L/s) | Elev. (Invert) (m) | Elev. (Rim) (m) | Elev. Ground (m) | Label
0.16 | 291.51 | 295.19 | 295.19 | MH-1
9.45 | 269.33 | 272.86 | 272.86 | MH-2
3.35 | 269.69 | 273.19 | 273.19 | MH-3
4.57 | 294.67 | 298.14 | 298.14 | MH-4
0.47 | 311.18 | 314.56 | 314.56 | MH-5
0.83 | 340.63 | 344 | 344 | MH-6
0.71 | 291.72 | 295.08 | 295.08 | MH-7
1.26 | 291.56 | 294.85 | 294.85 | MH-8
0 | 316.02 | 319.29 | 319.29 | MH-9
3.26 | 273.23 | 276.33 | 276.33 | MH-10
9.29 | 274.28 | 277.35 | 277.35 | MH-11
1.49 | 291.36 | 294.42 | 294.42 | MH-12
0.73 | 344.21 | 347.2 | 347.2 | MH-13
1.67 | 291.1 | 294.04 | 294.04 | MH-14
0.73 | 357.15 | 360 | 360 | MH-15
The results of some Manholes .

## Slide 40
Depth (Structure) (m) | Desired Sump Depth (m) | Flow (Total Out) (L/s) | Label
3.68 | 0.2 | 0.28 | MH-1
3.53 | 0.2 | 9.76 | MH-2
3.5 | 0.2 | 3.62 | MH-3
3.46 | 0.2 | 4.7 | MH-4
3.38 | 0.2 | 0.71 | MH-5
3.37 | 0.2 | 1.06 | MH-6
3.36 | 0.2 | 0.76 | MH-7
3.29 | 0.2 | 1.49 | MH-8
3.28 | 0.2 | 0.47 | MH-9
3.1 | 0.2 | 3.35 | MH-10
3.07 | 0.2 | 9.45 | MH-11
3.06 | 0.2 | 1.67 | MH-12
2.99 | 0.2 | 0.83 | MH-13
2.95 | 0.2 | 2.18 | MH-14
2.85 | 0.2 | 0.73 | MH-15
The results of some Manholes .

## Slide 41
Outfalls
Two outfalls were used

## Slide 42
Outfalls.
Two outfalls were conducted the first one covers three quarters of the total and the second one covers the rest , the water will be pumped using a pumping station from the second outfall to the first one because the last one is higher in the elevation
Total flow (out off) (m3/day ) | Hydraulic grade (m) | Elevation invert (m) | Elevation Ground (m) | Label
4365.61 (m3/day) | 266.03 | 266.03 | 267.48 | O-1
1317.39 (m3/day) | 255.48 | 255.48 | 256.89 | O-2

## Slide 43
Conclusion & Recommendations
. At the end of the project , a sewage network was designed and conducted with a good performance as an output of the project and all the components were within the standers and the specifications the total cost was studied also and it was within a good limit and budget at the value of 549216 $
. The proposed project has such good benefits on Tayassir town since it's like the end of a serious problem which is waste water , its recommended to apply this proposal to reality because it deserves application and it’s the target for the gap , no one can deny the huge needs for such projects like this to have a clean environment and safe from diseases .
. it’s also recommended to use trunk lines to transfer the wastewater to after gathering them in one outfall to the future treatment planet that maybe construct in the nearby rejoin .