## Slide 1: The possibility of transforming a traditional existing building into a sustainable building
By : Baraa Surakje
Bara’a Shaer

## Slide 2: Objectives:
1.The Palestinian reality and the importance of moving toward sustainable development
2.The possibility of retrofitting building to sustainable one.
3.Design a gray water reuse system and rainwater collection system for the College of Physical Education building at An-Najah National University.

## Slide 3
The main difference between them is that the green buildings is certified but the sustainable buildings do not get a certificate .
Sustainable Vs Green Construction

## Slide 4: Why Green & Sustainable Buildings ?
Green building has to save water 36-40%, save energy 30- 40% and save materials 25-40% compared to conventional building.

## Slide 5
WATER
WASTE
INSULATION
LIVING ROOF

## Slide 6
Chute System (Rubble Chute)
All Building
Advantages
Easy and fast installation
high impact resistant UV stabilized polyethylene
all kinds of climatic conditions
Waste:

## Slide 7
Insulation
OR
Compressed Stabilized Earth Brick (CSEB)
Waste plastic bottles
1-inorganic subsoil,
2-non-expansive clay, aggregates and
3-portland cement

## Slide 8
1.Gray Water Reuse System:
Water:
Gray water is wastewater from baths, showers, sinks and wash basins.

## Slide 9
Benefits of Gray Water Recycling:
• Lower fresh water use
• Less strain on failing septic tank or
treatment plant
• Less energy and chemical use.
• Plant growth.
• Saving cost.
.

## Slide 11
2- Water use
Many interviews and questionnaires were performed with different students in the college. The students were requested to give information on the frequency of use of the plumbing ﬁxtures and amount of time the water is used over
the working days and weekends.
For students and staff of the college:
The water ﬂow rate of each plumbing ﬁxture (liters per second). | Average time of use (seconds /time of use) | Frequency(times per day)/person | 
5liters for each time | - | 1.5 | Toilet flushing
0.033 | 15 | 2.4 | Hand Washing
.15 | 180 | .5 | Shower

## Slide 12
For foreign students:
The water ﬂow rate of each plumbing ﬁxture (liters per second). | Average time of use (seconds /time of use) | Frequency(times per day)/person | 
5liters for each time | - | .3 | Toilet flushing
.033 | 15 | .7 | Hand Washing
.15 | 0 | 0 | Shower

## Slide 13
Daily Water Consumption:
The daily water consumption can be calculated using this
:equation
For students and staff of the college:
:
Daily gray water consumption for all students(litre/day) | Daily water consumption of each plumbing ﬁxture (liters per day) | 
4275 | 7.5 | Toilet
627 | 1.1 | Hand Washing
7425 | 13.5 | Shower

## Slide 14
For foreign students
Daily gray water consumption for all students(litre/day) | Daily water consumption of each plumbing ﬁxture (litres per day) | 
600 | 1.5 | Toilet
136 | .34 | Hand Washing
 | 0 | Shower

## Slide 15
Total grey water consumption (L/d) | 
763 | Hand washing
7425 | Shower
8188 | Total
Total gray water for each day
By using hand washing and shower as gray water
Gray water= 8188 L/day
c=163.76 /month
For toilet:
C = 97.5 /month
Overflow= 163.76-97.5=66.26

## Slide 16
3-Water demand
:
Water demand(/month) | Month
60 | January
250 | February
304 | March
304 | April
60 | May
70 | June
70 | July
93 | August
250 | September
171 | October
250 | November
70 | December
Water demand per month in the college

## Slide 17: 2.Rainwater Harvesting System
RWH is the most traditional and sustainable method that has been used since ancient time in many regions in world in order to provide human needs for water where the basic water sources has not been able to provide

## Slide 18: Rainwater harvesting in Palestine

## Slide 19: Limitations and objective
Objective
(1) Technical elements (quantity of harvested water, water demand, Tank size)
(2) Economical dimensions (capital cost, economic added value,)
limitations
1-Cost
2-Limited area for storage
3-Data needed

## Slide 20: Climate and Rainwater
A Mediterranean climate, with hot, dry summers and mild, wet winters.
Great variations in rainfall and distribution
On average, 51 Rainy days
Mean rainwater in Nablus equals 660mm (Palestinian Central Bureau of Statistics )

## Slide 21: Uses
Agricultural irrigation
Residential potable water
Domestic toilet flushing (Non potable)

## Slide 22: Components
1-Catchment area
(Roofs ,metal ,clay , concrete)
Catchment area=Total Area of the college roof= 3602

## Slide 23
Runoff coefficient: Rainfall loss occurred from the system due to absorption by the roofing material, wind effects around the roof and gutter overflowing
Metal inclined roof (.75-.95)
2-Conveyance: channels or pipes that
transport the water from catchment
area to storage , Pumps.
3- Roof washing (first Flush Diverter):
Pollutants (bird droppings, leaves) that have settled on the roof from
reaching the cistern

## Slide 24
4-Storage tank:
Type , size, Location, cost
5- Purification or treatment
Analyzing

## Slide 25
Comparison

## Slide 26
chlorination system

## Slide 27: Methodology:
1-Supply : rainwater endowment

## Slide 28
Rainwater volume (l/month) = d ×R×A×1000
d=rain water depth in m, R: runoff coefficient,
A: catchment area in
3-Tank Size
2- Demand

## Slide 29
First: annual rainwater proportion

## Slide 31: Second :Water demand proportion
For 25% of total Toilet flushing demand

## Slide 32: Third : Monthly Average Rainfall Data

## Slide 33
Annual saving percentage = × 100%
Annual benefits= Water budget × water cost (3.1shekel/)

## Slide 34: Green Roof

## Slide 35: Advantages
1-Storm water management: reduces storm water runoff so there is less water directed into storm drains
2-Energy conservation
3-Urban heat islands
4-Aesthetic and social benefits

## Slide 36: Components

## Slide 38: Runoff Reduction
By using Runoff (RO, mm year−1)–rainfall
(P, mm) relationship
RO = 693 − 1.15P + 0.001P2 − 0.8 × S
Run off % =50 as average
In general, the thicker the substrate, the lesser is the discharge ratio so the percentage of runoff needed may determine the depth of the substrate.

## Slide 39
Thank You