## Slide 1: An-Najah National University Computer Engineering Department Hardware Project 2013-2014
CNC Engraving Machine
Supervised By: Dr. Luai M. Malhis
Examiners Committee: Dr. Sufyan Samara
& Dr. Hanal Abu-Zant
By: Abdullah Jaradat & Farouq Mousa

## Slide 2: OUTLINE
What is CNC and its types?
How CNC works?
CNC Mechanical part
CNC Electrical controller
CNC Computer software
Motivation and future work
Demo video

## Slide 3: What is CNC and its types
CNC :stands for Computer Numerical Control
  Mean controlling machine with numerical system called G-code generated and send by computer
G-code: numerical control language used to tell computerized machine what to do and how to do by set of movement instructions.

## Slide 4: CNC types
Milling : machine uses rotating cutter to remove material from the surface of a work piece
  The rotary moves perpendicular to its axis
Lathe : machine that rotates work piece on its axis to perform drilling and deformation operation
Plasma cutters : involves cutting a material using a plasma. used to cut steel and other metals
Water jet cutters : uses water pressure to cut materials

## Slide 5: CNC types
Milling machine

## Slide 6: CNC types
Lathe machine

## Slide 7: CNC types
Plasma cutters

## Slide 8: CNC types
Water jet cutter

## Slide 9: How CNC works
Commercial CNC perform cutting and engraving on material
Our CNC just perform engraving pictures on wood or plastic plates
Engraving process go through these steps
  Convert picture to our custom G-code
  Send G-code instruction via serial to arduino
  Arduino parses G- code string and get steps values
  Rotate stepper motors with exact number of steps

## Slide 10: CNC mechanical part
CNC consists of three axis's x , y and z
Z axis holds drilling bit
Each axis has a Stepper Motor joined to a lead screw via coupler
The end of lead screw is centered with bearing to keep rotational movement
We use nuts with lead screw to convert rotational movement to liner

## Slide 11: CNC mechanical part
Stepper , coupler ,lead screw and bearing

## Slide 12: CNC mechanical part

## Slide 13: CNC mechanical part

## Slide 14: CNC electrical part
Electrical part consist of:
  3 stepper motors
  Each one connected to power driver
  Arduino (MIC) which generate steps sequence

## Slide 15: CNC electrical part
we use unipolar stepper motor nema 23 type
Nema 23 stander dimension 5.7 * 5.7 cm
Each stepper has 6 wires
  2 common power (Vcc)
  4 connected to power driver

## Slide 16: CNC electrical part

## Slide 17: CNC electrical part
Power driver consist of:
  4 Darlington transistor acting as gates or switch's
  4 diodes to protect transistor from back EMF
  4 optoisolator to protect and isolate arduino from power side

## Slide 18: CNC electrical part

## Slide 19: CNC electrical parts
PCB of drivers

## Slide 20: CNC electrical part

## Slide 21: CNC electrical part
Stepper motor stepping mode:
    Full step
      One phase on
      Two phase on
    Half step : alternate between two phases on and a single phase on
    Microsteps : generate sine and cosine waveform of steps

## Slide 22: CNC electrical part

## Slide 23: CNC computer side
Computer side is responsible for generating G-code and send it to arduino
We used two C# programs
  One responsible for generating G-code
  Other one responsible for send G-code to arduino through serial port

## Slide 24: CNC computer side
Due to high constraint of stepper accuracy we cant do more than 5 stages of cutting depth
So first program convert image to gray scale image which has 256 different color vary from black(0) to white(255)
But because we have just 5 cut depth we need to generate image with just 5 color
Each threshold represent cut depth
We write simple algorithm to find longest pattern of same color

## Slide 25: CNC computer side

## Slide 26: CNC computer side

## Slide 27: CNC computer side
Second program is used to initiate the starting point of engraving process
Using arrows to move drilling head up/down left/ right and forward/backward
Or you can assign number of steps to each axis individually
Then open G-code file and start cycling

## Slide 28: CNC computer side

## Slide 29: Future work
Design commercial CNC with better accuracy
Design 3d printing CNC machine for educational purposes.

## Slide 30: Final picture

## Slide 31: Demo time