## Slide 1: Re-Design Of Nablus-Deir Sharaf Road
Prepared by
Enas Saleh
Haneen Hetti
Supervisor
Prof.Sameer Abu-Eisheh

## Slide 2: Outline
1- General information about the road.
2- Data Collections.
3- Analysis.
4- Design Control and criteria.
5- Geometric Design.
6- Traffic Control Device.
7- Design of intersections.
8- Bill of Quantities.
9- Summary.

## Slide 3: General information about the road.
Nablus-Deir Sharf road is a major road that connects Nablus city and Deir Sharf village and then branches to Tulkrem and Jenin .
The study case of the road is starting from Deir Sharaf intersection and ending at Tunis intersection. with length is about 7 km and ROW is 30m.
The road includes four major intersections; Deir Sharf, Quseen, Sheikh Mohammed bin Rashed Al-Maktoom and Tunis intersections

## Slide 4: General information about the road.
Start of the Road
End of the Road

## Slide 5: Data Collection
problems which observed:
Problem and defects found in the pavement.
The design of the lanes of the road with limited capacity that causes safety problem.
Insufficient lane width, which result problems in the intersections.
At commercial and residential area, we did not observe parking lanes.
Restricted sight distance at exist certain regions.

## Slide 8: Analysis
By analyzing the LOS for the two lane (which is the existing ) for a 20 years period, the LOS is founded to be D, which is not accepted for such highway.
So, the analysis is done based on four lane and founded to be B, which is suitable for such a highway.

## Slide 9: Analysis
LOS at the Intersections.
By using Syncro 2007 program. The result found for existing intersection.

## Slide 10: Design control and criteria
Functional classification
Nablus – Deir Sharf road is classified as an arterial; it has two regions; the urban area starting from Wadi At-Tuffah to Quseen intersection where the road can be classified as an urban arterial, and the rural area from Quseen intersection to Deir Sharf village where the road can be classified as a rural arterial.
So the general classification of the road is suburban arterial road.

## Slide 11: Design control and criteria
Design Vehicle.
Based on the proportion of trucks and the size of the largest vehicle pass on the road of Nablus-Deir Sharaf was selected vehicle WB-20.
Design Speed
the topography can be considered as a rolling terrain, and the road is suburban arterial, based on AASHTO standers the design speed considered should be between (50-100 km/h), so we have selected the design speed of 60km/h.

## Slide 12
Superelevation .
. For highway design in urban areas a maximum rate of 4% to 6% is applicable
This project lies in urban or suburban area that means the maximum superelevation is 6%.
Superelevation .
For 60 Km/h design speed and 6% superelevation the minimum radius is 135 m.

## Slide 13: Geometric Design
1- Design of Cross Section Elements.
2- Design of Horizontal and Vertical alignment.

## Slide 14: Design of Cross Section Elements.
      Lane width.
  According to percentage of trucks and high traffic volume and as for the road is classified an arterial. We consider taking 4 lanes, two lanes in each direction, with each lane has width 3.6m.
      Shoulders.
  According to road classified the shoulder width taken as 2.4 m

## Slide 15: Design of Cross Section Elements.
      Median
Nablus- Deir Sharf is classified as suburban arterial and the ROW is restricted, so we take the width of median 4m.
      Side Walks
In this project the sidewalk width will be 3.4m in urban area.
      Parking Lane.
Parking lane is parked at the commercial strip area, as usually restricted area, so parking lane is needed.
The parking lane width is 2.4m.

## Slide 17
Type | From Station | To Station
Sidewalk | 0+000 | 0+340
Sidewalk and Parking Lane | 0+340 | 1+120
Shoulder | 1+120 | 1+940
Sidewalk | 1+940 | 5+340
Sidewalk and Parking Lane | 5+340 | 6+000
Sidewalk | 6+000 | 6+784
      Location of Shoulder, sidewalk and parking Lane

## Slide 18: Design of alignments.
Horizontal
Alignment
Vertical
Alignment

## Slide 19: Horizontal Alignment

## Slide 20: Type of HC

## Slide 21: Existing Condition “ HC “
There are a lot of HC
Some Curve do not meet AASHTO standard
Restricted Sight distance in some curve

## Slide 22: Existing Condition “ VC “
All grades of VC are satisfied the Standard

## Slide 23: Design of H.A
22 curves
Lmin AASHTO 2001 = 3× v= 180

## Slide 24
Type | ID | PC | PT | Radius (m) | Length (m)
Simple | HC1 | 0+144.510 | 0+286.665 | 145 | 142.155
Simple | HC2 | 0+386.455 | 0+459.663 | 100 | 73.209
Simple | HC3 | 0+562.726 | 0+703.896 | 140 | 141.17
Simple | HC4 | 0+899.337 | 0+997.976 | 320 | 98.639
Simple | HC5 | 1+548.786 | 1+742.356 | 2200 | 193.57
Simple | HC6 | 1+837.490 | 2+017.509 | 500 | 180.019
Simple | HC7 | 2+133.284 | 2+329.643 | 1600 | 196.360
Simple | HC8 | 2+591.895 | 2+683.562 | 350 | 91.667

## Slide 25
Simple | HC9 | 2+855.507 | 2+947.635 | 300 | 92.132
Simple | HC10 | 3+152.685 | 3+228.321 | 190 | 75.636
Simple | HC11 | 3+626.907 | 3+685.894 | 420 | 58.986
Simple | HC12 | 4+006.179 | 4+117.561 | 500 | 111.382
Simple | HC13 | 4+469.067 | 4+712.574 | 3200 | 243.507
Simple | HC14 | 5+034.146 | 5+082.096 | 70 | 47.950
Simple | HC15 | 5+185.040 | 5+276.841 | 150 | 91.801
Simple | HC16 | 5+314.612 | 5+407.707 | 350 | 93.094

## Slide 26
Simple | HC17 | 5+577.463 | 5+664.017 | 200 | 87.154
Simple | HC18 | 5+759.055 | 5+868.245 | 270.377 | 112.184
Simple | HC19 | 6+095.812 | 6+167.038 | 200 | 71.226
Simple | HC20 | 6+220.280 | 6+248.859 | 135 | 28.579
Compound | HC21 | 4+847.398 | 4+937.243 | 160 | 44.804
 |  |  |  |  | 16.410
 |  |  |  |  | 24.310
Compound | HC22 | 6+632.351 | 6+697.202 | 110 | 34.279
 |  |  |  |  | 30.573

## Slide 27: Design of V.A
Profile

## Slide 28: Type of VC

## Slide 29
This road is
urban arterial in a rolling terrain
design speed is 60 K/hr.
so the maximum grade is 6%

## Slide 32: Intersections Design
Four major intersection
Minor intersection
Deir Sharaf intersection “ Three leg intersection “.
Quseen intersection “ Three leg intersection “.
Tunis intersection “ Three leg intersection “.
Sheikh Mohammed bin Rashed Al-Maktoom intersection “ Roundabout”.
Three leg
Four leg

## Slide 33: Intersections Design