## Slide 1: Tic Tac Toe Game
Amna Msalam & Rehan Alashqar
Supervised By: Dr. Aladdin Masri & Dr. Emad Natsheh

## Slide 2: Topics to be discussed!???
introduction
Tic Tac Toe(Description)
Why this project?
Project Features
Problems
Project implementation
Recommendations and Future work
Demo

## Slide 3: introduction
Games provide a real source of enjoyment in daily life.
Games also are helpful in improving the physical and mental health of human. Apart from daily life physical games, people also play computer games. These games are different than those of physical games in a sense that they do not involve much physical activity rather mental and emotional activities.

## Slide 4: introduction
Our project name is Tic-Tac-Toe. This game is very popular and is fairly simple by itself. It is actually a two player game, zero-sum game (gain equals the loss of other).
In this game, there is a board with n x n squares. In our game, it is 3 x 3 squares. The goal of Tic-Tac-Toe is to be one of the players to get three same symbols in a row - horizontally, vertically or diagonally - on a 3 x 3 grid.

## Slide 5: Tic Tac Toe(Description)
Our project is a Tic Tac Toe game which consist of a robot that paly against human player depend on the picture that a software program take it and analysis the image using alpha beta algorithm then send command to Arduino to make the robot take the piece from specific position and move it to one of the nine positions depend on which player was play, when the game finished and if the robot win music will start.

## Slide 6: Why this project?
As Artificial intelligence technology occupies the world, it becomes an essential part of all the fields around us; it aims to become more interactive and interesting.
So we try to employee artificial intelligence to play Tic Tac Toe in more interesting way.
Notes: اصبح الذكاء الاصطناعي موجود في كل مكان وحتى تكون الالعاب اكثر ذكاءا اصبحت تحتوي بشكل كبير على الذكاء الاصطناعي وهنا اليوم نقوم باستخدام الدكاء الاصطناعي لعمل روبوت يلعب الاكس او مع شخص عادي .

## Slide 7: Project Features
The game can start by any one of the two player.
The main features of our project that we can play any level of tic tac toe with the robotic arm (Simple, Medium, Hard).
The result after the game finish will see on the LCD.
After the game finished we put sound of music in microcontroller to control the music voice on or off depending on the result of the game.
The game can detect if the player play or not by itself without click any button to hint it.

## Slide 8: Project implementation
We divided the project into three parts
Software part.
Hardware implementation.

## Slide 9: Software part
We build application by using visual basic program to deal with the hardware part. This application consist of three parts these are communicate with each other to play a Tic Tac Toe game between robot and human player using the image processing to analyze the picture from camera and the alpha beta algorithm to determine the suitable position for the robot.

## Slide 10: Software part
This picture show the application to interacts with the hardware part.

## Slide 11: Software part
First part is a TicTacToe class this class control the board in the project the class consist off 3*3 array and function to set the current player may be player X or player O in the specifid position in the array, the psistion in the array speciefied by the AI algorithim in AI class for the player O, and when any position in the array is set by any player there is two function to detect the win or the eqality.
Second part is a TTTAI class this class will detect the best move for the robotic arm (Player O)

## Slide 12: Software part
The third part in the program is the frame window that shown to the user, this frame consist of web cam with size of 360*360 pixel to open the web cam connected to computer ,Picture Box which consist the picture taken by the camera every 200 milliseconds.

## Slide 13: Hardware part
First we constructed a mechanical arm capable of manipulating pieces to play the game.
Then in this part we determine the values for each motor on each position for the nine positions and store the values in different functions, then depend on the command received by serial we control the arm.
Lastly and the most important was the development of code to translate move of the tic-tac-toe program into actions of the physical system

## Slide 14: Analysis System Design

## Slide 15: Robot Design
We analyzed our project, searching through the internet of hardware component available, then we find that the best design for our project like this picture put this arm require 6 servo motors, but we reduce the number of servo motors to four to reduce the cost and the code needed to control all motors and can perform what we need use just four servo motors.

## Slide 16: Components
A robotic arm with gripper
Microcontroller
4 servo motors
Board of 3 x 3 squares
Red and white pieces
LCD
ISD1820 module for music
Web cam
Power supply

## Slide 17: Microcontroller:
    Arduino UNO
    Microcontroller : ATmega328P
    14 digital input/output pins (of which 6 can be used as PWM outputs).
    6 analog inputs.

## Slide 18: Servo motor
We use the MG996R with high torque (metal servo) because this type of servo endure high torque and if we use the plastic motor may be damaged fast, although we use metal servo this servo interrupt and stopped suddenly while we are working and the servo need time to become available so we start repair the suspended motor and we succeed fixed it so we don’t need to bought new one.
1 2 3

## Slide 19: Servo motor
We use four servo motors to control the movement of the robotic arm to access the nine positions of the 3*3 board and to access the position where the piece is found.
Servo motor with its components Internal contents for servo motor

## Slide 20: ISD1820
This component is used to store music on it and when the robot win this music play.

## Slide 21: Powers sources
First we use power charger with 5 volt and 2 ampere but because this charger not get the exact ampere needed to control the four servo motors of the robotic arm this cause the movement of the arm with shaking so to solve this problem we use power supply to get the motors the specific ampere it needed.
Power charger Power supply

## Slide 22: Problems
The components of the project is not available all the time.
One month to get the basic components.
Sudden damage in two motors and the motors become not available in market may reach after two weeks or more so we will try to fix its and we success do that.

## Slide 23: Problems
The servo motors require 5 volt and 2 amperes to work well, we buy power charger with 5 volt and 2 amperes, but the first two months the robotic arm suffer from shaking, we thought this because the arm not connected successfully, but we find that the vibration was caused by the charger because not give the suitable ampere, so we used the power supply from university lab to solve the problem.

## Slide 24: Recommendations and Future work
Before using any component make sure that is available and suitable for your project.
Using this robot for play more than one game with human according to the selected game from the application like chess game ,collecting sheets with colors and Tic Tac Toe game.

## Slide 25: Demo

## Slide 26: //هاي السلايد للفيديو خليتها فاضية

## Slide 27
Thank you for your attention :)