## Slide 1: Mapping Of Flooding Risk From Stormwater In The City Of Nablus And The Management And Design Of The Stormwater Drainage System
Prepared By: - Ekram Saleh
-Hassan Zeid
-Haya Abozant
-Mohammad Abu Sanfa
Under Supervision: Dr. Mohammad Al-Masri

## Slide 2: Table of Contents 05 06 03 04 01 02 Management Of The Problem Analysis By StormCAD The Questionnaire And Interviews Assessment To The Problem Introduction Study Area
08
07
Discussion
Redesign
09
Conclusion
10
Recommendation

## Slide 3: 01 Intoduction
Objectives
Methodology

## Slide 4
Objectives
Analyzing simulating the existing stormwater collection network by means of observations and StormCAD software in order to assess the efficiency and adequacy the network.
Spotlighting the problematic areas that has a flooding risk.
Management and Redesign of the current network .

## Slide 8: Assumptions
The characteristics of the catch basins were the same as those of the nearest manholes given by the DWS
Land cover/use was classified to three categories:
  Lands : C= 0.2
  Buildings : C =0.5
  Roads : C = 0.7
01
02
03
For catch basins 30% clogging factor was assumed due to bad general cleanliness condition of streets and catch basins

## Slide 11
Calculations:
The time of concentration was calculated by
Where:
to: Time of concentration (min).
C: Runoff coefficient.
L: Overland flow path length (ft).
S: Slope of the catchment (%).

## Slide 12
For overland flow, CIA method was used in StormCAD
Where :
Q = maximum runoff (ft3/sec)
C = runoff coefficient (-)
I = intensity of rainfall for a selected frequency and duration equal to at least the time of concentration (in/hour)
A = drainage area (acres)

## Slide 13
For gravitational flow in conduits manning equation was used in StormCAD

## Slide 14
Limitations:
there is a lack of previous studies and data about this subject and specially in Nablus city
01
02
The method of data collection of the catch basins was not that much accurate and depend on the accuracy of the GPS app , However, much efforts were dedicated to get higher possible levels of accuracy.

## Slide 15: 02 Description of the study area

## Slide 16
The average annual rainfall in Nablus city is around 660.1 mm. Nearly, 80% of this rain falls between December and March
Nablus city is witnessing an increasing speed of urbanization where impervious areas are increasing and leading for higher runoff coefficient ( c )
Nablus city is topographically divided into two parts eastern and western , the efforts of analysis were concentrated only on the western part and At-Tofah valley is considered as the outfall of western part .

## Slide 19: 03 The Questionnaire And Interviews

## Slide 20: Why? Questionnaire
For Whom?
Responses!
Questions?

## Slide 22: Field Investigation & Interviews

## Slide 23: 04 Assessment To The Problem

## Slide 24
There are different reasons for floods:
01
The topographic nature of Nablus
02
Large catchment area with insufficient and improper allocation of draining inlets and sometimes there is none
03
The low slopes of the roads (extremely flat) in these areas. This making them hardly able to drain the stormwater
04
Rapidly expanding urbanization where the drainage network still constant
05
Bad infrastructure

## Slide 26: 05 Management Of The Problem

## Slide 27: Management of the problem Maintenance Awareness Data Base Rehabilitation

## Slide 28: 06 Analysis By StormCAD

## Slide 29
Catchment Delineation:

## Slide 30
Overland Flow Path Length and Catchment Slope :

## Slide 31
Land Use/Cover and Runoff Coefficient:

## Slide 32
Calculations for Time of Concentration:

## Slide 33
Calculations for Time of Concentration:

## Slide 34
Storm Event Inputs :
The intensity 11.48 mm/hr

## Slide 35: 07 Redesign Process

## Slide 36
As the preliminary analysis indicated, the current network was not designed enough to handle the stormwater . So there was a need to redesign the network.
The intensity was 16.67 mm/hr for a return period 10 years

## Slide 37
Re-design criteria and standards
Velocity ranges between 0.5 m/s - 4 m/s.
Slope ranges between 1% - 10%.
Cover should not be less than 1 m and not exceed 6 m.
Partial flow not more than 90% of the capacity.

## Slide 38
After the completion of the design, rainfall data for Nablus City through 2016-2018 were analyzed to get the highest intensity for a duration equals the time of concentration

## Slide 39
the highest intensity was found between (1.Dec.2016 at 22:27:00 and 2.Dec.2016 at 00:10:00)
This intensity was 10.62 mm/hr of a total depth 18.4 mm of rainfall duration 104 min

## Slide 40: 08 Discussion

## Slide 45: 09 Conclusions

## Slide 46
The results of the preliminary analysis indicated to a failure in the system at a return period of only 2 years and intensity of nearly 11.48 mm/hr.
The redesign was based on a return period of 10 years and an intensity of 16.67 mm/hr
it is hard to track the behavior of water on the real conditions, which lead to inaccurate estimation of time of concentration and the delineation of catchments boundaries

## Slide 47
the proper distribution and the number of catch basins has a high impact on the behavior of the system and the drainage efficiency
The whole network requires replacement as the results of redesign shows.
After the redesign, the network was analyzed by an extreme storm event to ensure the capability of the system.

## Slide 48: 10 Recommendations

## Slide 49: Recommendations adding new and repositioning of catch basins documentation of rainfall events by the DWS specify staff possibility of making detention ponds
more surveying and statistical efforts

## Slide 50
Thank You