## Slide 1: Objectives
1-Csp financial analysis
2-Pv design and economical analysis
3- Comparison between Csp & PV

## Slide 2: Feasibility study for CSP:
The main average condition in Nablus city that depend in built this power plant with 1Mw capacity.
Parameter | Value
Average temperature | 17.00c
Average humidity | 68.1%
Slope | 2%
Area | Mountainous area

## Slide 3: Initial cost:
Initial cost criteria | Unit Cost ($)
Visibility study | 70,000
Development | 128,250
Engineering | 1,300,860
Solar thermal power | 1357
Road constriction | 50,000
Transmission line | 55,000
Substation | 250,000
Spar part | 40,713
Training commissioning | 25,000
Contingences | 3,236,617
Internes rat during construct | 3,286,983
Power system | 1,712,100
Balance of system & misc. | 139,498
Total initial cost | 3,350,708

## Slide 4: Annual running cost
Annual cost & debt payment($) | 86,355
Electricity export to grid(MWh) | 3,504
Electricity export rate($/MWh) | 175.00
Electricity export income($) | 613,200
Annual income:

## Slide 5: GHG Emission
Fuel Type | Fuel consumption (MWh) | GHG Emission (tCO2/MWh) | GHG Emission tCO2
Electricity | 3.504 | 0.710 | 2488.8
Solar | 3.504 | 0.000 | 0.000
Total | 105 | 0.710 | 74.7
table (8.9)

## Slide 6
GHG emission reduction summary
 | Base case GHG emission (tCO2) | Proposed case GHG emission (tCO2) | Gross annual GHG emission reduction (tCO2) | Net annual GHG emission reduction (tCO2)/yr
Power project | 2488.8 | 74.7 | 2414.1 | 2414.1

## Slide 7: Summary
Parameter | Value
Total Area (m² ( | 25,000m²
Area cost ($) | 25$/m²
Capacity MW | 1MW
Destination of general power | To grid
Total cost per Kw | 625$/Kw
Total Capital cost ($) | 3,350,708$
Total annual cost ($) | 86,355$
Maintenance cost ($) | 40,713$
Transmission line cost ($) | 55,000
GHG reduction cost($/tCO2) | 55
Net Annual GHG emission reduction cost | 2414.1 t(CO2)
Annual Saving and income ($) | 613,000
Simple payback (year) | 6.4 year
Cost per Kwh | 0.176 $/Kwh

## Slide 8: Csp storage system
 | Csp without storage | Csp with storage
Capital cost ($/kw) | 4725 | 5675
Capital cost ($) | 4,546,586 | 5,291,211
Capital cost ($) | 70,000 | 70,000
Solar thermal power $/MW | 1,357,100 | 1,357,100
Cost of energy ($/kw) | 0.173 | 0.183

## Slide 9: PV System Analysis
1- Tilt angel is 27˚
2- Azimuth angel is zero
3- free horizon
4- no shedding system

## Slide 10: PV System design Analysis
Modules :
Si-mono , Model SPR-E20-435-COM
Manufacturer : SunPower
435 Wp
Inverter :
Model Sunny Central 500CP XT
Manufacturer SMA
Unit Nom. Power 500 kWac

## Slide 11: PV System design Analysis
Number of modules | 2299 modules
Number of modules | In series: 7 modules In parallel: 328 strings
Inverter pack | 2 central inverter
Total area | Module area = 4964 m2

## Slide 12: PV System economical Analysis
 |  | Total ($)
Area cost | 25$/m² | 124,100
Modules | 550$/modules | 1,264,450
Inverter | 153200 $/inverter | 306,400
Wiring cost | 30$/m² | 
Annual cost | 544,106$ | 
Maintenance cost | 9,988$ | 

## Slide 13: Investment
PV modules (435 Wp ) 2299 unit | 1262800 $
Support / integration | 249690 $
Inverters (Prom=500 kw ac) | 306400 $
Setting, wiring, …. | 149814 $
Earth price | 124104 $
Solar PV System cost | 3495660 $
Transport and assembly | 79901 $
Engineering | 998760 $
Substation unseaworthy | -299628 $
Gross Investment (without taxes) | 6367500 $
Investment:
Table (9.5): Investment

## Slide 14: Financial
Gross Investment (without taxes) |  | 6367500 $
Taxes on investment (VAT) | Rate 10% | 636750 $
Gross investment (including VAT) |  | 7004250 $
Net Investment (include all taxes) |  | 7004250 $
Annuities | Loan 5% over 20 Years | 562039 $
Annual Running costs |  | 9988$
Total yearly cost |  | 572027 $
Financing:
Table(9.6):Financing

## Slide 15: Energy cost :
Produced energy = 1840 MWh/year
Cost of produced energy = 0.30 $/KWh

## Slide 16: Pv Vs Csp
Plant | CSP | PV
Total Area (m² ( | 25,000m² | 25,000m²
Area per) Mw ( | 25m²/Mw | 25m²/Mw
Area cost ($) | 25$/m² | 25$/m²
Total cost per Kw | 625$/Kw | 625$/Kw
Total Capital cost ($) | 3,350,708$ | 6,780,758
Total annual cost ($) | 86,355$ | 544,106
Maintenance cost ($) | 40,713$ | 9,988
Cost per Kwh | 0.176 $/Kwh | 0.3$/Kwh
Table (9.7): Comparing between CSP and PV