## Slide 1
Smart Car Robot
Prepared by
Mai Asem Abushamma
Shahd Samir Abdulhaq
Supervised by
Dr. Raed Al-Qadi
Dr. Samer Arandi

## Slide 3
    History of Robots
    Any robot has the following basic elements:
A moveable body,
A power source,
An electrical circuit,
A reprogrammable brain,
And a sensory system.

## Slide 4
    What is Ruby ?!
    Ruby is a smart car ROBOT with the following elements
a moveable body,
Plastic sheet with four wheels. moved by the DC gear motors.

## Slide 5
A power source,
Batteries.
the lab Power supply.
and usb connectors.
An electrical circuit.
    Ruby uses the Arduino Uno as the microcontroller to control the DC motors , the servo , and the sensor .
    Ruby's elements cont'd

## Slide 6
    Ruby's elements cont'd
A sensory system,
A proximity sensor to measure the distance between the car and any obstacle.
Consists of two eyes.
One eye sends the infrared light and the other eye receives the reflection of that infrared light.

## Slide 7
A reprogrammable brain
Ruby uses the BeagleBoard –Xm as its brain to do the image processing work and sends commands to the controller serially.
    Ruby's elements cont'd

## Slide 8
Why BeagleBoard ? !
Low Power (5 Volt).
Small computer in a single circuit board .
Supports many operating systems
Availability

## Slide 9
Why BeagleBoard ? !
USB webcam can be connected with the BeagleBoard through one of its usb ports.

## Slide 10
Choosing the operating system
There are many operating systems you can choose to use on your BeagleBoard such as Android, Ubuntu and Angstrom.
Angstrom is the default operating system, that is pre-installed on the BeagleBoard.

## Slide 11
Angstrom vs. Ubuntu
Angstrom
Faster
Lighter =>High performance
Less resources

## Slide 12
Angstrom vs. Ubuntu
Ubuntu
More stable.
Driver detection easy and automatically
Easier for using Wi-Fi
User friendly

## Slide 13
Programming languages
C++ for the processor “BeagleBoard “.
C for the microcontroller.

## Slide 14
Ruby main functionalities ?!
    The system functionality can be divided into three parts
    Obstacles avoidance.
    Traffics detection.
    PC Manual control and video streaming from the beagle to the PC.

## Slide 15
Obstacles avoidance ?!
    Obstacles avoidance done using the IR proximity sensor .
    The IR proximity sensor placed on a servo motor .
    The servo motor is controlled through the arduino.

## Slide 16
Ruby basic circuit for obstacles avoidance

## Slide 17
Traffics detection?!
    Here enters the BeagleBoard-xM.
    As mentioned the BeagleBoard –Xm is the system brain.
    The beagle receives the input from the camera, analyzes the input image, and issues commands to the microcontroller .

## Slide 18
Traffics detection?!
    This part can be divided into two sections:
    Light traffic detection
    Sign traffic detection

## Slide 19
Traffics detection?!
Light traffic detection
RED
Stop
Green
Move
Sign traffic detection
Turn right
Turn left

## Slide 20
Light traffic detection
Threshold the image based on the colors you want to detect
Start
Take frame from the webcam.
Smooth the image CV_GAUSSIAN
Convert from RGB to HSV
Apply filter
Elimination
Find convex hull
Find contour
Extract contours of specific color and size

## Slide 21
Sign traffic detection
We took the left sign and the right sign as samples.
The system uses a pattern matching technique to find the best match.
The system uses the surfFeatureDetector class.

## Slide 22
surfFeatureDetector class
What feature algorithms do is they find key points in two images and calculate their descriptors. And the descriptors are the ones which we will compare to determine whether the object was found in the scene or not.

## Slide 23
Sign traffic detection
the coming scene matching the right object
the coming scene not matching the right object at all.
the coming scene not matching the right completely

## Slide 24
Manual control mode
Desktop application on Ubuntu
Commands
BeagleBoard (processor)
Arduino (Controller)
Commands
H-Bridge
Signals
Motors

## Slide 25
Manual control mode
USB Wi-Fi adapter
Used to connect to the Internet wirelessly.
Easy to use, simply need to plug the Wi-Fi adapter into an available USB port and install the drivers.

## Slide 26
Manual control mode
USB Wi-Fi adapter
The application will send live video from the beagle to the laptop via internet and in return the laptop returns move commands to the beagle board.

## Slide 27
Manual control mode
USB Wi-Fi adapter
From where the command is sent to the arduino which will move the motors. Here BeagleBoard will act as server and the laptop will act as client

## Slide 28
Problems
Our work was somehow restricted by our existence at the university.
No stability using the internet access at the university.

## Slide 29
Problems
Webcam with higher quality, the system may give better results (The current results are satisfying)
Some main elements in our system were burned which led to rebuild the robot again.

## Slide 30
Problems
We had to start building the car model again, using stronger wheels, motors and car body
The old model

## Slide 31
Problems
The new model

## Slide 32
Problems
As working with image processing and embedded systems the time was a very critical factor.
Solutions
We decreased the frame size to 640 *480 .
Some code optimization was done

## Slide 33
Code optimization
As we are working on an embedded system Timing is a very important factor in this field.
Finally we achieved a timing of about 1.7 seconds in the best case and about 3.5 seconds in the worst case.

## Slide 34
Future work
The system can be extended to detect more signs. As we moved to use the pattern matching technique, any sign can be added to the system.
Speed control can be added to the system.
Direction control in more advanced way can be added

## Slide 35
Conclusion
We describe a project that introduces the field of image processing into embedded systems and robotics, as a part of the “PC On-Chip” concept.
The main goal of this project is to build a smart car robot dealing with robotics and embedded systems.