## Slide 1: An-Najah National University Engineering & IT Faculty Civil Engineering Department
Structural Design and analysis of
International Palestinian Airport
By: Majd M. Khader
Ahmad M. Halahla
Mohammad I. Hendi
Under supervision of : Dr. Mohammad Samaaneh

## Slide 2: Outline:
Introduction.
Gravity and Lateral loads.
3D modeling using SAP.
Design of Slab.
Design of Beams.
Design of Columns and Shear walls.
Design of Footings and Ground Beams.

## Slide 3
INTRODUCTION
Civil engineering is a major department of engineering, which is an applied science that deals with many branches such as design and analysis of any building type, environment, water, transportation facility, etc.
In this project, the knowledge of analysis and design of buildings is applied.

## Slide 4: Objectives
This project applies concepts of structural engineering learned over last years.
Different types of analysis and design are done in this project in order to choose the safest and most economical type and method for the design.

## Slide 5: Project information Location
The project under study is the proposal of the international Palestinian Airport building, which is Located 10 km south of Jericho, and 7 km west of Dead Sea, in Al-baqee'a area.

## Slide 6: Project information Structure Components
Our structure composed of five parts
as shown in the figure below:
Parts one, two, three, and four are
consist of two floors.
which are departures, arrivals,
and waiting hales, etc.…
Part five is a hole for reception,
check offices, shopping centres,
etc.…

## Slide 7
International Palestinian Airport Building

## Slide 8: Project information Site And Geology
Based on soil investigation report tests, soil in this project has 250 KN/m^2 bearing capacity, this will be illustrated when the footing designed.
based on this tests the design of foundations system and earthwork can be done.

## Slide 9: Methodology
At first the architectural drawings are studied, and the structural challenges are understood.
After that the most compatible structural system selected depending on strength, serviceability, safety and economy constrains.
So Set the locations of the columns and bearing walls.
the materials used and the materials strengths are selected.
preliminary sizing and design of the structural members
Design the buildings to resist gravity and lateral loads

## Slide 10: Design criteria
  Structural Materials
  1) Concrete:
  Used Compressive Strength (fc’) for Slabs, Beams, Columns and Footings is 35 MPa.
  Modulus of Elasticity = 27806 Mpa
  Unit Weight for used Concrete is 25 kN/m3

## Slide 11: Design criteria
Structural Materials
2) Reinforcing Steel
Yielding Stress for used Steel is 420 Mpa
Modulus of Elasticity is 200,000 MPa
3) Steel for structure
Yielding Stress for used Steel is 350 Mpa
Modulus of Elasticity is 200,000 MPa

## Slide 12: Design criteria
Non-structural material
Material | Density kN/m3
Mortar | 23
Tile | 25
Filling material | 18
insulation | 0.4

## Slide 13: Design criteria
Load assumption
Gravity loads:
Dead load
Live load
Super dead load
Load assumption
Lateral Loads
Earthquake
Wind load

## Slide 14
Codes
ACI 318-11 (American Concrete Institute)
UBC-97 (Uniform Building Code)
ASCE-2010 (American Society of Civil Engineers).

## Slide 15
Load Combination
U = 1.4D
U = 1.2D + 1.6L + 0.5(Lr or S or R)
U = 1.2D + 1.6(Lr or S or R) + (1.0L or 0.5W)
U = 1.2D + 1.0W + 1.0L + 0.5(Lr or S or R)
U = 1.2D + 1.0E + 1.0L + 0.2S
U = 0.9D + 1.0W
U = 0.9D + 1.0E

## Slide 16: Computer Programs
SAP2000
E-tabs
SAFE
RAM-connection
AutoCAD

## Slide 17
Structure dividing
Structural system (analysis and design)

## Slide 18: Structural system (analysis and design)
To improve and simplified the design the structure is divided into blocks, as shown:
blocks of concrete parts blocks of steel parts

## Slide 19: Structural system (analysis and design)
The parts on eand two are designed as a concrete structure, they are similar in all properties so they are have the same design.
The parts three and four are designed as a steel structure, they are similar in all properties so they are have the same design.
Part five is a concrete and steel trusses used to cover it.

## Slide 20: Preliminary Design
International Journal of Current Engineering and Technology
Comparison | Solid Slab | Ribbed Slab
Weight | Heavier than ribbed | Light
Area of steel | More | Less
Beams | Bigger | Smaller
framework | Approximately the same | 
Cost | Bigger | smaller
The choice of the system for slab in the building is very important to resist the internal forces and stability.

## Slide 21
Loads
Gravity
Lateral
Seismic
Dead
live
Superimposed
wind
Loads

## Slide 22
Gravity Loades
Lateral Loades
Lateral load taken in this project is seismic load(earthquake)

## Slide 23: Preliminary Design
Concrete parts
Frame equivalent method (FEM)
Divide the system into frames in each direction(transform the building from 3d to 2d)by taking the effect of lateral stiffness

## Slide 24: Preliminary Design
Concrete parts
Main idea of EFM
Calculating the stiffness for column ,and slab beam member
Kc= 104.6*104 KN.m
KSB = 107.84*104 KN.m
Kt . edge = =57.122 *104 * =114.244*104 KN.m
Kt . interior =76.82 *104 *= 153.64 * 104 KN.m
Then calculate df
Then use moment distribution method to find moment on frame
Then we have this results

## Slide 25: Preliminary Design
joint | A | B |  | C
member | ab | ba | bc | cb
df | 0.5 | 0.317 | 0.317 | 0.5
FEM | -5602.5 | 5602.5 | -5602.5 | 5602.5
cof | 0.505 | 0.505 | 0.505 | 0.505
balance | 2801.25 | 0 | 0 | -2801.25
cof | 0 | 1414.631 | -1414.63 | 0
balance |  |  |  | 
cof |  |  |  | 
total | -2801.25 | 7017.131 | -7017.13 | 2801.25
Concrete parts
Table moment distribution on first floor-frame one

## Slide 26: Preliminary Design
slab design
1.laods:
2. shear check:
3.Flexure design:

## Slide 27: Preliminary Design slab design

## Slide 28: Preliminary Design
Beam design
1.laods:
2. shear check:
3.Flexure design:

## Slide 29: Preliminary Design
For flexure
Beam design

## Slide 30: Preliminary Design
Beam design
Shear reinforcement
Av= 226.2 mm2
use double stirrup φ12 (2 φ12/110mm)

## Slide 31: Preliminary Design
Column design
Pu = 0.8 Ф [ 0.85 f’c (Ag - As) + Fy * As ]
As = ρ * Ag
ρ = 0.01 (economical percentage of steel)

## Slide 32: Preliminary Design
Column design
Longitudinal reinforcement
As = 0.01 * 785398 =7854 mm2
Use 12 Ф32 mm

## Slide 33: Preliminary Design
Column design
shear reinforcement
Av=226mm2
Use 1 Ф12mm/26cm

## Slide 34: Three Dimensional Structural model and check
The structure is modeled using SAP2000 program

## Slide 35: Three Dimensional Structural model and check
    Checks
Compatibility Check
  The following figure proves the compatibility of the model

## Slide 36: Three Dimensional Structural model and check
    Checks
2) Equilibrium Verification

## Slide 37: Three Dimensional Structural model and check
    Checks
    3) Stress strain relationship check
    Take the block shown to make verification
    The total factored moment will be compared on
    interior span for its live load applied on it

## Slide 38: Three Dimensional Structural model and check
    Checks
    3) Stress strain relationship check
m1= 1353KN.m
m2 =685KN.m
m3 =1363KN.m
So by SAP2000
M0= + m2 = +685 =2016KN.m
Total factored moment on span assume it simple
=WL*ln2 /8 =5*15*14.422/8=1950
Error% =3.27% < 10% so the stress strain check is acceptable

## Slide 39: m1
m2
m3

## Slide 40: Seismic Design And Analysis
Detailing requirements:
The seismic map of Palestine is shown, our
project is located in zone with red colour
which is equals to (Z=0.3, i.e. Zone 3)

## Slide 41: Seismic Design And Analysis
Detailing requirements:
so the SDC founded by Z-factor, according to table R1.1.9.1 in code of ACI-18.
According to table R21.1.1 in ACI 318-11, the detailing requirements for structure should be special moment frames.

## Slide 42: Seismic Design And Analysis
Detailing requirements:
Beam detailing
Column detailing

## Slide 43
Seismic Design And Analysis
Response spectrum analysis
  define and analyze a response spectrum function using SAP2000 on both blocks. Then, the results from response spectrum will be verified using Equivalent static
  method.

## Slide 44
Seismic Design And Analysis
Response spectrum analysis
Factors:
Z-factor: Z=0.3 for Jericho
Site Soil Classification Stiff soil profile → Soil type D.
find Ca and Cv based on site Soil Classification so so Ca=0.36
and Cv=0.54
Importance Factor (I):
the structure is considered as special occupancy structure, so from table From table 16-K—occupancy category in UBC-97 the factor I=1.
response modification factor (R): R=8.5 for special moment resisting frame, but it reduced to (6.5) to increase the seismic load on building.

## Slide 45
Seismic Design And Analysis
Response spectrum analysis
Definition of response spectrum function

## Slide 46
Seismic Design And Analysis
Response spectrum analysis
  Base Reactions:

## Slide 47
Seismic Design And Analysis
Response spectrum analysis
Modal Case (For modal mass participation ratio)

## Slide 48: Seismic Design And Analysis equivalent lateral force method
Total base shear can be calculated manually by this equation:
V(max)
V(min)

## Slide 49
Seismic Design And Analysis
    Period (T)Check:
T (Rayleigh) =
= 0.852 sec
%Difference = ×100%
= 0.001 % →0.001 %<<20% →OK

## Slide 50: Seismic Design And Analysis Final Design Slab design: Bottom and top reinforcement are the same

## Slide 51: Seismic Design And Analysis Final Design of slab Rib Details

## Slide 52: Seismic Design And Analysis Final Design of columns
An example taken is the column shown
Ultimate axial load from SAP (Pu) = 1981 KN
Ultimate moment Mu2 =2796KN.m
Ultimate moment Mu1 =2995 KN.m

## Slide 53: Seismic Design And Analysis Final Design of columns
Check if column is short or long
[(K*Lu)/r] < [34 – 12(M1/M2)] ………… for short column
K = 0.81 , Lu =7 m, r = 0.3h = 0.3*0.81 = 0.243
M1/M2 negative then double curvature
34 - 12(M1/M2) = 34 + 12 * (2796/2995) = 45.2
= (0.81 * 7000) / 225 = 25.2
So , [(K*Lu)/r] < [34 – 12(M1/M2)] ………………… short

## Slide 54: Seismic Design And Analysis Final Design of columns
Kn = = 0.073
Rn = = 0.146
ϒ = (750 – (100 + 24 + 32)) / 750 = 0.8
ρ = 1.9 %
Then As= 0.019 * 1600 * 750 = 22800 mm2
Using bars of φ32 then:
Then use 28 φ32

## Slide 55: Seismic Design And Analysis Final Design of columns
Column ID | Dimensions (mm) | ρ (SAP) | As (used) | No. of Bars | Av/s | S | Sused
C1 | 1600X 750 | 1.50% | 18000 | 24Ø32 | 3.635 | 124 | 120
C2 | 1600X 750 | 1.80% | 21600 | 28Ø32 | 4.919 | 91 | 90
C3 | D = 1600 | 1.28% | 25735.92702 | 32Ø32 | 3.951 | 60 | Spiral with 60
C4 | D = 1600 | 1% | 20106.19298 | 25Ø32 | 4.542 | 50 | Spiral with 50

## Slide 56: Seismic Design And Analysis Final Design of beams
For maximum negative moment: = (1- ) =0.0105 > p min = = 0.0033 Ok max =0.0225 > p= 0.0105  Ok
Cover of 110 mm so d= 1290 mm As = *b*d =0.0105*600*1290 = 8127 mm2
For maximum positive moment: = (1- ) =0.0037 > p min = = 0.0033 Ok max =0.0225 > p= 0.0037  Ok
Cover of 110 mm so d= 1290 mm
As = *b*d =0.0037*600*1290 =2864 mm2

## Slide 57: Seismic Design And Analysis Final Design of beams
Design beam for shear:
Vu = 1290 KN at distance d from the face of the column
Smax = min. { , 600 mm }  Smax = 600 mm
= =1.4 mm2/mm
()min = max. {0.062* * , }  0.5 < Ok
Assume stirrups diameter (12 mm ), so Av = 226 mm2
= 1.4  s = 162 mm <Smax
Use s = 170 mm1 φ 12 /17 cm

## Slide 58: Seismic Design And Analysis Final Design of beams
= mm2/mm
Using two leg stirrups = 2.08 mm2/mm
Spacing = 100 mm
So, Al = 1237.6 mm2
So, Al(min) = 3692.5 mm2
AL<A L..min , then use Al min. = 3692.5 mm2

## Slide 59: Seismic Design And Analysis Final Design of footings
in operation of design of footing, the SAFE program is used.
Pn = 8500 KN
Pu = 10800 KN
A= = 34 m2
so, take L = 6m, and B = 6m
Shear failure:
Punching Shear:
.
= 0.75 * (1/3) * 35 * ( 2 (1500+d))* d = 10800
then d= 900 mm

## Slide 60: Seismic Design And Analysis Final Design of footings(single)

## Slide 61: Seismic Design And Analysis Final Design of footings
 |  |  |  | reinforcement | 
 | B | L | Depth | parallel to B | parallel to L
F1 | 6 | 6 | 0.9 | 1φ20/11cm | 1φ20/11cm
F2 | 4.3 | 7 | 0.55 | 8φ16/m | 7φ25/m
F3 | 5 | 3.6 | 0.6 | 5φ25/m | 5φ25/m

## Slide 62: Seismic Design And Analysis Final Design of tie beams
Mu=2775.5 KN.m
ρ=0.0136
As = 7480 mm2
so use 1032
for shear reinforcement:
Vu=352.85 KN
Vc = 1.1 * 0.75 * * 500 then Vc > Vu
(Av/S)min = (0.436 , 0.416)
use (Av/S) = 0.436
Av = 2 * 10 * ( = 157 so S = 360 mm

## Slide 63: Seismic Design And Analysis Final Design of tie beams