## Slide 1
An-Najah National University
Facility of Engineering and Information Technology
Civil Engineering department
Structural design of Hebron Hospital II
Prepared by: Ja’far Sa’eed
Supervised by: MSc. Hind Tabileh

## Slide 2
Content:-
-Project description. -codes.
-Seismicity of Site and Structure. -Material.
-Loads and load combinations.
Introduction
01
-Columns -Beams.
-Slab. -Walls
-Footings.
Design philosophy
02
Design Checks
03
Design and Detailing
04
-Columns. -Beams.
-Slab. -Walls
-Footings.
-Columns -Beams.
-Slab. -Walls
-Footings.

## Slide 3
Hospital consist of 8 floors, once as basement floor, with total area of building 4291 with area as shown in the table.
01 Introduction
Project description:-
Hebron hospital project, is proposed to be built in Hebron city, near Palestine Polytechnic University in Wadi al-haria.
Floor | Area
BF | 4291
GF | 4191
F1 | 4191
F2 | 4191
F3 | 3981
F4 | 3816
F5 | 3412
F6 | 1528
Floor | 
BF | 4291
GF | 4191
F1 | 4191
F2 | 4191
F3 | 3981
F4 | 3816
F5 | 3412
F6 | 1528
Table-1: Floors Area.
Soil bearing capacity= 500KN/

## Slide 4
Project description:-
Figure-1: Basement floor plan.

## Slide 5
Project description:-
Figure-2: south-west site view.

## Slide 6
Project description:-
Figure-3: North-west site view.

## Slide 7
Project description:-
Figure-4: Blocks plan.

## Slide 8
IBC 2012.
01 Introduction
Codes and Standard:-
ACI318-11.
ASCE7-10.

## Slide 9
01 Introduction
Material:-
Material used in the project divide into two type:-
Structural material: Material which used in structural element, with properties as shown in the below table.
Table-2: Structural materials properties.
Material | Compressive strength | Modules of elasticity | Unit weight
Concrete | 28MPa | 24870MPa | 25 KN/
 | Yield strength | Modules of elasticity | Unit weight
Steel Gr (60)A615 | 413.7MPa | 200GPa | 78 KN/
Material | Compressive strength | Modules of elasticity | Unit weight
Concrete | 28MPa | 24870MPa | 
 | Yield strength | Modules of elasticity | Unit weight
Steel Gr (60)A615 | 413.7MPa | 200GPa | 

## Slide 10
Material:-
Non-structural material: Material which form non-structural element, with properties as shown in the below table.
Materials | Unit Weight (KN/)
Tiles | 26
Blocks | 12
Masonry Stones | 26.5
Filling Materials | 13
Plastering | 23
Aggregate | 16
Glass | 25.4
Concrete Mortar | 23
Materials | 
Tiles | 26
Blocks | 12
Masonry Stones | 26.5
Filling Materials | 13
Plastering | 23
Aggregate | 16
Glass | 25.4
Concrete Mortar | 23
Table-3: Non-Structural materials properties.

## Slide 11
01 Introduction
Seismicity of Site and Structure:-

## Slide 12
Seismicity of Site and Structure
Calculate Ss & S1:-
Z for Hebron = 0.15
=0.375
0.187
Multiply the values by factor 3/2 to convert from 10% to 2% .
(1.1)
(1.2)
Figure-5: Seismic Hazard Map and
Seismic Zone Factor for Palestine.

## Slide 13
Seismicity of Site and Structure
Site class:-
q = 500 >> Su =250
Table-4: Site classification procedure for seismic design.
In the table the value of Su for rock and hard rock more than 95.8 (2000 x 0.0479), and the available soil has value Su =250, then site class from Type B.

## Slide 14
Seismicity of Site and Structure
Calculate SDs & SD1:-
S1 & Ss values are general for Hebron city, actually type of soil under the structures has magnified effect on nature of Earthquake which affects on these structures, which mean these values must modify to take in consideration nature of soil by multiple Ss, S1 with site coefficients Fa, Fv respectively.
(1.5)
(1.6)
(1.3)
(1.4)

## Slide 15
Seismicity of Site and Structure
Calculate SDs & SD1:-
Table-5 ‎: Site coefficient for long period, Fv.
Table-‎6: site coefficient for short period, Fa.

## Slide 16
Seismicity of Site and Structure
Calculate SDs & SD1:-
=0.562
1 =0.281

## Slide 17
Seismicity of Site and Structure
Determine seismic design risk category:-
Determination of seismic design category depends on value of SDs, SD1 which evaluated in previous section, and risk category for intended structure as the following:
Table-7: Risk Category of Buildings and Other Structures for Earthquake, Ice Loads…etc.

## Slide 18
Seismicity of Site and Structure
Determine seismic design risk category:-
Table-9: Seismic Design Category Based on Short Period Response Acceleration Parameter.
Table-8: Seismic Design Category Based on long Period Response Acceleration Parameter.
Then, the seismic design category from table-9 and table-8 seismic design category C.

## Slide 19
Seismicity of Site and Structure
Determine seismic resistance system:-
Table-10: Design Coefficients and Factors for Seismic Force-Resisting Systems.
Then, the system which will be used dual system.

## Slide 20
01 Introduction
Loads and load combinations:-
Type of loads that in consideration in design the structure divided into two Type:
1- Gravity loads: live and dead loads.
Dead load composed of own wright of structure and Super dead load 6.2 KN/
Live loads =4.5 KN/.
2- Lateral load: Earthquake load and soil pressure.
Seismic load : Modal response method.
Soil pressure : Load as shown in the following figure

## Slide 21
Loads and load combinations:-
1-Service load combinations:
Load combination used with according to ASCE7-10 code divide into two type :
(1.32)
(1.33)
(1.37)
(1.38)
(1.39)
(1.40)
(1.41)
(1.42)

## Slide 22
Loads and load combinations:-
2-Ultimate load combinations:
(1.14)
(1.15)
(1.23)
(1.25)
(1.26)
(1.29)
Load combination used with according to ASCE7-10 code divide into two type :

## Slide 23
02 Design philosophy
Models:-
Figure-3: Block-1,
without footing.
Figure-2: Block-1,
without footing second model.
Figure-1: Block-1,
without footing.
Figure-4: Block-1,
without footing second model.

## Slide 24
columns:-
02 Design philosophy
Figure-5: Columns centers layout.
Preliminary column section 600400mm
Some column section need to be 900400mm
With according to ACI318-11 code, the shortest column
dimension shall be at least 30cm.
Also, The ratio of the shortest cross-sectional dimension
to the perpendicular dimension shall be at least 0.4.
Column 900  400 has the smallest ratio equal 0.44. OK.

## Slide 25
Beams :-
System of beam used is drop beams between all columns.
Preliminary dimension of beam will be 650  300
02 Design philosophy
Clear span at least equal 4d (23.2m), shortest clear span 3m , Ok.

## Slide 26
Slab :-
For 0.2 < αfm ≤ 2.0
For
Then, hs = =
To avoid excessive deflection, h will be increased by 10% then h becomes 23cm.
02 Design philosophy

## Slide 27
02 Design philosophy
Walls :-
Walls thickness will be as the following:
1- Basement wall:
With according to ACI318, minimum thickness 19cm. Which less than thickness used 40cm.
2- Shear walls:
With according to ACI318, minimum thickness as the following:
Then, used thickness 30cm more than 16.8cm, ok.

## Slide 28
Walls :-
Figure-6: Walls distribution plan.

## Slide 29
Walls :-
Figure-7: Walls Grid A .

## Slide 30
Walls :-
Figure-7: Walls Grid I .

## Slide 31
Walls :-
Figure-8: Walls Grid 7 .

## Slide 32
Walls :-
Table-1: Story max/avg drift.
Table-2: Story center of mass and center of rigidity.

## Slide 33
02 Design philosophy
Footings :-
Figure-9: Footings layout .

## Slide 34
Footings :-
Wall footings :-
Figure-10: Footing layout .
( ‎4.27)

## Slide 35
Footings :-
Single footings :-
Loads at bottom of columns will be determined from ETABS, and service load will be enlarged by 10% to take in consideration weight of backfill and weight of footing materials.
( ‎4.29)
2.
( ‎4.30)
( ‎4.31)
3.
4.
5.
( ‎4.35)
( ‎4.32)
( ‎4.33)
( ‎4.34)

## Slide 36
Single footing footings :-
Table-3:Single footings calculations data.

## Slide 37
Single footing footings :-
Table-5: Footing depth calculations.
Table-4: Footing type data.

## Slide 38
Footings :-
Combined footings :-
Table-5: Column forces.
Combined footing dimensions 7.5 .
Figure-11: Footings layout .

## Slide 39
Footings :-
Mat foundation:-
Figure-12: Footings layout .
Mat thickness will be calculated with conceptual rule say each story supported by mat will need 10cm, thickness of mat. Then, preliminary thickness will be 7 = 70cm.
For mat dimension, mat boundaries will be placed 0.7m offset from face of basement shear wall.

## Slide 40
03 Design checks
Beams :-
Longitudinal steel:-
Selected beam is beam-38 in second floor with section 650  300mm
Figure-12: Beams layout
M- right side = 168 KN.m
M+ = 115 KN.m
M- Left side = 128 KN.m
( ‎4.1)
Figure-13: Beam longitudinal steel.

## Slide 41
Beams :-
Shear reinforcement:-
Figure-14: Design shear force for beam
D+L
D+L
( ‎4.3)
( ‎4.4)
( ‎4.5)
( ‎4.6)
=1, and αfy, where α is set equal to 1.25.

## Slide 42
Beams :-
Shear reinforcement:-
Table-6: Probable moment capacity at end of beam from ETABS.
( ‎4.7)
( ‎4.8)
For positive moment at left side:

## Slide 43
Beams :-
Shear reinforcement:-
Table-6: Probable moment capacity at end of beam from ETABS.
Ln = 7.3-0.9 = 6.6m
Then, Vp = 55.3 KN.
Table-7: Design Forces from ETABS at right side.
Then, Vdesign = 55.3 + 109.9 = 165.2 KN.

## Slide 44
Beams :-
Shear reinforcement:-
Table-7: Design Forces from ETABS at right side.
( ‎4.9)
= 275 mm2/m from program as shown in the next figure 265.6, difference less than 10%, it’s ok.
Figure-15: Shear reinforcement result from ETABS.

## Slide 45
03 Design checks
Columns :-
Longitudinal steel:-
( ‎4.11)
For side 400mm:
Selected column is column-28 in second floor with section 900  400mm:
Slenderness effect check:
Braced system. The lateral stiffness of shear walls elements
are more than 12 times the stiffness of columns.
Figure-16: Columns layout .
, ok short column.

## Slide 46
Columns :-
Longitudinal steel:-
Selected column is column-28 in second floor with section 900  400cm
Using Bresler equation, check adequacy will performed on ETABS
reinforcing design result which is 1% for column-28
Figure-17: Columns-28 forces.
Chart: Interaction-diagram C 900 x 400
| 0 | 376.8177 | 585.35770000000002 | 749.88239999999996 | 870.98310000000004 | 956.39549999999997 | 1093.8788 | 1170.1615999999999 | 938.78309999999999 | 554.11509999999998 | 0
1% | 5185.2341 | 5185.2341 | 4918.4841 | 4218.3445 | 3485.045 | 2672.3866 | 2295.9713 | 1760.9419 | 796.1186 | -227.9171 | -1340.3556
p | 5197
( ‎4.16)
= 5197 KN
Then,
Figure-18: P-M2 interaction diagram.

## Slide 47
Columns :-
Longitudinal steel:-
( ‎4.17)
Table-8: 6/5(beam/column capacity) from ETABS
Manually:
For major axis ration = 6/5  (228/836.9) = 0.326
For major axis ration = 6/5  (244.5/1885) = 0.155
Then, program calculate the ration in correct way.
ETABS:

## Slide 48
Columns :-
Shear reinforcement:-
the maximum probable moment strengths of the beams framing into the column
( ‎4.21)
( ‎4.22)
( ‎4.23)
=1, and αfy, where α is set equal to 1.25.
Figure-19 : Design shears for columns.

## Slide 49
Shear reinforcement:-
Columns :-
( ‎4.24)
( ‎4.25)
Figure-20: Column shear force from maximum probable moment in beams.

## Slide 50
Shear reinforcement:-
Columns :-
Manually:
Vu2 = = 69.2 KN
Vu3 = = 72.3 KN
ETABS:
Table-9: ETABS design result.
( ‎4.26)

## Slide 51
03 Design checks
Walls :-
Figure-22 : Wall-5 plane.
Figure-21: Walls layout.
Wall-5 dimensions:
Lw = 5 m
h = 30cm
hw = 4.2m
d with accordance to section 11.9.4 ACI318-11 = 0.8 Lw. then, d= 4m.

For out of plane shear:

## Slide 52
Walls :-
Figure-22 : Wall-5 plane.
Figure-21: Walls layout.
( ‎4.36)
For in-plane shear:
Nu for this combination will be used =2385 KN
Then,
Ratio of horizontal shear reinforcement area to gross concrete area of vertical section, t, shall not be less than 0.0025.
Then, area of horizontal steel = 0.0025  0.3  4.2 = 3150.
For vertical steel, ratio of vertical shear reinforcement area to gross concrete area of horizontal section, L, , shall not be less than 0.0025.
Then, area of vertical steel = 0.0025  0.3  5 = 3750.

## Slide 53
Chart: Wall-5 interaction diagram
| 0 | 5666.3244000000004 | 9821.5612999999994 | 12811.996999999999 | 14653.2469 | 15359.644 | 17354.867200000001 | 18082.0759 | 13846.8889 | 7851.3209999999999 | 0
0.25% | 19243.2611 | 19243.2611 | 19015.9293 | 16585.2282 | 14118.3135 | 11596.8449 | 10643.2413 | 9153.3054 | 5699.5238 | 2245.5582 | -1246.266
p | 2384
Walls :-
From program forces on the wall will be as the following:
In design M2 is too small, then neglect it.
Figure-23: W-5 interaction diagram.
Then, 0.0025 satisfied.
Table-10: ETABS design result for wall-5.
ETABS:

## Slide 54
03 Design checks
Slab:-
Slab in all floors above the ground level with thickness 23cm.
Check adequacy on slab will be as the following:
Figure-24: Shear in slab.
Vu= 110.84 KN less than 132 KN. Then, slab thickness is adequate for shear.

## Slide 55
03 Design checks
Footings :-
Figure-25: Soil pressure values Block-1.
Figure-26: Soil pressure values Block-1 second model.
Figure-27: W-5 Punching check results.

## Slide 56
Footings :-
Figure-28: Footing in Block-1. before modification
Figure-29: Footing in Block-1. after modification
Figure-30: Punching check results.

## Slide 57
Footings :-
      Wide beam shear (one-way shear):
Figure-31: V13-F1 footing.
.
Figure-32: V13-F2 footing.
Maximum value for V13 is 326.4 KN/m and allowable 371 KN.
Maximum value for V13 is 254KN/m and allowable 303.60 KN.

## Slide 58
Footings :-
      Wide beam shear (one-way shear):
Figure-33: : V13-F3 footing
Figure-34: V13-F4 footing
.
Maximum value for V13 is 395.4 KN/m and allowable 438 KN
Maximum value for V13 is 334.4 KN/m and allowable 506 KN

## Slide 59
Footings :-
      Wide beam shear (one-way shear):
Figure-35: V13 for Wall-6.
Figure-36: V13 for Combined footing.
Maximum value for V13 is 117.147 KN/m and
allowable 236.13 KN.
Maximum value for V13 is 737.3 KN/m and
allowable 769 KN

## Slide 60
Combined footing dimensions 7.5 .
Wall footing with width B = 1.45m, and thickness h = 0.35m.
Mat foundation with thickness = 0.8m, and area as shown in drawings.
Single footing
Table-11: Single footings dimensions.
Footings Final dimension :-

## Slide 61
04 Design and detailing
columns :-
Column dimension | % of longitudinal steel | No. of bars | Section name
600 X 400 | 1.00 | 1018 | C1
 | 1.25 | 1218 | C2
 | 1.7 | 1420 | C3
 | 2.7 | 1425 | C4
900 X 400 | 1.00 | 1418 | C5
 | 1.7 | 1622 | C6
 | 2.5 | 1825 | C7
Table-1: Columns sections.
Based on longitudinal steel.

## Slide 62
columns :-
Based on Transvers steel.
Then, Lo, 900mm for column 900400 and 600mm for column 600400.
6db = 6 (smallest bar diameter is 18mm) = 6  18 = 108mm
One quarter smallest dimension = 400/4 = 100mm
S < So and So shall not be less than 100mm. Then no need to calculate it.
Then, S shall not exceed 100mm.

## Slide 63
( ‎4.19)
columns :-
Based on Transvers steel.
‎(4.20)
The total cross-sectional area of rectangular hoop reinforcement, Ash,
shall not be less than required by the following equations:
Then, for column 600 mm, Ash = 528.36 mm2 . Therefore minimum No. of legs needed 2 legs 12 and 2 legs 14.
Then, for column 900 mm, Ash = 215 mm2 . Therefore minimum No. of legs needed 2 legs 12.

## Slide 64
columns :-
Figure-1: column 600 mm sections.

## Slide 65
columns :-
Figure-2: column 900 mm sections.

## Slide 66
Group one: Tie beams.
Group Two: Ground, First, and second floor beams.
04 Design and detailing
Beams :-
Group one: Tie beams.
Tie beams shall be able to resist
tension force 10% SDs from
max gravity forced on columns
Figure-3: Tie beam sections.

## Slide 67
Beams :-
Figure-4: Grid 1 beams sections detailing.
Figure-5: Grid 1 beams reinforcement .

## Slide 68
On grade slab 15cm at basement floor, will be reinforced using minimum area of steel.
Use top and bottom steel mesh in two direction with minimum steel as the following:
.
04 Design and detailing
Slabs :-
Use top and bottom steel mesh in two direction with minimum steel as the following:
. .
2)Use Extra steel at locations have moment value more than minimum moment as the following:
slab 23cm in floors above ground level:

## Slide 69
Foundation :-
Figure-6: Footing layout.

## Slide 70
04 Design and detailing
Foundation :-
Single footing, F1 type with dimension 2.2  2m,
Then, M = 405 KN.m for 2.2m. Therefore, moment per 1m,
M = 184 KN.m.
Then, flexure steel in 2.2m-direction will be .
4
Then As,

## Slide 71
Then, M = 352 KN.m for 2m. Therefore, moment per 1m,
M = 176 KN.m.
3
Then As,
Then, flexure steel in 2m-direction will be .
Foundation :-
in each direction equal /2.
Then, use .

## Slide 72
Foundation :-
Figure-7: F-1 detailing.

## Slide 73
Foundation :-
combined footing:
Figure-8: combined footing detailing.

## Slide 74
Foundation :-
Wall footing:
Figure-9: Wall footing detailing.

## Slide 75
04 Design and detailing
Wall :-
Figure-10: Design detailed for basement wallA5-A6.
For vertical reinforcement use 4612, 23 bars on each face. Then 112/16 cm.
For horizontal reinforcement two layers with 112/20 cm.

## Slide 76
Wall :-
Figure-11: Basement wall detailing.

## Slide 77
Thank you.