## Slide 1
An-Najah National University
Building Engineering Department
Re-design for the “United Motor and Trading Company” building
Presented by:
Thabet Ghanem
Ameer Najjar
Manal Khader
Qamar Barham
Supervisor:
Eng. Ala’a Shaheen

## Slide 2
Outline:
PV
Design
Environmental Design
Cost Estimation
Introduction
Site Analysis and Architectural Design
Structural
Design
Electromechanical
Design
Safety System

## Slide 3
Introduction:
Background:
Such these buildings contain:
Showrooms.
Offices.
Repair shops.

## Slide 4
Introduction:
Project problem:
Improve the design to suit needs.
Work objectives:
Integrated design.
All points taken in Project 1 are considered in the design.

## Slide 5
Site analysis and Architectural Design

## Slide 6
Site Analysis:
The building of United Motor Trade (UMT) company is located in Mahmoud Abbas Street, Beit E’iba, Nablus, Palestine.

## Slide 7
Site Analysis:
Levels | Part 1 | Part 2 | Part 3 | Part 4
Ground level | 0.00 m | 0.00 m | 0.00 m | 0.00 m
First level | 3.674 m | 7.348 m | 3.674 m | 5.511 m
Second level | 7.348 m | 14.696 m | 7.348 m | 11.022 m
Third level | 11.022 m | - | - | 16.533 m
Fourth level | 14.696 m | - | - | 21.042 m
N
N
N

## Slide 8
Site Analysis:
New Building
Existing Building
1: 1st gate.
2: 2nd gate.
3 and 5: Parking for visitors.
4: Square for displaying the cars.
6: Septic tank.
7: Water tank.
8: Parking for customers and employees.
9 and 11: Parking for employees.
10: Square for cars like cars in showrooms.
1: Entrances for pedestrian. 2: Entrances for cars. 3: Guard room. 4: Car Ramp to arrive to the body and paint shop. 5: Entrance of body and paint shop. 6: Entrance of quick services. 7: Entrance of basement. 8: Car elevator. 9: Car parking for customers and some of employees.

## Slide 9
Architectural Design:
Basement Plan at Level -3.674m
Section in Car Ramp

## Slide 10
Architectural Design:
Plan at Level 0.00m

## Slide 11
Architectural Design- Car Showrooms:
Showrooms in New Building
Showrooms in Existing Building
N
N

## Slide 12
Architectural Design- Car Showrooms:
Green color indicates that the spaces are within recommendations.
Yellow color: A space is not matched with recommendations but relatively acceptable.
Orange color: The spaces are out of recommendations and not acceptable.
VW Showroom in Existing Building
Skoda Showroom in Existing Building
N

## Slide 13
Architectural Design- Car Showrooms:
Bubble Diagram for Showrooms in New Building

## Slide 14
Architectural Design- Repair Shop:
General Repair Shop in New Building
At Level 0.00m
General Repair Shop in existing building
N
N

## Slide 15
Architectural Design –Repair Shop:
Body and Paint Shop in New Building
At Level 7.35m
Body and Paint Shop in Existing Building
N
N

## Slide 16
Architectural Design –Repair Shop:
 | General repair shop | Body and paint shop
Existing building | 13 | 9
New Building | 12 | 13

## Slide 17
Architectural Design:
Plan at Level 3.674m
N
N
N

## Slide 18
Architectural Design -Offices:
N
Plan at Level 16.35m

## Slide 19
Architectural Design:
Southern Elevation

## Slide 20
Architectural Design:
Western Elevation
Northern Elevation

## Slide 21
Architectural Design:
Eastern Elevation

## Slide 22: Structural design

## Slide 23: Structural design – Excavation & Soil supporting
Table below describe the soil properties for the project:
Sample depth | Moister content (%) | Percent passing from sieves #200 | Plasticity index | Cohesion (KN/m2) | Angle of internal friction (Փ)
0-5 | 15 | 61.5 | 10.5 | 11 | 25
5-9 | 15.45 | 71 | 14.3 |  | 
9-11 | 21.2 | 32 | 11.4 |  | 
Lc = 𝐷𝑖𝑝𝑡ℎ 𝑜𝑓 𝑒𝑥𝑐𝑎𝑣𝑎𝑡𝑖𝑜𝑛 𝑤𝑖𝑡ℎ 𝑜𝑢𝑡 𝑠𝑜𝑖𝑙 𝑠𝑢𝑝𝑝𝑜𝑟𝑡𝑖𝑛𝑔 = 1.72m.
Where bearing capacity of the soil was 254KN/m2.

## Slide 24: Structural design – Excavation & Soil supporting
Excavation level compare with the natural earth

## Slide 25: Structural design – Excavation & Soil supporting
A cantilever retaining wall was used in this project with 6m and 8m height above the ground level, where the table below describe the parameter used in the design:
Soil bearing capacity (KN/m2) | Concrete shear capacity (stem and heel) (KN/m) | Concrete shear capacity (KN) | Soil friction factor | K active | K Passive
254 | 417 | 572 | 0.4 | 0.41 | 2.46

## Slide 26
Retaining wall details L=6.5m.

## Slide 27
Retaining wall details L=10.1m.

## Slide 30: Structural design – Concrete design parameters
Columns, footing, and walls concrete compressive strength | 32MPA
Reinforcement Rebar yielding strength | 420MPA
Slabs and beams concrete compressive strength | 28MPA
R | 5.5
Z(UBC-97) | 0.2
Ca(UBC-97) | 0.24
Cv(UBC-97) | 0.32
Ci(ACI-350&IBC-15) | 0.6
Cc(ACI-350&IBC-15) | 0.14
Ct(ACI-350&IBC-15) | 0.24

## Slide 31: Structural design – Steel design parameters
Parameters | Value
Steel yielding stress | 250MPA
Steel ultimate stress | 400MPA
Sections used according to | Euro code
Z(UBC-97) | 0.2
Ca(UBC-97) | 0.24
Cv(UBC-97) | 0.32
R | 8.5

## Slide 32: Structural design – Steel material properties
Name | Type | Design Strengths
A36 Steel | Steel | Fy=250 MPa, Fu=400 MPa
E60XX | Weld | Rn=412.8 MPa
E70XX | Weld | Rn=481.6 MPa
E120XX | Weld | Rn=825.6MPa
A325 | Bolts | Ft=620Ab MPa, Fv= MP414Aba
A490 | Bolts | Ft=780Ab MPa, Fv=520Ab MPa

## Slide 33: Structural design – Steel sections used
Section type | Section shape | depth | width | Flanges thickness | Web thickness
Columns | TUBO | 550mm | 550mm | 20mm | -
Main beams | IPE 750*173 | 760mm | 268mm | 21.6mm | 14.4mm
Beam on girder | ILS 550 | 547mm | 210mm | 15.7mm | 9mm
joist (L>3m) | HE260A | 250mm | 260mm | 12.5mm | 7.5mm
Cantilever joist | ILS 550 | 547mm | 210mm | 15.7mm | 7.5mm

## Slide 34: Structural design – Steel structure design
All the car show rooms was designed as a steel structure design because of it is curved shape in the two direction in as well as getting a long spans for facilitate the cars movement.

## Slide 35: Structural design – Steel structure design

## Slide 36: Structural design – Steel structure design

## Slide 37: Structural design – Steel structure design

## Slide 38: Structural design – Steel structure design

## Slide 39: Structural design – Steel structure design

## Slide 40: Structural design – Steel structure design

## Slide 41: Structural design – Steel structure design

## Slide 42: Structural design – Steel structure design

## Slide 43: Structural design – Steel structure design

## Slide 44: Structural design – Steel structure design

## Slide 45: Structural design – Steel structure design

## Slide 46: Structural design – Concrete structural design

## Slide 47: Structural design – Foundation design
A single, combined and wall footing was used in this project:

## Slide 48
Footing layout for part one of the project

## Slide 49
Footing one details.

## Slide 50
Footing layout for part two of the project:

## Slide 51
Section A-A details.

## Slide 52
Tie beam plane for the second part

## Slide 53
Section H-H detail

## Slide 54: Structural design – Columns design

## Slide 55
Part three columns layout.
Part four columns layout.

## Slide 57
Part one columns layout.

## Slide 59: Structural design – Columns design
All columns details was described in the drawing sheet

## Slide 60: Structural design – Shear wall design

## Slide 61
Part two shear wall layout.

## Slide 63: Structural design – Slabs design

## Slide 64: Structural design – Slabs design
Three type of columns systems were used as bellow:
1. Solid slab system was used where heavy live load was existed (cars work shops, cars show rooms, green areas and water tank storage).
2. Tow way ribbed slab system was used where normal live load was existed and spans more than 5m up to 7.5m and one way ribbed slabs were used for the spans which it is length less than 5m.(offices floor, wettings areas and stair case)
3. Waffle slab system was used where the span length more than 8m up to 12m.(basement floor).

## Slide 65: Structural design – Slabs design
Slab reinforcement for part two of the project

## Slide 66: Structural design – Slabs design

## Slide 67: Structural design – Slabs design

## Slide 68: Structural design – Slabs design

## Slide 69: Structural design – Slabs design
Beam layout for part one of the project

## Slide 70: Structural design – Slabs design
Section A-A

## Slide 71: Structural design – Slabs design 2B1 beam detail

## Slide 72: Structural design – Slabs design

## Slide 73: Structural design – Slabs design

## Slide 74: Structural design – Slabs design

## Slide 75: Structural design – Slabs design

## Slide 76: Structural design – Stair detail

## Slide 77: Structural design – Water tank design parameters used in the design of water tank.
Ci | I | Ri | K active | Cc | I | Rc
0.6 | 1.25 | 2 | 0.406 | 0.134242 | 1.25 | 1
kae | Ct | B | Ri | qny | Hi large | Hc large
0.406 | 0.24 | 1 | 2 | 75 | 3.3m | 5.9m

## Slide 78
Water tank footing plan

## Slide 79
Section A-A

## Slide 80
Section D-D

## Slide 81
Environmental Evaluation.

## Slide 82
ENVIRONMENTAL DESIGN
-Lighting Evaluation.
-Thermal Evaluation.
-Acoustical Evaluation.

## Slide 83
ENVIRONMENTAL DESIGN
Natural lighting
Evaluation day lighting for show room part using Design builder:
The amount of natural lighting is largely concentrated inside the showroom part because the facade is covered with glass

## Slide 84
ENVIRONMENTAL DESIGN
Natural lighting
Evaluation day lighting for office part
In the offices part, natural light is large around the counter

## Slide 85
ENVIRONMENTAL DESIGN
Natural lighting
Evaluation day lighting for repair shop part
the repair shop daylight is relatively low because the glass area compared with walls area is low

## Slide 86
ENVIRONMENTAL DESIGN
Heating Analysis
the operating temperature is 17.03 ° C which is good temperature for the office zone
Temperatures for offices part

## Slide 87
ENVIRONMENTAL DESIGN
Heating Analysis
the operating temperature is 15.03 ° C.
Temperatures for showroom part

## Slide 88
ENVIRONMENTAL DESIGN
Simulation
The simulation and total energy consumption for showroom part

## Slide 89
ENVIRONMENTAL DESIGN
Simulation
The simulation and total energy consumption for offices part
The total energy consumption for building equal 297748KWh

## Slide 90
ENVIRONMENTAL DESIGN
Simulation
Hour comfort in offices part
Hour comfort in showrooms part.

## Slide 91
ENVIRONMENTAL DESIGN
Acoustical Evaluation
RT60:
Values calculated from Ecotect program:
The reverberation time for the show room is equal .75 Sabine which is less than the standard that is 1-1.4 due to the huge area of the room.

## Slide 92
ENVIRONMENTAL DESIGN
Acoustical Evaluation
RT60:
Values calculated from Ecotect program:
The reverberation time for the office room is equal .56 Sabine within the standard 0.5-1.5

## Slide 93
ENVIRONMENTAL DESIGN
Acoustical Evaluation
RT60:
Values calculated from Ecotect program:
The reverberation time for the repairing room is equal 1.13 Sabine within the standard 1-1.5

## Slide 94
ENVIRONMENTAL DESIGN
external walls which must have a value of STC not less than 50dB to have a good sound proofing
In our project, the values of STC for exterior walls have a ranged from 50 to 75 and all of them within the standard
insulation design
Layers | Width (mm)
Stone | 50
Concrete cast-dense | 80
Lightweight Hollow Block | 70
Foam-polyurethane | 50
Concrete block - block hollow | 70
Plaster | 15
U-Value = 0.4 w/m^2.k
STC-Value = 57 dB
For external walls

## Slide 95
ENVIRONMENTAL DESIGN
For partition between adjacencies offices the values of STC should be equal 52 db or more and our values within the standard
insulation design
Layers | Width (mm)
Plaster | 15
Lightweight Block, hollow | 100
Plaster | 15
STC-Value = 54 dB
U-Value = 0.37 w/m^2.k
Notes: Layers
Width (cm)
Conductivity
Plaster
2
0.43
Lightweight Block, Perlite-Filled
10
0.17
Plaster
2
0.43

## Slide 96
ENVIRONMENTAL DESIGN
-Using VAV system.
-Using VRF system
-Main components of centralized system are:
  Outdoor unit.
  Inside unit (fan coil)
  Collectors
  Ducts.
  Diffusers.
  Grills.
HVAC System.
Notes: Layers
Width (cm)
Conductivity
Plaster
2
0.43
Lightweight Block, Perlite-Filled
10
0.17
Plaster
2
0.43

## Slide 97
ENVIRONMENTAL DESIGN
HVAC System.
Figure show the distribution of HVAC system
Notes: Layers
Width (cm)
Conductivity
Plaster
2
0.43
Lightweight Block, Perlite-Filled
10
0.17
Plaster
2
0.43

## Slide 98
Electromechanical
Design

## Slide 99
Electromechanical design-Lighting:
Basement :
 | Actual value | Recommend value
Illuminance (lux) | 566 | 500-700
Glare at 120cm | 15.3 | < 22
Uniformity | 0.65 | > 0.33
DIAlux analyses result and recommend values.

## Slide 100
Electromechanical design-Lighting:

## Slide 101
Electromechanical design-Lighting:
Skoda Showroom:
DIAlux analyses result and recommend values.
in room | Actual value | Recommend value
Illuminance (lux) | 570 | 500-1000
Glare | 14 | < 22
Uniformity | 0.47 | > 0.33

## Slide 102
Electromechanical design-Lighting:
Office room :
DIALux analyses result and the recommend values:
 | Actual value | Recommend value
Illuminance (lux) | 280 | 200-350
Glare | 12 | < 22
Uniformity | 0.47 | > 0.25

## Slide 103
Electromechanical design-Lighting:

## Slide 104
Electromechanical design-Lighting:
Wokstation Car :
DIALux analyses result and the recommend values .
 | Actual value | Recommend value
Illuminance (lux) | 518 | 500
Glare | 16.5 | < 19
Uniformity | 0.48 | > 0.6

## Slide 105
Electromechanical desgin-Lighting:

## Slide 106
Electromechanical design-Lighting:
Kitchen small:
DIALUX analyses result and the recommend values .
 | Actual value | Recommend value
Illuminance (lux) | 440 | 300-500
Glare | 10 | < 22
Uniformity | 0.65 | > 0.33

## Slide 107
Electromechanical design-Lighting:

## Slide 108
Electromechanical design-Water Supply:
Distributed water supply for ground floor .

## Slide 109
Electromechanical design-Water Supply:
Distributed water supply for zone 1 .
 | Ground floor |  | First floor |  | Second floor | 
 | Diameter (in) | Losses (psi) | Diameter (in) | Losses (psi) | Diameter (in) | Losses (psi)
Horizontal Pipes | 1.5" | 4 | 1.25" | 3.7 | 1.25" | 4.3
Branch Pipes | 0.75" | 4.9 | 0.75" | 5.1 | 1" | 4.2
Meters | 0.75" | 1.8 | 0.75" | 2 | 0.75" | 2.1
Total losses | - | 10.7 | - | 10.8 | - | 10.6
Allows losses | - | 11 psi | - | 11 psi | - | 11 psi
Assesment |  | OK |  | OK |  | OK

## Slide 110
Electromechanical design-Water Supply:
Distributed water supply for zone 3 .
 | Ground floor |  | First floor |  |  | Secondfloor |  |  | Third floor |  | 
 | Diameter (in) | Losses (psi) |  | Diameter (in) | Losses (psi) | Diameter (in) |  | Losses (psi) |  | Diameter (in) | Losses (psi)
Horizontal Pipes | 3/4" | 2.25 | 1.25" |  | 3.6 | 1.25" |  | 3.8 |  | 3/4" | 5.2
Vertical Pipes | 1.5" | 5 | 1.5" |  | 2.7 | 1.5" |  | 4.3 |  | 1" | 3.4
Branch Pipes | 0.75" | 1.98 | 0.75" |  | 2.1 | 2" |  | 2.5 |  | 1.25" | 2.1
Total losses | - | 9.23 | - |  | 8.4 | - |  | 10.6 |  | - | 10.8
Allows losses | - | 11 psi | - |  | 11 psi | - |  | 11 psi |  | - | 11psi
Assesment |  | OK |  |  | OK |  |  | OK |  |  | OK

## Slide 111
Electromechanical design-Water Supply:
Distributed water supply for zone2 .
 | Ground floor |  | First floor | 
 | Diameter (in) | Losses (psi) | Diameter (in) | Losses (psi)
Horizontal Pipes | 1.5" | 4.08 | 1.75" | 3.7
Vertical Pipes | 1.25" | 5 | 2" | 5.1
Branch Pipes | 0.75" | 1.6 | 1" | 2.2
Total losses | - | 10.68 | - | 11
Allows losses | - | 11 psi | - | 11 psi
Assesment |  | OK |  | OK

## Slide 112
Electromechanical design- Drainge Water:
Distributed drainge water for ground floor .

## Slide 113
Electromechanical design - Draing Water:
Details :

## Slide 114
Electromechanical design- Drainge Water:
Details workstation in GF .

## Slide 115
Electromechanical design-Elevators:
The result is 3 elevators with capacity 1750 lb with 450 fpm + 1 elevator for service .

## Slide 116
Electromechanical design -Power system:
The power design socket for ground floor :

## Slide 117
Electromechanical design-Power system:
The Office :
The Multipurpose :

## Slide 118
Electromechanical design -Fire system:
Fire fighting system:
In this building several types of fire extinguishing system were used in electrical room (FM-200) and hall cars (sprinkler water) and offices extinguisher foam .

## Slide 119
Electromechanical design -Fire system:
Distribution sprinkler in ground floor:

## Slide 120
Electromechanical design -Fire system:
Fire alarm system :
Manual system
Smoke detectores

## Slide 121
Electromechanical – Q.C:
Table Quantity survey and cost:

## Slide 122
Electromechanical – Q.C:
Table Quantity survey and cost:

## Slide 123
Cost Estimation:
Total Cost (NIS) | 17,523,319
Unit Cost (NIS/m2) | 1815.89

## Slide 124
PV Design:
The maximum project production is 145Kw.
The constant energy saved per year = 247.6 Mwh/year.
The capital cost for system = 217,500$ = 761,250 NIS (Dollar = 3.5 NIS).
The cost is returned through 4.78 year.
The constant annual cost saved from energy = 183,000 NIS.