## Slide 1
Faculty of engineering
Civil engineering
Project name:
House building
Prepared by:
asim salameh mohammad

## Slide 2
house building" is to be constructed in ramallah. It consists of four floor , the area of floor is 250m².
The structural elements are designed by manual (theoretical) then apply verification by sap.
Abstract

## Slide 3
Abstract

## Slide 4
: Design objectives
The designed structure should sustain all loads and deformation within limits for construction use, and should be durable.
Design stages:
In this project, house building will be designed as static design.
considering gravity loads: live and dead loads and lateral loads from soil
design based on scientific knowledge.
On the other hand, in this structure we use hand calculations and compared with sap calculations.
Chapter One: Introduction

## Slide 5
Use a- bearing capacity of (4kg/cm²) is considered from visiting to the site and show the excavating and assessing the value of (q) .
Structural concept:
one-way ribbed slab system in the floors : this system is used because no heavy loads in the floor .Slab thickness of (25cm), blocks of (17cm) height and (40cm) width will be used, the web width is (12cm), and the flange thickness is (8cm).
Project Description:

## Slide 6
Architecture description:
The building consists four floor , the ground floor including on basement wall and shear wall ,the shear wall remaining in the other floor , the area of each floor near 150 m2
Project Description:

## Slide 7
Unit weight of R.C= 25 KN/m³.
(fʹc)= 24MPa.
Ec = 23025 Mpa.
Yielding stress (Fy) = 420 Mpa.
Modulus of elasticity (Es) = 200GPa.
floor height=3.2m.
S.E.D=4Kn/ m2.
weight of parameter (masonry)wall=19.7kn/m2
Construction materials:

## Slide 8
the following methods and codes are used for design:
American Concrete institute (ACI-2008).
2.Ultimate strength method.
Codes and design methods :

## Slide 9
Vertical loads:
Dead loads:including the weight of the structural elements, (such as slabs, beams, columns, and foundations), and super imposed dead loads (SDL) .
Live loads: (LL) is considered to be (2.5KN\m2) because this building is house building .
Loadings:

## Slide 10
horizontal loads:
Soil load : Soil load includes the soil pressure due to the soil on the basement walls.
Load combinations : we use in this design two combination
Wu= 1.2D.L+ 1.6L.L
Wu=1.2D.L+1.6L+1.6soil
Loadings:

## Slide 11
Loadings:

## Slide 12
Loadings:

## Slide 13
Theoretical calculations:Dead Loads
Area of floor =11.95*12.10=145m2
Total dead load on slab =580+84.923+688.75=1354kn
DL from column=134.4kn
DL from masonry =947.6kn
Dl from staircase shear walls=290.4kn
Dl from basement walls=290.4kn
∑Dl(final)= 3016.8 KN
Live Loads:Live load=2.5KN\m²
=2.5*145=361.5kn
∑LL=361.5kn
Sap calculations:
dead load=2963 KN and live load=361.5 KN
The percentage of dead load error=(1.78%)<(5%) ok
The percentage of live load error = (0%)<(5%) ok
Check of equilibrium

## Slide 14
One way ribbed slab :
Preliminary design:

## Slide 15
One way ribbed slab :
Design of slab:

## Slide 16
One way ribbed slab :
Use slab thickness h=25cm
Use concrete blocks of 40*20*17cm.
Dimension of ribbed slab = 25*52 cm.
Width of rib = 12 cm. f′c= 24 mpa.
Fy = 420 mpa
Wdslab =2.37KN\m.=2.37/0.52=4.55kn/m2.
Total S.E.D.=2.88+1.125=4kn/m2
Wd=4.55+4=8.55 KN\m2
WL=2.5KN\m2
Wu=1.2*8.55+1.6*2.5=14.26KN\m2
Wu=14.26*0.52=7.42KN\m
Considering the cover to be 3 cm
d=22cm
Design of slab:

## Slide 17
One way ribbed slab :
Max.negative moment=4.05 KN.m
p =1.87e-3<<pmin=0.0033
use p=0.00333
As=0.0033*120*220=88 mm2.
As=2ø10(top)
Max.positive moment=2.8KN.m
P =1.42e-3<<pmin=0.0033
use p=0.00333
As=0.0033*120*220=88 mm2
As=2ø10(bottom)
Design of slab:
Use slab thickness h=25cm
Use slab thickness h=25cm
Use slab thickness h=25cm

## Slide 18
Check of shear:Max.Vu
Vu=1*Wu*Ln\2=1*7.42*2.45\2=9.1 KN
øVc=(1.1*0.75*(1\6)*120*220*√24)\1000=17.8 KN
Vu< øVc(no need for stirrup)
As shrinkage=0.0018*1000*80=144mm2\m
Max.spacing=min(5h or 30cm)=(40 or 30)cm
As(shrinkage) =1ø8\30cm
Design of slab:

## Slide 19
Design of slab:

## Slide 20
Design of beams:

## Slide 21
Design of beams:

## Slide 22
From table 9.5(a):
hmin = Ln\18.5 = 4.2/18.5 =23 cm
use h=25cm
beams (1,2,3,4,5,6 and 7)→use h=25cm ,b=70cm.
beam (a and f)→use h=25cm ,b=40cm.
Wu on slab=14.26 KN\m2.
weight of parameter (masonry)wall=19.7kn/m2
Design of beams:

## Slide 23
Design of beams:

## Slide 24
For beam # 1:
H=25cm b=70 cm
Own weight=4.375KN\m
Wu =47.6 KN\m
Max.positive moment= Wu*Ln2\14=60 KN.m
p=0.00493 As=758.8mm2 use4ø16
Pmin=0.00333<0.00493
Max.negative moment= Wu*Ln2\10= 84 KN.m
p=0.00706 Pmin=0.00333<0.00706
As=1087.45mm2 As=6ø16
Design of beams:

## Slide 25
:Sap results
Max top area of steel =1009mm2(sap)
%error(top steel)=((1009-1087.48)\1087.48)=7%
Max bottom area of steel =781mm2(sap)
%error(top steel)=((781-759)\759)=3%
Design of beams:

## Slide 26
For beam # 2:
H=25cm b=70 cm
Own weight=4.375KN\m
Wu =37.5 KN\m
Max.positive moment= Wu*Ln2\14=47.3 KN.m
Max.negative moment= Wu*Ln2\10= 66.2 KN.m
p=0.0055 Pmin=0.00333<0.0055
As=842mm2 As=5ø16 or 6ø14
For beam F:
weight of parameter (masonry)wall=19.7kn/m2.
H=25cm b=40 cm
Own weight=2.5KN\m Wu=31.1 KN\m
Max.+Ve moment=12.6kn.m
Max.negative moment=18.4kn.m
As=3ø12
Design of beams:

## Slide 27
Check for shear:
for beam 1:
Wu=47.6kn/m
Max. Vu = 1.15Wu*Ln\2= 115 KN.m
øVc=0.75*(1\6)*700*220*√24=94.3 KN
Vu at d= Vu-Wu*d = 104.5 KN
, check if Vs<(2/3)(fc^0.5)bw <502kn the cross section is large enough
Vs≤ (1/3)bw d≤251.5kn
VS=Vn-Vc=13.67 Kn
Smax.= min. ( d/2 , 60cm )
= min(110,600)
=110mm
assume d=8mm
Av=2*лd²/4=100.53
s≤679.5mm
Use s =11 cm. Av\s=1ø8\17.5cm
Design of beams:

## Slide 28: Design footing:
we choose critical footing to design it and check dimensions in this stare we design the footing to tolerate the load from four roof:
Pd=497kn.
LL=126.04KN.
ult.=797.9kn.
footing area=Pactual/q=(496.9+129.04)/400=1.565m².
square footing=B*L=1.25*1.25m
assume L=1.5m. b=1.2

## Slide 29: Design footing:

## Slide 30
ΦVc=263.3kn pu=828.544kn.
qu=Pu/Af=828.544/1.8=460.3kn/m.
Vu=qu*(L-d)=246.3kn<263.3kn.
vup=Pu-quA ̥=529.32kn
ΦVcp=1939kn>529.32kn. Ok
From sap:
desplacement=0.0073m<0.01m ok.
Design footing:

## Slide 31
M11:moment in x direction =61 KN.M
p =7.32*e-4
use Pmin=0.0018
Use As= 6Φ14
Design footing:

## Slide 32
M22 moment in Y direction =94 KN.M
p =9*e-4
use Pmin=0.0018
use 8Φ14
Design footing:

## Slide 33: Basement wall:

## Slide 34: Basement wall:

## Slide 36: design for flexure:
Bottom steel in Y direction
m22=moment for footing in y direction =1291kn.m
p =1.6e-3=0.0016<pmin=0.0018
bottom of As/m=Pbd=0.0018*1000*430=774 mm² use 1Φ14/20cm.
Top steel in Y direction:
use Pmin=0.0018
As/m=Pbd=0.0018*1000*430=774 mm²
use 1Φ14/20cm.in top.
in X direction use As min.
use 1Φ14/20cm.
.

## Slide 37
Steel in the wall in Z direction:
d=210mm. M=1635.2kn.m
p =8.993e-3=0.009>pmin=0.0033
use P=0.009
use 1Φ16/11cm.
As at support at z=3.5m→use As(min)
1Φ14/25cm but I want use 1Φ14/20cm.
For positive moment :
Mu=552kn.m use 1Φ14/25cm.
Steel in the wall in X direction:
Mu=72kn.m d=210mm b=3000mm.
p =1.45e-3=0.0016<pmin=0.0033
use 1Φ14/25cm.
Basement wall:

## Slide 38
.
Thank you