## Slide 1
AN-Najah National University
Faculty of Engineering & Information Technology
Building Engineering Department
Graduation Project – II
Redesign Al-Nabali and Al-Fairs residential building
Prepared by:
Bara Raed Faqeeh
Asmaa Kokash
Shahd Hijab
Rakan Ayyoub
Supervised by:
Eng. Alaa Shaheen

## Slide 2: TABLE OF CONTENTS 02 03 05 06 Enviromental Aspects 01 Quantity Survaying and Cost Estimation Introduction Structural Aspects 04 Architectural Aspects Eloctro-Mechanical Aspects

## Slide 3: Introduction
Project Description
Methodology
Project Location
Redesign Al-Nabali and Al-Fairs residential building

## Slide 4: Introduction – Project Description
In this graduation project, a public library consisting of residential building with a total area of 4539.57 square meters was analyzed and re-designed.

## Slide 5: Introduction – Site Location
The project is located in the center of Ramallah
The project is situated on Khalil Al-Sakakini Street is located just 160 meters from the Ramallah Municipality.
The site is located in a classification area B
The Al-Nabali and Al-Faris residential building features a strategic location close to public services and amenities in the heart of the Al-Nuzha neighborhood, making it an ideal choice for residence.

## Slide 6: Introduction - Methodology

## Slide 7: Architectural Aspects
Site Analysis
Architectural Plans
Rendered Shots

## Slide 8: Site Analysis – Environmental Effect
Wind Direction
Noise Sources
Sun Path

## Slide 9: Architectural Aspects – Architectural Modifications
1. Parking Modifications
CELLAR2 FLOOR
Before Modifications
CELLAR1 FLOOR
Before Modifications

## Slide 10: Architectural Aspects – Architectural Modifications
1. Parking Modifications
After Modifications
CELLAR1 FLOOR

## Slide 11: Architectural Aspects – Architectural Modifications
2. Basement Floor Modifications
Before Modifications
After Modifications

## Slide 12: Architectural Aspects – Architectural Modifications
Before Modifications
After Modifications
3. Ground Floor Modifications

## Slide 13: Architectural Aspects – Architectural Modifications
Before Modifications
After Modifications
4. Roof Floor Modifications

## Slide 14: Architectural Aspects – Architectural Modifications
5. Site Plan

## Slide 15: Architectural Aspects – Elevations
SOUTHWEASTERN ELEVATION
NORTHWESTERN ELEVATION

## Slide 16: Architectural Aspects – Elevations
NORTHWESTERN ELEVATION
SOUTHWESTERN ELEVATION

## Slide 17: Architectural Aspects – Sections
Section A-A
Section B-B

## Slide 18: Architectural Aspects – Rendered Views

## Slide 19: Environmental Aspects
Design Builder Simulation and Results
Daylight Factor Analysis
Shading System
Heating & Cooling load

## Slide 20: Environmental Aspects– Daylight Factor
Modifications
We put insulation in the external wall and roof slab.
Added louvers in each of the glass on east and west elevation with 45 °angles.
Added Cantilever on south elevation to prevent glare.

## Slide 21: Environmental Aspects– Daylight Factor
Daylight Factor Analysis Basement Floor Plans
Before Modifications
After Modifications

## Slide 22: Environmental Aspects– Daylight Factor
Daylight Factor Analysis all 5th floor Plans
Before Modifications
After Modifications

## Slide 23: Environmental Aspects – Shading Analysis
Shading in summer
At 8:00 am
At 3:00 pm
At 12:00 pm

## Slide 24: Environmental Aspects – Shading Analysis
Shading in Winter
At 8:00 am
At 3:00 pm
At 12:00 pm

## Slide 25: Environmental Aspects– Design Builder Analysis and Results
Wall Layers
Wall Section U-Value
Design Builder Simulation Analysis

## Slide 26: Environmental Aspects– Design Builder Analysis and Results
Roof Layers
Roof Section -Value

## Slide 27: Environmental Aspects– Design Builder Analysis and Results
Window Definition
Glass U-Value
Window Section

## Slide 28: Environmental Aspects– Design Builder Analysis and Results
Design Builder Simulation Results

## Slide 29: Environmental Aspects– Design Builder Analysis and Results
Energy Baseline Comparison
Predicted Mean Value

## Slide 30: Environmental Aspects– Design Builder Analysis and Results
The total design cooling capacity for the building equal 172.38 KW
 | Design Capacity (kW) | Design Flow Rate (m3/s)
Total for one floor | 28.7 | 2.14
Total for all floors | 172.4 | 12.84
The total design heating capacity for the building equal 131.4 KW
 | Design Capacity (kW)
Total for one floor | 21.9
Total for all floors | 131.4

## Slide 31: Structural Aspects
Preliminary Checks
Seismic Checks
Design Details

## Slide 32: Structural Aspects – Structural System
The following specific codes were used in the structural design:
ACI318-14 for reinforced concrete structural design
ASCE 7 2010 for loads and combinations.
UBC-97 for seismic design.
ACI 350 For septic tank design.

## Slide 33: Structural Aspects – Design Data
Concrete - () = 28 MPa.
Steel - (Fy) = 420 Mpa
Soil Bearing Capacity= 200kN/m2
Dead load
Superimposed Loads (SID) = 4.50 kN/m2
Live Loads = 2 kN/m2
Wall load = 20kN/m
Design Data
Materials
Loads

## Slide 34: Structural Aspects – Design Data
Columns centers

## Slide 35: Structural Aspects – Design Data
Beams

## Slide 36: Structural Aspects – Design Data
Beams | Thickness, mm | Width, mm
B1 | 650 | 400
B2 | 650 | 400
B3 | 650 | 400
B4 | 650 | 400
B5 | 650 | 400
B6 | 650 | 400
B7 | 650 | 400
B8 | 650 | 400
Walls | Thickness, m | Height, m
For Stair | 0.25 | 27.10
For elevator | 0.25 | 27.10
For emergency stair | 0.30 | 27.10
internal shear wall | 0.40 | 23.60
retaining wall | 0.25 | 2.60
Slabs | Type | Area, m2 | thickness, m
Parking ceiling | Voided slab | 774.84 | 0.38
Residential floor ceiling | Voided slab | 478.93 | 0.38
Stair Slab | solid slab | 13.76 | 0.25
Elevator slab | solid slab | 10.22 | 0.25
Emergency ceiling | solid slab | 18.56 | 0.25
Preliminary dimensions of the Slabs
Preliminary dimensions of the Walls
Preliminary dimensions of the Beams
Columns | Number | Width, mm | Depth, mm
C1 | 2 | 600 | 1200
C2 | 3 | 500 | 1200
C3 | 2 | 500 | 1000
Preliminary dimensions of the column

## Slide 37: Structural Aspects – Design Data
for large span (Ln) = 10m.
solid slab thickness = Ln/33 = 10/33=0.303m.
equivalent Flat voided slab thickness = 0.303*1.10=0.33m, take 38cm.
Slab Thickness

## Slide 38: Structural Aspects – Structural Checks
Compatibility Check
This check is performed to ensure that all elements are interconnected and moving together (They move as one group). OK

## Slide 39: Structural Aspects – Structural Checks
Equilibrium Check
Result from ETABS

## Slide 40: Structural Aspects – Structural Checks
Slab | Area, m2 | Open's area m2 | Total area, m2 | LL (kN/m2) | Total LL, kN
Slab1 | 774.84 | 34.66 | 740.18 | 2 | 1480.37
Slab 2 | 478.93 | 34.66 | 444.27 | 2 | 888.55
Slab 3 | 478.93 | 34.66 | 444.27 | 2 | 888.55
Slab 4 | 478.93 | 34.66 | 444.27 | 2 | 888.55
Slab 5 | 478.93 | 34.66 | 444.27 | 2 | 888.55
Slab 6 | 478.93 | 34.66 | 444.27 | 2 | 888.55
Slab 7 | 478.93 | 34.66 | 444.27 | 2 | 888.55
Solid 1 | 13.76 | 0 | 13.76 | 2 | 27.52
Solid 2 | 18.56 | 0 | 18.56 | 2 | 37.12
Solid 3 | 10.22 | 0 | 10.22 | 2 | 20.44
 |  | Summation of Live Load, kN |  |  | 6896.74
Results | ETABS | Manual | Error% | Comment
Live load, kN | 6885.882 | 6896.74 | 0.157 | OK
Live load manual
Result of live load and error
Manual Live load calculation

## Slide 41: Structural Aspects – Structural Checks
Walls | Parameter, m | # Of floors | Load, kN/m | Total load, kN
 | 71.91 | 7 | 20 | 10067.4
Manual SID load calculations for walls
Slab | Area, m2 | Open's area m2 | Total area, m2 | SID (kN/m2) | Total SID
Slab1 | 774.84 | 34.66 | 740.18 | 4.5 | 3330.83
Slab 2 | 478.93 | 34.66 | 444.27 | 4.5 | 1999.23
Slab 3 | 478.93 | 34.66 | 444.27 | 4.5 | 1999.23
Slab 4 | 478.93 | 34.66 | 444.27 | 4.5 | 1999.23
Slab 5 | 478.93 | 34.66 | 444.27 | 4.5 | 1999.23
Slab 6 | 478.93 | 34.66 | 444.27 | 4.5 | 1999.23
Slab 7 | 478.93 | 34.66 | 444.27 | 4.5 | 1999.23
Solid 1 | 13.76 | 0 | 13.76 | 4.5 | 61.92
Solid 2 | 18.56 | 0 | 18.56 | 4.5 | 83.52
Solid 3 | 10.22 | 0 | 10.22 | 4.5 | 45.99
 |  | Summation of SID on slabs, kN |  |  | 15517.66
Manual SID load calculations for slabs
SID manual
ETABS | Manual | Error
25561.03 | 25585.06 | 0.094
Result of SID and error

## Slide 42: Structural Aspects – Structural Checks
Dead Load Manual
Column | # Of columns | Length, m | Width, m | height, m |  | Weight, kN
C1(120*60) | 2 | 1.2 | 0.6 | 23.6 | 25 | 849.6
C2(120*50) | 3 | 1.2 | 0.5 | 23.6 | 25 | 1062
C5(100*50) | 2 | 1 | 0.5 | 23.6 | 25 | 590
 |  |  |  | Total columns weight, kN |  | 2501.6
Column | # Of columns | Length, m | Width, m | height, m |  | Weight, kN
C1(120*60) | 2 | 1.2 | 0.6 | 23.6 | 25 | 849.6
C2(120*50) | 3 | 1.2 | 0.5 | 23.6 | 25 | 1062
C5(100*50) | 2 | 1 | 0.5 | 23.6 | 25 | 590
 |  |  |  | Total columns weight, kN |  | 2501.6
Beams | # Of floors | Length, m | Width, m | height, m |  | Weight, kN
Main beams 1 | 7 | 71.91 | 0.4 | 0.65 | 25 | 3271.905
Main beams 2 | 1 | 27.65 | 0.4 | 0.5 | 25 | 138.25
 |  |  |  | Total Beams weight, kN |  | 3410.155
Beams | # Of floors | Length, m | Width, m | height, m |  | Weight, kN
Main beams 1 | 7 | 71.91 | 0.4 | 0.65 | 25 | 3271.905
Main beams 2 | 1 | 27.65 | 0.4 | 0.5 | 25 | 138.25
 |  |  |  | Total Beams weight, kN |  | 3410.155
Manual dead load calculation for columns
Manual dead load calculation for Beams

## Slide 43: Structural Aspects – Structural Checks
Dead Load Manual
Shear walls | Height, m | length, m | width, m |  | weight, kN
Wall 1 | 23.6 | 7.4 | 0.4 | 25 | 1746.40
Wall 2 | 27.1 | 17.45 | 0.25 | 25 | 2955.59
Wall 3 | 27.1 | 22.45 | 0.3 | 25 | 4562.96
Wall 4 | 2.6 | 126.88 | 0.25 | 25 | 2061.80
 |  | Total weight of shear walls, kN |  |  | 11326.76
Shear walls | Height, m | length, m | width, m |  | weight, kN
Wall 1 | 23.6 | 7.4 | 0.4 | 25 | 1746.40
Wall 2 | 27.1 | 17.45 | 0.25 | 25 | 2955.59
Wall 3 | 27.1 | 22.45 | 0.3 | 25 | 4562.96
Wall 4 | 2.6 | 126.88 | 0.25 | 25 | 2061.80
 |  | Total weight of shear walls, kN |  |  | 11326.76
Manual dead load calculation for Walls
Slabs Weight

## Slide 44: Structural Aspects – Structural Checks
Dead Load Manual
Slab | Area, m2 | Open's area m2 | Total area, m2 | DL (kN/m2) | Total DL
Slab1 | 774.84 | 34.66 | 740.18 | 6 | 4649.06
Slab 2 | 478.93 | 34.66 | 444.27 | 6 | 2873.60
Slab 3 | 478.93 | 34.66 | 444.27 | 6 | 2873.60
Slab 4 | 478.93 | 34.66 | 444.27 | 6 | 2873.60
Slab 5 | 478.93 | 34.66 | 444.27 | 6 | 2873.60
Slab 6 | 478.93 | 34.66 | 444.27 | 6 | 2873.60
Slab 7 | 478.93 | 34.66 | 444.27 | 6 | 2873.60
Solid 1 | 13.76 | 0 | 13.76 | 6.25 | 86.00
Solid 2 | 18.56 | 0 | 18.56 | 6.25 | 116.00
Solid 3 | 10.22 | 0 | 10.22 | 6.25 | 63.88
 |  | Summation of SID on slabs, kN |  |  | 22156.56
Results | ETABS | Manual | Error | Comment
Dead load, kN | 39439.89 | 39395.75 | 0.11 | OK
Result of Dead load and error
Manual dead load calculation for Slabs

## Slide 45: Structural Aspects – Structural Checks
Stress-Strain Check – Columns
For column (From LL)
From ETAB'S = 377.88kN.
Manual = (44.08 * 1 * 2) + (24.42 * 6 * 2) = 381.20kN.

## Slide 46: Structural Aspects – Structural Checks
Stress-Strain Check – Columns
For column (From LL)
Results | ETABS, kN | Manual, kN | Differences % | Comment
 | 377.88 | 381.20 | 0.87 | OK
Result for columns and differences

## Slide 47: Structural Aspects – Structural Checks
Stress-Strain Check – Beams
For Beam (From 1.2DL+1.6LL)
Load transferee |  | Manual Beams load | Result | Unit | Moment | Unit
Wu from slab |  | 1.2 (6+4.5) +1.6(2) *4.45 | 70.31 | kN/m | 342.89 | kN.m
Wu from self-weight |  | 0.40*0.65*25*1.2 | 7.80 | kN/m | 57.06 | kN.m
Wu from wall |  | 1.2*20 | 24.00 | kN/m | 175.57 | kN.m
 |  |  | Total moment |  | 575.52 | kN.m

## Slide 48: Structural Aspects – Structural Checks
Moment From ETAB'S |  | Unit
M1(-) | -286.39 | kN.m
M2(-) | -236.5 | kN.m
M3(+) | 124.24 | kN.m
Total moment | 529.42 | kN.m
Result | From ETAB'S, kN.m | From Manual, kN.m | %Difference | Comment
 | 529.42 | 575.52 | 8.01 | OK

## Slide 49: Structural Aspects – Structural Checks
Deflection Checks
Deflection from dead load
Deflection from SID load
Deflection from Live load

## Slide 50: Structural Aspects – Structural Checks
Deflection Checks
L(mm) | State | deflection (mm) | Comment
 | L/180 | 55.56 | Ok
10000 | L/360 | 27.78 | 
 | L/480 | 20.83 | 
 | L/240 | 41.67 | 
Manual deflection calculation
Deflection limits (extract from ACI318-14)

## Slide 51: Structural Aspects – Structural Checks
Seismic Checks
Factor | Value
Z | 0.15
Soil profile type | Sd
I | 1.00
R | 5.50
Ca | 0.22
Cv | 0.32
Ramallah is located in the zone 2A and Z= 0.15
Result of Factors for seismic design

## Slide 52: Structural Aspects – Structural Checks
Seismic Checks
Define EQx in ETAB'S
Diaphragm is a horizontal or nearly horizontal system acting to transmit lateral forces to the vertical-resisting elements

## Slide 53: Structural Aspects – Structural Checks
Period Check
Term | Result | Note
seismic zone | 2A | Ramallah
Ct | 0.0488 | Other building
hn (m) | 27.1 | ***
Ta (sec) | 0.579 | ***
(1.40-1.45) Ta | (0.812-0.839) | ***
Tmax (sec) | 0.829 | Mode 1
Tx, etab (sec) | 0.709 | Mode 2
Ty, etab (sec) | 0.587 | Mode 3
Code requirement | Tetab < 1.45Ta | UBC-97
Verification | OK | Tx, Ty, Tmax
      Time period check
The value of T from Method B shall not exceed a value 30 percent greater than the value of T obtained from Method A in Seismic Zone 4, and 40 percent in Seismic Zones 1, 2 and 3 [9].
T obtained from method B = T obtained from ETAB'S
period check and result

## Slide 54: Structural Aspects – Structural Checks
Base shear check
W = DL + SID + 0.20LL = 39699.80 + 25561.03 +
(0.20*6885.88) = 66638.006 kN.

## Slide 55: Structural Aspects – Structural Checks
Base shear check
Dead Load (kN) | 39699.80 | Cv | 0.32 | I | 1
SID (kN) | 25561.03 | Ca | 0.22 | R | 5.5
Live load (kN) | 6885.88 | Tx (sec) | 0.709 | Vx | 5468.43
Weight (kN) | 66638.00 | Ty (sec) | 0.585 | Vy | 6627.56
Vetab-x | 5417.64 | Vmanual -x | 5468.43 | Error | 0.93
Vetab-y | 6566.99 | Vmanual -y | 6627.56 | Error | 0.93
manual Base shear calculation and result
%Error > 5% it's OK.

## Slide 56: Structural Aspects – Structural Checks
Drift Check
Displacement for first story from ETAB'S
Story drifts shall be computed using the Maximum
Inelastic Response Displacement ΔM.
The Maximum Inelastic Response Displacement, ΔM,
shall be computed as follows:
ΔM = 0.70RΔS.
ΔS = Design Level Response Displacement, which is the
total drift or total story drift that occurs when the structure is
subjected to the design seismic forces.
Calculated. Calculated story drift using M shall not
exceed 0.025 times the story height for structures having a
fundamental period of less than 0.7 second.
For structures having a fundamental period of 0.7 second
or greater, the calculated story drift shall not
exceed 0.020 times the story height

## Slide 57: Structural Aspects – Structural Checks
Drift Check
Story | Height | DIS_X | DIS_Y | Drift_X | Drift_Y | ∆M_X | ∆M_Y | ∆Limit | State
 | mm | mm | mm | mm | mm | mm | mm | mm | *
0 | 0 | 0 | 0 | * | * | * | * | * | *
1 | 2600 | 0.439 | 0.429 | 0.438 | 0.429 | 1.69 | 1.65 | 52 | OK
2 | 3500 | 2.104 | 1.885 | 1.666 | 1.456 | 6.41 | 5.61 | 70 | OK
3 | 3500 | 4.523 | 3.968 | 2.419 | 2.083 | 9.31 | 8.02 | 70 | OK
4 | 3500 | 7.349 | 6.413 | 2.826 | 2.445 | 10.88 | 9.41 | 70 | OK
5 | 3500 | 10.351 | 9.035 | 3.002 | 2.622 | 11.56 | 10.09 | 70 | OK
6 | 3500 | 13.478 | 11.687 | 3.127 | 2.652 | 12.04 | 10.21 | 70 | OK
7 | 3500 | 16.235 | 14.243 | 2.757 | 2.556 | 10.61 | 9.84 | 70 | OK
8 | 3500 | 19.902 | 15.397 | 3.667 | 1.154 | 14.12 | 4.44 | 70 | OK
Drift check calculation and result
DIS_X from ETAB'S.
DIS_Y from ETAB'S.
Drift_X = Summation of (DIS_X)
for pervious stories.
Drift_Y = Summation of (DIS_Y)
for pervious stories.
∆M_X = 0.70 * R * Drift_X
∆M_Y = 0.70 * R * Drift_Y
∆Limit = If T > 0.70 = 0.025*h(mm) and If T< 0.70 = 0.020*h(mm)

## Slide 58: Structural Aspects – Structural Elements Design
Slab Design
Slabs Main Top Reinforcement

## Slide 59: Structural Aspects – Structural Elements Design
Slab Design
Slabs Main Bottom
Reinforcement

## Slide 60: Structural Aspects – Structural Elements Design
Slab Design
Slabs additional top Reinforcement

## Slide 61: Structural Aspects – Structural Elements Design
Slab Design
Slabs additional
Bottom Reinforcement

## Slide 62: Structural Aspects – Structural Elements Design
Columns Design
Columns C1

## Slide 63: Structural Aspects – Structural Elements Design
Beams Design
Beam -B6

## Slide 64: Structural Aspects – Structural Elements Design
Beams Design
Beam -B6

## Slide 65: Structural Aspects – Structural Elements Design
Beams Design
Beam -B6

## Slide 66: Structural Aspects – Structural Elements Design
      Basement Retaining walls
Concrete compressive strength Fc = 28Mpa
Steel yielding strength Fy = 420Mpa
soil bearing capacity 200kN/m2.
Soil unit weight 𝜸= 18kN/m3.
Soil friction internal angle 𝞍 =300.
Base Friction coefficient F1 = 0.50
For surcharge w = 20 kN/m2.
Surcharge load is live load.
Soil Pressure is live load.

## Slide 67: Structural Aspects – Structural Elements Design

## Slide 68: Structural Aspects – Structural Elements Design
h = 250mm, d =200mm
For Mu = 23. 34kN.m
V=72kN Vu = 108.27 = 115.20kN.

## Slide 69: Structural Aspects – Structural Elements Design
      Basement Retaining walls - Detailing

## Slide 70: Structural Aspects – Structural Elements Design
Surcharge Load = Ka * q = 0.333 * 20 = 6.66kN/m2.
Soil Load = Ka * Ɣs * Hs = 0.333*18 * 2.60 = 15.60kN/m2.
Water Load = Ɣw * Hw = 10 * 2.60 = 26kN/m2.
      Cantilever Retaining walls

## Slide 71: Structural Aspects – Structural Elements Design
      Cantilever Retaining walls
M= 70 kN.m
Mu = 1.6 * 70 = 112kN.m
h = 250mm, d =200mm.
V=72kN. Vu = 1.60*72 = 115.20kN.
Thickness of wall = 250mm, two layers of steel are to be used
Vertically use 8𝞥16/m on soil side and use minimum steel 4𝞥12/m on the other side.
Horizontally use 4𝞥10/m (1/2 As,min. Horizontally) for each side. Use 5𝞥10/m for spacing requirements.

## Slide 72: Structural Aspects – Structural Elements Design
      Cantilever
      Retaining walls –
      Detailing

## Slide 73: Structural Aspects – Structural Elements Design
Foundations Design
Mat Foundation
Final trial thickness = 1000mm.
Soil Pressure for final trial

## Slide 74: Structural Aspects – Structural Elements Design
Foundations Design
Mat Foundation
Final trial thickness = 1000mm.
Punching shear check for final trial

## Slide 75: Structural Aspects – Structural Elements Design
Foundations Design
Mat foundation detailing

## Slide 76: Structural Aspects – Structural Elements Design
Foundations Design
Mat foundation detailing

## Slide 77: Structural Aspects – Structural Elements Design
Foundations Design
Mat foundation Additional reinforcement

## Slide 78: Structural Aspects – Structural Elements Design
Foundations Design
Mat foundation detailing

## Slide 79: Structural Aspects – Structural Elements Design
Staircase Design
LL = 2.50kN/m2.
SID = 6kN/m2.
Thickness (Ht) = 200mm.
d = 200-30 = 170mm

## Slide 80: Structural Aspects – Structural Elements Design
Staircase Design
Use minimum area of steel (4𝞥12/m). in both directions.

## Slide 81: Structural Aspects – Structural Elements Design
Staircase Design

## Slide 82: Structural Aspects – Structural Elements Design
Septic tank Design
The quantity of water supplied = per capita rate * #of users
Per capita rate = 95 – 120 Litter /person. Use max. = 120litter/person.
Number of persons = #Of floors * #of apartments * #of person in each apartment.
= 6 * 4 * 4 = 96person (user).
The quantity of water supplied = 120 * 96 = 11520litters.
Assumed that 80% of water supplied becomes sewage
The quantity of sewage produced = 0.80 * 11520 = 9216litters.
Assumed the detention time = 3days.
So, the sewage quantity = 9216 * 3 = 27648litter.
Consider the deposited sludge rate as 25 litter/person/year and the cleaning period each one year.
Sludge quantity = 25 * 96 * 1 = 2400litter.
Total required capacity of tank = sewage + sludge = 27648 + 2400 = 30.048litter = 30m3.

## Slide 83: Structural Aspects – Structural Elements Design
Septic tank Design
Length = 3.20m, width = 3.20m and height = 3m (Volume = 3.20*3.20*3 = 30.72m3)
Water pressure = Ɣw *Hw = 10 * 3 = 30kN/m2.
Soil Load = K/o * Ɣs * H/s = 0.5*18 * 3 = 27kN/m2.
Sewage pressure = Ɣw *Hw = 10 * 3 = 30kN/m2.
Soil considered as live load.
Water and sewage considered as Dead load.
.
Load combination:
    1.2DL +1.60LL 2) 1.40 DL
Underground tanks are designed for the worst of the following cases:
The presence of external water and soil on the walls (the condition of backfilling behind the walls).
Presence of internal water only (tank test condition).
The presence of water from the inside and soil and water from the outside.

## Slide 84: Structural Aspects – Structural Elements Design
Septic tank Design

## Slide 85: Structural Aspects – Structural Elements Design
Septic tank Design
Check thickness for vertical shear:
Check thickness for Tension

## Slide 86: Structural Aspects – Structural Elements Design
Septic tank Design

## Slide 87: Structural Aspects – Structural Elements Design
Septic tank Design
Vertical Reinforcement (Outside and Inside Surface).
M11 = Horizontal moment = 74 kN.m/m
S = 200mm, thickness = 400mm so, Fs,max = 145Mpa (Two way-severe exposure).

## Slide 88: Structural Aspects – Structural Elements Design
Septic tank Design

## Slide 89: Structural Aspects – Structural Elements Design
Septic tank Design
Horizontal Reinforcement
M11 = Horizontal moment = 74 kN.m/m
suppose distance between movement joints less than 6m.

## Slide 90: Structural Aspects – Structural Elements Design
Septic tank Design
Horizontal reinforcement distribution
Nearby the corner: (Tension and moment)
Far away from the corner: (Only tension)

## Slide 91: Structural Aspects – Structural Elements Design
Septic tank Design

## Slide 92: Structural Aspects – Structural Elements Design
Septic tank footing Design
Soil Pressure for tank foundation

## Slide 93: Structural Aspects – Structural Elements Design
Septic tank footing Design
No additional reinforcement.

## Slide 94: Electro-Mechanical Aspects
Water Supply and Drainage
HVAC System
Power Design
Firefighting system
Artificial Lighting

## Slide 95: Electro-Mechanical Aspects – Artificial Lighting
All lighting element luminaires is LED with step control elements.
The daylight factor should be in between this ringing (2-6) present
Light Levels (Illuminance) for indoor area as levels of Residential building standard.
The reflection percentage it’s for floor its 0.6, ceiling its 0.75 and wall its 0.3
Limitation:
Indoor lighting design:

## Slide 96: Electro-Mechanical Aspects – Artificial Lighting
DIALux has been used for this Analysis and Design.
Designed Spaces:
Living room
Kitchen& Dinning room
Bathroom
Bedroom
Corridor
Parking

## Slide 97: Electro-Mechanical Aspects – Artificial Lighting
Living room
The parameter for design this room is 200 lux min as standard.

## Slide 98: Electro-Mechanical Aspects – Artificial Lighting
Kitchen
The parameter for design this room is 300 lux min as standard.

## Slide 99: Electro-Mechanical Aspects – Artificial Lighting
Bathroom
The parameter for design this room is 200 lux min as standard.

## Slide 100: Electro-Mechanical Aspects – Artificial Lighting
Bedroom
The parameter for design this room is 200 lux min as standard.

## Slide 101: Electro-Mechanical Aspects – Artificial Lighting
Corridor
The parameter for design this room is 100 lux min as standard.

## Slide 102: Electro-Mechanical Aspects – Artificial Lighting
Parking
The parameter for design this room is 75 lux min as standard.

## Slide 103: Electro-Mechanical Aspects – Artificial Lighting
Lighting Plans
Basement floor – 5th floor
Parking

## Slide 104: Electro-Mechanical Aspects – Power Design
Socket and Distribution Boards Plans
Basement floor – 5th floor
Parking

## Slide 105: Electro-Mechanical Aspects – Power Design
After designing wire for the worst case for each floor

## Slide 106: Electro-Mechanical Aspects – Water Supply and Drainage
Water Tanks
We Used 24 tank to all Building 1 Apartment    3000 Liter
Boiler Electricity
48 water heater devices in all building

## Slide 107: Electro-Mechanical Aspects – Water Supply and Drainage

## Slide 108: Electro-Mechanical Aspects – Water Supply and Drainage
Water Supply Plans
Floor Plan
Roof Plan

## Slide 109: Electro-Mechanical Aspects – Water Supply and Drainage
Drainage System
Used Diameters
W.C Horizantal Pipe = 4″ at slope of 1%
Lavatory Horizantal Pipe = 2″ at slope of 2%
Kitchen Sink Horizantal Pipe = 2″ at slope of 2%
Main Manhole’s Pipe = 6″ at slope of 1%
Branch Manhole’s Pipe = 4″ at slope of 1%

## Slide 110: Electro-Mechanical Aspects – Water Supply and Drainage
Drainage System Sample Plans

## Slide 111: Electro-Mechanical Aspects – Water Supply and Drainage
Rainwater System and Manholes Plan

## Slide 112: Electro-Mechanical Aspects – HVAC Design
VRF System has been considered.
A VRF system is an excellent choice for cooling and heating large commercial and residential buildings.
HVAC System Used Components:
Outdoor Unit
Fan coil Unit
Ducts
Diffusers

## Slide 113: Electro-Mechanical Aspects – HVAC Design
Design Capacity = 172.4 kW
Total Design Flowrate = 12.84 m3/sec.
Outdoor Unit Catalogue
Outdoor Location in building

## Slide 114: Electro-Mechanical Aspects – HVAC Design
Indoor unit – Fan coil unit
In our project - chose fan coil units
• Capacity zone1 = 7.19KW  chose FCU capacity= 7.57KW
• Capacity zone2 = 8.25KW  chose FCU capacity= 8.49KW
• Capacity zone3 = 7.19KW  chose FCU capacity= 7.57KW
• Capacity zone4 = 6.02KW  chose FCU capacity= 6.65KW
Intdoor Unit Catalogue
Zone location

## Slide 115: Electro-Mechanical Aspects – HVAC Design
Duct sizing
Using the airflow per zone and the airflow per diffuser, the duct size is calculated
Duct size calculation

## Slide 116: Electro-Mechanical Aspects – HVAC Design
Diffusers.
In our project - chose Ceiling Diffusers.
Diffusers calculation
Diffusers Unit Catalogue

## Slide 117: Electro-Mechanical Aspects – HVAC Design
Ventilation
fresh air intake calculation
fresh air intake Catalogue
CFM ehaust =10681.4 cfm
CFM fresh = (0.85-0.9) CFM ehaust =9613.3 cfm
max. Air flow = 5080/1.699 = 2990 cfm
Number of exhaust fan = 10681.4/2990 = 4
For one exhaust fan = 10681.4/4 = 2670.4 cfm
Number of fresh fan = 9613.3/2990 = 4
For one fresh fan = 9613.3/4 = 2403.3 cfm

## Slide 118: Electro-Mechanical Aspects – HVAC Design
HVAC Plans
Basement
Parking

## Slide 119: Electro-Mechanical Aspects – HVAC Design
HVAC Plans
1St – 5th Floor
Basement

## Slide 120: Electro-Mechanical Aspects – Fire Fighting System
Used Fire-fighting System
Heat & Smoke detectors
Fire Hose Stations Class III Cabinets
Fire alarm System
Dry Powder – Standard extinguisher
Fire-fighting Signs

## Slide 121: Electro-Mechanical Aspects – Fire Fighting System
1St – 5th Floor Fire Hose Stations&detectors

## Slide 122: Electro-Mechanical Aspects – Fire Fighting System
1St – 5th Fire-Fighting Plan
Fire-fighting Symbols

## Slide 123: Quantity Surveying & Cost Estimations
Preliminary Cost Estimation of the Library has been conducted based on the Unit base method.

## Slide 124: Cost Estimation
Columns cost calculations

## Slide 125: Cost Estimation
Columns cost calculations

## Slide 126: Cost Estimation

## Slide 127: Cost Estimation
Project area, S.M | Total Cost, ILS | ILS/S.M
3649 | 5,929,990 | 1625.1

## Slide 128: THANKS
Does anyone have any questions?