## Slide 1
Prepared by:
Eman Qaqa
Dunia Saffarini
Angel

## Slide 2
Outline
What is Angel?
Motivation
How does it work?
Technical choices.
Constraints.
Future work

## Slide 3
What is Angel?
Angel is a robot that helps nurses and hospital employees to deliver the appropriate diet to the appropriate patient.

## Slide 4
Motivation
• Save time and efforts.
• Sensitive duties for hospital employees.
•Delivering the appropriate diet to the appropriate patient.
•No errors while delivering the diets.

## Slide 5
How does it work?
Our Angel starts the movement from a starting point Which is the kitchen in the hospital.

## Slide 6
2) It will start the movement after putting the diets or the medicine in the turntable part of our robot

## Slide 7
3) It will follow a speciﬁc black line and deliver the appropriate diet to the appropriate room and determine the rooms by distance

## Slide 8
The distance between the rooms will be the same, our robot can deliver up to 3 rooms right now

## Slide 9
4) In front of each room the turntable inside the robot will turn until match the right room & the right dish

## Slide 10
5) The door will open after specific delay which is enough to take the dish the door will close

## Slide 11
6) if there are line to inside the room which need to turn right or left Our Angel can turn based on IR Sensors

## Slide 12: Technical choices
1- Moving the wheels:
DC motor
Dual H-Bridge driver
IR sensors
2- The Turntable Disk:
Stepper motor
IR sensors
3- The door: Servo motor
4- Controller: Arduino Mega

## Slide 13: The Movement part
Line Following Process:

## Slide 14: The Movement part
1-Line Following process(Cont.)
We used 2 IR sensor module
1- IR transmitter and IR receiver.
2- white surface is a reflected surface but the black not.

## Slide 15: The Movement part
2- 4 DC motors to move the wheels of the Robot.
3- L298n Dual H-Bridge Driver:
interface between arduino and motors.
control 2 motors independently in both directions.

## Slide 17: The Turntable Part
1- Stepper motor.
To achieve a precise motion control to the turntable part.
2- A4988 stepper motor driver.
Control rotation of Stepper motor by using 2 pins.
3- 3 IR sensors.

## Slide 19: The Door
1- Servo motor .
push and rotate an object with a specific angle.
open the door: rotate it by -180 degree
close door : rotate by 180 degree

## Slide 22
Constrains
1- IR sensors can’t detect the right color that because it only detects it by a speciﬁc distance.
2-The motors and the wheels always need to tied them up.
3- Fraction of stepper motor with the turntable part.

## Slide 24: Conclusion and future work
1- Adding more rooms to be serviced
2- Controlling the movement and the process by a mobile app.
3- Involve image processing system to detect the rooms automatically.
4- Involve AI to detect the shortest Path to deliver the food.