## Slide 1
SynLab
PROJECT PRESENTATION
By: Adel Qadi, Ghassan Qasrawi.
Supervisors: Dr. Raed Qadi, Dr. Manar Qamhieh
NNU - COMPUTER ENGINEERING GRADUATION PROJECT 2

## Slide 2
PROJECT OVERVIEW
  SynLab is a modular IoT-based electronics laboratory
  Integrates multiple lab instruments into one system
  Instruments communicate wirelessly
  Controlled via display + mobile application
  Designed for education, experimentation, and accessibility
SYNLAB

## Slide 3
PROBLEM STATEMENT
Traditional lab equipment can be further improved to solve the many issues users suffer from. using SynLab these can be tackled simultainously
SYNLAB
BULKY AND EXPENSIVE STANDALONE INSTRUMENTS
01
02
03
04
NO INTERCONNECTIVITY BETWEEN DEVICES
LIMITED REMOTE ACCESS
LACK OF SMART, UNIFIED, SCALABLE LAB ENVIRONMENTS

## Slide 4
SYNLAB
PROJECT OBJECTIVES
01
DESIGN A SMART MODULAR ELECTRONIC LAB
02
  IC Tester
  Oscilloscope
  Function Generator
  PIC Programmer
  AC/DC Monitoring
INTEGRATE PARTS:
03
ENABLE REAL-TIME MONITORING AND CONTROL
04
IMPLEMENT IOT COMMUNICATION
05
IMPROVE LEARNING EXPERIENCE FOR STUDENTS

## Slide 5
SYSTEM CONCEPT
SYNLAB
ALL MODULES CONNECTED VIA IOT (WI-FI)
MODULAR SYSTEM: EACH INSTRUMENT IS INDEPENDENT
01
02
SCALABLE AND EXPANDABLE DESIGN
  Nextion Display
  Mobile Application
CENTRALIZED CONTROL THROUGH
03
04

## Slide 6
MQTT
Protocol
TECHNOLOGIES USED
SYNLAB
Microcontrollers
Communication
Software
HMI
ESP32
Arduino MEGA
Arduino UNO
Wifi
Arduino IDE
C++

## Slide 7
MAIN SYSTEM MODULES
SYNLAB
  FUNCTION GENERATOR
  IC TESTER
  OSCILLOSCOPE
  PIC PROGRAMMER
  AC MONITOR
  DC MONITOR
2
1
3
4
6
5

## Slide 8
ESP32
FUNCTION GENERATOR MODULE
  Generates Sine, Square, Triangle waveforms
  Based on ESP32 DAC & PWM
  Adjustable frequency and amplitude
  Integrated with Nextion touchscreen
SYNLAB
PAGE 03
02
Wave parameters are controlled in real time through the system interface.
Low-cost waveform generation suitable for education and prototyping.
KEY ADVANTAGE:
DAC /PWM
AMP
OUTPUT

## Slide 9
IC TESTER MODULE
  Supports 74xx (TTL) and 40xx (CMOS) IC families
  Uses Arduino Mega 2560
  ZIF socket for safe IC insertion
  Communicates with system via serial
SYNLAB
PAGE 04
02
Designed to quickly verify logic IC functionality without external equipment.
  Auto Mode: IC detected automatically
  Manual Mode: User selects IC type
  Detailed Mode: Shows test process step-by-step
OPERATING MODES

## Slide 10
OSCILLOSCOPE MODULE
SYNLAB
PAGE 05
02
Optimized for educational use and low-frequency electronic experiments.
  ESP32-based digital oscilloscope module
  Real-time analog signal acquisition
  Wireless data transmission between nodes
  Designed for educational and prototyping use
  Uses ESP32 ADC1 (GPIO33)
  12-bit resolution (0–4095)
  11 dB attenuation for wider input range
  256 samples per frame
  Target sampling rate: 20 kHz
  Captured frame is down-sampled to 15 points
  Values scaled from 12-bit → 8-bit (0–255)
  Data sent wirelessly using ESP-NOW
  ESP32 operates in Wi-Fi station mode
  Packets sent to a paired receiver ESP32 via ESP-NOW

## Slide 11
PIC 18F4XXX PROGRAMMER MODULE
  Arduino Uno is used as a custom programmer to communicate directly with the PIC microcontroller using low-voltage ICSP.
  Programming is done by manually driving the PIC’s programming pins:
SYNLAB
PAGE 06
02
Eliminates the need for separate programming hardware.
  PGC – Programming Clock
  PGD – Programming Data
  PGM – Programming Mode Enable
  MCLR – Reset / Programming Control
  Operations:
  Program : programs a hex file into the PIC Flash memory
  Erase : erases the flash memory of the device
  Read: reads a single line of flash memory
  Dump: reads the entire Flash memory

## Slide 13
  AC Power Monitor (PZEM-004T)
  Measures AC :
  Operates on 220 V mains
  Arduino Uno reads data from the PZEM via UART
  Data is sent to an ESP32, then transmitted using ESP-NOW.
AC MONITOR MODULE
SYNLAB
PAGE 08
02
Allows safe observation of AC electrical behavior without direct exposure.
  VOLTAGE
  CURRENT
  POWER
  FREQUENCY
  POWER FACTOR

## Slide 14
  Uses an INA219 sensor to measure:
  ESP32 directly reads measured values and transmits them wirelessly through ESP-NOW
  A second ESP32 receives the data and displays it on the TFT screen
DC MONITOR MODULE
SYNLAB
PAGE 09
02
  DC voltage
  Current
  Power

## Slide 15
MOBILE APPLICATION
  Built using Flutter
  Real-time system monitoring
  Module control and data logging
  Simple and clean interface
SYNLAB

## Slide 16
DISCUSSION
Compared to traditional labs, SynLab provides better coordination and usability.
SYNLAB
PAGE 07
  ALL MODULES OPERATED INDEPENDENTLY AND COLLECTIVELY WITHOUT CONFLICTS
  STABLE IOT COMMUNICATION BETWEEN ESP32 NODES
  REAL-TIME DATA VISUALIZATION ACROSS INTERFACES
  SMOOTH SYNCHRONIZATION BETWEEN HARDWARE AND SOFTWARE
SYSTEM PERFORMANCE
  REDUCED SETUP TIME FOR EXPERIMENTS
  EASIER UNDERSTANDING OF RELATIONSHIPS BETWEEN INSTRUMENTS
  INCREASED STUDENT ENGAGEMENT THROUGH INTERACTION
  SUPPORTS HANDS-ON AND EXPLORATORY LEARNING
EDUCATIONAL IMPACT

## Slide 17
PAGE 09
LIMITATIONS
  Limited measurement precision due to the use of microcontroller internal ADCs/DACs and low-cost sensors, which do not match commercial lab accuracy.
  Breadboard-based hardware may introduce noise, loose connections, and reduced long-term reliability.
  ESP32 processing and load constraints when handling real-time sampling, wireless communication, and user interface updates simultaneously.
  Dependence on wireless communication (ESP-NOW / MQTT), which may be affected by interference or network congestion.
  High-voltage AC measurements require enclosed and controlled operation for safety reasons.

## Slide 18
FUTURE WORK
SYNLAB
PAGE 07
  Replace breadboards with custom PCBs
  Improve signal conditioning and filtering
  Increase sampling rates and accuracy
  Add more lab instruments
  Cloud-based experiment logging

## Slide 19
SYNLAB
PAGE 10
THANK YOU FOR YOUR ATTENTION
By: Adel Qadi, Ghassan Qasrawi.
Supervisors: Dr. Raed Qadi, Dr. Manar Qamhieh