## Slide 1
An-Najah National University
Faculty of Engineering & Information Technology
Civil Engineering Department
Graduation Project II
Structural Analysis and Design of Illar Basic Girls' school
Prepared by:
Tahleel Ghanem Dunya Abbas
Ayah Abudura Mira Alkayyal
Supervisor : Dr. Munther Diab
2020-2021

## Slide 2: Outline:
Project Description
Structural System Design and Analysis .
Modeling and Checks
Design of structural elements

## Slide 3: Project Description

## Slide 4: Project Description :
This project is Analysis and Design of Illar Basic Girls' school .
The building consists of seven floors, and located on three different levels. The building contains two basement floors and five above the ground .
This building includes classrooms, laboratories and meeting rooms and the fourth floor is stage.

## Slide 5
Floor | Height (m) | Area (m2)
The second basement | 3.64 | 274.15
The first basement | 3.64 | 346.68
The ground floor | 3.64 | 609.77
The first floor | 3.64 | 609.77
The second floor | 3.64 | 609.77
The third floor | 3.64 | 609.77
The fourth floor | 3.64 | 678.17
Area and height floor

## Slide 6
Architectural Plans:
For second basement

## Slide 7
Architectural Plans:
For first basement

## Slide 8
Architectural Plans:
For Ground floor

## Slide 9
Architectural Plans:
For Ground floor

## Slide 10
Architectural north elevation :

## Slide 11
Architectural south elevation :

## Slide 12
Architectural west elevation :

## Slide 13
Architectural east elevation :

## Slide 14
3D Model

## Slide 15
  Codes and standards:
American Society of Civil Engineer (ASCE 7-16): For Live load & lateral combination values
American Society for Testing and Materials (ASTM): For materials
American Concrete Institute (ACI 318-14): For design
INTERNATIONAL BUILDING CODE (IBC-2012)

## Slide 16
Software :
ETABS 18.0.2.
AUTOCAD 2017.

## Slide 17
There are two type of load on structural :
Gravitational loads such as live, dead and superimposed dead loads.
Lateral loads such as wind, earthquakes, and soil pressure.
gravity loads:
Dead Load :
Known as static loads, are those that remain relatively constant over time such as the weight of a building’s structural elements like beams, walls, and structural flooring components.
Types of Loads

## Slide 18
Live Load :
Can know it as Loads that change over time. Typical live loads may include; People, furniture, or other movable objects.
Occupancy or use | Uniform Live Load (kN∕m2)
Classrooms | 2.00KN/m2
First-floor corridors | 4.79 KN/m2
Stairs and exit ways | 5.00 KN/m2
Training Rooms | 5.00KN/m2
Offices | 3.00KN/m2
Lab and Library | 3.00KN/m2
Use the value of live load = 5 KN/m2 for all stories. Use the value of live load in book story = 5 KN/m.

## Slide 19
Superimposed dead load :
The weight of all construction materials incorporated into the building, including walls, floors, roofs, partitions, finishes .
superimposed dead load for layers of floors :
Total SID in slab = 3.65 KN/m2 take it 4KN/m2 (for all room except bath room)
Total SID in slab = 5.65 KN/m2 take it 6KN/m2 .(for bath room)

## Slide 20
superimposed dead load for partitions :
Wall1 weight (Hollow blocks 10cm + 3cm isolator +15cm concrete +5cm stone) =
= 1.94+0.03*0.5+.15*23+.05*27= 6.785 KN/ m²
= 6.785 *3.44 (height) = 23.3 (KN/m) use 30 KN/m

## Slide 21: Lateral Load:

## Slide 22: Risk category of building

## Slide 23: Importance Factor, Ie

## Slide 24: Seismic zone factor (z)
Ss = 0.4
S1 = 0.1

## Slide 25: Site classification
Bearing capacity of the soil is 278 kN/m2
The type of soil as site is C.

## Slide 26: Determination of response accelerations SMS & SM1
Short-Period site coefficient - Fa (at 0.2 s-period) = 1.3
Long-Period site coefficient - Fv (at 0.1 s-period) = 1.5
𝑆𝑀s = 𝐹𝑎 × 𝑆𝑠
= 1.3× 0.4
= 0.52
𝑆𝑀1 = 𝐹𝑣 × 𝑆1
= 1.5× 0.1
= 0.15

## Slide 27: Calculate the design spectral accelerations SDS & SD1
For 2% probability of exceedance of return period 50 years.
SDS = 2/ 3 SMS
= 2/ 3 × 0.52
= 0.3467
SD1 = 2 /3 SM1
= 2/ 3 × 0.15
= 0.1

## Slide 28: Seismic Design Category
As the value of 𝑆𝐷𝑆 = 0.3467 is less than 0.5 and the value of 𝑆𝐷1 = 0.1 less than 0.2, then the seismic design category is C.
From the results above, the seismic design category is C

## Slide 29
1. Ultimate Load Combinations
Load Combinations
For gravity load : Ultimate Load Combination
1.4D+1.4SD
1.2 D +1.2SID+ 1.6 L
-For earthquake load : Ultimate Load Combination
1.32D + L + Sex
1.32D + L + Sey
0.78 D + Sex
0.78 D + Sey
=sum of Service Load

## Slide 30
2. Service Load Combinations
Load Combinations
For gravity load : Service Load Combination
D
D+L

## Slide 32: Structural System Design and Analysis

## Slide 33
Structural Element:
Slab System
Beams System
Columns System
Shear wall System

## Slide 34
Preliminary Design :
Slab Thickness :
The ratio of the longer to the shorter side (Lx/Ly) of the slab greater than two so it’s preferable to design the slab as one way slab.
For critical panel :

## Slide 35
Slab thickness for one way slabs are design according to ACI code :
type | Simply supported | One end continues | two end continues | cantilever
Solid one way slab | L/20 | L/24 | L/28 | L/10
Beam and one way ribbed | L/16 | L/18.5 | L/21 | L/8
One way solid:
h=L/28=3.46/28=0.12 m take it 0.15 solid in X
One way solid: ( for stage )
h min =Ln/28 =3.1/28 =0.11 m Use h =0.12 m

## Slide 36
Beams Dimensions :
Beams have been designed according to the ACI code
Beam | Depth (mm) | Width (mm)
B1 | 600 | 300
B2 | 600 | 200
B3 | 900 | 400
B4 | 1500 | 400

## Slide 37
Beams Dimensions :
Beam Layout

## Slide 38
Column Dimensions :
Column | Width(mm) | Depth(mm)
Interior column | 350 | 700
Edge column 1 | 350 | 700
Edge column 2 | 400 | 1500
Corner column | 350 | 700

## Slide 39
Wall Thickness :
Wall | Depth (mm)
SW1 | 300
SW2 | 250

## Slide 40
  Type of structural system
For this system,
( R ) = 5,
( Ωo )=3
( Cd ) = 4.5 .

## Slide 41: Modeling and Checks

## Slide 43
Modifiers
For slab
For beam

## Slide 44
Modifiers
For column
For wall

## Slide 45
Structural Model Verification
Compatibility Check

## Slide 46
Structural Model Verification
    Equilibrium Check
    Total live load from hand calculation = 15957.40 KN
    Total live load from ETABS :
%Error=0.00%

## Slide 47
Internal Forces Check
From live load :
Error < 10 OK
 | Hand calculation | From ETABS
Slab | 8.55 | 8.36
Beam | 67.62 | 68.195
Column | 305.20 | 305.64
 | Slab | Beam | Column
Error | 2.2 | 0.80 % | 0.1 %

## Slide 48
Deflection Check
Allowable long term Deflection
Long term Deflection = 2D+2SID+1.25L
Long term Deflection=(11.67+ 20.25)/2 -23.88=7.92
Allowable Deflection = L/240=3700/240 = 15.42 mm> 7.92 mm

## Slide 49
Shear Check for Slab
∅𝑉𝑐 = ∅ 1/ 6 𝜆√𝑓𝑐 ′ 𝑏𝑤𝑑 = 0.75 × 1/ 6 × √24 × 1000 × 120 ×1.1= 80 KN
Vu < ∅𝑉𝑐 OK

## Slide 50
    Modal mass participation ratio
From the table above, it obvious that the summation of modes are more than 0.9, which is mean that most masses of the structure move in these modes ( the main motion are in X and Y direction ) .

## Slide 51
Period calculations
The project case is all other structural systems with Ct =0.0488 and X =0.75
Ta = Ct*hnx=0.0488×25.48.75 = 0.553439 sec.
T= Cu Ta = 0.783 sec
Fundamental period for the structure = 0.382 sec which is less than 0.783 sec.

## Slide 52
Base shear
      hand calculation using ELF method
The value of Cs =0.1115
W = Dead load + Superimposed load
= 83269.25Kn.
V Manual = Cs×W
= 0.1115×83269.25
= 9284.521 Kn.

## Slide 53
Definition of ELF in ETABS

## Slide 54
ETABS calculation
For response spectrum in X – direction :
Scale factor =* *1000
=* *1000 = 5,242.8
For response spectrum in Y – direction :
Scale factor =* *1000
=* *1000 = 4575.04893

## Slide 55
    Drift Check
Allowable story drift ( Δa) ≤ 0.02hx
All values of drift are less than the allowable drift.
    Torsional irregularity check
Structure transverse ratio should not exceeds 1.4
So according to all ratios, there is no torsional irregularity or extreme torsional irregularity in Y-Direction & X-Direction.

## Slide 56
    P – delta check
P- delta effects on story shears and moments, the resulting member forces and moment, and the story drifts induced by these effects can be ignored if the stability coefficient ( 𝜃 ) is equal or less than 0.1
So according to all ratios less than 0.1, there is no P-delta effects in Y-Direction & X-Direction

## Slide 57: Design of structural elements

## Slide 58
Slab Design
Design for flexure:
Slab shrinkage steel

## Slide 59
Slab Design
Design for flexure:

## Slide 60
Slab Design
Design for flexure:

## Slide 61
Beam Design
Sample Calculation for one beams: Beam (30X90)
Flexural Reinforcement

## Slide 62
Beam Design
Sample Calculation for one beams: Beam (30X90)
Shear Reinforcement for Beam

## Slide 63
Beam Design

## Slide 64
Column Design

## Slide 65
Column Design

## Slide 66
Column Design
Cross section for Column 700 X 350

## Slide 67
  Footing design

## Slide 68
  Footing design

## Slide 69
  Footing design

## Slide 70
  Footing design

## Slide 71
  Footing design

## Slide 72
  Shear wall design

## Slide 73
  Shear wall design

## Slide 74
Thanks
For
Listening