## Slide 1
An-Najah National University
Faculty of Engineering
Mechanical Engineering Department
District Heating Network
Prepared by:
Mahmoud Salem
Mahmoud Ghanem
Basem Daghlas
Mohammad Daragmeh
Supervisor:
Eng. Luqman Hirzallah

## Slide 2
Contents :
Introduction
Benefit of DH
System Components
Literature Review in Palestine
Module
Network design
Calculations
Recommendations

## Slide 3
District Heating Network : is a system for distributing heat generated in a centralized location for residential and commercial for heating and production of domestic hot water.
District heating replaces individual boilers it uses less energy costs and make cities more organized places.
Introduction :
Definition

## Slide 4
Benefit of DH:
Organize the heat production
Reduce the risk and maintenance
Easy to use and control

## Slide 5
Boiler
Pipe Network isolated
Pumps
Heat Exchanger for each building
Valve and accessories
The System consist of
Components :

## Slide 6: : Boiler
We select model REX7- REX 30 and Rex 450 for the center Boiler.
We select vertical centrifugal pump with 6 bar and mass flow 20 l/s
: Pumps
We select stainless steel pipe with Insulation u= 0.136-0.41 w/m.c
: Pipes

## Slide 8
This project will be the first in Palestine
It has not been implemented yet in Palestine even though there is need for such a project.
Prices of electricity and gas are high
Motivation

## Slide 9: Model :
Representation of reality
It is required to perform the calculation
In DH networks the following assumption :
One dimensional geometry
Junctions between components occurs in points

## Slide 10: Network design
Topological representation
  we use graph theory to determine nodes and branch's
Physical representation
  we use fluid dynamic equations and thermal equation

## Slide 11: Topological representation
A graph is a representation of a set of connected objects.
This representation is based on two concepts: the node and the branch
Nodes are used to describe a section at which two or more components are connected. the nodes of fluid network usually correspond to junctions
A branch is a line that is bounded by two nodes

## Slide 12: Physical representation
  Momentum equation
  Continuity equation
    A. G+Gex = 0
    =
  Energy equation

## Slide 13: Incidence matrix
The interconnection between the nodes and branches is expresses by the incidence matrix

## Slide 14: Calculations :
We have assumed heating loud is 120w per area and we have 38 building as shown in fig

## Slide 15: Mass flow rate
Chart: nodes
| 4 | 6 | 8 | 10 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27 | 29 | 31 | 33 | 35 | 37 | 39 | 41 | 43 | 46 | 48 | 49 | 52 | 55 | 57 | 58 | 60 | 62 | 64 | 67 | 68 | 70 | 72 | 74 | 76 | 77
mass flow rate | 0.50037 | 0.47014 | 0.23841 | 0.64502 | 0.93262 | 0.35794 | 1.1836 | 0.99262 | 0.93783 | 0.31417 | 0.30653 | 0.038711 | 0.17923 | 0.86488 | 1.1462 | 0.062522 | 0.5983 | 1.2973 | 0.29073 | 0.041681 | 0.99264 | 0.08753 | 0.32998 | 0.15214 | 0.1636 | 0.85967 | 0.57989 | 0.9769 | 0.71066 | 0.21049 | 0.67304 | 0.14276 | 0.052101 | 0.13755 | 0.42306 | 0.27822 | 0.29177 | 0.5627

## Slide 16: Temperature
Chart: nodes
| 4 | 6 | 8 | 10 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27 | 29 | 31 | 33 | 35 | 37 | 39 | 41 | 43 | 46 | 48 | 49 | 52 | 55 | 57 | 58 | 60 | 62 | 64 | 67 | 68 | 70 | 72 | 74 | 76 | 77
temp | 122.3 | 122.4 | 122.2 | 122.3 | 122.2 | 122.2 | 122.2 | 122 | 121.9 | 121.6 | 121.9 | 120.4 | 121.7 | 121.8 | 121.8 | 121 | 121.7 | 121.8 | 121.4 | 121.4 | 121.5 | 120.7 | 121.1 | 120 | 122.2 | 122.4 | 122.5 | 122.2 | 122.4 | 122.1 | 122.2 | 122 | 121.8 | 122.2 | 122 | 122.1 | 121.8 | 121

## Slide 17: Pressure loss
Chart: Nodes NO
#REF! | 1
#REF! | 1

## Slide 18: Compressed fluid check
From compressed thermodynamics table flow the pressure found 5 bar at 120°C ,so using a pump greater than 5 bar to take over friction to be fluid compressed liquid .
Pump Cavitation check
By net positive suction head (NPSH )
NPSH = 48.5 >
 Will not occur cavitation to the pump

## Slide 19: Laminar or turbulent flow in pipes
The losses throw laminar is less than turbulent flow
In this System we have the flow is laminar
 The flow is laminar

## Slide 20: Comparison between traditional and central district heating systems
Chart: 
| Fuel consumptiion | CO2 emission
traditional | 647128.4 | 1941385
central district heating | 629909 | 1889728

## Slide 21: Conclusion:
This system in our country is not feasible due to the high cost of oil derivatives.
This system can be applied in our country only through the converting waste to energy furnace or utilizing gas located on Gaza Strip.

## Slide 22
Thank you for listening
Questions ?