## Slide 1
An-Najah National University
Faculty of Engineering & Information Technology
Building Engineering Department
Graduation Project II
Green Residential Building in Hebron
Supervised by: Dr. Mutasim Baba
Prepared by: Duha Hijab
Noor Subbagh
Saja Rabayaa
Zeina Qamhia

## Slide 2
Outline
Introduction
Comparative study
Architectural design
Environmental design
Structural design
Electro-Mechanical design
Survey and cost estimate

## Slide 3
Introduction
This project is aim to redesign a three residential buildings located in Hebron as green buildings. Because the classical buildings are neither energy efficient nor comfortable for their resident due to lack of environmental design of these buildings and insufficient thermal insulation.
Green residential means applying the houses with a minimum energy, water and natural resources that provide good air quality, comfort environment and reduce wastes.

## Slide 4
Comparative study
Location: Alma'ajen area in Nablus.
Part of our project was to conduct a study on typical residential buildings and to evaluate their energy performance and the comfort for their residents.

## Slide 5
Site plan
plan

## Slide 6
Questionnaire results
Chart: Percentage of satisfaction of people from their home during the day
| Temperature | Sound level | Natural light | Humidity | Air movement | Air exchanges | Smells (air quality) | Sunshine
not at all satisfied | 0.088 | 0.206 | 0.088 | 0.265 | 0.029 | 0.029 | 0.059 | 0.088
2 | 0.147 | 0.147 | 0.059 | 0.118 | 0.176 | 0.176 | 0.088 | 0.059
3 | 0.265 | 0.265 | 0.294 | 0.176 | 0.176 | 0.176 | 0.324 | 0.265
4 | 0.324 | 0.176 | 0.147 | 0.118 | 0.353 | 0.382 | 0.206 | 0.294
very satisfied | 0.176 | 0.206 | 0.412 | 0.324 | 0.265 | 0.235 | 0.324 | 0.294
TOTAL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Percentage of satisfaction of people from their home during the day
| Temperature | Sound level | Natural light | Humidity | Air movement | Air exchanges | Smells (air quality) | Sunshine
not at all satisfied | 0 | 0.069 | 0 | 0.034 | 0 | 0 | 0.069 | 0.069
2 | 0 | 0.069 | 0 | 0.069 | 0.034 | 0 | 0 | 0.069
3 | 0.138 | 0.345 | 0.172 | 0.345 | 0.276 | 0.276 | 0.31 | 0.172
4 | 0.552 | 0.379 | 0.517 | 0.345 | 0.483 | 0.517 | 0.379 | 0.448
very satisfied | 0.31 | 0.138 | 0.31 | 0.207 | 0.207 | 0.207 | 0.241 | 0.241
summer
winter

## Slide 7
Chart: Percentage of people feeling hot on their homes
| never | rarely | occasionally | quite often | very often
The day | 0.029 | 0.059 | 0.353 | 0.353 | 0.206
The night | 0.059 | 0.176 | 0.382 | 0.235 | 0.147
Chart: The oreintation of bed rooms which people feeling hot at it
| north | south | east | west | NE | NW | SE | SW
During the day | 0.147 | 0.118 | 0.088 | 0 | 0.029 | 0.029 | 0 | 0.029
At night | 0.118 | 0.088 | 0 | 0 | 0.029 | 0 | 0 | 0
In summer

## Slide 8
Chart: Percentage of people feeling cold on their homes
| never | rarely | occasionally | quite often | very often
The day | 0.138 | 0 | 0.586 | 0.241 | 0.034
The night | 0.138 | 0 | 0.345 | 0.345 | 0.172
Chart: The oreintation of bed rooms which people feeling cold at it
| north | south | east | west | NE | NW | SE | SW
During the day | 0.034 | 0.034 | 0 | 0.069 | 0.069 | 0.138 | 0.034 | 0.034
At night | 0 | 0.034 | 0.034 | 0.069 | 0.069 | 0.172 | 0.034 | 0.069
In winter

## Slide 9
Chart: Electricity consumption per month at summer
| up to 100 | 100 - 150 | 150 - 200 | 200 - 250 | 250 - 300 | 300 350 | 350 plus
Fréq. | 0.029 | 0.235 | 0.441 | 0.088 | 0.118 | 0.059 | 0.029
Chart: Electricity consumption per month at winter
| up to 80 | 80 - 120 | 120 - 160 | 160 - 200 | 200 - 240 | 240 - 280 | 280 plus
Fréq. | 0.069 | 0.172 | 0.207 | 0.207 | 0.138 | 0.172 | 0.034
Chart: Gas consumption per month at winter
| up to 40 | 40 - 80 | 80 - 120 | 120 - 160 | 160 - 200 | 200 - 240 | 240 plus
Fréq. | 0.241 | 0.207 | 0.103 | 0.414 | 0 | 0 | 0.034
Energy consumption

## Slide 10
    Environmental analysis
Design builder model

## Slide 11
Building 1 heating & cooling design

## Slide 12
 | Total Energy [kWh] | Energy Per Total Building Area [kWh/m2] | Energy Per Conditioned Building Area [kWh/m2]
Total Site Energy | 471593.86 | 140.66 | 140.66
Net Site Energy | 471593.86 | 140.66 | 140.66
Total Source Energy | 1359313.48 | 405.45 | 405.45
Net Source Energy | 1359313.48 | 405.45 | 405.45
Building 1 simulation
Site and Source Energy

## Slide 13
 | Winter Clothes [hr] | Summer Clothes [hr] | Summer or Winter Clothes [hr]
Facility | 6144.00 | 7038.50 | 3872.50
 | Electricity [kWh] | Natural Gas [kWh] | Additional Fuel [kWh] | District Cooling [kWh] | District Heating [kWh] | Water [m3]
Heating | 0.00 | 0.00 | 0.00 | 0.00 | 215022.95 | 0.00
Cooling | 0.00 | 0.00 | 0.00 | 123449.77 | 0.00 | 0.00
Interior Lighting | 59300.73 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
Interior Equipment | 5603.59 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
Water Systems | 0.00 | 0.00 | 0.00 | 0.00 | 68216.82 | 1068.21
Total End Uses | 64904.32 | 0.00 | 0.00 | 123449.77 | 283239.77 | 1068.21
Time Not Comfortable Based on Simple ASHRAE 55-2004
End Uses

## Slide 14
Our project design
The three buildings are symmetrical in shape but different orientations.
We changed the dimensions and orientations of internal zoning to satisfy the standards.
Architectural design

## Slide 15
To make energy efficient buildings:
Change the orientation of the buildings to achieve the optimum usage of the south direction as possible as we can.
Use a sufficient thermal insulation.
Use solar window in the south elevation by providing adequate shading.

## Slide 16
Site and location

## Slide 17
Contour plan

## Slide 18
Site and orientation of the original buildings

## Slide 19
Plan of the original buildings

## Slide 20
Site plan and orientation after modification

## Slide 21
Internal zoning after modification

## Slide 22
Furniture plan

## Slide 23
North elevation

## Slide 24
South elevation

## Slide 25
East elevation

## Slide 26
West elevation

## Slide 27
Section A-A

## Slide 28
Section B-B

## Slide 29
3D model

## Slide 33
Environmental design

## Slide 34
External walls
Insulations

## Slide 35
Ground floor

## Slide 36
Flat roof

## Slide 37
Glazing detention

## Slide 38
Activity and schedule

## Slide 40
Building 3 heating & cooling design

## Slide 41
Building 3 simulation
 | Total Energy [kWh] | Energy Per Total Building Area [kWh/m2] | Energy Per Conditioned Building Area [kWh/m2]
Total Site Energy | 66381.78 | 72.21 | 72.21
Net Site Energy | 66381.78 | 72.21 | 72.21
Total Source Energy | 167308.10 | 181.99 | 181.99
Net Source Energy | 148878.12 | 161.95 | 161.95
Site and Source Energy

## Slide 42
 | Winter Clothes [hr] | Summer Clothes [hr] | Summer or Winter Clothes [hr]
Facility | 3389.50 | 5617.50 | 2506.50
 | Electricity [kWh] | Natural Gas [kWh] | Additional Fuel [kWh] | District Cooling [kWh] | District Heating [kWh] | Water [m3]
Heating | 0.00 | 0.00 | 0.00 | 0.00 | 15574.55 | 0.00
Cooling | 0.00 | 0.00 | 0.00 | 24540.59 | 0.00 | 0.00
Interior Lighting | 7091.81 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
Interior Equipment | 8153.02 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
Water Systems | 0.00 | 0.00 | 0.00 | 0.00 | 11021.82 | 172.59
Total End Uses | 15244.83 | 0.00 | 0.00 | 24540.59 | 26596.37 | 172.59
Time Not Comfortable Based on Simple ASHRAE 55-2004
End Uses

## Slide 43
New orientation | Old orientation | 
61.32 | 80.34 | Site energy intensity (KWh/m2)
13739.42 | 30776.19 | Heating capacity (KWh)
16363.87 | 19462.32 | Cooling capacity (KWh)
2988 | 5542 | Uncomfortable hour (hr.)
Also we make simulation for building 1 before rotate it to the south direction to compare the results between two cases

## Slide 44
Structural system
One way ribbed slab with hidden beams.
Slab thickness = 25 cm
Structural design
Structural elements
Structural elements | Dimensions
Main beams | 60*25 cm
Secondary beams | 40*25 cm
Columns | 60*25 cm
The soil profile is a soft soil, with 250 KN/m2 Bearing Capacity.
Site And geology

## Slide 45
Loads
Type of load | Load (KN/m2)
Super Imposed Dead | 4.5
Live Load | 3
Super imposed dead & live loads values
Materials
The material that used for beams, slabs and shear walls is concrete B300 (24 MPa) and for columns is concrete B350 (28MPa).
Reinforcing steel yield strength (𝐹𝑦) = 420 MPa.
Design codes
1. ACI -318-08 for reinforced concrete structural design.
2. UBC -97 for earthquake load computations.

## Slide 46
3D ETABS model

## Slide 47
Checks :
Compatibility Check :
The following figures explain the compatibility check from ETABS:
Deformed shape from dead load
Deformed shape from live load
Check is OK.

## Slide 48
Equilibrium check :
Loads | Manual | ETABS | %Error
live load | 3994.6687 KN | 3847.8316 KN | 3.675%
Dead load | 13907.664 KN | 13358.9227 KN | 3.94%
Super Imposed Dead | 10521.4 KN | 10983.6343 KN | 4.39%
Results of error %
Internal forces check (Stress – Strain Check):
Structural elements | Manual moment(KN.m) | ETABS moment(KN.m) | Error %
Secondary beam | 3.93 | 3.8653 | 1.64%
Main beam | 23.69 | 23.5131 | 0.74%
Slab | 4.77 | 4.034 | 15.4%
Results of error %

## Slide 49
For Columns:
Columns | Manual force(KN) | ETABS force(KN) | Error %
C1 | 26.736 | 21.5 | 4.48%
C2 | 714.56 | 718.113 | 0.5%
Error % for two columns
To perform the dynamic analysis and design for building we need this parameters using UBC97 design code:
I = 1
PGA = 0.15g
Cv = 0.15
Ca = 0.15
R = 5.5
Dynamic Analysis (Response spectrum analysis):

## Slide 50
Checks :
1. Period
Manual solution:
T = 0.48 sec.
The period from ETABS found to be:
T = 0.478 sec.
Check is OK
Time period from ETABS
2. Manual Base shear
Weight of the building = 25826.92 KN
Base shear (V) = 2027.5 KN.
Mass participation ratio is larger than 90% in X, Y.
Check is OK.
Modal participating mass ratios

## Slide 51
3. Drift :
For X-direction : ∆m = 6.63 mm.
Maximum deflection ∆m = (L/400) for ( T < 0.7 sec) 6.63mm < (3500/400) = 8.75mm …OK
For Y-direction : ∆m = 7.91 mm. 7.91mm < 8.75 mm …OK
Check is OK.

## Slide 52
Design for flexure moment
Section of ribbed slab
Slab reinforcement
Slab reinforcement

## Slide 53
Main Beams
Secondary Beams
Beams reinforcement
Beams | As(top) (mm2) | Reinforce | As(Bottom) (mm2) | Reinforce
B1 | 495 | 3Ø16mm | 495 | 3Ø16mm
B2 | 560 | 3Ø16mm | 495 | 3Ø16mm
B3 | 800 | 4Ø16mm | 755 | 4Ø16mm
Beams | As(top) (mm2) | Reinforce | As(Bottom) (mm2) | Reinforce
B8 | 330 | 3Ø14mm | 330 | 3Ø14mm
B9 | 386 | 3Ø14mm | 330 | 3Ø14mm

## Slide 54
main beam :
Cross section in beam
Beam detailing
Beams layout

## Slide 55
Columns reinforcement :
As from ETABS = 1500 mm2.
Use 8Ø16 mm/m for each one.
Cross section in column
Stirrups detailing in column

## Slide 56
Section in staircase
Stair reinforcement :

## Slide 57
Footing | No. of footing | Dimensions | Longitudinal reinforcement | Transverse reinforcement
F1(isolated footing for middle columns ) | 6 | 3*2.65*0.45 | 9Ø12 mm/m | 9Ø12 mm/m
F2(isolated footing for edge column ) | 2 | 1.5*1.15*0.47 | 8Ø12 mm/m | 8Ø12 mm/m
F3(wall footing) | 16 | Ex: 2.1*1*0.4 2.15*1.6*0.4 | 7Ø12 mm/m | 7Ø12 mm/m
F4(combined footing) | 2 | 4.7*1 *0.41 | 9Ø20 mm/m | 7Ø12 mm/m
Longitudinal and transverse reinforcement
Footing reinforcement :

## Slide 58
Cross section in footing
Reinforcement details for footing
Isolated footing :
Footings layout

## Slide 59
Wall footing :
Cross section in footing
Reinforcement details for footing
Cross section in footing
Combined footing :
Reinforcement details for footing

## Slide 60
Shear wall reinforcement :
This table shows the reinforcement for shear walls:
Shear wall | Vertical steel (for one side) | Boundary steel (for one side) | Horizontal steel (for one side)
S.W.1 | 10Ø12mm/m | 10Ø12mm/m | 3Ø12mm/m
S.W.2 | 4Ø12mm/m | 3Ø12mm/m | 3Ø12mm/m
S.W.3 | 4Ø12mm/m | 3Ø12mm/m | 3Ø12mm/m
S.W.4 | 10Ø12mm/m | 5Ø12mm/m | 3Ø12mm/m
Longitudinal and transverse reinforcement

## Slide 61
Shear wall layout

## Slide 62
Stirrups detailing in shear wall
Shear wall reinforcement
Shear wall reinforcement :

## Slide 63
Electro-Mechanical design
Electric and lighting design
HVAC design
Drainage design
Water supply design
Acoustical design
Safety design
Elevator design

## Slide 64: Electrical and lighting design
Artificial Lighting system is essential in residential building design because of huge usage in every area in building especially at night, it must distribution in good way with contain energy efficient to provide comfortable, relaxed and good visibility without glare for people

## Slide 65
Reflection factor
Recommended illumination

## Slide 66
For Guest room :
Guest room form by DIALux
We used DIALux program to design artificial lighting for each room.

## Slide 67
Luminaires used :
Luminaires used with details

## Slide 68
Guest room isolines:
Guest room isolines

## Slide 69
3D For Model Guest room :

## Slide 70
Electrical wiring
1.5 mm diameter electrical wires used for lighting system.
2.5mm diameter for sockets and special loads from circuit breakers to the lighting system in the house.
Use 6 mm² cross section area for main wire.
Number of sockets | Room
3 | Master Bedroom
3 | Bedroom
3 | Living room
1 | Bathroom1
4 | kitchens
3 | Bed room
3 | Guest room2
Total number of sockets in each space

## Slide 71
lighting distribution

## Slide 72
Main distribution board

## Slide 73
Distribution board

## Slide 74: HVAC system design
Split Air Conditioner System
A split air conditioner consists of two main parts: the outdoor unit and the indoor unit. The outdoor unit is installed on or near the wall outside of the room or space that you wish to cool. The unit houses the compressor, condenser coil and the expansion coil or capillary tubing.
The indoor unit contains the cooling coil, a long blower and an air filter.

## Slide 75
Split unit distribution

## Slide 76: Drainage system
In drainage water system, drained water movement depends on the natural flow and diameter of pipe. Manholes were used to collect the water pipes that come from W.C's, lavatories, bathtub and floor drains. In our building we separated between black and gray water, each connected to a stack through the shafts but both are connected to the public sewage.
Each floor contain 3 water closet – Flash valve each one has 4dfu with 4″ pipe, 3 lavatory each one has 2dfu with a 2″ pipe, 1 kitchen sink has 2dfu with 2″ pipe, 1 Dish washer has 2dfu with 2″ pipe, 2 shower has 2dfu with2″ pipe, 1 washing machine has 2dfu with2″ pipe, and the water from all of the pipes go out with a 4″ pipe with a total of 25dfu.
Stack diameter is 4 ˝
Slope for pipe 4 ˝ (horizontal pipe) = 1 %
Slope for pipe 2 ˝ = 2 %

## Slide 77
Drainage pipes distribution

## Slide 78
Water drainage in roof

## Slide 79
Water lines:
we will use five water tank, the first main tank under the ground with dimension of (5 * 3 * 2)) capacity 30 m3) and the second one is a roof tank to be installed above the roof of the stairs with dimension of (2.5 * 2 * 1) (capacity 5 m3) the tank on the stair will be faded of water from the main tank located under the ground, we also use gray water tank under the ground (3 m3 capacity ) and another on the roof with (1 m3 capacity ) we will also use storm water tank under the ground with (120 m3 capacity ).
Water supply design

## Slide 80: water system :
we use water system (Gray water , fresh water and storm water) to reduce fresh water usage and to reduce output sewage .
We use Gray water for flushing the toilet after filtered and disinfections , storm water for domestic purposes it's going to be filtered and disinfected then it will be .pumped to fresh water tank

## Slide 81
Water lines

## Slide 82
 | Main feeder | Flat feeder | Branch B.T W.C LAV
FU | 72 | 18 | 2 3 2
gpm | 36 | 14 | 2 3 2
Total FUs for feeders and there demand in G.P.M.

## Slide 83
Diameter | 3.5 | 3 | 2.5 | 2 | 1.5 | 1.25
Loss/100 | .13 | .2 | .5 | 1.5 | 5 | 12
Loss/90.75 | .12 | .18 | .45 | 1.36 | 4.54 | 10.89
Main feeder pipe:- Equivalent length = 55.5ft
Main feeder pipe loss
Diameter | 2 | 1.5 | 1.25 | 1 | 3/4
Loss/100 | .25 | .8 | 2 | 6 | 20
Loss/5.85 | .02 | .05 | .12 | .35 | 1.17
Flat feeder pipe Equivalent length = 5.85ft.
Flat feeder pipe loss
Diameter | 1 | 3/4 | .5 | 3/8
Loss/100 | .2 | .65 | 3.9 | 12
Loss/12.87 | .03 | .08 | .50 | 1.54
Branch feeder pipe loss
Branch pipe :- Equivalent length = 12.87ft.

## Slide 84
 | Diameter | Diameter | Diameter
Options (dim) inch | 1 | 3/4 | 5/8
Loss (psi) | 8 | 4 | .4
meter loss
Loss in meter:

## Slide 85
Pressure =17.37 Psi,
Critical pressure = 12Psi (shower) from table above.
Maximum loss = 17.37-12 = 5.37Psi.
In meter, loss = 0.4 at 5/8 in.
In main feeder, loss = 1.36 at 2 in.
In flat feeder, loss = 0.35 at 1 in.
In branch, loss = 0.5 at 0.5in for shower, and 0.08 at 3/4in for lavatory.
Total loss = 0.4 + 1.36 + 0.35 + 0.5
= 2.61 Psi < 5.37Pis ACCEPTED.

## Slide 86
Water layout
Water supply pipes distribution inside flat

## Slide 87
Water supply pipes distribution for one apartment
water supply pipes distribution inside bathroom

## Slide 88
Sound insulation for external wall
Transmission loss of a two-element composite barrier
External wall STC about (52) dB.
The back ground noise in our site about (65) dB
For external wall with window:
We use aluminum window with (double glazing low eminency 6mm air gap) which will have STC of (29) dB according to specification.
Acoustical design

## Slide 89
Transmission loss of a two-element composite barrier as a function of the relative transmission loss of the components.
TL1 - TL2 = 52 – 29 = 23dB
(S2 / S1) * 100% = ((200 * 225) / (525 * 300)) * 100% = 28.6%
TL1 – TLC = 16
52 – 16 = TLC = 36dB
65 – 36 = 29dB
This is acceptable and quite.
Sound insulation for Internal wall

## Slide 90
According to specification we can assume that the internal wall STC (48) dB
and if we add plaster in both side it will give 48 + 4 = 52 dB which is enough in our cause .
STC Rating of Walls
Improvements in STC Rating of
Lightweight Concrete Block

## Slide 91
result | Actual | Real STC | partition
OK | 52 | 48 | Bedroom-Bedroom
OK | 52 | 50 | Living room-Bedroom
OK | 52 | 52 | Bathroom-Bedroom
OK | 52 | 48 | Corridor-Bedroom
OK | 52 | 48 | Kitchen-Living room
OK | 52 | 50 | Bathroom-Living room
OK | 52 | 48 | Corridor-Living room
OK | 52 | 48 | Bathroom-Kitchen
OK | 52 | 48 | Corridor-Kitchen
OK | 52 | 46 | Corridor-Bathroom
Actual and real STC for internal walls

## Slide 92
Sound insulation for Slab
The slab IIC about (48)dB and with carpet in the floor it will give above 52dB which is enough in our cause according to specification.
result | Actual | Real IIC | partition
OK | 52 | 52 | Bedroom-Bedroom
OK | 52 | 52 | Living room-Living room
OK | 52 | 50 | Bathroom-Bathroom
OK | 52 | 48 | Corridor-Corridor
OK | 52 | 52 | Kitchen-Kitchen
Actual and real IIC for slabs

## Slide 93
Safety design
  It is process to minimize the risks of injury.
  cars parking we found that the safety can be achieved by take in consideration the circulation movement of cars outside and inside the buildings.
  Inside the buildings we choose Fire extinguishers to be used.
Hose and extinguishers cabinet

## Slide 94
According to the tables, we need three elevators. One elevator for each building.
The recommended speed of the elevator is 100 foot per minutes.
The recommended capacity is 1500 pounds which it mean 6 persons.
Elevators

## Slide 95
Survey and cost estimation
The total cost for one building = 601945 $. Thus, the total cost for the three buildings approximately in USD $ 1805835.
Total cost per meter square = 601945/1335 = 450 $/m2.
The total cost for one apartment equal in USD $ 75245.
( with out the cost of the land )
When we take the land cost in consideration the total cost for one apartment equal 85324 $