## Slide 1
Under floor Heating
Graduation Project
submitted By:
Adli Mosleh
Husam weld Ali
Supervisor:
Eng.luqman Herzallah

## Slide 2: Presentation outline:
Abstract
Introduction
Constrains
Literature review
Methodology
Discussion and analysis
Future plan
Conclusion

## Slide 3: Abstract
Under Floor Heating system is central heating system that use three modes of heat transfer radiation, convection and conduction by embedded pipes.
Under Floor Heating system is widely adopted by residential and commercial sectors.
compatibility with different heating device.
heat pumps (Air/water, geothermal heat pumps) with high efficiency, solar power and fuels.

## Slide 4: Introduction
Problem
Heating the house
by environmental friendly and cost effective system.
system
Under floor Heating system
Source of Energy
Air to water Heat Pump vs Gas boiler
Target
Design a UFS for a house in Nablus with minimum cost

## Slide 5: Constraints
choosing a suitable architectural plan
designing the UFH system according to ASHRAE codes.
finding catalogs heat pumps and PEX pipes.
Method of comparison between devices.
How to estimate running cost.
Team management.

## Slide 6: Literature review
UFH Parameters
Heat Transfer Modes
Thermal Comfort
History
Gas Boiler
Heat Pumps
Under Floor Heating

## Slide 7: Methodology
Heat load calculation
Panel Design
Pipe Design
MATLAB
Codes
Economic
Study

## Slide 8: Heat load calculation
select outside design condition T= 4.7 , 5 m/s ,
select inside design condition T= 22 , no change in humidity.
find , for each room.
find U for walls , ceiling , window , floors , doors.
find the sum of heat loss in each room.
find Q for the building.

## Slide 9
Finding water flow rate for each room by this equation (4.21)
The water velocity in pipes should be in range 0.2 to 1.2 m/sec and maybe increased to 2.4 m/sec.
Finding the longest loop from the storage tank.
Find pump flow rate.
Select circulating pump.
Select each main diameter for each room by finding
Select the appropriate diameter with appropriate .

## Slide 10: Infiltration load calculation
Room | l/s | Q (W)
Guest | 40 | 830.4
bed 1 | 30 | 622.8
bed 2 | 50 | 1038
bed 3 | 25 | 519
C 1 | 20 | 415.2
C 2 | 31 | 643.56
Living | 40 | 830.4
Kitchen | 40 | 830.4
Dining | 40 | 830.4
Room | Area (m^2) | Volume(m^3) | ACH
Guest | 22.74 | 90.96 | 1.5
bed 1 | 20.41 | 81.64 | 1
bed 2 | 23.52 | 94.08 | 2
bed 3 | 20.7 | 82.8 | 1
C 1 | 9.75 | 39 | 1.5
C 2 | 14.1 | 56.4 | 2
Living | 27 | 108 | 1.5
Kitchen | 23.6 | 94.4 | 1.5
Dining | 22.6 | 90.4 | 1

## Slide 11: External and internal wall losses
External Walls Losses |  |  | 
Room | Area () | A*U | Q(W)
Guest | 38.575 | 28.12118 | 486.4963
bed 1 | 19.415 | 14.15354 | 244.8562
bed 2 | 35.05 | 25.55145 | 442.0401
bed 3 | 41.125 | 29.98013 | 518.6562
C 1 | 0 | 0 | 0
C 2 | 4.575 | 3.335175 | 57.69853
Living | 26.525 | 19.33673 | 334.5253
Kitchen | 37.525 | 27.35573 | 473.254
Dining | 0 | 0 | 0
External Walls Losses |  |  | 
Room |  |  | Q(W)
Guest | 38.575 | 28.12118 | 486.4963
bed 1 | 19.415 | 14.15354 | 244.8562
bed 2 | 35.05 | 25.55145 | 442.0401
bed 3 | 41.125 | 29.98013 | 518.6562
C 1 | 0 | 0 | 0
C 2 | 4.575 | 3.335175 | 57.69853
Living | 26.525 | 19.33673 | 334.5253
Kitchen | 37.525 | 27.35573 | 473.254
Dining | 0 | 0 | 0
Internal Walls Losses |  |  |  | 
Room | Area | T un (℃) | A*U | Q(w)
Guest | 0 | 13.35 | 0 | 0
bed 1 | 9.6 | 13.35 | 17.2896 | 83.04
bed 2 | 11.4 | 13.35 | 20.5314 | 98.61
bed 3 | 17 | 13.35 | 30.617 | 147.05
C 1 | 15 | 13.35 | 27.015 | 129.75
C 2 | 8 | 13.35 | 14.408 | 69.2
Living | 0 | 13.35 | 0 | 0
Kitchen | 7.2 | 13.35 | 12.9672 | 62.28
Dining | 0 | 13.35 | 0 | 0
Internal Walls Losses |  |  |  | 
Room |  | T un (℃) |  | Q(w)
Guest | 0 | 13.35 | 0 | 0
bed 1 | 9.6 | 13.35 | 17.2896 | 83.04
bed 2 | 11.4 | 13.35 | 20.5314 | 98.61
bed 3 | 17 | 13.35 | 30.617 | 147.05
C 1 | 15 | 13.35 | 27.015 | 129.75
C 2 | 8 | 13.35 | 14.408 | 69.2
Living | 0 | 13.35 | 0 | 0
Kitchen | 7.2 | 13.35 | 12.9672 | 62.28
Dining | 0 | 13.35 | 0 | 0

## Slide 12: Window and door losses
Windows Losses |  |  | 
Room | Area (M^2) | A*U ( ) | Q(w)
Guest | 5.625 | 19.6875 | 340.5938
bed 1 | 1.875 | 6.5625 | 113.5313
bed 2 | 3.75 | 13.125 | 227.0625
bed 3 | 1.875 | 6.5625 | 113.5313
C 1 | 0 | 0 | 0
C 2 | 0 | 0 | 0
Living | 1.875 | 6.5625 | 113.5313
Kitchen | 1.875 | 6.5625 | 113.5313
Dining | 0 | 0 | 0
Windows Losses |  |  | 
Room | Area (M^2) |  | Q(w)
Guest | 5.625 | 19.6875 | 340.5938
bed 1 | 1.875 | 6.5625 | 113.5313
bed 2 | 3.75 | 13.125 | 227.0625
bed 3 | 1.875 | 6.5625 | 113.5313
C 1 | 0 | 0 | 0
C 2 | 0 | 0 | 0
Living | 1.875 | 6.5625 | 113.5313
Kitchen | 1.875 | 6.5625 | 113.5313
Dining | 0 | 0 | 0
Door Losses |  |  | 
Room | Area (m^2) | A*U ( ) | Q (W)
Guest | 0 | 0 | 0
bed 1 | 0 | 0 | 0
bed 2 | 1.615 | 4.522 | 39.1153
bed 3 | 0 | 0 | 0
C 1 | 1.615 | 0 | 0
C 2 | 1.615 | 21.67 | 341
Living | 0 | 0 | 0
Kitchen | 0 | 0 | 0
Dining | 0 | 0 | 0
Door Losses |  |  | 
Room | Area (m^2) |  | Q (W)
Guest | 0 | 0 | 0
bed 1 | 0 | 0 | 0
bed 2 | 1.615 | 4.522 | 39.1153
bed 3 | 0 | 0 | 0
C 1 | 1.615 | 0 | 0
C 2 | 1.615 | 21.67 | 341
Living | 0 | 0 | 0
Kitchen | 0 | 0 | 0
Dining | 0 | 0 | 0

## Slide 13: Floor and Ceiling losses
Floor Losses |  |  | 
Room | Area | A*U ( ) | Q (W)
Guest | 22.74 | 4.50252 | 54.03024
bed 1 | 20.41 | 4.04118 | 48.49416
bed 2 | 23.52 | 4.65696 | 55.88352
bed 3 | 20.7 | 4.0986 | 49.1832
C 1 | 9.75 | 1.9305 | 23.166
C 2 | 14.1 | 2.7918 | 33.5016
Living | 27 | 5.346 | 64.152
Kitchen | 23.6 | 4.6728 | 56.0736
Dining | 22.6 | 4.4748 | 53.6976
Floor Losses |  |  | 
Room | Area |  | Q (W)
Guest | 22.74 | 4.50252 | 54.03024
bed 1 | 20.41 | 4.04118 | 48.49416
bed 2 | 23.52 | 4.65696 | 55.88352
bed 3 | 20.7 | 4.0986 | 49.1832
C 1 | 9.75 | 1.9305 | 23.166
C 2 | 14.1 | 2.7918 | 33.5016
Living | 27 | 5.346 | 64.152
Kitchen | 23.6 | 4.6728 | 56.0736
Dining | 22.6 | 4.4748 | 53.6976
Ceiling |  |  | 
Room | Area (m^2) | A*U ( ) | Q (W)
Guest | 22.74 | 22.49259 | 389.1217862
bed 1 | 20.41 | 20.18794 | 349.2513482
bed 2 | 23.52 | 23.2641 | 402.4689715
bed 3 | 20.7 | 20.47478 | 354.2137632
C 1 | 9.75 | 9.64392 | 166.839816
C 2 | 14.1 | 13.94659 | 241.2760416
Living | 27 | 26.70624 | 462.017952
Kitchen | 23.6 | 23.34323 | 403.8379136
Dining | 22.6 | 22.35411 | 386.7261376
Ceiling |  |  | 
Room | Area (m^2) |  | Q (W)
Guest | 22.74 | 22.49259 | 389.1217862
bed 1 | 20.41 | 20.18794 | 349.2513482
bed 2 | 23.52 | 23.2641 | 402.4689715
bed 3 | 20.7 | 20.47478 | 354.2137632
C 1 | 9.75 | 9.64392 | 166.839816
C 2 | 14.1 | 13.94659 | 241.2760416
Living | 27 | 26.70624 | 462.017952
Kitchen | 23.6 | 23.34323 | 403.8379136
Dining | 22.6 | 22.35411 | 386.7261376

## Slide 14: Total heat load
Total heat load for each room |  |  |  | 
Room | Q(w) | Q(KW) | A (m^2) | q (W/M^2)
Guest | 2100.642 | 2.100642 | 22.74 | 92.37652
bed 1 | 1461.973 | 1.461973 | 20.41 | 71.63023
bed 2 | 2303.18 | 2.30318 | 23.52 | 97.92434
bed 3 | 1701.634 | 1.701634 | 20.7 | 82.20456
C 1 | 734.9558 | 0.734956 | 9.75 | 75.38008
C 2 | 1386.236 | 1.386236 | 14.1 | 98.31462
Living | 1804.627 | 1.804627 | 27 | 66.83802
Kitchen | 1939.377 | 1.939377 | 23.6 | 82.17698
Dining | 1270.824 | 1.270824 | 22.6 | 56.23114
summation | 14703.45 | 14.70345 | 184.42 | 80.34183

## Slide 15: Panel design

## Slide 16: It composed of four main layers :
Layer | Material | Thickness (mm) | K (w/m.k) | R (
Tiles | Ceramic | 6 | 1 | 0.0006
Concrete slab | Concrete | 200 | 1.3 | 0.153
Insulating | Polystyrene | 140 | 0.035 | 4
Compacted | 50% of sand | 250 | 1.625 | 0.153
Gravel | 50% of stone |  |  | 
Layer | Material | Thickness (mm) | K (w/m.k) | 
Tiles | Ceramic | 6 | 1 | 0.0006
Concrete slab | Concrete | 200 | 1.3 | 0.153
Insulating | Polystyrene | 140 | 0.035 | 4
Compacted | 50% of sand | 250 | 1.625 | 0.153
Gravel | 50% of stone |  |  | 

## Slide 17: Pipe design
UFH Parameters:
There are two ways for designing appropriate combination of these parameters.
First one is by equations and iteration solution which is complicated,
Second way is using ASHRAE figure.

## Slide 19: Final results
Room | AUST | Q | AUST - T in
Guest | 20.56881 | 92.37652 | -1.431188885
bed 1 | 20.78135 | 76.71597 | -1.218649577
bed 2 | 20.34693 | 97.92434 | -1.653072402
bed 3 | 19.98063 | 97.24804 | -2.019373548
C 1 | 20.28009 | 75.38008 | -1.71991393
C 2 | 20.89079 | 118.9274 | -1.10921219
Living | 21.35759 | 82.2158 | -0.642409518
Kitchen | 20.31633 | 77.77868 | -1.683668185
Dining | 21.95294 | 83.78866 | -0.047056
Room | q̋ | Tf | M | Tw | Di | Do
Guest | 92.37652 | 29 | 25 | 47.5 | 21.5 | 25
Bed Room 1 | 71.63023 | 28 | 35 | 47.5 | 21.5 | 25
Bed Room 2 | 97.92434 | 29.5 | 20 | 47.5 | 21.5 | 25
Bed Room 3 | 82.20456 | 28 | 20 | 47.5 | 21.5 | 25
C 1 | 75.38008 | 27 | 35 | 47.5 | 21.5 | 25
C 2 | 98.31462 | 29.5 | 22.5 | 47.5 | 21.5 | 25
Living | 66.83802 | 27 | 30 | 47.5 | 21.5 | 25
Kitchen | 82.17698 | 27.5 | 35 | 47.5 | 21.5 | 25
Dining | 56.23114 | 27.5 | 30 | 47.5 | 21.5 | 25

## Slide 20: MATLAB Results

## Slide 21: Electricity demand of the heat pump

## Slide 22: Heat Pump consumption
Month | Period | To | COP | heat load | kwh/10 days | kwh/month
Nov | 1st 10 days | 9 | 2.99786 | 18.75456 | 1030.39713 | 1632.34738
 | 2nd 10 days | 16.1 | 3.88043536 | 5.11488 | 217.102141 | 
 | 3rd 10 days | 12.1 | 3.64841264 | 8.5248 | 384.848109 | 
Dec | 1st 10 days | 14.6 | 3.79253787 | 6.3936 | 277.667242 | 1281.80156
 | 2nd 10 days | 11.2 | 3.59159226 | 9.37728 | 430.030211 | 
 | 3rd 10 days | 7.8 | 3.42397584 | 11.93472 | 574.104106 | 
Jan | 1st 10 days | 13.1 | 3.70570714 | 7.67232 | 341.008123 | 1492.68177
 | 2nd 10 days | 9.6 | 3.50725067 | 10.656 | 500.42214 | 
 | 3rd 10 days | 6.2 | 3.34176779 | 13.21344 | 651.251503 | 
Feb | 1st 10 days | 14.4 | 3.79253787 | 6.3936 | 277.667242 | 1382.05777
 | 2nd 10 days | 10.5 | 3.56335987 | 9.80352 | 453.139024 | 
 | 3rd 10 days | 6.7 | 3.34176779 | 13.21344 | 651.251503 | 
Mar | 1st 10 days | 17.2 | 3.96939963 | 3.83616 | 159.17725 | 1024.79417
 | 2nd 10 days | 13 | 3.70570714 | 7.67232 | 341.008123 | 
 | 3rd 10 days | 8.8 | 3.47937386 | 11.08224 | 524.608792 | 
The total electricity consumption is 6813.618 KWH/Season.
The total running cost is 6813.618*0.55 = 3747.524 Nis

## Slide 23: Gas boiler Degree Day
Month | Nov | Dec | Jan | Feb | Mar | summation
temp | 16.1 | 11.2 | 9.6 | 10.5 | 13 | 893.2
days | 30 | 31 | 31 | 28 | 31 | 
DD | 57 | 210.8 | 260.4 | 210 | 155 | 

## Slide 24: Economic study
HEAT PUMP:
the average investment cost with installation were obtained from contracting companies as 37000 Nis. From calculations the seasonal running cost for the system were 3747 Nis.
GAS BOILER:
the average investment cost with installation were obtained from contracting companies as 6500 Nis. From calculations the seasonal running cost for the system were 6800 Nis.
RUNNING COST PERCENTAGE AND PAYBACK PERIOD
3747/6800 *100% = 55% .
Payback period is 9.99

## Slide 25: Conclusion
UFH is environmental friendly “it works on low operating temperature”
Electric air to water heat pump is safe for local environment.
UFH is profitable investment.
Air to water heat pump is good investment !!

## Slide 26
Any question !!