## Slide 1
An-Najah National University
Faculty of Engineering
Civil Engineering Department
Water Distribution Networks and WasteWater Networks of Tammon Town
Prepared by:
Ahmad AL-Qanni Hassan Mhamed
Emran Bsharat Mohammad Fuqaha
Supervisor:
Dr. Amal Al-Hudhud
may 2012

## Slide 2: Introduction

## Slide 3: Presentation Layout
Introduction
Objectives
Plan
Description of the location
Design WDN & Sewer net work
Conclusion

## Slide 4: INTRODUCTION
Importance of water
قال الله تعالى :{ وجعلنا من الماء كل شئ حي} صدق الله العظيم. سورة الأنبياء الآية 30
Importance of Water Distribution Networks (WDNs)
People who live in different locations, whom their homes are not located in the same area and there is considerable distance between them they need to have water distribution networks (WDNs).

## Slide 5: Objectives
Apply the theoretical background which we have learned through the last four years with the reality and practical life.
Design the water distribution net work of Tammon by using WATERCAD software.

## Slide 6
Studying and analyzing the water consumption and estimating the losses.
cost estimating for the project .
Design wastewater net work.
Secondary Goals

## Slide 7: Study area

## Slide 8: DESCRIPTION OF THE STUDY AREA
Location
  Tammon is a Palestinian town in the Tubas governorate, located 23 kilometers northeast of Nablus and five kilometers south of Tubas in the northeastern Wes Bank.
Population
  The number of the population, according to the statistics in 2007 is about 10,687 persons.

## Slide 9: DESCRIPTION OF THE STUDY AREA
Rain
Average annual rainfall in Tammon = 350 mm.
The average number of rain days = 40-60 days./year
Temperature
Rates of temperature in summer about (25° – 35°) C.
Rates of temperature in winter about (12° – 14° ) C.

## Slide 10: DESCRIPTION OF THE STUDY AREA
From question area :
Per capita consumption of water 64 L/capita/day.
Average number of persons per family 6.

## Slide 11: DESCRIPTION OF THE STUDY AREA
Monthly per capita income:
Notes: This diagram shows the monthly income per capital in Tammoun. We got theses numbers after analyzing the questionnaires we already distributed in Tammoun city.

## Slide 13: Methodology
Site Investigation
زيارة الموقع
Collecting Data
جمع المعلومات للمشروع
Tammon Council
مجلس قروي طمون
Jenin Municipality
بلدية جنين
Working with Data
معالجة المعلومات
Supply
التزويد
AutoCAD map
Consumption
الاستهلاك
AutoCAD
Software
GIS
Analyze the WDN
تحليل الشبكة
WaterCAD
Software
Results
النتائج
Demand
Pipes and Nodes
Pump
Question area

## Slide 14: WATER CAD Software
Water CAD is a computer software used for analyze the water distribution networks. It can be used for different types of application in the distribution system analysis such as a simple network design.
Water CAD analysis output are : the flow for each pipe in the network and the velocities, the pressure for each node and the total head, the head loss in each pipe and more of hydraulic output analysis.
Water CAD

## Slide 15: wdn analysis
Present per Capita Water Demand
Present water based on questioner is 64 L/C/d. The future water consumption will be 64 + (25*1.5) =101.5L/C/d.
Design water supply is 101.5 /(1-15%)=119.41.
the future water consumption is 120 L/C/d
Geometric growth method:
Population of the Tammon is estimated to be 10687capita according to PCBS (2007). The population growth rate can be calculated by taking the population between two period like 1997and 2007(7635 and 10687) respectively. And applying the geometric growth.
Pf = Pp (1+r) ⁿ
-1}*100%
10687 = 7635 (1+r)10
Then r =3.42% use r=3.5% in this project
Present Per Capita Water Demand & estimate growth rate

## Slide 16: wdn analysis
Future per Capita Water Demand
To estimate future water demand for each node, the nodal water demand shall be multiplied by the future demand factor; this factor was found as following formula
Factor = () *() *average # of person
Present demand = 64 liter/capita/day
Future demand = 120 liter/capita/day
Present population = 12693 persons (according to 2012 year)
Future population = 29997 persons (for year 2037)
Average number of person from questionnaire = 6*2 (assume we have Two floors inTammon town )
Then factor = 54.
Present vs. Future Per Capita Water Demand

## Slide 17: WDN Analysis
Calculate the demand for each node:
J-11: Number of houses=12
Demand= .12*54*12=78 m3/day

## Slide 18: Design wdn
TAMMOUN WDN
172 nodes
207 Pipes
36Loops
Reservoir = 406

## Slide 19: Output data description:
Figure : the pressure head at nodes before raising the reservoir.

## Slide 20: Output data description:
Figure 6.5: velocity for each pipe before raising the reservoir

## Slide 21: Design wdn
Reservoir = 440 m
8 inch
6 inch
4 inch
3 inch
2 inch
Reservoir 440m

## Slide 22: Output data description:
Figure : the pressure head at nodes after raising the reservoir

## Slide 23: Output data description:
Figure 6.6: Velocity for each pipe.

## Slide 25: Recommendation and conclusion
In Tammon there is no WDN so we recommended starting in implementation WDN as soon as possible.
The maximum difference in node elevations is about 122.11 m.
Maximum velocity in the network equal 2.36 m/s and the minimum velocity 0.2 m/s.
I choose a pump give a head (35 m) to give at least 20m pressure head at nodes to reach all citizens.

## Slide 26: Design Of Tammon Waste Water Network

## Slide 27: Objectives:
To design a wastewater network collection system for Tammon town.
There is no wastewater collection system in the town, so people get red of the wastewater by using cesspits.
This way of disposal is not good because:
Bad smell especially during pumping.
Economical problems since it cost them (pumping process).
Its location near the collection wells.

## Slide 28: Layout of The System:
The lay out of the system is made by drawing the manhole along the streets take into consideration that the flow is by gravity.
We use Excel Program to design wastewater collection system.

## Slide 29
Design of sewer network

## Slide 30
Design of sewer network
12 inch
10 inch
8inch

## Slide 31: Sewer line and manholes for our project
Used 196 manholes totally of the collection system.
The total length of sewer line is approximately 11.11 kilometers (km).
The trunk main line sizes vary from (8 to 12) inch.

## Slide 33
Drawing network using AutoCAD:
Manholes
Line
polygon

## Slide 34
2. taking some information from the map in AutoCAD:
Number of person in each polygon.
Length of the pipe.
Elevation of each manholes.
3. Using Excel sheet to design:
Calculate maximum hourly flow
Slope
Velocity(use manning)

## Slide 35: Procedure
Calculate the future population by the following equation:
P=p0 *(1+r)n
The population of Tammon in 2042 is35627 person
We assumed the water demand =(100) L/C/D.
80% of demand taken as waste water.
Using excel sheet to design.

## Slide 36: excel sheet for design

## Slide 37: main characteristics for the design
Velocity (0.6-3.5)m/s.
Slope (0.008-0.17)m/m.
Distance between manholes: should not exceed 80 m.
Main characteristics for the design

## Slide 38: Main characteristics for the design
Manning coefficient =0.01.
Full flow velocity= (1/n) x (R2/3) * (S0.5)
From PWA the minimum size for pipe equal 8in.

## Slide 40: Sewer lines
This table show length of diameter used:
Diameters of Pipe(in) | Length(m)
8 | 8411
10 | 1687
12 | 1011

## Slide 41: Velocity for pipes
Chart: No.Pipe

## Slide 42: Problems of sewer in our project
On slope of sewer line dose not located with range (0.008-0.17). Used drop manhole.
In some pipes the velocity is small than minimum0.6 m/s because this pipes is sub pipe and there is a little flow income to it.

## Slide 44: Conclusion and Recommendation
In Tammon there is no wastewater so we recommended starting in implementation wastewater as soon as possible.
In the design we depend on gravity to transport the wastewater and we didn't need any pump .
Maximum velocity in the network equal 3.5 m/s and the minimum velocity 0.278 m/s

## Slide 45
Thank You…
THANKS FOR YOUR ATTENTION