## Slide 1: An-Najah National University Building Engineering Department
Redesign of the Nissan Car Showroom in Ramallah
Presented By: Supervisor:
Hamza Nayef Dr. Muhannad Haj Hussein
Mosab Abdulghani
Omar Jamal Ali Date: December 24, 2018
Ihab Aqraa

## Slide 2: Presentation Outline
Site Analysis
Architectural Design
Structural Design
Environmental Design
Electro-Mechanical Design
Safety Design
Cost Estimation

## Slide 3: Site Analysis

## Slide 4: Site Location
The showroom is located at Al-Bireh city, which is a city in the central West Bank.
The area of the site is about 2349 m2. This site has one street with 7 m wide.

## Slide 5: Climate Conditions
Temperature

## Slide 6: Climate Conditions
Wind Direction & Wind Speed

## Slide 7: Accessibility and Circulation

## Slide 8: Nearby Buildings and Services

## Slide 9: Architectural Design

## Slide 10: Architectural Facilities
Main Entrance
Main Showroom
Offices
Maintenance Area
Ramps
Washing and Preparation Station
Painting Station
Body Shop Stations
Storage Space

## Slide 11: Second Basement Floor

## Slide 12: First Basement Floor

## Slide 13: Ground Floor

## Slide 14: First Floor

## Slide 15: Second Floor

## Slide 16: Western Elevation

## Slide 17: Eastern Elevation

## Slide 18: Northern Elevation

## Slide 19: Southern Elevation

## Slide 20: Section A-A

## Slide 21: Section B-B

## Slide 24: Environmental Design

## Slide 25: Thermal Design
U Value for Building Envelope
Component | U-value (W/m2.k)
External Wall | 0.444
Internal Wall | 2.032
Floor | 0.434
Roof | 0.363
Windows (In Southern, Eastern and Western Elevations) | 1.493
Windows (In Northern Elevation) | 2.511

## Slide 26: Thermal Design
3D Model in DesignBuilder

## Slide 27: Thermal Design
Shading
Louvers System
CNC
Nearby Buildings

## Slide 28: Thermal Design
Shading
In Summer Day
21 July at 8 AM
21 July at 12 PM

## Slide 29: Thermal Design
Shading
In Winter Day
21 January at 8 AM
21 January at 12 PM

## Slide 30: Thermal Design
Heating and Cooling Loads
Cooling Load = 94.61 kW
Heating Load = 76.6 kW
Site and Source Energy

## Slide 31: Thermal Design
Comfort PMV-Set

## Slide 32: Daylight
Daylighting Data

## Slide 33: Daylight
Summary Results

## Slide 34: Acoustical Design
Absorption Coefficient
Element | Finish Material | Absorption Coefficient (α) |  |  |  |  |  |  |  | 
 |  | 63 Hz | 125 Hz | 250 Hz | 500 Hz | 1000 Hz | 2000 Hz | 4000 Hz | 8000 Hz | 16000 Hz
Windows | Double Glaze 6 mm | 0.12 | 0.10 | 0.06 | 0.04 | 0.03 | 0.03 | 0.03 | 0.04 | 0.04
Floor | Tile | 0.01 | 0.02 | 0.06 | 0.14 | 0.37 | 0.6 | 0.65 | 0.6 | 0.7
Walls | Plaster | 0.03 | 0.04 | 0.05 | 0.06 | 0.08 | 0.04 | 0.06 | 0.05 | 0.06
Roof | Plaster Decorative Panels | 0.1 | 0.2 | 0.22 | 0.18 | 0.15 | 0.15 | 0.16 | 0.15 | 0.16
Doors | Hollow Core Plywood | 0.44 | 0.41 | 0.35 | 0.25 | 0.2 | 0.15 | 0.15 | 0.13 | 0.12

## Slide 35: Acoustical Design
RT60 for the Showroom
The Recommended Range (1.0–1.4)
At 50 % Occupancy | 
FREQ.. | RT60
63 Hz | 4.75
125 Hz | 4.18
250 Hz | 2.51
500 Hz | 1.04
1 kHz | 0.53
2 kHz | 0.46
4 kHz | 0.49
8 kHz | 0.51
16 kHz | 0.48

## Slide 36: Acoustical Design
RT60 for the Manager Office
The Recommended Range (0.6–1.2)
At 50 % Occupancy | 
FREQ.. | RT60
63 Hz | 3.03
125 Hz | 2.67
250 Hz | 1.89
500 Hz | 0.93
1 kHz | 0.50
2 kHz | 0.44
4 kHz | 0.44
8 kHz | 0.42
16 kHz | 0.40

## Slide 37: Acoustical Design
STC for the External Wall
The Recommended Range (50 – 60) dB

## Slide 38: Acoustical Design
STC for the Manager Office adjacent to the next office
The Recommended Value = 45 dB

## Slide 39: Acoustical Design
IIC for Floor
The Recommended Range (35 – 55) dB

## Slide 40: Structural Design

## Slide 41: Codes and Loads
Codes
ACI 318-14 for reinforced concrete design
UBC 97 for seismic design and its load combinations
ASCE 7 for load combinations
Loads
Dead Load
Superimposed Load = 4 kN/m2
Live Load = 5 kN/m2

## Slide 42: Structural System
Materials
Concrete B350 and B400
Yield Strength of Steel= 420 MPa
Soil Bearing Capacity = 350 kN/m2
Structural System
One Way Solid Slab with Drop Beams

## Slide 43: Structural System
Sections Dimensions
Member | Width | Depth
Slab | 30 cm Thickness | 
Main Beams | 150 cm | 100 cm
Secondary Beams | 60 cm | 30 cm
Column 1 | 160 cm | 70 cm
Column 2 | 70 cm | 50 cm
Shear Wall | 40 cm Thickness | 

## Slide 44: Structural System
Seismic Analysis Parameters
Seismic Zone: 2B (Z=0.2)
Soil Profile: SB
Acceleration Seismic Coefficients Ca = 0.2
Velocity Seismic Coefficient Cv = 0.2
Importance Factor I = 1.0
Force Reduction Factor R = 5.5

## Slide 45: Structural System
Model in ETABS

## Slide 46: Model Checks
Equilibrium Check
 | Manual | ETABS | Error % | Assessment
Live Load | 10540.85 | 10475.91 | 0.62 % | OK
Superimposed Load | 18646.64 | 18861.53 | 1.14 % | OK
Dead Load | 66727.13 | 65646.18 | 1.65 % | OK

## Slide 47: Model Checks
Compatibility Check

## Slide 48: Model Checks
Internal Forces Check
All columns, beams and slab that checked, the difference between ETABS and hand calculations was been less than10%.

## Slide 49: Model Checks
Deflection Check
Maximum Allowable Deflection = L/240 = 12/240 = 50 mm

## Slide 50: Model Checks
Period Check
Method A Period = 0.497 sec
Method B Period (From ETABS) = 0.689 sec
Method B Period < 1.4 Method A Period
0.689 sec < 0.696 sec → OK

## Slide 51: Model Checks
Base Shear Check
Vx Manual = 7920.6 kN
Vy Manual = 4598.3 kN
Vx ETABS = 7930 kN
Vy ETABS = 4599 kN
V Manual < V ETABS → OK

## Slide 52: Model Checks
Drift Check
Story | Δmx (mm) | Δmy (mm) | Limitation (mm) | Assessment
BF2 | 0.34265 | 3.7576 | 80 | OK
BF1 | 0.7392 | 11.52305 | 80 | OK
GF | 4.67005 | 5.26295 | 94 | OK
F1 | 7.4921 | 35.13895 | 94 | OK
F2 | 9.2708 | 36.4056 | 94 | OK

## Slide 53: Beams Distribution

## Slide 54: Structural Elements Details
Slab Reinforcement

## Slide 55: Structural Elements Details
Beams Reinforcement

## Slide 56: Structural Elements Details
Columns Reinforcement

## Slide 57: Structural Elements Details
Footings Reinforcement

## Slide 58: Electrical Design

## Slide 59: Ground Floor Sockets Plan

## Slide 60: Luminaires Layout

## Slide 61: 3D Rendering Model (DIALux)
First Floor

## Slide 62: Ground Floor Lighting Plan

## Slide 63: Power Consumption Estimation
Type | Consumption (kW/day) | Consumption (kW/month) | Cost (NIS/day) | Cost (NIS/month)
Lighting | 205.31 | 4106.11 | 147.82 | 2956.4
Power | 426.40 | 8528.06 | 307.01 | 6140.2
Total | 632 | 12634 | 455 | 9097

## Slide 64: Mechanical Design

## Slide 65: Water Supply System
Number of Tanks = 8 Tanks

## Slide 66: Drainage System

## Slide 67: Drainage System

## Slide 68: Elevators
Three elevators were designed in the project:
Elevator for Staffs
Elevator for Costumers
Hydraulic Elevator for Cars

## Slide 69: HVAC System
VRF System Used
From DesignBuilder
Total Cooling Load = 94.61 kW
Total Heating Load = 76.6 kW

## Slide 70: HVAC System
VRF System
Outdoor Unit Selected from TOSHIBA Company with:
Total Cooling Load = 96 kW
(MMY-AP3414FT8-E) Model

## Slide 71: HVAC System
VRF System
Fan Coil from Daikin Company with:
Total Cooling Capacity = 16.4 kW
Total Heating Capacity = 19.81 kW
Volumetric flow rate = 0.83 m3/s
(FWD16AT) Model

## Slide 72: Ground Floor HVAC System Layout

## Slide 73: Firefighting and Safety Design

## Slide 74: Emergency Fire Protection System
Fire Extinguishers
Hose Stations
Sprinklers
Warning Signs

## Slide 75: Emergency Fire Protection System

## Slide 76: Heat Detector System

## Slide 77: Quantity Surveying and Cost Estimation

## Slide 78: Cost Estimation
Total Direct Project Cost | 5,807,252
Total Building Area = 3106 m2
Direct Unit Cost = 5807252/3106
= 1870 NIS/m2
Direct Unit Cost = 361 JOD/m2

## Slide 79: Done! Thanks a Lot