## Slide 1: An-Najah National University Faculty Of Engineering Civil Engineering Department
DESIGN OF WATER & WASTEWATER NETWORK FOR SHWAIKA VILLAGE
Prepared By :
Anas S. Awwad
Amr A. Sleebi
Ahmed N. Hamdan
Supervision of Dr. Sameer Shadeed

## Slide 2: Outline:
Objectives of the project.
Significance of the work.
Study area.
Methodology.
Modeling and design.
Results and conclusions.

## Slide 3: Objectives
Design efficient water distribution network (WDN) for SHWAIKA village.
Design wastewater collection network(WWCN) for SHWAIKA village.

## Slide 4: Significance of the work
To supply water at an adequate pressure and flow.
To transport sewage through SHWAIKA VILLAGE to sewage treatment plants.
To have an economic design as possible for both networks.

## Slide 5
Study area

## Slide 6
Data Collection:
Contour, Houses, roads, Boundary, aerial photo and amount of consumption water for each consumer,… etc. manhole, conduits, road contour and outfall for the village.

## Slide 7
Area and land use:
The present population is 16,400 persons.
The area is approximately 6932 donum Which include agriculture lands 800 donum and buildings is 412 donum.
Shwaika village is a flat land, The ground surface in the village varies from 100 m to 450 m (A.M.S.L) (where the water tank is located).

## Slide 8
Water Resources and Water Supply:
Almsnawy well which established at 2001 with depth 125 m and it is supply village with water by (188 cm/hr).
Almal'ab (established at 1973), the depth of well is 155 m and it is supply village with water by (190 cm/hr).
Althahra tank which has a volume 550 cm and this tank get water from Almsnawy and Almal'ab wells by the pump station.

## Slide 9
Population Prediction:

## Slide 11: WDN
Design constraints:
Pressure at junction between (20-100) m.H2O.
Velocity in pipe (0.3-3.0) m/s.

## Slide 13
Location & Connecting Manhole
Before starting the design we should consider that the manholes must be located at the roads networks wherever there is:
An intersection.
Change in slop.
Change in direction.
Maximum distance of (30-50) m.

## Slide 15
Design constraints:
Partial full flow conditions 80 %
Cover depth [0.6 - 5.0] m
Slope [1 - 10] %
Velocity [0.6 - 3.0] m/s

## Slide 16
MODELING AND DESIGN

## Slide 17: Methodology

## Slide 18
Firstly, we will divide this village to three regions because we have different population density which are:
Shwaika 1
Shwaika Center
Shwaika 2
WDN

## Slide 20
Secondly, The load on each region calculate by:

## Slide 22
WWCN

## Slide 24
Loads on manholes
The loads on the manholes must be calculated based on the number of the houses that are connected to each manhole, but this going to need a lot of data that are missing, so we calculate the load as we are going to explain.

## Slide 25
Export Manholes and conduit from SewerCAD
Create Digital Elevation Model (DEM)

## Slide 26
Preparation of manholes and conduits
Excavate Manholes and conduits
Find the catch basin catchments

## Slide 28
By finding the catchment of each manhole using ArcHydro Tool we can find the population for each manhole as follows:

## Slide 29
Results And Discussion

## Slide 30: WDN

## Slide 31: Pressure (m H2O)

## Slide 32
So we want to solve this problem by add pumps to increase the pressure with acceptable limits.
Five pumps were added to the water network with the following characteristics:

## Slide 33
Chart: Velocity Variation

## Slide 34
Chart: Pressure Variation

## Slide 35: WWCN

## Slide 36
Velocity (m/s)
Chart: Velocity (m/s)

## Slide 37
Slope (%)
Chart: `Slope (Calculated) (%)

## Slide 38
Chart: 
Cover (m)

## Slide 39
Profile

## Slide 40
After the end of design process we got the following conclusions:
The majority percentages of water pipes are 2 and 4 inch.
The sewer material is PVC because it's easy to site.
Most sewer network conduits diameters are 8 inch.
ArcHydro tools save a lot of time in calculates loads.
Conclusions

## Slide 41
Recommendations
A periodic maintenance should be done and the damaged parts should be replaced.
If possible treatment plant is considered as a feasible project.
Suitable space between water pipes and wastewater pipes must be achieved (water pipes must be above wastewater pipes).