## Slide 1
An-Najah National University
Facility of Engineering and Information Technology
Civil Engineering department
Apple Media Center-Structural Design
Prepared by: Haya Khalil Ataire
Baraha Omar Saleh
Supervised by: Dr. Mohammad Sammaneh

## Slide 2: Content
Introduction
01
Seismic Design
02
Seismic Design Check
03
Concrete Design
04
Steel Design
05

## Slide 3: Introduction
Project description
Apple Media center Located in Nablus City, near the Nablus commercial complex
The building is composed of 21 stories and is wrapped to 120 degrees with two typical type of plane area, one consists of 560m2 and the other one repeated after each five stories with an area 812m2.

## Slide 4: Apple Media Tower

## Slide 5: Checks
Model check
Equilibrium check
ETABS result
load | Manually (kN) | Program(kN) | Error %
Dead | 122961.34 | 120886.5 | 1.7%
live | 60060 | 58650.6 | 2.3%
SD | 77836.4 | 7686.2 | 1.6%
The errors is less than 5% so the result is acceptable

## Slide 6: Checks
Deflection check
Check the deflection from live load only
Max deflection ≤L/180
→9.071mm >166.67mm
→Ok

## Slide 7: Checks
Deflection check
Check the long-term deflection
Maximum deflection from dead load
Maximum deflection from
superimposed load
ΔL= 9.071mm
ΔD= 16.267mm
ΔLS= 12.092mm
Using equation:
ΔLT= ΔL + λ∞ ΔD + λ t ΔLS
ΔLT= 61.5mm
Max deflection ≤L/480
→61.5mm > 62.5mm
→Ok

## Slide 8
Stress-Strain Check
For moment in the X-direction, M11
M= = 346.5kN.m
M= = 269. 3kN.m
Error= 28% OK
For moment in the Y-direction, M22
M= = 404.3kN.m
M= = 542kN.m
Error= 25% OK
Checks

## Slide 9: Seismic Design
Introduction
An earthquake is the shaking of the surface of the Earth resulting from a sudden release of energy in the Earth's lithosphere that creates seismic waves. In earthquake design, the building is subjected to random motion of the ground at its base, which induces inertia forces in the building that in turn cause stresses, this is displacement-type loading.

## Slide 10
Site Classification
(D) stiff soil
Risk Categorization
III (Buildings and other structures, the failure of which could pose a substantial risk to human life).
The importance factor (Ie) is equal to 1.25.
Site Seismic Characteristics
Seismic Zone Factor (Z) in Palestine
range from 0.075 to 0.30.
In Nablus Z is equal to 0.20.
Criteria Selection
Seismic Design

## Slide 11
Structural System
From ETABS find out that columns and other frames
carry out 83889.4946kN, from 120886.4686kN, so the frames resist 30% of the base shear and it is more
than 25%.
so the structure is dual system with moment frames capable of resisting at least 25% of prescribed seismic forces.
and it is special reinforced concrete shear walls since the height of the structure is 63m.
Criteria Selection
Seismic Design

## Slide 12
Response Modification Coefficient (R)
R is equal to 7.
Deflection Amplification Factor Cd)
Cd is equal to 5.50.
Over Strength Factor (Ω0)
Ω0 is equal to 2.50.
Mapped Acceleration Parameters, S1 and Ss
S1 = 0.375.
Ss = 0.75.
Procedure Used in the Calculations
Seismic Design

## Slide 13
Site Coefficient, Fa and Fv
Fa is equal to 1.2.
Fv is equal to 1.9.
Maximum considered earthquake spectral response acceleration adjusted for site class effects, SMS and SM1
SMS= 0.90.
SM1= 0.7125.
Procedure Used in the Calculations
Seismic Design

## Slide 14
Design Spectral Acceleration Parameters, SDS and SD1
SDS= 0.60.
SD1= 0.475.
Seismic Design Category
The seismic design category is D.
Procedure Used in the Calculations
Seismic Design

## Slide 15
The calculation of CS
CS= 10.71%
CS= 10.71% ≥ CS, min= 3.3% …. OK
CS= 10.71% ≥ CS, max= 7.8%
CS= 7.8%
Base Shear Calculation Using ELF Procedure
Seismic Design

## Slide 16
The calculation of W
W= 212135.2783kN.
The manual value of base shear (VManual)= 16465.52kN
Base Shear Calculation Using ELF Procedure
Seismic Design
Load Pattern | Weight (Manual) (kN)
Dead | 120886.4676
0.25 Live | 14662.64268
SD | 76586.167
Total Weight (W) | 212135.2783

## Slide 17
We have three methods of design:
Equivalent lateral force analysis.
Modal response spectrum analysis.
History analysis.
In the project will use Equivalent lateral force & Modal response spectrum analysis.
Methods of Design
Seismic Design

## Slide 18
Equivalent lateral force
In seismic analysis loads, are historically taken as equivalent static accelerations modified by certain factors depending on the seismicity of the location, soil properties and the natural frequencies of the structure and the intended use.
The idea of equivalent lateral force method is to distribute part of the seismic force (base shear) to every floor, which are able to transfer lateral loads.
Methods of Design
Seismic Design

## Slide 19
Modal response spectrum analysis
In this method, structures are modeled as multiple degree of freedom systems where the resulting frequencies and mode shapes are extracted. For each mode, the spectral forces and displacements are found and then combined. The combined forces are then divided by the response modification factor (R).
In the calculation of response for each horizontal direction, the combined number of modes is taken to include at least 90% of the participating mass of the structure.
Methods of Design
Seismic Design

## Slide 20
Equivalent Lateral Force (ELF) Procedures
ETABS Procedures
Seismic Design

## Slide 21
Equivalent Lateral Force (ELF) Procedures
ETABS Procedures
Seismic Design

## Slide 22
Equivalent Lateral Force (ELF) Procedures
The value of base shear from ETABS, in both directions X
and Y and considering 0.05 eccentricities of the diaphragms.
ETABS Procedures
Seismic Design
Manual Base Shear (kN) | 16465.52 | Error% 2.24% > 5% OK
ETABS Base Shear (kN) | 16833.6236 | 

## Slide 23
Response Spectrum Analysis
ETABS Procedures
Seismic Design

## Slide 24
Response Spectrum Analysis
ETABS Procedures
Seismic Design

## Slide 25
Response Spectrum Analysis
ETABS Procedures
Seismic Design

## Slide 26
Response Spectrum Analysis
Base Shear Response Spectrum Procedure
Scale factor= x
ETABS Procedures
Seismic Design

## Slide 27
Period Check
Tmodel= Tn= 2.17 seconds from ETABS.
Ta= 1.09 seconds.
Cu x Ta= 1.526
Tn < Cu x Ta OK
Design Checks
Seismic Design

## Slide 28
Story Drift Check
Δa= 0.045
Design Checks
Seismic Design
Story | Elastic Drift (X) | Inelastic Drift (X) | Comparison with code limit (< 0.045)
Story21 | 0.068023 | 0.20951084 | FALSE
Story20 | 0.064101 | 0.19743108 | FALSE
Story19 | 0.004084 | 0.01257872 | TRUE
Story18 | 0.004111 | 0.01266188 | TRUE
Story17 | 0.004106 | 0.01264648 | TRUE
Story16 | 0.047687 | 0.14687596 | FALSE
Story15 | 0.004126 | 0.01270808 | TRUE
Story14 | 0.004072 | 0.01254176 | TRUE
Story13 | 0.004025 | 0.012397 | TRUE
Story12 | 0.003955 | 0.0121814 | TRUE
Story11 | 0.028235 | 0.0869638 | FALSE
Story10 | 0.003756 | 0.01156848 | TRUE
Story9 | 0.003603 | 0.01109724 | TRUE
Story8 | 0.003394 | 0.01045352 | TRUE
Story7 | 0.003112 | 0.00958496 | TRUE
Story6 | 0.010769 | 0.03316852 | TRUE
Story5 | 0.007958 | 0.02451064 | TRUE
Story4 | 0.002083 | 0.00641564 | TRUE
Story3 | 0.001657 | 0.00510356 | TRUE
Story2 | 0.001184 | 0.00364672 | TRUE
Story2 | 0.000146 | 0.00044968 | TRUE
Story1 | 0.000607 | 0.00186956 | TRUE

## Slide 29
Story Drift Check
Δa= 0.045
Design Checks
Seismic Design
Story | Elastic Drift (Y) | Inelastic Drift (Y) | Comparison with code limit (< 0.045)
Story21 | 0.069117 | 0.21288036 | FALSE
Story20 | 0.065175 | 0.200739 | FALSE
Story19 | 0.004229 | 0.01302532 | TRUE
Story18 | 0.004256 | 0.01310848 | TRUE
Story17 | 0.004299 | 0.01324092 | TRUE
Story16 | 0.049546 | 0.15260168 | FALSE
Story15 | 0.004334 | 0.01334872 | TRUE
Story14 | 0.004291 | 0.01321628 | TRUE
Story13 | 0.004235 | 0.0130438 | TRUE
Story12 | 0.004116 | 0.01267728 | TRUE
Story11 | 0.02868 | 0.0883344 | FALSE
Story10 | 0.003785 | 0.0116578 | TRUE
Story9 | 0.003615 | 0.0111342 | TRUE
Story8 | 0.003406 | 0.01049048 | TRUE
Story7 | 0.003141 | 0.00967428 | TRUE
Story6 | 0.011053 | 0.03404324 | TRUE
Story5 | 0.008186 | 0.02521288 | TRUE
Story4 | 0.00217 | 0.0066836 | TRUE
Story3 | 0.001728 | 0.00532224 | TRUE
Story2 | 0.000156 | 0.00048048 | TRUE
Story2 | 0.001226 | 0.00377608 | TRUE
Story1 | 0.00062 | 0.0019096 | TRUE

## Slide 30
P-Delta Check
Load combination equal to Dead Load + Live Load + Superimposed Live Load.
Design Checks
Seismic Design

## Slide 31
P-Delta Check
Design Checks
Seismic Design

## Slide 32
P-Delta Check
Design Checks
Seismic Design

## Slide 33
P-Delta Check
While
Δ= = 62.8012mm
θ= = 0.032143851
During to the results, all the stories have θ less than 0.10, so there is no need to include the P-Delta effect in the analysis.
Design Checks
Seismic Design

## Slide 34
Torsional Irregularity Check
Torsional Irregularity Check in X-Direction
Design Checks
Seismic Design

## Slide 35
Torsional Irregularity Check
Torsional Irregularity Check in X-Direction
While
Ax= = 2.4885
% Eccentricity= 2.4885 x 0.05
= 0.124
Eccentricity Absolute length= DX x % Eccentricity
= 15.5 x 0.124
= 1.929
Design Checks
Seismic Design

## Slide 36
Torsional Irregularity Check
Torsional Irregularity Check in X-Direction
Design Checks
Seismic Design

## Slide 37
Torsional Irregularity Check
Torsional Irregularity Check in X-Direction
Design Checks
Seismic Design

## Slide 38
Torsional Irregularity Check
Torsional Irregularity Check in Y-Direction
Design Checks
Seismic Design

## Slide 39
Torsional Irregularity Check
Torsional Irregularity Check in Y-Direction
While
Ax= = 2.4859
% Eccentricity= 2.4859 x 0.05
= 0.124
Eccentricity Absolute length= DX x % Eccentricity
= 19 x 0.124
= 2.362
Design Checks
Seismic Design

## Slide 40
Torsional Irregularity Check
Torsional Irregularity Check in Y-Direction
Design Checks
Seismic Design

## Slide 41
Torsional Irregularity Check
Torsional Irregularity Check in Y-Direction
Design Checks
Seismic Design

## Slide 42
Stiffness Irregularity Check
Stiffness Irregularity Check in X-Direction
Design Checks
Seismic Design

## Slide 43
Stiffness Irregularity Check
Stiffness Irregularity Check in X-Direction
While
K20=
=1.79 > 0.7 …. ok
Km18 = avg. (Ki-1, i-2, i-3)
=
=43168.27
Km18=
=25.88 > 0.8 …. ok
Design Checks
Seismic Design

## Slide 44
Stiffness Irregularity Check
Stiffness Irregularity Check in Y-Direction
Design Checks
Seismic Design

## Slide 45
Stiffness Irregularity Check
Stiffness Irregularity Check in Y-Direction
While
K20=
=1.81 > 0.7 …. ok
Km18 = avg. (Ki-1, i-2, i-3)
=
=41891.05
Km18=
=25.59 > 0.8 …. ok
Design Checks
Seismic Design

## Slide 46
Mass-Weight Irregularity Check
Mass-Weight Irregularity in X-Direction
While
M19=
=1 < 1.5 …. Ok
Design Checks
Seismic Design

## Slide 47
Mass-Weight Irregularity Check
Mass-Weight Irregularity in Y-Direction
While
M19=
=1 < 1.5 …. Ok
Design Checks
Seismic Design

## Slide 48: Design
Introduction
The primary purpose of a structure is to transmit or support loads. If the structure is improperly designed or fabricated, or if the actual applied loads exceed the design specifications, the device will probably fail to perform its intended
function, with possible serious consequences.
A well-engineered structure greatly
minimizes the possibility of costly failures.

## Slide 49: Design
Final Design for Gravity and Lateral Loads
Checking Slab Shear Stress
ØVc= x x 1000 x 280
= 221.36kN
All of shear values are >221.36kN, which means that slab section is adequate to resist shear and there’s no need to shear reinforcement. But use the minimum shear reinforcement.
Slabs

## Slide 50: Design
Final Design for Gravity and Lateral Loads
Checking Slab Shear Stress
= 0.57mm2/mm
Assume Av= 2 x 113
= 226mm2
S= 400mm
Check S
Smax ≤ 600mm
≤ mm= 140mm < 400mm
S= 140mm
Use 1Ø12/140mm
Slabs

## Slide 51: Design
Final Design for Gravity and Lateral Loads
Slab Reinforcement for Moments
Slabs
 | As(mm2/m) |  | Main Slabs | Extended Slabs
 | Main Slabs | Extended Slabs |  | 
Top Steel in X-D | 1400 | 2000 | 10Ø14/m | 10Ø16/m
Bottom Steel in X-D | 800 | 1200 | 8Ø12/m | 8Ø14/m
Top Steel in Y-D | 1900 | 1000 | 10Ø16/m | 10Ø18/m
Bottom Steel in Y-D | 2500 | 1200 | 9Ø12/m | 8Ø14/m

## Slide 52: Design
Final Design for Gravity and Lateral Loads
Slabs Sections
Main Slabs
Slabs
X-Direction
Y-Direction

## Slide 53: Design
Final Design for Gravity and Lateral Loads
Slabs Sections
Extended Slabs
Slabs
X-Direction
Y-Direction

## Slide 54: Design
Final Design for Gravity and Lateral Loads
Beams Steel Reinforcement
Main Beams:
As, Bottom= 1672mm2
4Ø25
As, Top= 3932mm2
8Ø25
Shear Walls Beams:
As, Bottom= 530mm2
3Ø18
As, Top= 545mm2
3Ø18
Beams

## Slide 55: Design
Final Design for Gravity and Lateral Loads
Shear and Torsional reinforcement
Main Beams:
= 2.34mm2/mm
= 0.28mm2/mm
= 2.34mm2/mm
S= 95mm
Check S
Smax ≤ 600mm
≤ mm= 150mm > 95mm
Use S= 95mm
1Ø12/95mm
Beams

## Slide 56: Design
Final Design for Gravity and Lateral Loads
Shear and Torsional reinforcement
Shear Walls Beams:
= 0.33mm2/mm
= 0.28mm2/mm
= 0.33mm2/mm
S= 475mm
Check S
Smax ≤ 600mm
≤ mm= 150mm < 475mm
Use S= 150mm
1Ø10/150mm
Beams

## Slide 57: Design
Final Design for Gravity and Lateral Loads
Beams Sections
Beams
Main Beams
Shear Walls Beams

## Slide 58: Design
Final Design for Gravity and Lateral Loads
Sway-Non Sway Check
This check was performed for all stories in the X and Y directions.
Q=
Its Non Sway
Slenderness Check
=
= 18.18
should be less than 34 − 12 x
34 − 12 x = 33.84 > 18.18
so is a short column
All columns are considered short.
Columns

## Slide 59: Design
Final Design for Gravity and Lateral Loads
Columns Steel Reinforcement
Columns
Columns Group Number | Columns Diameter (mm) |  | As Required (mm2) | As of the Columns
1 | 1100 |  | 34027 | 43Ø32
2 | 950 |  | 23794 | 30Ø32
3 | 700 |  | 16643 | 21Ø32
 | Depth (mm) | Width (mm) |  | 
Shear Walls Columns | 1000 | 300 | 13189 | 17Ø32

## Slide 60: Design
Final Design for Gravity and Lateral Loads
Shear reinforcement
Main Columns
Asp= 154mm2 (Ø14)
All the distance between the rings for all columns is less than 75mm.
Use spirals: Ø14/50mm.
Columns
Columns Group Number | Columns Diameter (mm) | Dc (mm) | Ag (mm2) | Ach (mm2) | ρs | S (mm)
1 | 1100 | 968 | 950332 | 735937 | 0.01249 | 50
2 | 950 | 818 | 708822 | 525529 | .014948 | 50
3 | 700 | 568 | 384845 | 253388 | 0.02223 | 50

## Slide 61: Design
Final Design for Gravity and Lateral Loads
Shear reinforcement
Shear Walls Columns
Since Vc > , so minimum shear reinforcement can be used. And figure (6-19) shows columns reinforcement key for shear walls columns.
3Ø14/100mm
Columns

## Slide 62: Design
Final Design for Gravity and Lateral Loads
Columns Sections
Columns
1.1m-Diameter Columns
0.95m-Diameter Columns

## Slide 63: Design
Final Design for Gravity and Lateral Loads
Columns Sections
Columns
0.70m-Diameter Columns
Shear Walls Columns

## Slide 64: Design
Final Design for Gravity and Lateral Loads
Longitudinal Reinforcing for Shear Wall
As = 114500mm2 (For two faces).
As = = 57250mm2/one face.
Use (1∅32/85 mm)/face.
Shear Reinforcing for Shear Wall
As = 7800mm2/m for two faces of shear wall.
As = 3900mm2/m for one face of shear wall.
As = 3900 x 6= 23400mm2 along 6m.
Use (1∅25/125mm)
Shear Walls

## Slide 65: Design
Final Design for Gravity and Lateral Loads
Shear Wall Section
Shear Walls

## Slide 66: Design
Steel Connections
To connect the element of steel structure we use connection, connection is structure element used for joining different member of a structure steel frame work.
The connection type will be used:
• Bolts.
• Plate.
The connected member:
• Steel Column-Steel Column.
• Steel Beam-Steel Column.
• Steel Beam-Concrete Column.
Introduction

## Slide 67: Design
Steel Connection
Using RAM Connection program.
 Customize Connection Design

## Slide 68: Design
Steel Connection
 Load Condition and Load Combination

## Slide 69: Design
Column-Steel Connection
Joint Data

## Slide 70: Design
Column-Steel Connection
Load

## Slide 71: Design
Column-Steel Connection
The Shape of Designed Column
After using the RAM connection program get this shape of
connection for columns.

## Slide 72: Design
Column-Steel Connection
Details of Connection
For Shear
Details of Connection for Shear
Family: Column splice (CS).
Type: Shear web plate(s).

## Slide 73: Design
Column-Steel Connection
For Shear
General Information
The Connector

## Slide 74: Design
Column-Steel Connection
For Shear
General Information
Members
Material: A36
Top column
Top column section: EN_HE 1000 M
Bottom column
Bottom column section: EN_HE 1000 M
Connector
Section: PL 7x632.4x292.1
tp (Plate thickness): 7mm

## Slide 75: Design
Column-Steel Connection
For Shear
General Information
Members
Material: A36
Top side column
Bolts: 3/4" A325 N
nc (Bolt columns): 4
nr (Rows of Bolts): 3
s (Transverse bolt spacing): 76.2mm
g (bolts spacing): 120mm

## Slide 76: Design
Column-Steel Connection
The Result of Shear Connection
Design Check

## Slide 77: Design
Column-Steel Connection
The Result of Shear Connection
Design Check

## Slide 78: Design
Details of Connection
For Moment
• Details of Connection for Moment
Family: Column splice (CS).
Type: Flange-plated.
Column-Steel Connection

## Slide 79: Design
Column-Steel Connection
For Moment
General Information
Members
Material: A36
Flange Plate
Connector
Plate: PL 25x376x786
Consider interior plate: Yes
b (Plate width): 376mm
tp (Plate thickness): 25mm
Material: A36
Bolts: 1" A325 N

## Slide 80: Design
Column-Steel Connection
For Moment
General Information
Bolts: 1" A325 N
Connection type: Bolted
Top side column
Ls (Top part length): 393mm
nc (Bolt columns): 4
nt (Rows of bolts): 5
Bottom side column
Li (Bottom part length): 393mm
nc (Bolt columns): 4
nt (Rows of bolts): 5

## Slide 81: Design
Column-Steel Connection
The Result of Moment Connection
Design Check

## Slide 82: Design
Column-Steel Connection
The Result of Moment Connection
Design Check

## Slide 83: Design
Beam-Column Steel Connection
Using RAM Connection program
Joint Data

## Slide 84: Design
Beam-Column Steel Connection
Load

## Slide 85: Design
Beam-Column Steel Connection
The Shape of Designed Column
After using the RAM connection program get this shape of connection for beam-columns.

## Slide 86: Design
Beam-Column Steel Connection
Details of Connection
For shear
Details of Connection for Shear
Family: Column splice (CS)
Type: Shear web plate(s)

## Slide 87: Design
Beam-Column Steel Connection
For shear
• General Information
Members
Material: A36
End Plate
Connector
Section: PL 8x165.1x304.8
L (Plate length): 304.8mm
B (Plate width): 165.1mm
tp (Plate thickness): 8mm
Material: A36

## Slide 88: Design
Beam-Column Steel Connection
For shear
• General Information
Beam side
Plate position on beam: Center
Welding electrode to beam: E70XX
Support side
Connection type: Bolted
Bolts: 3/4" A325 N 140
nc (Bolt columns): 2
nr (Rows of Bolts):4

## Slide 89: Design
Beam-Column Steel Connection
The Result of Shear Connection
Design Check

## Slide 90: Design
Beam-Column Steel Connection
The Result of Shear Connection
Design Check

## Slide 91: Design
Beam-Column Steel Connection
Details of Connection
For Moment
Details of Connection for Moment
Family: Beam - Column web (BCW).
Type: Flange-plated.

## Slide 92: Design
Beam-Column Steel Connection
For Moment
• General Information
Members
Material: A36
Flange Plate
Connector
L (Top plate length): 502.7mm
B (Top plate width ): 175mm
tp (Top plate thickness): 20mm
Plate material: A36

## Slide 93: Design
Beam-Column Steel Connection
For Moment
• General Information
Beam side
Connection type: Bolted
Bolts: 3/4" A325 N
nc (Bolt columns): 2
nr (Rows of Bolts): 6
Support side
Top and bottom welding electrode to support and column : E70XX
D1 (Top weld size to support (1/16 in) ): 6
D2=D4: 2
D3: 7

## Slide 94: Design
Beam-Column Steel Connection
The Result of moment Connection
Design Check

## Slide 95: Design
Beam-Column Steel Connection
The Result of Shear Connection
Design Check

## Slide 96: Design
Steel Beam-Concrete Column Connection
The idea of designing column-steel connection is using Ramp connection program, that we assume the concrete column is steel column and applied the load on it, to
make sure it’s safe and under specification.
After the concrete column have been design and the area of steel has been determined, which is 43Ø32 for
Column Diameter 1100mm, some of the area steel will be used to connect between the column and the steel
beam.

## Slide 97: Design

## Slide 98: Design
Steel Beam-Concrete Column Connection
Joint Data

## Slide 99: Design
Steel Beam-Concrete Column Connection
Load

## Slide 100: Design
Steel Beam-Concrete Column Connection
The Shape of Designed Column
After using the RAM connection program get this shape of connection for steel beam-concrete column.

## Slide 101: Design
Steel Beam-Concrete Column Connection
Details of Connection
For Shear
• Details of Connection for Shear
Family: Beam - Column flange (BCF).
Type: End plate

## Slide 102: Design
Steel Beam-Concrete Column Connection
For Shear
General Information.
Members
Material: A36
End Plate
Connector
Section: PL 8x165.1x304.8
L (Plate length): 304.8mm
B (Plate width): 165.1mm
tp (Plate thickness): 8mm
Material: A36

## Slide 103: Design
Steel Beam-Concrete Column Connection
For Shear
General Information.
Beam side
Plate position on beam: Center
Welding electrode to beam: E70XX
Support side
Connection type: Bolted
Bolts: 3/4" A325 N
nc (Bolt columns): 2
nr (Rows of Bolts): 4

## Slide 104: Design
Steel Beam-Concrete Column Connection
The Result of shear Connection
Design Check

## Slide 105: Design
Steel Beam-Concrete Column Connection
The Result of shear Connection
Design Check

## Slide 106: Design
Steel Beam-Concrete Column Connection
Details of Connection
For Moment
• Details of Connection for Moment
Family: Beam - Column flange (BCF)
Type: Flange Angles/Flange Tees

## Slide 107: Design
Steel Beam-Concrete Column Connection
For Moment
General Information.
Members
Material: A36
Angels/Flange Tees
Connector
Is angle/tee: Angle
Angle section: LU 8X6X1
Angle short leg on beam: No
Connection type: Bolted
C (Length): 434mm
Material: A36

## Slide 108: Design
Steel Beam-Concrete Column Connection
For Moment
General Information.
Beam side
Bolts: 1" A325 N
nr (Rows of Bolts): 2
nc (Bolt columns): 4
Support side
Bolts: 1" A325 N
nr (Rows of Bolts): 1
nc (Bolt columns): 4

## Slide 109: Design
Steel Beam-Concrete Column Connection
The Result of moment Connection
Design Check

## Slide 110: Design
Steel Beam-Concrete Column Connection
The Result of moment Connection
Design Check

## Slide 111
Thank you