## Slide 1
Prepared by:
Sameh Arabasi
Obada Natoor
Ayyash Essam
Supervisor:
Dr.Muhannad Haj Hussein
An-Najah National University
Faculty of Engineering
Building Engineering Department
Graduation project 2 (An Integrated Design For Nablus Municipality)

## Slide 2
Contents:
Architectural Aspects
Environmental Aspects
Structural Aspects
Quantity Surveying & Cost Estimate
Mechanical aspects
Electrical aspects
2

## Slide 3
Contents:
Architectural Aspects
Environmental Aspects
Structural Aspects
Quantity Surveying & Cost Estimate
Mechanical aspects
Electrical aspects
3

## Slide 4
4
Architectural Aspects
Introduction
Site analysis
Architectural modifications

## Slide 5
5
Architectural Aspects
Introduction
Site analysis
Architectural modifications

## Slide 6
6
Architectural Aspects
Introduction
Site analysis
Architectural modifications

## Slide 7
7
Architectural Aspects
Introduction
Site analysis
Architectural modifications

## Slide 8: Adjacent Building:
Nablus Municipality
( proposed location )
Nablus International Stadium
Green area
Nablus Mall
Roman amphitheater
Cultural Center - Hamdi Mango
Keys Plan for figure:
8

## Slide 9: Accessibility:
Al kfair street
King fisal street
Haifa road
Ameer Muhamad street
Jafffa street
Keys Plan for figure:
9

## Slide 10: Noise level:
10
Noise level in site from surroundings
At 12:00 PM
At 3:00 PM
At 8:00 AM

## Slide 11
11
Architectural Aspects
Introduction:
Site analysis
Architectural modifications

## Slide 12
12
Architectural Aspects
Introduction:
Site analysis
Architectural modifications

## Slide 13: Parking
13
After modification
The add second basement floor
with 56 car parking
N

## Slide 14: Parking
14
First basement after modification
First basement before modification
24 car parking
54 car parking
N
N

## Slide 15: Ground floor
15
Ground floor after modification
Ground floor before modification
N
N

## Slide 16: First floor
16
First floor after modification
First floor before modification
N
N

## Slide 17: Second floor
17
Second floor after modification
Second floor before modification
N
N

## Slide 18: Third floor
18
Third floor after modification
Third floor before modification
N
N

## Slide 19: Fourth floor
19
Fourth floor after modification
N

## Slide 20: South elevation
20
After modification
Before modification

## Slide 21: North elevation
21
After modification
Before modification

## Slide 22: East elevation
22
After modification
Before modification

## Slide 23: West elevation
23
After modification
Before modification

## Slide 24: Sections
24

## Slide 25: Summary
Conclusion | Project after modification (m2) | Case study (m2) | Standard (m2) | Space Type
We are within standards, this room is ok | 165.3 | 72 | 74. 8 | Multipurpose room
This room is ok | 92.3 | 33.87 | 34 | reception hall
This room is ok | 116 | 36.77 | 40 | Fees collecting hall
This room is ok | 115 | 34.94 | 40 | public room
In this part, the areas of each type of room used in the building were compared with the special standards to get an impression of the spaces that have been modified and their compatibility with other approved projects.
25
space area summary

## Slide 26
Conclusion | Project after modification (m2) | Case study m2)) | Standard m2)) | Space Type
We have a problem with only one of the offices and its area is 8.7 m2 | 8-22 | 8-11 | 14.45 | Offices for one employee
All within standards | 18-37 | 8-15 | 18.5 | Offices for two employees
Offices are ok | 28-60 | 11.36 | 22.5 | Offices for three employees
Ok | 67.3 | 11-16 | 22.5 | Offices for four employees
ok | 14-21 | 12.35 | 10 | Waiting rooms
ok | 8.3 | 5 | 7 | Kitchenette
ok | 1.26 | 1.55 | 1.23 | Bathrooms
Conclusion | Project after modification (m2) | Case study (m2) | Standard (m2) | Space type
ok | 92.4 | 20.26 | 36.42 | Mayor’s office
ok | 2.7 *4.7 | ---- | 4. 5 * 2.25(m) | Parking
So big | 142 | 5 | 10-15 | store
ok | 2m | 1.44 | 1.2m (width) | Corridors
26
space area summary

## Slide 27
27

## Slide 33
Contents:
Architectural Aspects
Environmental Aspects
Structural Aspects
Quantity Surveying & Cost Estimate
Mechanical aspects
Electrical aspects
33

## Slide 34
Contents:
Architectural Aspects
Environmental Aspects
Structural Aspects
Quantity Surveying & Cost Estimate
Mechanical aspects
Electrical aspects
34

## Slide 35
35
Structural aspects:
Structural concept and code
Preliminary Design
Checks
Materials and loads
Sections modifier
Elements design

## Slide 36
36
Structural aspects:
Structural concept and code
Preliminary Design
Checks
Materials and loads
Sections modifier
Elements design

## Slide 37: Structural concept and code
37
Structural concept
The concrete reinforcement system was used in this project with with the Two Way U-boat system and large spans and the structure designed for seismic resistance Building frame system type.
Code:
ACI 318-14 for design
ASCE 7-16 for load design
UBC 97 code for seismic design
Load combinations for gravity loads
ASCE 7-16, Section 2.3.1, provide equations to calculate Service and ultimate gravity load as shown in below equations.
Service = 1.0D + 1.0L
Ultimate U1 = 1.2D + 1.6L
Ultimate U2 = 1.4D

## Slide 38
38
According to UBC 97 code and seismic maps of Palestine was used characteristics used in seismic design
Z-value
Soil properties
Seismic coefficient Ca
Seismic coefficient Cv
Name | R | I | Soil profile | Z zone 2B | Cv | Ca
Value | 5.5 | 1.25 | SD | 0.20 | 0.4 | 0.28
Summary of characteristics
seismic design characteristics:

## Slide 39
39
    Combination for seismic loads
According to UBC97 code we have ultimate and service equations for seismic forces as show:
Ultimate equation is:
→1.4D
→1.2D+1.6L
→1.34D+L+EQx+0.3EQy
→1.34D+L+0.3EQx+EQy
→0.76 D+EQx+0.3EQy
→0.76 D+0.3EQx+EQy
service equation is:
→D
→D+0.714EQx+0.214EQy
→D+0.214EQx+0.714EQy
→0.9D+0.714EQx+0.214EQy
→0.9D+0.214EQx+0.714EQy
→D+0.75L+0.54EQx+0.16EQy
→D+0.75L+0.16EQx+0.54EQy

## Slide 40
40
Structural aspects:
Structural concept and code
Preliminary Design
Checks
Materials and loads
Sections modifier
Elements design

## Slide 41
41
Structural aspects:
Structural concept and code
Preliminary Design
Checks
Materials and loads
Sections modifier
Elements design

## Slide 42: Materials and loads
42
Concrete compressive strength
Then the concrete Density = 2500 Kg/m3
And for reinforcement steel
Density = 7800 Kg/m3
Fy = 420 Mpa
Live load =5 KN/m2 for all spaces in the building.
Super dead load (SID) = 4 KN/m2
Modula's of elasticity (E) | concrete Type Fc | Structure type
26587.2 | 32 MPa | Slab
26587.2 | 32MPa | Column
26587.2 | 32MPa | Shear wall
Load of external walls:
Take load of external wall 10 KN/m.
Horizontal Section in wall

## Slide 43
43
Structural aspects:
Structural concept and code
Preliminary Design
Checks
Materials and loads
Sections modifier
Elements design

## Slide 44
44
Structural aspects:
Structural concept and code
Preliminary Design
Checks
Materials and loads
Sections modifier
Elements design

## Slide 45: center of column
45

## Slide 46: Preliminary Thickness of Slabs
46
ACI 318-14, Section 8.3.1.2, provide min thickness of two- way solid slab depending on stiffness . For flat slab αfm=0
For =0 without edge beams:
Where
= minimum slab thickness.
= length of clear span in long direction measured face-to-face of beams.
The figure below show the critical panel in all Storey.
critical panel
Compute thickness of slab:
Redaction factor according to catalogue=0.65
In this project it was used thickness of voided slab =500 mm.
U-boot slap catalogue

## Slide 47
47
There two type of columns are used in this project:
Type 1: Rectangle column (C1)
Tributary area for C1
Column C1 | 
Story | Tributary area
B1 | 111.5
B2 | 111.5
GF | 60.9
F1 | 60.9
F2 | 90.2
F3 | 90.2
F4 | 90.2
Total Area | 615.4
Add Wight of column to Pu by add 3%
Fc=40 MPa
Use α%= 5%
In this project, dimensions of column type C1 assumed (500*1400) mm
    Preliminary Dimensions of Columns

## Slide 48
Type 2: circular column (C2)
48
Tributary area of column C2
Column C2 | 
Story | Tributary area
B1 | 53.6
B2 | 53.6
GF | -
F1 | -
F2 | 40.7
F3 | 40.7
F4 | 40.7
Total Area | 229.3
Add Wight of column to Pu by add 3%
Fc=40 MPa
Use α%= 1%
So Diameter =587 mm
In this project, diameter of column Type C2 assumed 700 mm with

## Slide 49
49
Structural aspects:
Structural concept and code
Preliminary Design
Checks
Materials and loads
Sections modifier
Elements design

## Slide 50
50
Structural aspects:
Structural concept and code
Preliminary Design
Checks
Materials and loads
Sections modifier
Elements design

## Slide 51
51
Slab modifiers in ETABS
Columns modifiers in ETABS
Stair Beams modifiers in ETABS
    Sections modifier

## Slide 52
52
Slab modifiers in ETABS
Columns modifiers in ETABS
Stair Beams modifiers in ETABS
    Sections modifier

## Slide 53
53
Slab modifiers in ETABS
Columns modifiers in ETABS
Stair Beams modifiers in ETABS
    Sections modifier

## Slide 54
54
Slab modifiers in ETABS
Columns modifiers in ETABS
Stair Beams modifiers in ETABS
    Sections modifier

## Slide 55
55
Structural aspects:
Structural concept and code
Preliminary Design
Checks
Materials and loads
Sections modifier
Elements design

## Slide 56
56
Structural aspects:
Structural concept and code
Preliminary Design
Checks
Materials and loads
Sections modifier
Elements design

## Slide 57: Checks
57
To insure that the structure in ETABS is acceptable we must do the checks (compatibility, equilibrium, and stress strain) to obtain the results and use it in calculations.
    Compatibility check
The structure is compatible since the deformed structure moves as one rigid body. This means that the meshing of the slab and shear areas is obtained correctly.
Type | limitation | 
2. Equilibrium check |  | 
3.1.Axial load |  | 
3.2.Moment distribution |  | 
Type | limitation | 
2. Equilibrium check |  | 
3.1.Axial load |  | 
3.2.Moment distribution |  | 

## Slide 58: 4. Modal mass participate ratio check [MMPR]
58
The Modal mass participation ratio according to UBC 97 code shall be greater than 90% to use response spectrum analysis method.
Case | Mode | Period sec | UX | UY | UZ | Sum UX | Sum UY
Modal | 1 | 1.094 | 0.1338 | 0.0882 | 0 | 0.1338 | 0.0882
Modal | 2 | 0.976 | 0.0003 | 0.2688 | 0 | 0.1341 | 0.357
Modal | 3 | 0.891 | 5.08E-06 | 0.0016 | 0 | 0.1341 | 0.3586
Modal | 74 | 0.069 | 1.07E-06 | 0.0002 | 0 | 0.9014 | 0.9217
As show in the previous table MMPR greater than 90% so we can use response spectrum analysis method.

## Slide 59: 4. Modal mass participate ratio check [MMPR]
59
The Modal mass participation ratio according to UBC 97 code shall be greater than 90% to use response spectrum analysis method.
Case | Mode | Period sec | UX | UY | UZ | Sum UX | Sum UY
Modal | 1 | 1.094 | 0.1338 | 0.0882 | 0 | 0.1338 | 0.0882
Modal | 2 | 0.976 | 0.0003 | 0.2688 | 0 | 0.1341 | 0.357
Modal | 3 | 0.891 | 5.08E-06 | 0.0016 | 0 | 0.1341 | 0.3586
Modal | 74 | 0.069 | 1.07E-06 | 0.0002 | 0 | 0.9014 | 0.9217
As show in the previous table MMPR greater than 90% so we can use response spectrum analysis method.

## Slide 60: 5. Base Shear check
60
According to UBC97 code the base shear of response spectrum method equal or more than base shear from equivalent static method as following equation.
Load Case/Combo | FX | FY | FZ
 | kN | kN | kN
Dead | 1.09E-05 | -4.85E-06 | 107908.5976
Live | 113.3 | 8.80E-06 | 31008.8449
Sid | 4.36E-06 | -6.51E-07 | 32744.9288
EQx Max | 15566.26 | 6873.5486 | 0.0004
EQy Max | 6441.434 | 15250.5467 | 0.0003
Where:
W=weight=1D+0.25L
T=period and minimum from T limit and T ETABS
Axis | T ETABS | T limit | T used | V ETABS | V manual | old scale factor | New scale factor
x | 1.09 | 0.92 | 0.92 | 15566.263 | 14664.6 | 2561 | 2413
y | 0.97 | 0.92 | 0.92 | 15250.547 | 14664.6 | 1944 | 1869
The equivalent base shear more response spectrum its ok.
Base shear force

## Slide 61: 6. Period calculation
61
The UBC97 code provides you with two ways to calculate the period [T], and the method A will be adopted.
hn = High of building and equal 32m.
Ct = (0.0488) for all other buildings.
= 0.66 sec.
T limit = 1.4 * T method A = 1.4 * 0.66 = 0.92 sec.
Axis | T ETABS | T Limit
x | 1.094 | 0.92
y | 0.976 | 0.92
The value of period its acceptable but me must check drift and p-dalta
period calculation

## Slide 62: 7. Drift check
62
UBC 97 code give you maximum permissible displacement to the floor from the under floor and should not exceed it.
ΔM =0.7 * R * Δ s.
Where:
ΔM (drift) = Maximum Inelastic Response Displacement.
R: Confidant of seismic system type.
Δ s= Displacement of the floor from the under floor at center of mass.
And ΔM story drift shall not exceed 0.020 times the story height if period greeter than 0.7 sec.
So the drift limitation =0.02*4000=80 mm
Story | height (mm) | Ux | Uy | ΔS x | ΔS y | ΔM x | ΔM y | ΔM max
0 | 4000 | 0 | 0 | - | - | - | - | -
1 | 4000 | 0.5 | 0.31 | 0.5 | 0.31 | 1.925 | 1.1935 | 80
2 | 4000 | 0.66 | 0.66 | 0.16 | 0.35 | 0.616 | 1.3475 | 80
3 | 4000 | 9.3 | 10.3 | 8.64 | 9.64 | 33.264 | 37.114 | 80
4 | 4000 | 19 | 20 | 9.7 | 9.7 | 37.345 | 37.345 | 80
5 | 4000 | 30 | 34 | 11 | 14 | 42.35 | 53.9 | 80
6 | 4000 | 42 | 46 | 12 | 12 | 46.2 | 46.2 | 80
7 | 4000 | 53 | 58 | 11 | 12 | 42.35 | 46.2 | 80
8 | 3000 | 61 | 71 | 8 | 13 | 30.8 | 50.05 | 60
Drift check
All drift value less than limitation so it’s acceptable.

## Slide 63: 8. P-delta check
63
Where:
θ= The stability coefficient.
𝑃= The total vertical design load at and above Level (KN).
Δ s= Displacement of the floor from the under floor at center of mass (mm) .
𝑉= The seismic shear force acting(KN).
ℎ=The story height (mm).
θ max=0.1 and if θ less than θ max its ok(NO P-DELTA)

## Slide 64
64
Story | H floor (mm) | P gravity load combination(KN) | Vx(KN) | Ux(mm) | ∆SX (mm) | ƟX | Conclusion
Story8 | 3000 | 852.8859 | 258.3846 | 61 | 8 | 0.00880 | NO P-DELTA
Story7 | 4000 | 21836.1107 | 4962.3656 | 53 | 11 | 0.0121 | NO P-DELTA
Story6 | 4000 | 42703.7115 | 7946.7105 | 42 | 12 | 0.0161 | NO P-DELTA
Story5 | 4000 | 55521.0388 | 10281.8708 | 30 | 11 | 0.0148 | NO P-DELTA
Story4 | 4000 | 74021.8194 | 11792.1384 | 19 | 9.7 | 0.0152 | NO P-DELTA
Story3 | 4000 | 92522.9371 | 12786.0361 | 9.3 | 8.64 | 0.0156 | NO P-DELTA
Story2 | 4000 | 160716.1556 | 14639.9856 | 0.66 | 0.16 | 0.0004 | NO P-DELTA
Story1 | 4000 | 219602.4263 | 16318.332 | 0.5 | 0.5 | 0.0017 | NO P-DELTA
P-delta check in x direction
Story | H floor (mm) | P gravity load combination(KN) | EY(KN) | Uy(mm) | ∆Sy (mm) | ƟY | Conclusion
Story8 | 3000 | 852.8859 | 274.3843 | 71 | 13 | 0.01347 | NO P-DELTA
Story7 | 4000 | 21836.1107 | 4261.0696 | 58 | 12 | 0.01537 | NO P-DELTA
Story6 | 4000 | 42703.7115 | 6932.9149 | 46 | 12 | 0.01848 | NO P-DELTA
Story5 | 4000 | 55521.0388 | 8999.3629 | 34 | 14 | 0.02159 | NO P-DELTA
Story4 | 4000 | 74021.8194 | 10239.2566 | 20 | 9.7 | 0.01753 | NO P-DELTA
Story3 | 4000 | 92522.9371 | 11074.1372 | 10.3 | 9.64 | 0.02014 | NO P-DELTA
Story2 | 4000 | 160716.1556 | 12482.7326 | 0.66 | 0.35 | 0.00113 | NO P-DELTA
Story1 | 4000 | 219602.4263 | 13884.6412 | 0.31 | 0.31 | 0.00123 | NO P-DELTA
P-delta check in Y direction
As shown in pervious tables in x,y direction all value of Ɵ less than maximum limitation.

## Slide 65
65
Structural aspects:
Structural concept and code
Preliminary Design
Checks
Materials and loads
Sections modifier
Elements design

## Slide 66
66
Structural aspects:
Structural concept and code
Preliminary Design
Checks
Materials and loads
Sections modifier
Elements design

## Slide 67: Slab design
67
Punching check:
All value is small than ratio 0.9 and that’s ok
Punching shear for 3rd floor
Punching shear for basement floor

## Slide 68
68
Deflection check:
Maximum allowable intermediate deflection from service load =L/240=12.3/240=51.25 mm
Deflection from service load

## Slide 69
69
Shear check:
81.8 kN/m
Shear force V23
Shear force V13
There are some values above the permissible limit and they have been reinforced to resist the shear forces.

## Slide 70: Slab reinforcement and detail:
70
Plan reinforcement
Plan reinforcement around column

## Slide 71
71
Section c-c for slab detail of link reinforcement
General Section b-b
Section a-a in drop panel

## Slide 72: Column design
72
Type of Column and sizes
In this project we have five type of column depended on diminution and shape of
cross section. Design of columns use ETABS software and the detail drawing by use
revit software Dimension of columns as shown below in the table.

## Slide 73
73
We take the results from ETABS program as follows :
Longitudinal reinforcement of C1
Shear rebar design for C1

## Slide 74: Column reinforcement and details:
74
Longitudinal section Column C1
Column C1 a-a section
For Column C1:
1.40

## Slide 75
Longitudinal section Column C2
Column C2 a-a section
For Column C2:
75
1.40
1.40

## Slide 76
For non-Prismatic column(C6):
Column C6 a-a section at top
Longitudinal section Column C6
76
1.90

## Slide 77: Design of beams
Type of structure system flat slab without edge beams and add stair beams to install curtain glass. Model in ETABS software add stair beam only but we added beams in edges of slab (B1) in plans of structure, this beam was reinforced minimum area steel.
77

## Slide 78
For stair beams:
stair beam detail
Stair beam section 1-1
    Beams reinforcement and details:
78

## Slide 79: Shear wall design
ETABS result for shear wall 2
From the data from ETABS the required reinforcement ratio = 0.0025 more than or
equal minimum ratio0.25% for the longitude bars and the spaces equal
For vertical Use 1 Ø 12 / 30 cm for each layer
For horizontal use 1 Ø 10/ 20 cm for each layer
79
In this project all shear force resisted by shear wall only as building frame system.
We take the results form ETABS as follow .

## Slide 80
section detail of reinforcement for SW2
details of reinforcement for SW2
80

## Slide 81: Design of footing
To obtain the best design we use the safe program to design our foundation in our project we use the mat foundation because the soil capacity is small which equal =200kn/m2. In our model we use thickness of it = 0.8 m and use drop panels for punching shear to obtain the correct checks.
81

## Slide 82: Soil pressure check
The allowable soil pressure is 200 kn/m^2
Then the results from ETABS = 185.1 kn/m^2
Soil pressure result
82

## Slide 83: Punching shear check:
punching check
All columns have a punching < 0.9 so its ok
83

## Slide 84: Statement check :
Settlement in footing
For Settlement check the Settlement must small 10 mm for mat footing in safe equal =
8 mm <10mm so its ok .
84

## Slide 85: Footing reinforcement and detail
Reinforcement M22 | Reinforcement M11 | Moment | ρ M11 | ρ m22 | ρ M11 | ρ M22
bottom | 1505 | 1700 | 0.0075 | 0.0086 | 12Ø 25 / m | 11Ø 28 / m
top | 152 | 364 | 0.0007 | 0.0017 | 7Ø 16 / m | 7Ø 16 / m
Moment results
We note that ρ M11 & ρ M22 is more than minimum ρmin =0.0018 so we use result ρ
As = ρ *b*d
At M=1505 KN.m ρ=0.00756
= 0.00756* 1000*750 = 5658.8 mm2
We need 12Ø 25 / m
85

## Slide 86: Detail of footing :
reinforcement for mat footing
86

## Slide 87: Detail of footing
reinforcement for drop panel with mat footing
section in reinforcement for mat footing
87

## Slide 88: Water tank design
Element | Mu (KN.m/m) | Sd | Mu design (KN.m/m) | ρ | As (mm2/m) | As min (mm2/m) | Bars # Ø db
Wall-H | 24.2 | 1.29 | 31.21 | 0.00051 | 86.7 | 1000 | 7 Ø 14
Wall-V | 23.3 | 1.29 | 29.28 | 0.00047 | 79.9 | 600 | 9 Ø 12
Top slab | 6 | 1.29 | 7.74 | 0.00012 | 20.4 | 306 | 4 Ø 10
Show the calculation for reinforcement in water tank
Sd = 1.29 for water.
Mu design = Mu * Sd * 1.06
ρ =
As = (ρ * b* d)
As min for footing and top slab = (0.0018 * b * h)
As min for wall horizontally = (0.005 * b * h)
As min for wall vertically = (0.003 * b * h)
88

## Slide 89: Water tank Detail :
detailing section for water tank
detailing for water tank from the top view
89

## Slide 90: Design of sheet piles
Soli properties
To start work on the excavations of the project and because the depth is 8 meters
below the surface of the earth, methods must be devised to prevent the collapse of the
soil, and in this for a project we used the sheet pile to prevent soil from collapsing
during the work. By used GEO5 software program sheet piles designed and by used
Revit program draw of detail.
90

## Slide 91: Details of sheet piles:
Diameters and spaces between piles
Pile reinforcement details
Distribution of sheet piles
91
Sheet pile depth result

## Slide 92
Contents:
Architectural Aspects
Environmental Aspects
Structural Aspects
Quantity Surveying & Cost Estimate
Mechanical aspects
Electrical aspects
92

## Slide 93
Contents:
Architectural Aspects
Environmental Aspects
Structural Aspects
Quantity Surveying & Cost Estimate
Mechanical aspects
Electrical aspects
93

## Slide 94
94
Environmental Aspects
Shading analyses
Daylight factor
CFD analyses
Thermal comfort analyses

## Slide 95
95
Environmental Aspects
Shading analyses
Daylight factor
CFD analyses
Thermal comfort analyses

## Slide 96
96
we did a shading analyses for the building before we use the reflected glass and the solar radiation values were high after we used the reflected glass the solar radiation values improved as shown below:

## Slide 97
97
Environmental Aspects
Shading analyses
Daylight factor
CFD analyses
Thermal comfort analyses

## Slide 98
98
Environmental Aspects
Shading analyses
Daylight factor
CFD analyses
Thermal comfort analyses

## Slide 99: Daylight factor analyses:
Daylight factor is an index for how much natural lighting is in the space that we have , we made an analyses for all floors and we took the max and min values of the daylight factor in each floor , so we need bigger windows or shading system.
99

## Slide 100
Daylight factor analyses
Ground floor
First floor
100

## Slide 101
Second floor
Third floor
101
Fourth floor

## Slide 102
102
Environmental Aspects
Shading analyses
Daylight factor
CFD analyses
Thermal comfort analyses

## Slide 103
103
Environmental Aspects
Shading analyses
Daylight factor
CFD analyses
Thermal comfort analyses

## Slide 104: External CFD
Internal CFD
104
As shown in the figures of the external CFD we can note that the windows that we put for the infiltration has a good location, also we can see that from the internal CFD the velocity of the inside air is good and between the comfortable values 0.3 - 0.9 m/s.

## Slide 105
105
Environmental Aspects
Shading analyses
Daylight factor
CFD analyses
Thermal comfort analyses

## Slide 106
106
Environmental Aspects
Shading analyses
Daylight factor
CFD analyses
Thermal comfort analyses

## Slide 107
Thermal design:
Element | U-Value(W/M2.K)
External walls | 0.471
Roof | 0.39
Floor | 0.535
Windows | 2.6
107
U-Value for elements
layers of the external walls
layers for roof
layers for floor
Glass catalogue

## Slide 108
PMV CHART
108

## Slide 109
Heating Design:
temperatures and heat loss
109

## Slide 110
Contents:
Architectural Aspects
Environmental Aspects
Structural Aspects
Quantity Surveying & Cost Estimate
Mechanical aspects
Electrical aspects
110

## Slide 111
Contents:
Architectural Aspects
Environmental Aspects
Structural Aspects
Quantity Surveying & Cost Estimate
Mechanical aspects
Electrical aspects
111

## Slide 112: Lighting design:
112
    As show design for Mayors' office:
Standard | Achieved | Type
 | 510 | lux
 | 0.6 | uniformity
 | 13.7 | UGR

## Slide 113: Power in first floor
Lighting distribution for first floor
113

## Slide 114: Main distribution board and circuit breaker in the building:
Main distribution board
circuit breaker for the lighting
circuit breaker for the HVAC
114

## Slide 115: Elevators power
Circuit breaker for elevators
115
Elevators power connection

## Slide 116
Contents:
Architectural Aspects
Environmental Aspects
Structural Aspects
Quantity Surveying & Cost Estimate
Mechanical aspects
Electrical aspects
116

## Slide 117
Contents:
Architectural Aspects
Environmental Aspects
Structural Aspects
Quantity Surveying & Cost Estimate
Mechanical aspects
Electrical aspects
117

## Slide 118: HVAC – design
In this project, we contain multiple spaces, and part of them needs mechanical ventilation, such as the conference room, corridors, assembly rooms, and spaces that do not require mechanical ventilation, such as offices, which depend on natural ventilation, and the design will be based on the use of the cassette for places that not need mechanical ventilation and the fan coil unit for places that need mechanical ventilation.
118

## Slide 119: HVAC Units:
Fan coil unit:
119
cassette catalogue

## Slide 120
Zone | Sensible cooling (kW) | Latent cooling(kW) | Cooling Design Capacity (kW) | Cooling Design Flow Rate (m3/s) | Heating loads (kW)
Zone20 | 3.28 | 0.54 | 4.39 | 0.212 | 
Zone9 | 67.21 | 2.81 | 80.53 | 4.45 | 16.85
Zone6 | 1.43 | 0.23 | 1.91 | 0.0911 | 0.6
Zone3 | 1.29 | 0.21 | 1.72 | 0.083 | 0.9
Zone7 | 0.93 | 0.14 | 1.23 | 0.0644 | 0.34
Zone1 | 3.25 | 0.56 | 4.69 | 0.0226 | 0.282
Zone12 | 1.34 | 0.13 | 1.79 | 0.086 | 0.31
Zone21 | 2.31 | 0.19 | 2.87 | 0.144 | 0
Zone22 | 0.99 | 0.18 | 1.34 | 0.06 | 0.62
Zone2 | 3.76 | 0.59 | 5 | 0.24 | 0
Zone4 | 1.6 | 0.26 | 2.14 | 0.105 | 0
Zone8 | 1.38 | 0.21 | 1.82 | 0.089 | 1.16
Zone5 | 2.66 | 0 | 3.06 | 0.1891 | 0
Zone23 | 0.94 | 0.06 | 1.15 | 0.064 | 0.24
Zone17 | 1.91 | 0.16 | 2.39 | 0.1193 | 0
Zone18 | 2.53 | 0.21 | 3.16 | 0.158 | 0
Zone15 | 1.83 | 0.15 | 3.28 | 0.114 | 0
Zone19 | 1.87 | 0.16 | 2.34 | 0.116 | 0
Zone16 | 0.91 | 0.06 | 1.19 | 0.064 | 0.77
Zone14 | 1.46 | 0.01 | 1.8 | 0.0911 | 0
Total for the floor | 103.3 | 7 | 126.8 | 6.8 | 24.6
Heating and cooling load:
cooling and heating loads for fourth floor
120
Fourth floor zone number

## Slide 121: HVAC detail :
Distribution of Hvac system in fourth floor
121

## Slide 122: water drainage HVAC:
We use drainage for Hvac With 1.5’’ with slope 1% for pipes as show in figure.
water drainage HVAC for fourth floor
122

## Slide 123: Acoustical Design
We design the acoustical system for Multipurpose and corridor .
123
speaker Specifications

## Slide 124: Selected materials:
floor material absorption coefficient
stage material absorption coefficient
124
Celling material absorption coefficient
walls material absorption coefficient

## Slide 125
125
SPL direct for area at 1000 Hz
Total SPL at frequency 1000 Hz

## Slide 126
For corridors
Calculation of coverage radius:
Where:
H: net height of floor=3.5m
H’: Standing people height =1.6m
=Tan (50) =
𝑟/3.5-1.6
So r =2.20 m
Coverage area = 𝜋 *2.2² =15.2 m².
126

## Slide 127: Acoustical Detail
section for corridors speaker
Speakers distribution for first floor
127

## Slide 128: Water supply system
Ground Floor
Use 1.5"fort vertical pipes, 1.25"∅horizontal pipes, 3/4"for branches
First floor
Use 1.5"fort vertical pipes, 3/4"∅horizontal pipes, 3/4"for branches
Second floor
Use 1.5"fort vertical pipes, 3/4"∅horizontal pipes, 3/4"for branches
Third floor
Use 1.5"fort vertical pipes, 1.25"∅horizontal pipes, 3/4"for branches
Fourth floor
Use 1.5"fort vertical pipes, 3/4"∅horizontal pipes, 3/4"for branches
128

## Slide 129: Water supply system
first floor water supply system
Ground floor water supply system
129

## Slide 130: Drainage System Design
Fixture un total | Floor | Type | Fixture unit(dfu) | Number
Ground Floor | lavatory | 2 | 7 | 14
W.C | 4 | 7 | 28 | 
First floor | Lavatory | 2 | 6 | 12
W.C | 4 | 6 | 24 | 
Kitchen sink | 2 | 1 | 2 | 
Second floor | lavatory | 2 | 6 | 12
W.C | 4 | 6 | 24 | 
Kitchen sink | 2 | 1 | 2 | 
Third floor | lavatory | 2 | 6 | 21
W.C | 4 | 6 | 24 | 
Kitchen sink | 2 | 1 | 2 | 
Fourth floor | lavatory | 2 | 8 | 16
W.C | 4 | 8 | 32 | 
Kitchen sink | 2 | 1 | 2 | 
fixture | diameter | Slope | pipe
sewer | 2 | 2 | PVC
sewer | 4 | 4 | PVC
drainage | 4 | 1 | PVC
stack | 4 | 0 | PVC
vent | 2 | 0 | PVC
diameter& slope for fixtures
Show the calculation for (dfu) in all stories in the building
130

## Slide 131: Drainage System Detail
Piping distribution and connection for Forth floor
Piping distribution and connection for Third floor
131

## Slide 132: Design of Firefighting System.
We use deferent types of fire fighting :
1 – Fire distinguisher
We use a fire extinguisher with foam material because we have a paper and archive books so we cant use water , usually used as a primary option in small fires and are used in the corridors so we put it in corridors in our project.
In our project we use a class A.
132

## Slide 133: Design of Firefighting System
Smoke detector
CO2 Sprinklers
hose stations
Hose station
Co2 Sprinkler
Smoke detector
133

## Slide 134: Firefighting detail
Distribution fire system for ground floor
Distribution fire system for typical floor
134

## Slide 135: Firefighting detail
Emergency exit
The fire exit and the away to escape .
135

## Slide 136
Contents:
Architectural Aspects
Environmental Aspects
Structural Aspects
Quantity Surveying & Cost Estimate
Mechanical aspects
Electrical aspects
136

## Slide 137
Contents:
Architectural Aspects
Environmental Aspects
Structural Aspects
Quantity Surveying & Cost Estimate
Mechanical aspects
Electrical aspects
137

## Slide 138: Work Breakdown Structure (WBS)
138
Total cost =23,013,615.69 NIS and unit cost=2,467 NIS/SM

## Slide 139
Thank you for listening