## Slide 1: Design and Construction of Automatic Demolding Machine for Artificial Stone Graduation Project 2 An- Najah National University Faculty of Engineering & Information Technology Department of Industrial and Mechanical Engineering
Prepared by:
Ehab Alfe
Tahseen Odeh
Waled Rashed
Supervisor
Dr.Ahmad Ramahi
4.7.2024

## Slide 2: OUTLINE 01 04 02 05 03 06
INTRODUCTION
METHODOLOGY
Manufacturing and Assembly Operation
Preliminary Financial Analysis
Design of the Automatic Demolding Machine
CONCLUSION

## Slide 3: INTRODUCTION 01

## Slide 4: Problem Statement
Problem
Solution
Automate the production processes in the Artificial stone industry, in particular, automate the demolding process.
The main goal of this project Design and fabricate an automatic demolding model for artificial stone to replace human labor.
Increased demand for artificial stone.
However, factories rely on manual labor in the demolding process.
Manual demolding has limited production capacity.

## Slide 5: METHODOLOGY 02

## Slide 6
Conduct a preliminary market study
Explore the different working principles of machines
Choose the best working principle of the machine
Implement the working principle with all necessary components on SolidWorks.
Design and Fabrication
financial analysis

## Slide 7
The demolding process represents a bottleneck.
The manual demolding rate is 157 stones/hour
Stone demolding machines have been studied around the world.
After practical trials, the vibrator was chosen

## Slide 8: Design of the Automatic Demolding Machine 03

## Slide 9
1- Machine building blocks (Processes)

## Slide 10
Chart: 
Feeding Conveyer

## Slide 11
Vibrator

## Slide 12
Unloading Conveyor

## Slide 13
Spraying conveyor

## Slide 14
Detailed design
1-Belt Design
For the Design of the belt conveyor for feeding
Total Length
The width
Load in conveyor
Mass of belt = Total Area

## Slide 15
The Power of Motor
Linear Speed of conveyor
Demolding rate 450 stone/hr ------0.125stone/seconds------8 seconds for each stone.
Take safety factor
The diameter of the Idler Roller is 5cm,
So The angular velocity
Speed of motor
Torque
Feeding motor: 0.33 hp, 1200 rpm, Three-phase motor.`

## Slide 16
For the Design of the belt conveyor for Unloading
Total Length
Total Width
Load in conveyor
Power of motor
Speed of motor
Torque
Unloading motor: 0.5 hp, 1200 rpm, Three-phase motor.`

## Slide 17
2-V-belt
Spraying motor: 0.33 hp, 1200 rpm, Three-phase motor.`

## Slide 18
We notice that the force exerted by the vibrator on the stone is greater than 580 N in both samples and thus the demolding process is expected to be successfully achieved.
3- Vibrator

## Slide 19
 |  |  |  |  |  |  |  |  | F | 
Sample 1 | 6.66 | 62.08 | 16517.31 | 13380.38 | 0.03 | 3.18 | 75.92 | 109.81 | 731.53 | 2.66
Sample 2 | 20.65 | 66.60 | 18126.14 | 13380.38 | 0.03 | 3.18 | 324.4 | 50.96 | 1052.57 | 0.47
 |  |  |  |  |  |  |  |  | F | 
Sample 1 | 6.66 | 62.08 | 16517.31 | 13380.38 | 0.03 | 3.18 | 75.92 | 109.81 | 731.53 | 2.66
Sample 2 | 20.65 | 66.60 | 18126.14 | 13380.38 | 0.03 | 3.18 | 324.4 | 50.96 | 1052.57 | 0.47

## Slide 20
The maximum height that the vibrating body reaches is 2.66 mm, which is a good number so that the vibrating body stays very close to the height of the conveyors, and this height was taken into account in the design.
Vibrator motor: A 0.5 HP, Three-phase motor with a rotation speed of 3600 rpm was selected for the vibrator, connected to an inverter to control the rotation speed.

## Slide 21
4 Selection of Standard Component
Bearing selection
Design of Bearing :
The load acting on the bearing is
Fx = Friction Force
Fy = weight of roller
.

## Slide 22
We have added three flood nozzles in the spraying stage to ensure complete coverage of the Mold with insulating material.
Nozzle selection

## Slide 23: Manufacturing and Assembly Operation 04

## Slide 24
1- Manufacturing of Feeding Conveyor

## Slide 26
2- Manufacturing of Unloading Conveyor

## Slide 27
3- Manufacturing of Spraying Conveyor

## Slide 28
4- Manufacturing of Vibrator

## Slide 31
Material | Amount | Unit
Steel 1010 (U section) | 20 | m
Sheet metal 5mm | 2 | 
Sheet metal 8mm | 2 | 
Sheet metal 2mm | 3 | 
Roller | 33 | -
Wheels | 10 | -
V-Belt | 1 | -
Belt | 2 | -
Damper | 12 | -
Rubber spring | 4 | -
Steel rod | 2.5 | m
Motor | 4 | -
Material | Amount | Unit
Steel 1010 (U section) | 20 | m
Sheet metal 5mm |  | 
Sheet metal 8mm | 2 | 
Sheet metal 2mm | 3 | 
Roller | 33 | -
Wheels | 10 | -
V-Belt | 1 | -
Belt | 2 | -
Damper | 12 | -
Rubber spring | 4 | -
Steel rod | 2.5 | m
Motor | 4 | -
After presenting the design to multiple manufacturers and considering the cost, the average has been calculated. Approximate cost of manufacturing the machine = 22,000 Nis

## Slide 32: Preliminary Financial Analysis 05

## Slide 33
Manual Production:
  4 workers produce 157 stones per hour
Machine Production:
  Operates with 2 workers and produces 450 stones per hour.
Production Efficiency:
Operating Expenses:
  Electricity cost: 1.5KW*1hr*1NIS/Kwhr =1.5 NIS/hr.
  Maintenance cost plus contingencies: 5 NIS/hr.
  The machine's annual cost: UAC=IC(A/P, i, n), i=0.06, n=8.
  UAC=22000(0.161)=3542 NIS/yr
  3542/(50*6*2.5) = 4.7 NIS/hr
  The wage of one worker is 15 NIS per hour.

## Slide 34
Daily Operational Cost Comparison:
  Manual Demolding: 4 workers* 15 NIS/hr * 6 hr/day = 360 NIS/day
  Automatic Demolding:
  (2 workers* 15 NIS/hr + 4.7 NIS/hr + 1.5 NIS/hr + 5 NIS/hr) * 2.5 hr/day = 103 NIS/day
Daily Operational Cost Savings:
  The daily operational cost saving = Manual daily cost – Automatic daily cost
  = 360 – 103 = 257 NIS
  Unit cost saving = daily manual cost/(157 stone/hr* 6 hr) – daily automatic cost/ (450 stone/hr *2.5) = 360/942 – 103/1125 = 0.29 NIS/stone
Daily Operational Cost Analysis:

## Slide 35
Payback Period Calculated based the daily savings :
  Payback Period = Initial Investment / daily savings
  Payback Period = 22,000 Nis / 257 NISs/day =85.6 day.
  Payback Period = Approximately 85 days / 26 days/ months =3.5 months
  The payback period is very encouraging to replace the manual demolding with automatic demolding.
Payback Period:

## Slide 36: 05
Conclusion
and RECOMMENDATIONS

## Slide 37
Conclusion
There is a great demand for automatic stone demolding machines in Palestine.
The proposed design is relatively simple which has a positive reflection on the cost of the machine.
The entire machine was designed using Solid Work software.
The Vibrator was manufactured and the concept of demolding by vibration was proved.

## Slide 38
Recommendations
Optimize the design by automating the stone loading and mold unloading processes.
The current model is specific to certain types and dimensions of molds; it is recommended to improve the design to accommodate all available molds.
Improve the design to reduce the weight and cost of the machine and create modified versions for commercial purposes.

## Slide 39: THANKS!