## Slide 1: Wireless Music Player
Designed By :
Fadi Ne’irat
Mohammad Barham
Wireless Music
Player
Fadi Neirat
Mohammad Barham

## Slide 2: Content
Introduction
Device parts
Working procedures
Problems
Future Plans

## Slide 3: Introduction
Our wireless music player allows the user to listen to uncompressed digital audio streamed over a wireless link.
The music player reads uncompressed audio data from an SD card in an immobile "base station." A pair of Xbee transceiver modules are used to stream data and control signals between the base station and a portable module.

## Slide 4: Overview
Why using wireless ?
Wider range : approximately 100 m
Separated Controller
Why use of file with .wav extention

## Slide 5: Consist of Tow Parts
Main Station
Portable station

## Slide 6
Main Station
Portable Station
Audio Stream
Control Signals

## Slide 7: Main Station
Begin
Start SPI
Initialize SD-Card
Initialize FAT file System
Get First File
Buffer 2KB of data
Chek for and implement file skip request, or stop command
Data Request
Transmit Data

## Slide 8: Portable Station
Yes No
No
Yes
Begin
Initialize SPI (DAC)
Initialize USART, with receive interrupt
Initialize timer2 with 8Khz interrupt
Buffer low?
Request Data
Button pressed?
Send Command
Halt palyback if pause or stop

## Slide 9
Working Procedure

## Slide 10
Initialize SD-CARD
Initialize
File System
List all files And read first packet from first file(2KB)
This controller must be ready
Send Command for play(as example)
Processing request and send packets as needed
Read packet and send it to DAC

## Slide 11: Problems
SD card Initialization
File System
Sensitivity of XBEE
XBEE communication
DAC output

## Slide 12: Future Plans
Develop our project to work on client-server application using PIC
Increase sound resolution to get a sound with better quality