## Slide 1: Seismic Analysis and Design for Centrum Shopping Center
Abdel Rahman Yousef – 11612522
Ameer Alawneh – 11642619
Hala Khammash – 11610429
Sereen Abu Aita – 11642884
Under Supervision of: Dr. Shaker Bitar
Graduation Project I

## Slide 2: 01. Introduction. 02. Preliminary design. 03. Three-dimensional analysis and design. 04. Appendices. 05. References. Table of Contents

## Slide 3: INTRODUCTION Chapter 1

## Slide 4: Project Objectives Objective 1 Objective 2 Objective 3 Objective 4
Apply the methods of structural analysis and design to understand the real life problems.
Modeling the structure consedring seismic design requirments.
Solving architectiral challenges.
Design a 5-story building taking into consideration strength, serviceability, safety and economy aspects.
Notes: اهداف المشرؤع التطبيق العملي للمساقات الانشائية على مول 5طوابق عشان نحقق المكتوبين فوق ونعملها مودل زلزالي وبنفس الوقت نحل المشاكل المعمارية(سبانات طويلة,كانتيليفر 4ز65متر) ونراعي الشكل المعماري.

## Slide 5: Centrum Shopping Center Project Description
The site is located on the main highway between Nablus and Tulkarm opposite to Nadi Al-Madina.
The shopping center consists of one basement floor, ground floor, first, second and third floors, in addition to an exterior parking.
Notes: المشروع عبارة عن مول تجاري موجود على الشارع الرئيسي الي بشبك بين نابلس وطولكرم بجانب نادي المدينة
هاد امشروع بتكون من طوابق,ومصف خارجي

## Slide 6: What We Are Working On Main architectural plan. 3D architectural view.

## Slide 7: Geometrical Data for The Building
Level | Floor height (m) | Parameter (m) | Area (m2) | Volume (m3)
Basement floor | 4.5 | 764.79 | 6772.88 | 30477.96
Ground floor | 4.5 | 631.28 | 10044.09 | 45198.38
First floor | 4.5 | 1153057 | 8490.70 | 38208.14
Second floor | 4.5 | 1112.31 | 8806.97 | 39631.35
Third floor | 4.5 | 1112.31 | 8806.97 | 39631.35
Notes: بنركو على المساحة وارتفاع الطابق

## Slide 8: Methodology Analysis assumption. Codes and standards. Data analysis. Project constraints.
1
3
2
4
5
Design phase
Notes: 1- احنا عملنا ابعاد اولية اي سي اي
2-عملنا اناليسس مودل وعملنا عليه تشيكات
3-باستخدام كودات اي بي سي اي اس سي اي
4-سبانات كبيرة,كانتيليفر

## Slide 9: Project Stages Stage 1 Stage 2 Stage 3
Preliminary dimensions.
Analysis for gravvity.
Seismic analysis.
Stage 5
Three dimensional design

## Slide 10: Load Assumptions and Calculations
Load type | Load direction | Load value(kN/m2)
Dead Load | Gravity | volume of the member x unit weight of materials
Superimposed | Gravity | 4.5
Live Load | Gravity | 5
Snow Load | Gravity | Zero
Soil Pressure | Lateral | 4.5

## Slide 11
Seismic Load Parameters.

## Slide 12: Seismic Load Parameters
Parameter | Parameter Value | Reference
Risk Category | II | Table 1.5-1 from ASCE 7-10.
Importance Factor | 1 | Table 1.5-2 from ASCE 7-10.
Mapped Acceleration Parameters(Ss) | 0.4 | Section 11.3, from ASCE7-10.
Mapped Acceleration Parameters(S1) | 0.12 | Section 11.3, from ASCE7-10.
Site Classification | C-very dense soil and soft rock | Table 20.3.1 from ASCE 7-10.
Site Coefficients(Fa ,Fv) | 1.2,1.68 | Table 11.4.1+2 from ASCE 7-10.
Spectral Response Acceleration Parameters(SM1,SMs) | 0.2,0.48 | SM1 = Fv*S1 SMS= Fa*Ss
Design Spectral Acceleration Parameters (SDs,SD1) | 0.32,0.13 | SDs =2/3*SMS SD1= 2/3 * SM1
Long-Period Transition Period(TL) | 9 | “Israeli” maps TL 2%,50y
Structural Period | 0.426 | Ta =Ct*hnx =0.0488*180.75=0.426

## Slide 13: Seismic Design Category
The seismic design category depends on SDS and SD1 values, so as shown in tables 11.6-1,11.6-2, from ASCE 7-10, it will be taken as C since it’s more risky.

## Slide 14: Analytical Procedure
Notes: Bn7dr vid, l2no design category C e5trna Seismic force resisting system 3la asas building frame system :oridinary reinfornced shear system , almd2 alasae lhad alsystem frames: vertical.
Walls: lateral.

## Slide 15: Seismic Force Resisting System
Since the design category is C, so the Building Frame system(ordinary reinforced concrete shear walls) will be used.
In this system the frames will resist almost 100% of the vertical loads. on the other hand, shear walls will resist almost 100% of the lateral loads.
Other factors that are determined depending on the seismic force resisting system:
Response modification coefficient R=5
Over strength Factor Ω=2.5
Deflection amplification factor Cd=4.5
Notes: Bn7dr vid, l2no design category C e5trna Seismic force resisting system 3la asas building frame system :oridinary reinfornced shear system , almd2 alasae lhad alsystem frames: vertical.
Walls: lateral.

## Slide 16: Future
Sa= Spectral Response Accelerations.
T0=0.2*(SD1/SDS)
Ts=(SD1/SDS)
Response Spectrum Design Curve
Notes: Bnla7z t3’yre qemat Sa belawal linear b3dha constant b3dha parabola, b2wl ajza2 mn althanyah mn alzelzal bkun bel peaks tb3o

## Slide 17: Load Combinations
Ultimate Combinations
Eq. No. from ASCE 7-10 | Eq. from ASCE 7-10 | Load combinations
1 | 1.4D | 1.4D
2 | 1.2D + 1.6L + 0.5(Lr or S or R) | 1.2D + 1.6L
5 | 1.2D + 1.0E + L + 0.2S | 1.264D+EQx+0.3EQy+L
 |  | 1.264D-EQx-0.3EQy+L
 |  | 1.264D+EQy+0.3EQx+L
 |  | 1.264D-EQy-0.3EQx+L
7 | 0.9D + 1.0E | 0.836D+EQy+0.3EQx
 |  | 0.836D-EQy-0.3EQx
 |  | 0.836D+EQx+0.3EQy
 |  | 0.836D-EQx-0.3EQy
Notes: modat one wave from EQ,period parameter mn alcode w7sba P

## Slide 18: Load Combinations
Service Combinations
Eq. No. from ASCE 7-10 | Eq. from ASCE 7-10 | Load combinations
1 | D | D
2 | D + L | D + L
5 | D + (0.6W or 0.7E) | 1.0448D+0.7EQx+0.21EQy
 |  | 1.0448D+0.7EQy+0.21EQx
6b | D + 0.75L + 0.75(0.7E) + 0.75S | 1.0336D+0.525EQx+0.1575EQy+0.75L
 |  | 1.0336D+0.525EQy+0.1575EQx+0.75L
8 | 0.6D + 0.7E | 0.5552D+0.7EQx+0.21EQy
 |  | 0.5552D+0.7EQy+0.21EQx
Notes: modat one wave from EQ,period parameter mn alcode w7sba P

## Slide 19: Preliminary Design Chapter 2

## Slide 20: Now
General
To reduce the effect of thermal loads and control seismic movement, the project will be divided into 6 main blocks separated by expansion separators as shown in the figure.
Notes: Almashro3 kteer kber ,3shan nhml thermal w3shan seismic, bs e7na ma wjdna belcodes kam length alfa9l fs2lna aldocs w7kulna ef9lo kul 60m,bs e7na 7awlna nra3e alq63 ma ykun ella 3nd alpartitions+columns.

## Slide 21
Preliminary Dimension Summary
Member | Section Dimensions(mm)
Beams | 600X700
Columns | 500X500,600X600,700X700
Solid slab(two-way) | Depth=250
Walls | Width=250

## Slide 22: Three-Dimensional Analysis Chapter 3

## Slide 23: Structural Modeling of The Project

## Slide 24: ETABS Model

## Slide 25
Sections Modifiers
Slab Modifiers
Beams Modifiers
Notes: Belnesba lal slab 3shan n3tbr cracks elha 7tena modifiers 0.25, etjah moment out of plane

## Slide 26
Sections Modifiers
Columns Modifiers
Walls Modifiers
Notes: Columns modifiers depend on the designing assumption of having a cracked or uncracked section

## Slide 27: Response spectrum analysis method is used to find the maximum/peak response of the structure to a certain dynamic loading.
Functions
Response Spectrum Function
Notes: Had hu alzlzal ele r7 ydrb almodel, nd5lo function 3shan nwjd peak response lalmbna 3shan y6l3 m3na aldynamic load elel b2thr 3la almbna.

## Slide 28: Scale factor = = = 1962 . This value may be changed after calculating the base shear check.
Load Cases
Response Spectrum Case for EQx/EQy
Notes: V=value from curve*g*m*(I/R)

## Slide 29: The story weight taken when calculating the seismic actions should comprise the full permanent load (Dead + Superimposed) plus the variable load (Live) multiplied by a factor that mainly varies between 20% - 30% . For this project 25% of the live load will be taken.
Masses
Mass Source
Notes: Columns modifiers depend on the designing assumption of having a cracked or uncracked section

## Slide 30
Verification of Structural Analysis for Gravity Loads.

## Slide 31: Compatibility Check
Notes: Tmask almbna wbt7rk ka one unit

## Slide 32: Equilibrium Checks
1. Dead load error = 1.1% < 5%  OK.
2. Superimposed dead load error = 0.0%  OK.
3. Live load error = 0.0%  OK.
4. Soil load error = 0.0%  OK.
Notes: Dead=The reason of this error is the beam’s own weight is calculated from face to face by ETABS, but in the hand calculations it’s calculated from center to center.
loadX area and dead own weight.

## Slide 33: Verification of Internal Forces(DDM method)
Error in column = 1.297 < 10%  OK.
Member | Average moment (Hand) | Average moment (ETABS) | Difference (%) | Check (≤25%)
Frame | 2051.60 | 2083.32 | 1.50 | OK
Slab column strip | 230.80 | 519.43 | 55.50 | NOT OK
Slab middle strip | 512.90 | 312.95 | 63.80 | NOT OK
Beam | 1307.90 | 1336.25 | 2.12 | OK
Notes: akhdna frame in x direction 3shan n6l3 almoment lal frame, t2kdna mn allimitations lala method 7sb alcode wkan kulu tamam, fa mshena 3la al dddm method mn alcode w6l3na qym almoment hay.
3na error bel Slab cs wel ms l2no ddm dareqa taqrebyah weldistribution ma ba5d b3en ele3tbar aldimensions mthln albeam mhma kan kbeer eza alphaL/L>1 ba5d 0.85 bs eletabs ba5d had ele5tlaf b3en ele3tbar wkul ma kan albeam akbr kul ma kan moment 3leh akbr.

## Slide 34: Evaluation of Preliminary Dimensions Preliminary sections dimensions. Deflection check. Shear check. New sections dimensions.
1
3
2
4
5
Shear check.
6
Deflection check.
OK
Not OK
OK
OK
7
Check
designed
Members.
OK
Notes: B3d ma 7sbna checks gravity , jena nt2kd mn alab3ad al2wlya, shear check kan ok , 7sbna aldeflection, 6l3 deflection canti kteer akbr mn allowable fqrrna eno nkbr sections,bs lsa a3ta deflection 3ale , fa qrrna n3ml beam girder system,m3 non prismatic cantileiver beams.3mlna shear check w3mlna deflection check w6l3 aql mn allowable(L/240)(L/120 canti).
B3dha 3mlna design 3al members , kbrna almember ele 9ar feha failure.

## Slide 35: Beam-Girder System
Notes: Shear walls endafo 3la asas seismic resisting system. Torsion modifiers rj3nahm

## Slide 36: Non-Prismatic Beam
Notes: 3mlnah 3shan n7afz 3la alshkl alm3mare ,l2no belcorridors.

## Slide 37: New Beams modifiers New walls modifiers
Notes: 3mlnah 3shan n7afz 3la alshkl alm3mare ,l2no belcorridors.

## Slide 38
New Dimension Summary
Member | Section Dimensions(mm)
Main Beams | 900X1200
Cantilever main beams | Non-Prismatic (1500X900 - 1200X900 - 700X900)
Columns | 500X500 700X700 900X900
Solid slab(Two-way) | Depth=270
Walls | Width=250

## Slide 39
Verification of structural analysis for seismic loads.

## Slide 40: Verification of Structural analysis for Seismic Loads. Mass participation ratio. Base shear. Period. Story drift check.
1
3
2
4
5
P-Delta check.

## Slide 41: Mass Participation Ratio Check
The analysis shall include a sufficient number of modes to obtain a combined modal mass participation of at least 90 percent of the actual mass in each horizontal direction.
Notes: Mjmoh msahmat almodes twsl 90% mn actual mass aw aktr, 6l3naha mn ETABS w6l3 m3na almode 5bel y, 7 bel x bwslna 0.9

## Slide 42: Period Check
Periods in each direction are considered to be the largest from all modes.
From ETABS, period in X-direction= 0.665s ,period in Y-direction=0.523s.
From ASCE7-10 table 12.8.1 Cu=1.632.
Tlimit=Cu*Ta= 0.696s
where: Cu: Coefficient for upper limit on
      Calculated period.
Since TETABS < Tlimit , then Tfinal =TETABS.
Notes: 6l3na Cu mn altable ele b3tmd 3la Sd1 wbn6l3 T limit ele r7 nqarnha m3 T ETABS hun 6l3 m3na Tfinal hya T ETABS I both directions

## Slide 43: Base Shear Check
V = W*Cs
In X-direction:
W=WDL-W(DL for half of the first story )+WSD+0.25WLL. =147176.46 kN.
Cs final=Cs,max. =0.0404.
V=0.0404*147176.46=5949.027 kN.
Axis | Base shear hand | Base shear ETABS | Preliminary scale factor | New scale factor | New base shear ETABS
X-direction | 5949.027 | 5448.204 | 1962 | 2142 | 5948.039
Y-direction | 7564.251 | 22539.499 | 1962 | 658 | 7559.118
Where: V: base shear.
W:Weight of structure.
Cs: the seismic response coefficient.
Notes: Bnqarn base shear response spectrum m3 albase shear lal equivilant static, lazm response akbr aw ysawe equivilant 3shan hek bn3dl alscale factor.
Cs 6l3t akbr mn Csmax 3shan hek akhdna Csfinal=Csmax

## Slide 44: Story Drift Check
Notes: 9e3’ belarabe

## Slide 45: Story Drift Check
From ASCE 7-10 Table 12.12-1,the allowable story drift is 0.02h, since all the drift values less than 0.02, the drift values are acceptable.
Story # | ETABS elastic drift(mm) | Inelastic drift(mm)= | Check. (OK, not OK)
Story 5 | 0.000376 | 0.001692 | Ok.
Story 4 | 0.000451 | 0.0020295 | Ok.
Story 3 | 0.000461 | 0.0020745 | Ok.
Story 2 | 0.000395 | 0.0017775 | Ok.
Story 1 | 0.000326 | 0.001467 | Ok.
Story # | ETABS elastic drift(mm) |  | Check. (OK, not OK)
Story 5 | 0.000376 | 0.001692 | Ok.
Story 4 | 0.000451 | 0.0020295 | Ok.
Story 3 | 0.000461 | 0.0020745 | Ok.
Story 2 | 0.000395 | 0.0017775 | Ok.
Story 1 | 0.000326 | 0.001467 | Ok.

## Slide 46: P-Delta Check
P-delta effects on story shears and moments, the resulting member forces and moments, and the story drifts induced by these effects are not required to be considered where the stability coefficient (θ) is equal to or less than 0.10 .
Px = the total vertical design load at and above Level x.
= the design (Real) story drift.
Ie = the importance factor.
Vx = the seismic shear force acting between Levels x and x – 1.
hsx = the story height below Level x.
Cd = the deflection amplification factor.
Since = and Sx= where, Sx is the story stiffness.
the equation can be simplified to
Notes: e7na lazm nshuf kam alzaywah ele bmel feha almbna l2no had alt7rk b3ml shear wsecondary moment fa e7na bdna nqarn theta m3 0.1 3shan nshuf eza lazm n3ml p delta analysis.
" "e7na lazm nshuf kam alzaywah ele bmel feha almbna l2no had alt7rk b3ml shear wsecondary moment fa e7na bdna nqarn theta m3 0.1 3shan nshuf eza lazm n3ml p delta analysis.

## Slide 47: P-Delta Check
Since in all stories, P-delta effect is neglected.
Story # | Stiffness X(kN/m) | Stiffness Y(kN/m) | P(kN) | θx | θy | Check. (OK, not OK)
Story 5 | 1487016.1 | 1407908.44 | 29899 | 0.0044 | 0.00471 | Ok.
Story 4 | 2547400.8 | 2378198.27 | 68311 | 0.0059 | 0.00638 | Ok.
Story 3 | 3362060.6 | 3155293.66 | 109241 | 0.0072 | 0.00769 | Ok.
Story 2 | 4864239.2 | 4190060.43 | 150177 | 0.0068 | 0.00796 | Ok.
Story 1 | 5348454.9 | 5876349.46 | 215854 | 0.0089 | 0.00816 | Ok.

## Slide 48
Structural Separation.

## Slide 49: Separation Width
All portions of the structure shall be designed and constructed to act as an integral unit in resisting seismic forces unless separated structurally by a distance sufficient to avoid damaging contact as set forth in this section. Separations shall allow for the maximum inelastic response displacement (δM).
δM=
The separation width δMT for two adjacent blocks is given by the equation:
δMT=
Notes: B3d ma fslna almbna la 6 blocks bdna separation width 3n 6req eno njeb max inelastic drift 3la 7fat kul block mjawer elo

## Slide 50: Separation Width

## Slide 51
Structural Irregularities

## Slide 52: If ( /)>1.2 , then the structure is irregular . If ( /)>1.4 , then the structure is extremely irregular .  Horizontal irregularities
Torsional Irregularity (applicable)
Torsional irregularity check in X-direction.
Story # | Max. drift | Avg. drift | Ratio | Check torsional irregularity | Check extreme-torsional irregularity
Story 5 | 0.00004900 | 0.00004200 | 1.158 | Regular | Regular
Story 4 | 0.00009700 | 0.00007800 | 1.243 | Irregular | Regular
Story 3 | 0.00011900 | 0.00009600 | 1.240 | Irregular | Regular
Story 2 | 0.00013100 | 0.00010300 | 1.267 | Irregular | Regular
Story 1 | 0.00004900 | 0.00004200 | 1.158 | Regular | Regular

## Slide 53
Multiply , Mta the torsional moment due to accidental torsion by a torsional amplification A , ( ASCE 7-10 , Section 12.8.4.3 )
Torsional irregularity check in Y-direction.
2. Perform a 3D dynamic analysis with due consideration for diaphragm stiffness . Use cracked section properties concrete elements . Include P-delta effects ( ASCE 7-10 , Section 12.7.3 )
3. Compute story drift ,( ASCE 7-05 , Section 12.12.1 ) .
Story # | Max. drift | Avg. drift | Ratio | Check torsional irregularity | Check extreme-torsional irregularity
Story 5 | 0.00010400 | 0.00010100 | 1.035 | Regular | Regular
Story 4 | 0.00013700 | 0.00012900 | 1.067 | Regular | Regular
Story 3 | 0.00014600 | 0.00013800 | 1.061 | Regular | Regular
Story 2 | 0.00014100 | 0.00013000 | 1.085 | Regular | Regular
Story 1 | 0.00012800 | 0.00011600 | 1.095 | Regular | Regular
Notes: Accidental torsion bn7ka bel slides ele b3d .
P-delta lazim n7dur ele7aka ermaan.

## Slide 54: Reentrant Corner Irregularity Diaphragm Discontinuity Irregularity Out-of-Plane Offset Irregularity
Not applicable
Not applicable
Applicable

## Slide 55: Non-parallel System Irregularity (applicable)
1. Perform a 3D dynamic analysis with due consideration for diaphragm stiffness . Use cracked section properties concrete elements . Include P-delta effects ( ASCE 7-10 , Section 12.7.3 )
2. Use 100x + 30y , ( ASCE 7-05 , Section 12.5.3 ) .

## Slide 56: Ax=(δmax/(1.2 δavg)) 2 , (Ax) shall not be less than 1 and is not required to exceed 3.0. Accidental Torsion Where : Ax = amplification factor δmax = the maximum displacement at Level X computed assuming Ax = 1 (in. or mm). δavg = the average of the displacements at the extreme points of the structure at Level Xcomputed assuming Ax = 1 (in. or mm).
Ecc. % = Ax * Damping ratio
Ecc. Absolute length = Dx * Ecc. %
Where : Dx =length of the structure in X-direction.

## Slide 57: Accidental torsion
Story # | Dx(m) | Ratio | Ax | Eccentricity % | Eccentricity Absolute length(m)
Story 4 | 49.93 | 1.220 | 1.034 | 0.051 | 2.580
Story 3 | 49.93 | 1.243 | 1.073 | 0.054 | 2.679
Story 2 | 49.93 | 1.229 | 1.049 | 0.052 | 2.619

## Slide 58: Stiffness-Soft Story Irregularity Stiffness-Extreme Soft Story Irregularity Vertical Irregularities
Not applicable
Not applicable

## Slide 59: Vertical Geometric Irregularity Weight (Mass) Irregularity Vertical Irregularities
Not applicable
Not applicable

## Slide 60: In-Plane Discontinuity in Vertical Lateral Force-Resisting Element Irregularity Vertical Irregularities
Applicable

## Slide 61: Discontinuity in Lateral Strength–Extreme Weak Story Irregularity Vertical Irregularities Discontinuity in Lateral Strength–Weak Story Irregularity
Applicable
Not applicable

## Slide 62
Seismic Force-Resisting System Evaluation

## Slide 63: Seismic Force-Resisting System Evaluation
The seismic force-resisting system is building frame system with ordinary reinforced concrete shear walls, and for this system to be viable, the base shear resisted by it must be at least 85% of total base shear acting on the structure in both directions.
Percentage resisted by shear walls:
Notes: B3d ma fslna almbna la 6 blocks bdna separation width 3n 6req eno njeb max inelastic drift 3la 7fat kul block mjawer elo

## Slide 64
New Column Modifiers
Notes: To make sure that 100% of seismic loads are resisted fully by the lateral resisting system, columns shear modifiers are set to zero.

## Slide 65
Design of Structural Elements

## Slide 66: Design of Slabs
Vu = Wu ( - - d) = 93.841 kN
c = bwd = 128 kN
→Since c Vu No need for shear reinforcement in general.
But there is some areas need shear reinforcement.
Shear reinforcement:
Notes: B3d ma fslna almbna la 6 blocks bdna separation width 3n 6req eno njeb max inelastic drift 3la 7fat kul block mjawer elo

## Slide 67: Design of Slabs
As,min=0.0018*b*h=486 mm2/m
Ø 12 was used.
Number of bars = 5 bars
Spacing=200mm.
Maximum spacing of critical sections the lesser of 2h and 450 mm
Maximum spacing= 450 mm
Maximum spacing at other sections the lesser of 3h and 450 mm
Maximum spacing is 450 mm
Flexural reinforcement:
Notes: B3d ma fslna almbna la 6 blocks bdna separation width 3n 6req eno njeb max inelastic drift 3la 7fat kul block mjawer elo

## Slide 68: Slab Reinforcement Summary
Story | Direction | Top reinforcement | Bottom reinforcement
Story 1 | X | 1Ø18/200 | 1Ø12/200
 | Y | 1Ø18/200 | 1Ø12/200
Typical Story | X | 1Ø16/250 | 1Ø12/200
 | Y | 1Ø16/250 | 1Ø12/200
Story 5 | X | 1Ø12/200 | 1Ø12/200
 | Y | 1Ø12/200 | 1Ø12/200
Notes: Additional reinforcement bel structural drawings

## Slide 69
Longitudinal slab reinforcement sections for basement floor.
Sections In Slab.
Shear slab reinforcement section for typical story.

## Slide 70: Design of Beams
Design of beams will be made to ensure all the requirements below are satisfied:
ϕMn ≥ Mu
ϕVn ≥ Vu
ϕTn ≥ Tu
ϕPn ≥ Pu
Reinforcement design stage will go through 4 phases:
Flexural design.
Shear design.
Checking for the necessity for skin reinforcement.
Torsion design.
Notes: سوبر:حسبناه من النون ستركشرل طلع معنا انو توتال =4.5
سنو: الخرائط اي سي اي غير كافية واخدنا اردني لانو اقرب اشي طلع معنا نفس ما مكتوب

## Slide 71
Flexural reinforcement:
Design of Beams
Asmin=0.00333*900*1140=3420 mm2.
As-L=2909mm2< Asmin=3420 mm2 Use 7Ø25.
As-R=3237mm2< Asmin=3420 mm2 Use 7Ø25.
As+=2626mm2< Asmin=3420 mm2
Use 7Ø25.

## Slide 72
Shear reinforcement:
Design of Beams
Av=703.71 mm2/m=0.703 mm2/m
Av min=0.75mm2/mm.
Av min > Av → Av min will be used.
Using Ø10 stirrups →110/200 mm

## Slide 73: Design of Beams
For non-prestressed with h exceeding 900mm, longitudinal skin reinforcement shall be uniformly distributed on both side faces of the beam for a distance h/2 from the tension face .
All Beams have depth >900 mm, so skin reinforcement is required
Tu=From ETABS
Tth= ,If Tu<Tth then Torsion doesn’t need to be considered.
Torsion transverse reinforcement
Total torsion transverse reinforcement
=+
Torsion longitudinal reinforcement
Torsion reinforcement
Skin reinforcement
Notes: سوبر:حسبناه من النون ستركشرل طلع معنا انو توتال =4.5
سنو: الخرائط اي سي اي غير كافية واخدنا اردني لانو اقرب اشي طلع معنا نفس ما مكتوب

## Slide 74
Sample for beams Cross sections.
Structural Drawings

## Slide 75
Sample for beams longitudinal sections.
Structural Drawings

## Slide 76: Design of Columns
Longitudinal reinforcement :
For the selected column, the required longitudinal reinforcement is 8100 mm2 and as it has a square shape, number of bars on the right and left face of the section must equal number of bars on the upper and lower face of the section, so 28 will be used as it gives 8792 mm2 which is adequate to 8100 mm2.
Notes: B3d ma fslna almbna la 6 blocks bdna separation width 3n 6req eno njeb max inelastic drift 3la 7fat kul block mjawer elo

## Slide 77: Design of Columns
Shear reinforcement :
For shear design, the columns in building frame system don’t resist shear as they only resist axial loads, shear forces are resisted by shear walls so there will be no design verification for the shear in the columns.
Notes: B3d ma fslna almbna la 6 blocks bdna separation width 3n 6req eno njeb max inelastic drift 3la 7fat kul block mjawer elo

## Slide 78: Reinforcment of All Columns summery
Column number/Location | Given section name | Given reinforcement
(7,14,21,22,23,24,25,26,27,28,29,30,31,32,33,34,35,36,37,38,39/all floors) | C1 | 28ø20
(24,F1) +(30/Base) + (31/Base) + (32/Base) | C2 | 36ø25
(23/Base)+(25/Base)+(29/base) | C3 | 36ø32
(24/F1) | C4 | 28ø32
(24/Base) | C5 | 44ø32
(25/F1) | C6 | 32ø32
(26/F1) | C7 | 24ø25
(26/Base) | C8 | 40ø32
(1,2,3,4,5,6,8,9,10,11,12,13,15/all floors) | C9 | 20ø14
(16,17,18,19,20,40/ all floors) | C10 | 20ø18
Notes: Additional reinforcement bel structural drawings

## Slide 79
Cross-sectional section in column C1.
Sections In Columns.
General longitudinal section

## Slide 80: Design of Walls
If in-plane Vu ≤ 0.5ϕVc, min. ρℓ and min. ρt shall be in accordance with Table 11.6.1 but if in-plane Vu ≥ 0.5ϕVc, (a) and (b) shall be satisfied:
(a) ρℓ shall be at least the greater of the value calculated by Eq. (11.6.2) and 0.0025.
ρℓ ≥ 0.0025 + 0.5(2.5 – hw/ℓw)(ρt – 0.0025) (11.6.2)
(b) ρt shall be at least 0.0025
Max. Spacing = min. of (Lw/5=1400mm,3h=1200mm,450mm.)
Pier reinforcement:
Notes: B3d ma fslna almbna la 6 blocks bdna separation width 3n 6req eno njeb max inelastic drift 3la 7fat kul block mjawer elo

## Slide 81: Design of Walls
Pier reinforcement summary :
Wall# | Thickness (mm) | Transverse ( horizontal) | longitudinal (vertical)
W1 | 300 | 1Ø14/400 | 1Ø14/400
W2 | 250 | 1Ø14/325 | 1Ø14/450
W3 | 400 | 1Ø14/250 | 1Ø14/250
W4 | 400 | 1Ø14/250 | 1Ø14/300
W5 | 500 | 1Ø14/200 | 1Ø16/300
W6 | 600 | 1Ø14/200 | 1Ø16/200
W7 | 300 | 1Ø14/325 | 1Ø14/400
Notes: B3d ma fslna almbna la 6 blocks bdna separation width 3n 6req eno njeb max inelastic drift 3la 7fat kul block mjawer elo

## Slide 82: Design of Walls
Minimum reinforcement =0.00333*b*h
Spandrels reinforcement:
Spandrels# | Top | Bottom | Ties
S1 | 10Ф25 | 6Ø25 | 2Ø12/100
S2 | 10Ф25 | 6Ø25 | 2Ø12/100
S3 | 11Ф25 | 6Ø25 | 2Ø12/100
Notes: B3d ma fslna almbna la 6 blocks bdna separation width 3n 6req eno njeb max inelastic drift 3la 7fat kul block mjawer elo

## Slide 83
Cross-sectional section in wall 4
Longitudinal section in wall 4
Notes: Mjmoh msahmat almodes twsl 90% mn actual mass aw aktr, 6l3naha mn ETABS w6l3 m3na almode 5bel y, 7 bel x bwslna 0.9

## Slide 84
Cross-sectional section in spandrel 1
Longitudinal detail section in spandrel 1
Notes: Mjmoh msahmat almodes twsl 90% mn actual mass aw aktr, 6l3naha mn ETABS w6l3 m3na almode 5bel y, 7 bel x bwslna 0.9

## Slide 85
Analysis and Design of Mat Foundation

## Slide 86: Why Mat Foundation Should Be Used?
Summation of the columns load (kN) | Bearing capacity(kN/m2) | Area required for the mat footing (m2) | 50% of floor area (m2) | Case
252835.61 | 250 | 1011.34244 | 966.63 | Use mat
Notes: akhdna frame in x direction 3shan n6l3 almoment lal frame, t2kdna mn allimitations lala method 7sb alcode wkan kulu tamam, fa mshena 3la al dddm method mn alcode w6l3na qym almoment hay.
3na error bel Slab cs wel ms l2no ddm dareqa taqrebyah weldistribution ma ba5d b3en ele3tbar aldimensions mthln albeam mhma kan kbeer eza alphaL/L>1 ba5d 0.85 bs eletabs ba5d had ele5tlaf b3en ele3tbar wkul ma kan albeam akbr kul ma kan moment 3leh akbr.

## Slide 87
Mat thickness will be determined according to this conceptual design equation:
Mat thickness = Number of floors *10 cm
Since the structure has 5 floors, mat preliminary thickness will be 50 cm.
Preliminary Mat Thickness

## Slide 88
Punching shear check:
Evaluation of Preliminary Dimensions
The value of punching shear ratio must be lower than 1 for the depth to be adequate. However punching shear values were larger than 1 in most of the columns

## Slide 89
Final Mat Dimensions

## Slide 90
Punching shear check:
Footing Checks

## Slide 91
Soil Pressure Check:
Footing Checks
  Soil pressure reactions will be taken from envelope service combination, all the values should be negative and less than the bearing capacity multiplied by 1.33.

## Slide 92
Settlement Check:
Footing Checks
  Settlement will be taken from envelope service combination, all settlement values should be negative, and less than the maximum allowable value which is 25mm.

## Slide 93
Longitudinal reinforcement:
Mat Design
  Mat with 1300 mm thickness:
  use 125/200 mm bottom bars in X-direction.

## Slide 94
Longitudinal reinforcement:
Mat Design
  Mat with 1300 mm thickness:
  use 125/200 mm top bars in X-direction.

## Slide 95
Longitudinal reinforcement:
Mat design
  Mat with 1300 mm thickness:
  use 125/200 mm bottom bars in Y-direction.

## Slide 96
Longitudinal reinforcement:
Mat design
  Mat with 1300 mm thickness:
  use 125/200 mm top bars in Y-direction.
Notes: El additional reinforcement lal mat 600 w drops mwd7en bl autocad

## Slide 97
Mat design
Notes: El additional reinforcement lal mat 600 w drops mwd7en bl autocad

## Slide 98: Shear Reinforcement for Mat Foundation
The design of cross sections subjected to shear shall be based on:
n Vu
n = Nominal shear strength
Vu = Ultimate shear force
= Strength reduction factor = 0.75
n = Vc + Vs
Vc = Nominal shear strength provided by concrete
Vs = Nominal shear strength provided by shear reinforcement.
Vc = bwd
Notes: B3d ma fslna almbna la 6 blocks bdna separation width 3n 6req eno njeb max inelastic drift 3la 7fat kul block mjawer elo

## Slide 99
Design of Stairs

## Slide 100: Design of Stairs
Load applied on the flight:
Mu+ = 18.19 kN.m ,, Mu- = 12.12 kN.m ,, Vu = 24.25 kN
Shear check:
ØVc = 0.75 x 1/6 x 1000 x 120 = 73.45 kN > Vu = 24.25 kN, OK.
Flexural design:
As,min = 0.0018 bd = 0.0018 x 1000 x 120 = 216 mm2
Mu- = 12.12 kN.m, ρ = = 0.0026, As = ρbd = 312 mm2, use 1Ø12/250 mm.
Mu+ = 18.19 kN.m, ρ = 0.004, As = ρbd = 480 mm2, use 1Ø14/250 mm.
Design of landing
Design of flight
Load applied on the flight:
Mu+ = 33.08 kN.m ,, Vu = 50.9 kN.
Shear check:
ØVc = 0.75 x 1/6 x 1000 x 120 = 73.48 kN > Vu = 50.9 kN, OK.
Flexural design:
As,min = 0.0018 bd = 0.0018 x 1000 x 120 = 216 mm2, 1Ø12/250 mm.
Mu+ = 33.08 kN.m, ρ = = 0.0072, As = ρbd = 864 mm2, use 1Ø16/200 mm.
Notes: سوبر:حسبناه من النون ستركشرل طلع معنا انو توتال =4.5
سنو: الخرائط اي سي اي غير كافية واخدنا اردني لانو اقرب اشي طلع معنا نفس ما مكتوب

## Slide 101: Stairs Reinforcement
Notes: B3d ma fslna almbna la 6 blocks bdna separation width 3n 6req eno njeb max inelastic drift 3la 7fat kul block mjawer elo

## Slide 102: Appendices Chapter 4

## Slide 103: Appendices
The previous analysis was made on the rest of the blocks. Also, the design was made on block number 1 .

## Slide 104: References Chapter 5

## Slide 105: References
ACI 318 2014. Building code requirements for structural concrete (ACI 318M-14): an ACI Standard : Commentary on building code requirements for structural concrete (ACI 318M-14), Farmington Hills, MI, American Concrete Institute.
ASCE 2010. Minimum design loads for buildings and other structures, Reston, Va., American Society of Civil Engineers: Structural Engineering Institute.
ASTM, C. (1958). ASTM Standards. Philadelphia: American Society for Testing Materials.‏
Cambridge University Dictionary (2020, November 12). Meaning of Civil Engineering. Retrieved from https://dictionary.cambridge.org/dictionary/english/civil-engineering.
Guzman, T. (2017). Modeling concrete cracked section properties for building analysis. CSI Computers & Structures Inc. (2020) Retrieved from https://wiki.csiamerica.com/display/etabs/Modeling+concrete+cracked+section+properties+for+building+analysis.
INTERNATIONAL CODE COUNCIL 2014. International building code 2015, Country Club Hills, Ill., ICC.
Moore, K.(2009) Seismic Force-Resisting Systems. Structure magazine, 18-21.
Watkins, R., Keil, B., Mielke, R., & Rahman, S. (2010). Pipe zone bedding and backfill: a flexible pipe perspective. In Pipelines 2010: Climbing New Peaks to Infrastructure Reliability: Renew, Rehab, and Reinvest (pp. 426-438).
الجمعية العلمية الملكية مركز بحوث البناء,( ٢٠٠٦), كودات البناء الوطني الأردني: كودة الأحمال والقوى. الاردن, عمان: المكتبة الوطنية

## Slide 106: Thanks!
Do you have any questions?
Feel free to ask.