## Slide 1: Pilot Study on Smart Campus:
Modeling Pedestrian Behavior at NNU, New Campus Feras Elsaid Watheq Sayeh Supervisor: Prof. Sameer Abu-Eisheh

## Slide 2: Why not smart ?!
Study Area
Objectives
Literature Review
Methodology
Data Collection
Data Analysis
Results
Future work

## Slide 3: Study Area

## Slide 4: Objectives
Detecting pedestrians’ problems
Understanding behavior of pedestrians
Utilizing new technology, mainly smartphones, in transportation aspects
Basis and first step of research in this field in Palestine

## Slide 5: Done so far ..
Van Langelaar and van der Spek (2010)
Ghanim and Abu-Eisheh (2014)
Asadi-Shekari, Moeinaddini and Shah (2014)
Sahania, R. and P. K. Bhuyan (2013)
Christopoulou and Pitsiava-Latinopoulou (2012)

## Slide 6: Done so far ..
Some studies utilized smartphones for urban planning purposes, others studied transportation aspects of pedestrians movement, like LOS, but no one considered both aspects.

## Slide 7: Our work
No such a study in Palestine!

## Slide 8: Methodology
Do a surveillance in the study area to detect problems
Collect data (both manual and smart)
Analyze data
Review past solutions
Conclude and recommend

## Slide 9: Data collection
Manual data (simultaneously):
speed study of vehicles
count of pedestrians
count of vehicles
Mobile phone data:
11 volunteers

## Slide 10: ArcGIS Work
WGS-84 as spatial reference
Representing of data

## Slide 11: ArcGIS Work
Lines representing the direction and length of each movement

## Slide 12: ArcGIS Work
Lines representing the directional mean of each group

## Slide 13: ArcGIS Work
The directional mean of all movements

## Slide 14: ArcGIS Work
Using Excel : calculating the distance between each successive points
Spherical law of cosines.
where
= latitude value of the first point
= latitude value of the second point
= Difference in longitude values
Noting that (acos) is the cosine inverse function.
R: the radius of earth which is 6371000 m(6371 km)

## Slide 15: ArcGIS Work

## Slide 16: Results
Speed Variations

## Slide 17: Level Of Service(LOS) Analysis
PLOS: Main gate of the campus
Pedestrian Level of Service (PLOS)

## Slide 18: PLOS: Main gate of the campus
Period | Direction of movement | Total Pedestrian per hour(flow rate) | max 15 min-interval volume | Peak 15 min
Mon. 7:36 – 8:36 am | Entering the campus | 2274 | 1220 | 7:44 - 7:59
Sun. 2:00 – 3:00 pm | Leaving the campus | 1778 | 849 | 2:45 – 3:00
Wed. 12:30 – 13:24 pm | Entering the campus, Leaving the campus(Total) | 1773 | 614 | 12:30 -12:45
Sun. 7:42 – 8:42 am | Entering the campus | 2538 | 1275 | 7:48 – 8:03

## Slide 19: PLOS: Main gate of the campus
Period | max 15 min-interval volume | Effective width =1.4 m |  | Effective width =2.30 m | 
 |  | Flow Rate (p/min/m) | PLOS | Flow Rate (p/min/m) | PLOS
Mon. 7:36 – 8:36 am | 1220 | 58.10 | E | 35.36 | D
Sun. 2:00 – 3:00 pm | 849 | 40.43 | D | 24.61 | C
Wed. 12:30 – 13:24 pm | 614 | 29.24 | C | 17.80 | B
Sun. 7:42 – 8:42 am | 1275 | 60.71 | E | 36.96 | D

## Slide 20: PLOS: Crosswalk in front of the campus
Date | Day | Time | PLOS Score | PLOS
20/10/2015 | Tuesday | 2:45-3:45 | 4.0 | E
21/10/2015 | Wednesday | 8:45-9:45 | 3.5 | F
22/10/2015 | Thursday | 2:45-3:34 | 3.8 | F
Day | Time interval | Total pedestrian volume | Peak 15-min pedestrians’ volume
Thursday | 3:57 – 3:12 | 1468 | 581
Wednesday | 9:20 – 9:35 | 1556 | 540
Tuesday | 2:50 – 3:05 | 1283 | 580

## Slide 21: Vehicular Level of Service (VLOS)
HCM (2010) was used to calculate VLOS for the street in front of the campus as a multilane highway for the current the traffic situation
Upgrade |  |  | 
Day | Time interval | Peak 15-min vehicles’ volume | VLOS
Thursday | 2:47 – 3:02 | 229 | B
Wednesday | 9:15 – 9:30 | 265 | B
Tuesday | 3:00 – 3:15 | 265 | B

## Slide 22
Downgrade |  |  | 
Day | Time | Peak 15-min vehicles’ volume | VLOS
Thursday | 2:47 – 3:02 | 252 | B
Wednesday | 9:20-9:35 | 270 | B
Tuesday | 3:15 – 3:30 | 225 | B
Vehicular Level of Service (VLOS)

## Slide 23: But… Synchro
Direction | East Bound | West Bound
Number of lanes | 2 | 2
Width of lane (m) | 3.6 | 3.6
Grade (%) | -9% | 9%
Peak Volume (pc/hr) | 1080 | 1060
Percentage of heavy vehicles (%) | 2 | 2
Pedestrian Volume (ped/hr) | 2160 | 2160
Sign control | Yield | Yield
Approach LOS | E | E

## Slide 24: VLOS using Synchro

## Slide 26: REVIEW OF SOME PROPOSED SOLUTIONS
“Evaluation and Re-Design of the Transportation System Around the New Campus of An-Najah National University”

## Slide 27: Cross-section

## Slide 28: Plan view

## Slide 29
Designed as:
Underpass ,Two-way Two-lane highway
Width of lane= 3.20m , width of shoulder = 1.40m
Grade greater than 4%
530 m long

## Slide 30: LOS of Two-way, two-lane Underpass
Assumptions:
class II highway as:
Serves as a way to an arterial two-lane highway
Limited length
Specific grade method as the grade of this segment greater than 4 %

## Slide 31: LOS of Two-way, two-lane Underpass
40 % of total traffic as through traffic
VLOS by this solution:
Proposed growth rate (Ashqar, Atair & Shoman, 2012) : 4.4%
Heavy vehicle percentage: 2%
LOS for the upgrade direction (critical):
= 429 pc/hr
437 pc/hr
Future values of and would be: 892 and 909, respectively
LOS is E
However,
If growth rate were 3.0%,
Future values of and would be : 709 and 723, respectively
LOS is D

## Slide 32: Total Cost of the project
Cost (2012) = $630,000
Road Cost Index (RCI) was 114.55 (2012, Base year=2008) most recent RCI reached 110.47 (25/11/2015, Base year=2008).
Cost (2015) = $ 607,600

## Slide 33: New Campus’s Master Plan

## Slide 34: Modeling Multimodal Effect on Vehicular Speeds
West Bound Direction
Using Regression analysis for the collected data including: Vehicles’ volume, pedestrians’ volume and vehicles’ speeds
Date | Day | Time | Constant | Vehicular volume Coefficient | Pedestrian Volume Coefficient | R Square
20/10/2015 | Tuesday | 2:40-3:40 | 39.880 | -0.012 | -0.108 | 0.828
21/10/2015 | Wednesday | 8:45-9:45 | 43.445 | -0.111 | -0.020 | 0.650
22/10/2015 | Thursday | 2:47-2:37 | 53.146 | -0.526 | -0.002 | 0.781

## Slide 35: Modeling Multimodal Effect on Vehicular Speeds
East Bound Direction
Date | Day | Time | Constant | Vehicular volume Coefficient | Pedestrian Volume Coefficient | R Square
20/10/2015 | Tuesday | 2:40-3:40 | 16.894 | 0.099 | -0.056 | 0.866
21/10/2015 | Wednesday | 8:45-9:45 | 29.266 | 0.080 | -0.122 | 0.356
22/10/2015 | Thursday | 2:47-2:37 | -30.613 | 0.682 | 0.032 | 0.839

## Slide 36: Summary
Cross walk PLOS: F
VLOS:
Current situation:
Manually, was B.
Using Synchro, was E.
Proposed by Ashqar, Atair and Shoman, (after 17 years): D
Pedestrians tend to cross the road randomly, might be diagonally, so they do not stick to the cross walk.
Average speed of pedestrians in front of the campus was 1.2m/s.

## Slide 37: Future work’s Recommendations
Image processing
Real-time vehicular traffic information.
The proposed solution by Ashqar, Atair and Shoman.
Multimodal models:
Increase the study period and consider the analysis period as least as one or two minute.
Measure all the multimodal parameters in the field, e.g., parking maneuvers, etc…
Take surrounding environment hindrances into account.
Consider safety issue in front of the campus.

## Slide 38: Thank you for listening