## Slide 1
Investigating Black Spots and Proposing Solutions for the Western Part of Nablus City
Graduation Project 2
Prepared by:
Osaid Salman
Mohammad Abu-Bshara
Omar Abu-Zaineh
Under supervision: Prof. Sameer Abu- Eisheh

## Slide 2
Outline of the project:
Introduction and description.
Methodology of the project.
Literature review.
Data collection.
Analysis and results.
Proposed solutions.
Conclusions and recommendations.

## Slide 3
Background of the project
Why this project?
Increasing the number of crashes
Congestion.
Black Spots
Traffic safety

## Slide 4
Objectives:
To collect all relevant data related to crashes in the study area in order to make proper analysis.
To determine the problems and causes that are related to black spots crashes within the western part of Nablus City.
To find feasible solution alternatives for the studied crash traffic locations to select the best solution based on a specified criterion.
To identify recommendations to the responsible authorities to adopt the approach to be considered and to start implementing the proposed remedial measures.

## Slide 5
Study Area:
The study area includes the western part of Nablus City, which forms a large part of the city and where traffic crashes are occurred relatively high so, it needs to study this area.

## Slide 7
Analysis and Results
Literature Review
Data Collection
Criteria
Methodology
Proposed solutions
Conclusions and Recommendations

## Slide 8
Literature Review
The countries that are considered in literature review include:
Palestine
USA
India
Germany
Hungary
Norway
China
Saudi Arabia
Austria

## Slide 9
Definition of Black Spots:
Palestine: It is to be stated that the Traffic Police consider the black spots in any part of the road to not more than 1000 meters or any intersection which recur 8 crashes and more (i.e., through ranking) that have recorded during 1 year, without taking into account traffic volumes.
    S= 20F + 10D + 2M + L
where:
      S: Risk coefficient.
      F: Number of fatalities.
      D: Number of serious injuries.
      M: Number of medium-serious injuries.
      L: Number of light injuries

## Slide 10
Austria:
In order to identify black spots according to the Austrian Guideline Code.
one of the following two criteria has to be met:
3 or more similar injury accidents within 3 years and a relative coefficient of at least 0.8.
At least 5 accidents (including property damage only) of similar type within one year.

## Slide 11
The critical value of 0.8 of the relative coefficients will be reached under the following circumstances:
3 injury accidents in 3 years and an AADT up to 10,700 vehicles/24 hours
4 injury accidents in 3 years and an AADT up to 16,700 vehicles/24 hours
5 injury accidents in 3 years and an AADT up to 22,600 vehicles/24 hours
6 injury accidents in 3 years and an AADT up to 28,600 vehicles/24 hours

## Slide 12
The collected data include information about location, time of occurrence, main causes for occurrence, number of injuries, and severity for each crash (fatal, personal injury and property damages), and the number of cars colliding.
A sample of data collected from the Traffic Police as shown
Data collection

## Slide 13
الرقم | مكان الحادث | عدد الاصابات | درجة كل إصابة | وقت الحدوث | عدد السيارات المشاركة بالحادث ونوعها | سبب وقوع الحادث
1 | شارع رفيديا - مفرق البدوي | - | - | 17:30 | خ × د. ن. | عدم تأمين الاستدارة لليسار
2 | شارع رفيديا - مفرق البدوي | - | - | 16:00 | خ × خ | عدم ترك مسافة آمنة للتوقف
3 | شارع رفيديا - مفرق البدوي | 2 | بسيطة | 15:20 | خ × خ × خ | استدارة خاطئة
4 | شارع رفيديا - مقابل الأكاديمية | 1 | بسيطة | 23:15 | ع (دهس) | عدم اتخاذ التدابير اللازمة لعابري الطريق
5 | شارع رفيديا - مقابل الأكاديمية | 1 | وفاة | 22:00 | د. ن. | السوق بسرعة لا تتفق مع ظروف الطريق
6 | شارع رفيديا - نزلة بليبلة | 1 | بسيطة | 13:40 | خ (دهس) | عدم اتخاذ التدابير اللازمة لعابري الطريق
7 | شارع رفيديا - مقابل مسجد الروضة | - | - | 18:00 | خ × خ | التحول عن مسلك السير
8 | شارع رفيديا - مقابل حلويات البيك | - | - | 18:00 | خ × خ × ع | عدم ترك مسافة آمنة للتوقف
9 | شارع رفيديا - مقابل المتميزون | 6 | بسيطة | 09:40 | خ × خ | عدم ترك مسافة آمنة للتوقف
10 | شارع رفيديا - مقابل المدرسة الاسلامية | 3 | بسيطة | 09:00 | خ × خ × خ | عدم السير على المسلك الايمن
11 | شارع رفيديا - مقابل الأكاديمية | 3 | بسيطة | 12:00 | ع × ع | عدم ترك مسافة آمنة للتوقف
12 | شارع رفيديا - مقابل البنك العربي | - | - | 12:00 | خ × ع | عدم ترك مسافة آمنة للتوقف
13 | شارع رفيديا - طلعة عبد الرحيم محمود | - | - | 12:50 | خ × خ | عدم الامتثال لإشارة قف
14 | شارع رفيديا - طلعة عبد الرحيم محمود | - | - | 14:00 | خ × ع | الرجوع للخلف
15 | شارع رفيديا | 1 | متوسطة | 07:20 | خ × خ (دهس) | عدم اتخاذ التدابير اللازمة لعابري الطريق
16 | شارع رفيديا | - | - | 17:00 | خ × خ | تجاوز خاطئ

## Slide 14
After that, the team refer to many previous traffic studies to obtain traffic volumes within study area. There include:
Al Basateen Street.
Beit Iba Street.
Al Sikka Street.
Beit Wazan.
Street Almakhfeiah Street.
Tunis Street.
Rafidia Street.
Al Mureij Street.

## Slide 15
Haifa Street.
Jaffa Street.
Arab Hospital.
Rafidia Hospital.
Almajean.
Zawata Street.
Al Muntazaht Street.
15th Street.
Al Najah Street.
24 Street.
25 Street.
Intersection of Al Salam Mosque.

## Slide 16
Data Collection for all study area (Veh/hr)
Year | Peak Hourly Volume (PHV) | Location | Number
2008 | 1416 | شارع الشويترة - مفرق الفاطمية | 1
2013 | 2131 | رفيديا - مقابل مسجد الروضة | 2
2013 | 2187 | رفيديا - مقابل شركة جوال | 3
2008 | 2000 | رفيديا مقابل مستر بيكر | 4
2008 | 882 | رفيديا مقابل عمارة الزكاة | 5
2008 | 984 | رفيديا مقابل المسجد القديم | 6
2008 | 897 | رفيديا بعد نزلة الاتصالات | 7
2008 | 1043 | رفيديا مقابل ناصر سنتر | 8
2008 | 1599 | شارع الأكاديمية -بجانب الجنيد | 9
2008 | 649 | المخفية مقابل مديرية الصحة | 10
2008 | 835 | شارع النجاح القديم | 11
2008 | 1012 | شارع حيفا مقابل محكمة الصلح | 12
2008 | 1090 | شارع بيت ايبا | 13
2008 | 409 | شارع تونس | 14
2008 | 281 | طلعة عبد الرحيم محمود | 15
2018 | 2474 | تقاطع ملعب البلدية مع شارع يافا | 16
2018 | 3326 | مفرق السلام | 17
2018 | 750 | شارع المريج | 18
2019 | 1200 | مفرق تونس - أم سلمة | 19
2019 | 2860 | شارع رفيديا - مفرق الاتصالات | 20
2013 | 1963 | شارع رفيديا - مفرق مدرسة ابن قتيبة | 21
2013 | 2071 | شارع رفيديا - مفرق البدوي | 22
2013 | 2327 | شارع رفيديا - مفرق تونس | 23
2013 | 2265 | شارع رفيديا - مقابل كوكتيل بردى | 24
2013 | 2764 | مفرق مستشفى رفيديا -العربي | 25
2018 | 2051 | تقاطع شارع حيفا مع تونس | 26
2018 | 2776 | مفرق البساتين | 27
2018 | 2691 | شارع المنتزهات | 28
2017 | 524 | شارع 25 | 29
2018 | 1591 | شارع يافا | 30
2018 | 2575 | دوار زواتا | 31

## Slide 17
Data collection

## Slide 18
Data collection

## Slide 19
Data collection

## Slide 20
Data collection

## Slide 21
Data collection

## Slide 22
Data collection

## Slide 23
Criteria
Austrian criteria
Palestinian criteria

## Slide 24
Data Analysis
All data were entered in Excel. The data were first cleaned to then exclude data a crashes outside the study area
الرقم | مكان الحادث | عدد الاصابات | درجة كل إصابة | وقت الحدوث | عدد السيارات المشاركة بالحادث ونوعها | سبب وقوع الحدث
شهر 1 |  |  |  |  |  | 
1 | طلعة تونس | - | - | 15:00 | خ × خ | الرجوع للخلف
2 | حرم النجاح القديم | - | - | 19:30 | خ × خ | عدم ترك مسافة آمنة للتوقف
3 | شارع رفيديا | - | - | 13:30 | خ × خ | عدم الامتثال لإشارة قف
4 | مفرق زواتا | 1 | بسيطة | 07:40 | خ × ع | التحول عن مسلك السير
5 | شارع المريج | - | - | 07:00 | خ × ت | الرجوع للخلف
6 | أمام مخيم العين | 1 | بسيطة | 08:20 | خ (دهس) | عدم اتخاذ التدابير اللازمة لعابري الطريق
7 | شارع السكة | - | - | 19:10 | خ × ع | السوق بسرعة لا تتفق مع ظروف الطريق
8 | شارع العين - أمام القلعة | - | - | 16:30 | خ × خ × خ × خ | التحول عن مسلك السير
9 | شارع بيت وزن | - | - | 18:45 | خ × خ | التحول عن مسلك السير
10 | شارع رفيديا | 1 | بسيطة | 14:30 | د. ن. (دهس) | عدم اتخاذ التدابير اللازمة لعابري الطريق
11 | خلف الأكاديمية | 2 | بسيطة | 08:30 | خ (ذاتي) | الانحراف عن مسلك السير
12 | شارع 24 | 7 | بسيطة | 00:00 | خ × خ × خ | الانحراف عن مسلك السير
13 | شارع رفيديا | - | - | 18:30 | خ × خ | عدم تأمين الالتفاف
14 | شارع المريج | - | - | 19:00 | خ × خ | التحول عن مسلك السير
15 | شارع رفيديا - مقابل مسجد الروضة | - | - | 10:45 | عمومي × عمومي | عدم ترك مسافة آمنة للتوقف

## Slide 25
Data Analysis
After that all data sorted according to the location in addition to type and severity of injuries.
الرقم | مكان الحادث | عدد الاصابات | درجة كل إصابة | وقت الحدوث | عدد السيارات المشاركة بالحادث ونوعها | سبب وقوع الحادث
80 | شارع بيت وزن | 1 | بسيطة | 19:00 | ت (دهس) | عدم اتخاذ التدابير اللازمة لعابري الطريق
81 | شارع بيت وزن | 1 | بسيطة | 10:30 | خ × خ | عدم ترك مسافة آمنة للتوقف
82 | شارع بيت وزن | 1 | بسيطة | 13:00 | خ × ع | تجاوز خاطئ
83 | شارع بيت وزن - قرب برافو | 1 | بسيطة | 22:30 | خ (ذاتي) | التحول عن مسلك السير
84 | شارع بيت وزن - قرب برافو | 2 | وفاة 1بسيط | 08:40 | خ × خ | التحول عن مسلك السير
85 | شارع تونس | 5 | بسيطة | 11:30 | ع × ع × ش | عدم تأمين الحمولة
86 | شارع تونس | 2 | بسيطة | 14:30 | خ × خ | التحول عن مسلك السير
87 | شارع تونس | 1 | بسيطة | 20:20 | خ × د. ن. | التحول عن مسلك السير
88 | شارع تونس | 1 | بسيطة | 11:30 | خ × د. ن. | عدم الامتثال لإشارة قف الضوئية
89 | شارع حيفا | 1 | بسيطة | 18:00 | خ (دهس) | عدم اتخاذ التدابير اللازمة لعابري الطريق
90 | شارع حيفا | 2 | بسيطة | 17:00 | خ × ع | عدم تأمين الاستدارة
91 | شارع حيفا | 1 | صعبة | 13:00 | خ (دهس) | عدم اتخاذ التدابير اللازمة لعابري الطريق
92 | شارع حيفا | 1 | متوسطة | 10:30 | خ (دهس) | عدم اتخاذ التدابير اللازمة لعابري الطريق
93 | شارع حيفا | 1 | بسيطة | 15:00 | خ × د. ه. | عدم ترك مسافة آمنة للتوقف
94 | شارع حيفا | 1 | بسيطة | 19:00 | خ (ذاتي) | التحول عن مسلك السير
96 | شارع حيفا - مقابل المحكمة | 6 | بسيطة | 08:10 | خ × خ × ش | عدم ترك مسافة آمنة للتوقف
97 | شارع حيفا - مقابل المحكمة | 8 | بسيطة | 19:25 | خ × خ | التحول عن مسلك السير
98 | شارع حيفا - مقابل المحكمة | 2 | بسيطة | 22:10 | خ × خ | عدم اعطاء حق الاولوية للقادم من اليمين
99 | شارع حيفا - مقابل المحكمة | 4 | بسيطة | 10:10 | خ × ش | الرجوع للخلف
100 | شارع حيفا - مقابل المحكمة | 2 | بسيطة | 17:00 | خ × خ | استدارة خاطئة

## Slide 26
Data Analysis
Traffic volumes obtained from previous traffic studies were collected during the period from 2008 to 2019. Therefore, it's needed to find the average annual growth factor in order to be have consistent traffic volume data with traffic crashes data (i.e., for the same year of 2017, 2018 and 2019) for each link and intersection.
The growth factor was determined from previous traffic study that performed for 2008 and 2013 within the same location so it is easy to determine the growth factor.
 Take Growth factor = 4 %

## Slide 27
Data Analysis
In order to calculate AADT, the general equation that relates this with the peak volume is used:
PHV = K * AADT
where:
PHV: peak hourly volume.
K: factor define as the proportion of annual average daily traffic occurring in an hour ranges from 8% to 12 % and in Palestine, Taken K = 10 %.
AADT: Average annual daily traffic.

## Slide 28
Rafidia Street was divided into five sections and these sections are shown below:
Data Analysis

## Slide 29
All traffic volumes were handled in the same way using Excel as shown:
Number | Location | Peak Hourly Volume (PHV) | AADT | AADT | Year
1 | شارع الشويترة - تقاطع الفاطمية | 1416 | 14160 | 21799 | 2008
2 | رفيديا - مقابل مسجد الروضة | 2131 | 21310 | 25927 | 2013
3 | رفيديا - مقابل شركة جوال | 2187 | 21870 | 26609 | 2013
4 | رفيديا مقابل مستر بيكر | 2000 | 20000 | 30789 | 2008
5 | رفيديا مقابل عمارة الزكاة | 882 | 8820 | 13578 | 2008
6 | رفيديا مقابل المسجد القديم | 984 | 9840 | 15149 | 2008
7 | رفيديا بعد نزلة الاتصالات | 897 | 8970 | 13809 | 2008
8 | رفيديا مقابل ناصر سنتر | 1043 | 10430 | 16057 | 2008
9 | شارع الأكاديمية -بجانب الجنيد | 1599 | 15990 | 24616 | 2008
10 | المخفية مقابل مديرية الصحة | 649 | 6490 | 9992 | 2008
11 | شارع النجاح القديم | 835 | 8350 | 12855 | 2008
12 | شارع حيفا مقابل محكمة الصلح | 1012 | 10120 | 15579 | 2008
13 | شارع بيت ايبا | 1090 | 10900 | 16781 | 2008
14 | شارع تونس | 409 | 4090 | 6297 | 2008
15 | طلعة عبد الرحيم محمود | 281 | 2810 | 4326 | 2008
16 | تقاطع ملعب البلدية مع شارع يافا | 2474 | 24740 | 25729 | 2018
17 | مفرق السلام | 3326 | 33260 | 34591 | 2018
18 | شارع المريج | 750 | 7500 | 7800 | 2018
19 | مفرق تونس - أم سلمة | 1200 | 12000 | 12000 | 2019
20 | شارع رفيديا - مفرق الاتصالات | 2860 | 28600 | 28600 | 2019
21 | شارع رفيديا - مفرق مدرسة ابن قتيبة | 1963 | 19630 | 24839 | 2013
22 | شارع رفيديا - مفرق البدوي | 2071 | 20710 | 26205 | 2013
23 | شارع رفيديا - مفرق تونس | 2327 | 23270 | 29444 | 2013
24 | شارع رفيديا - مقابل كوكتيل بردى | 2265 | 22650 | 27558 | 2013
25 | مفرق مستشفى رفيديا -العربي | 2764 | 27640 | 33629 | 2013
26 | تقاطع شارع حيفا مع تونس | 2051 | 20510 | 21331 | 2018
27 | مفرق البساتين | 2776 | 27760 | 28871 | 2018
28 | شارع المنتزهات | 2691 | 26910 | 27987 | 2018
29 | شارع 25 | 524 | 5240 | 5668 | 2017
30 | شارع يافا | 1591 | 15910 | 16547 | 2018
31 | دوار زواتا | 2575 | 25750 | 26780 | 2018

## Slide 30
To identify black spots according to the Austrian Guideline Code for the Planning, and to have a location to be classified as a black spot, one of the following two criteria has to be met:
3 or more similar injury accidents within 3 years and a relative coefficient of at least 0.8.
At least 5 accidents (including property damage only) of similar type within one year.
where:
AADT: Annual Average Daily Traffic (vehicles/24hours)
U: Number of injury accidents within 3 years

## Slide 31
Sample calculations for a street to identify Black spots:
Total number of accidents that have the same cause for Al – Montazahat St.
مجموع الحوادث | عدد الحوادث عام 2019 | عدد الحوادث عام 2018 | عدد الحوادث عام 2017 | سبب الحادث
3 | *** | 1 | 2 | التحول عن مسلك السير
1 | *** | *** | 1 | الدخول بعكس اتجاه السير
2 | *** | 1 | 1 | عدم اتخاذ التدابير اللازمة لعابري الطريق
4 | *** | 3 | 1 | السوق بسرعة لا تتفق مع ظروف الطريق
5 | 2 | 1 | 2 | عدم الامتثال لإشارة قف
3 | *** | 2 | 1 | عدم الامتثال لإشارة قف الضوئية
3 | 2 | *** | 1 | عدم تأمين الاستدارة لليمين
14 | 7 | 4 | 3 | عدم ترك مسافة آمنة للتوقف
1 | *** | 1 | *** | الانحراف عن مسلك السير
1 | *** | 1 | *** | التجاوز الخاطئ
1 | *** | 1 | *** | عدم الامتثال لإشارة تمهل
1 | *** | 1 | *** | لا يوجد
2 | 2 | *** | *** | عدم السير بالحيوان على اليمين
2 | 2 | *** | *** | قضية عامة
2 | 2 | *** | *** | عدم الانصياع للإشارة الضوئية

## Slide 32
In 2019, AADT = 27987 veh/ 24 hr
U = 13 crashes
= 5.28
U = 13 crashes >3 & = 5.28 > 0.8 Therefore, the street may considered as a Black Spot.
The value of AADT = 27987 less than 28600 and the total number of injuries over three years at the same location = 13 more than the critical value = 6 so, it is considered as Black Spots
Data Analysis

## Slide 33
Total number of accidents that have the same cause for For Al- Maajean St.
The highest number of accidents that have the similar cause for Al- Maajean St. = 2 < 3. Since one of the conditions did not meet the standard, this street cannot be considered as a black spot.
مجموع الحوادث | عدد الحوادث عام 2019 | عدد الحوادث عام 2018 | عدد الحوادث عام 2017 | سبب الحادث
1 | 1 | - | - | عدم إعطاء حق أولوية
1 | 1 | - | - | عدم تأمين فتح باب
2 | 1 | - | 1 | عدم اتخاذ التدابير اللازمة لعابري الطريق
2 | 1 | - | 1 | السوق بسرعة لا تتفق مع ظروف الطريق
1 | - | - | 1 | عدم الامتثال لإشارة قف
1 | - | - | 1 | عدم ترك مسافة آمنة للتوقف

## Slide 34
Summary of all results shows values:

## Slide 35
According Palestinian criteria
For Al-Basateen Intersection:
The number of crashes during 2019 = 22 > 8 the intersection is considered as a Black Spot.
F = 0, D = 0, M = 0, L = 21
S= 21 ( Low severity ).

## Slide 37
Results
According Austrian criteria, the black spots in the western part of ​​Nablus where they were as follows, ranked from the most severe location.
1. Al Basateen intersection.
2. Almakhfeiah Street.
3. Rafidia Street – Section 3.
4. Rafidia Street – Section 1.
5. Haifa Street (From Alain to Al-Maajeain).
6. Jaffa Street (From Ain-Alsebian to Wadi Altofah ).
7. Beit-Iba Street.
8. Tunis street.
9. Muntazahat Street.
10. Intersection of Al Salam.

## Slide 38
Results
11. Rafidia Street – Section 2.
12. An Najah old Street (First section).
13. Moh'd Bin Rashid Al-Maktom Street.
14. Al-Shewitri - Al-Fatimiah intersection.
15. An Najah old Street (Third section ).
16. Rafidia Street – Section 4.
17. Haifa Street (From Al-Salam to Alain).
18. Haifa Street (From Al-Maajeain to Tunis intersection).
19. Jaffa Street (From Municipal stadium to Al-qala).
20. Mahmoud Abbas Street.

## Slide 39
Results
According Palestinian criteria, the black spots in the western part of ​​Nablus where they were as follows, ranked from the most severe location.

## Slide 43
PROPOSED SOLUTIONS
In general, there are several reasons for crashes to occur in those areas, where the team worked to find some possible alternatives in order to eliminate or reduce the chance of their occurrence, the most important of which were:

## Slide 44
PROPOSED SOLUTIONS
Isolating the movements from each other as possible for intersections.
Separating between lanes and directions by marking the sections and intersections.
Preventing the illegal parking.
Securing sidewalks for pedestrian.
Using control signs as needed to help the drivers to cross safely in the desired lane.
Proper path and island design using Vehicle Tracking on Civil3D.

## Slide 45
PROPOSED SOLUTIONS
Item | Width
Lane Width | 2.7-3.6m
Sidewalk Width | 1.2-2.4m
Median Width | 1.2-7.5m

## Slide 46
  Design & Redesign of Sections, Intersections, and Roundabout
Part of Al Montazahat Street.
Al-Salam, Al-Basateen intersections.
Al-Wakalah intersections.
Al-Zaytuna intersections.
Design a roundabout at the intersection of Moh'd Bin Rashid Al-Maktom Street and Yasir Arafat Street.

## Slide 47
  For Al-Basateen, Al-Salam intersections, and part of Al-Montazahat street
Current situation

## Slide 48
  part of Al-Montazahat street
Proposed solution

## Slide 49
  For Al-Basateen intersection
Proposed solution

## Slide 50
  For Al-Salam intersection
Current situation

## Slide 51
  For Al-Salam intersection
Proposed solution

## Slide 52
  For Al-Wakalah intersection
Current situation

## Slide 53
  For Al-Wakalah intersection
Proposed solution

## Slide 54
  For Al-Zaitonah intersection
Current situation

## Slide 55
  For Al-Zaitonah intersection
Proposed solution

## Slide 56
For Roundabout on Moh'd Bin Rashid Al-Maktom Street and Yasir Arafat Street intersection:
Current situation

## Slide 57
For Roundabout on Moh'd Bin Rashid Al-Maktom Street and Yasir Arafat Street intersection:
Proposed solution

## Slide 58
Vehicle tracking
Single Unit 12

## Slide 59
Vehicle tracking
Bus-45

## Slide 60
In this study, the team collected crash and other relevant information for the western part of the Nablus City in order to know what are the most dangerous intersections and sections locations (black spots) in order to propose solutions to them.
Therefore, the team used the collected information to further analyze them, considering the appropriate procedures, after the team reviewed criteria used in selected countries to investigate the black spots. The team compared the outcome considering the Austrian and Palestinian criteria and found close in the results. Finally, the team adopted the Palestinian criteria in order to identify black spots, for inside the cities although was originally used for external roads.
Conclusions

## Slide 61
  Recommendations
To the Traffic Police:
      Improve the process of archiving crashes related data and focus on accurately identifying locations of crashes using GPS technologies.
      Take strict measures against those who violate the traffic laws.

## Slide 62
  Recommendations
Work to develop agreed upon the Palestinian procedures for investigating black spots, with the participation of all relevant ministries and institutions.
To the MOT and MOPWH: Work on conducting studies and research that improve traffic safety.
For institutions and ministries related to traffic safety: Plan and implement education and awareness programs for various road users, drivers and pedestrians, on the importance of traffic safety practices.

## Slide 63
  Recommendations
To Nablus Municipality:
    Review the proposed solutions to reduce crashes in black spots and work to implement them.
    Follow up the maintenance and operation of the streets and intersections by the Nablus Municipality if any defect occurs.
    Make studies and possible solutions to all sections and intersections classified as black spots to reduce the likelihood of crashes.
    Maintaining the right of way and removing all violations.

## Slide 64
Thanks for all