## Slide 2
Project Name: Smart Weather Station Supporting Dual Communication (Wi-Fi + PLC)
🎓 Graduation Project 1 University: An-Najah National University Faculty: Faculty of Engineering
Department: Electrical Engineering Department
Prepared by: Ali Mohammed Ali Al-Khalili, Fathi Fadi Rashed, Kamel Shareef Kamel Quraan, and Mohammed Imad Jawad Zaid
Supervised by: Dr. Omar Al-Tamimi Academic Year: 2024 / 2025

## Slide 3
Introduction
This project aims to design and implement a smart weather station capable of accurately measuring and analyzing weather conditions in real time, with support for dual communication methods, including wireless (Wi-Fi) and power line communication (PLC).
Despite the advancements in weather systems, there is still a clear gap in areas with weak communication network infrastructure.
This gap includes:
The inability to transmit data in real time.
The lack of wireless communications in some areas.

## Slide 4
Here comes the unique solution:
Power Line Communication (PLC).
Power line data transmission technology is not common in weather stations, but it represents an innovative solution to address this gap.
This enhances its usability in various environments, whether with advanced or limited infrastructure. The station relies on a set of precise sensors to monitor variables such as temperature, humidity, atmospheric pressure, wind speed, rain, and gas sensors. A central control unit collects and analyzes this data, then transmits it to an electronic display interface that facilitates real-time monitoring of weather conditions.
This station is an effective tool that can be employed in various fields, such as smart agriculture, energy management, and environmental planning, especially in remote areas or areas where reliable climate data is difficult to access. The project has the potential to be developed to integrate with smart forecasting systems or automated environmental systems in the future

## Slide 5
Importance of the Project
Solving the Problem of Poor Infrastructure:
In many rural and remote areas, there is no robust wireless infrastructure or fixed internet networks, which hinders real-time data collection and analysis. This project provides a practical and effective alternative by using existing power lines for data exchange (PLC), eliminating the need to build new, costly communications networks.
Repurposing Electrical Grids:
The project demonstrates how traditional electrical grids, already in place in most places, can be used as a reliable means of transmitting digital data, without the need for radical changes to these networks or massive infrastructure development investments.

## Slide 6
Importance of the Project
Serving Strategic Sectors:
The project directly contributes to improving the efficiency of smart agriculture by providing accurate and real-time climate data, helping farmers make better decisions related to irrigation, fertilization, and harvesting. It also helps the energy sector improve resource management and load control based on climatic conditions, and supports environmental protection efforts through continuous monitoring of weather conditions.
Opening future horizons for PLC technologies:
The project promotes the use of PLC technology in many future applications, such as smart irrigation systems that rely on monitoring soil and weather conditions, or industrial control systems that require reliable data transmission in environments that may be technically complex for wireless data transmission.

## Slide 7
Importance of the Project
Enhancing security and efficiency:
The project reduces the systems' reliance on wireless networks, which may be vulnerable to interference or hacking, enhancing data security and improving system efficiency in various environments.

## Slide 8
Project Objectives
First: Technical Objectives
1. Design an intelligent, automated system:
Collect real-time weather data (temperature, humidity, pressure, wind, etc.).
Analyze this data and transmit it to a display interface.
2. Use dual-communication technology (Wi-Fi + PLC):
Wi-Fi: In areas with wireless coverage.
PLC: In areas lacking communications infrastructure, where the power line is used as a means of transmitting data.
3. Reduce costs and increase efficiency:
Rely on existing electrical infrastructure without the need to dig or extend new communication cables.
Possibility of using solar energy to power the system in remote areas.

## Slide 9
Project Objectives
4. Scalability and integration:
Possibility of connecting the station to smart systems such as automatic irrigation or weather forecasting systems in the future.
5. Create a visual user interface:
A dashboard to display real-time data to users (via a website or mobile app).

## Slide 10
Second: Community Objectives
1. Supporting Environmental Sustainability:
Reducing water consumption through weather forecasting and linking data to smart irrigation systems.
Monitoring air quality and solar radiation, which enhances local environmental awareness.
2. Increasing community preparedness for natural disasters:
Early warnings in the event of heavy rain or wind.
Supporting civil defense efforts in emergency situations.

## Slide 11
Project Concept and Features (in More Detail)
• Adopting Wi-Fi and PLC communication methods to ensure greater reliability:
The project combines wireless (Wi-Fi) communication with power line data transmission (PLC) technology. This feature ensures continuous data transmission even in environments with weak or interrupted wireless network coverage, making the system more stable and reliable in the long term. • Self-powered solar operation with an alternative electrical source:
The system is equipped with two power options: a conventional electrical source (220V) and a solar power system that can be used when the main electrical source is unavailable. It is also an integrated solar power system with batteries for energy storage and operation during power outages. This flexibility ensures the station's continuous operation under various conditions.

## Slide 12
• Flexible installation and expansion:
The system's design allows for easy installation in various locations, whether rural or urban, without the need for complex equipment. The system's open architecture also allows for the addition of additional sensors in the future to read new data (such as air quality, solar radiation, soil moisture, etc.), or to integrate the system with other smart systems such as irrigation systems or smart city networks.
• Diverse data readability:
The system is capable of collecting diverse climate data such as temperature, humidity, atmospheric pressure, light intensity, wind speed and direction, rainfall amount, and the presence of harmful gases, etc., making it an integrated platform for accurate and comprehensive weather monitoring.
Project Concept and Features (in More Detail)

## Slide 13
(Main power source 220V, Adapter SMPS )
Types of Power Supply Units Used
Power Source Used in the Project
Component | Function
Main Power Supply 220V | An electrical power source used as the primary energy supply, typically connected through a transformer to a voltage regulator.
Adapter SMPS | An electrical adapter that converts voltage from 220V to or 3.3V or 12V or 5V or

## Slide 14
Complete System Diagram
Complete Wiring Diagram
• A wiring diagram showing how to connect:
All sensors and modules to the Arduino Mega
Communication line to the Raspberry Pi

## Slide 15
Line 1: From the main power supply

## Slide 17
Ingredients Used
Hardware Components
Components used in the Smart Weather Station project
Type | Component Used
Controller Unit | Arduino Mega 2560 – Responsible for reading sensors, processing, and sending to communication units.
Input Units | Sensor set includes: " Temperature Sensor Pressure Sensor Humidity Sensor (BME280) Rain Sensor (MH-RD) Gas Sensor (MQ-9) Wind and Direction Sensor Light Meter Sensor
Display Interface | LCD Screen (1280×400) to display data + Raspberry Pi Zero W for a local graphical interface.
Communication Units | • Wi-Fi Module (e.g., NRF24L01) • PLC Module for data transmission over power lines.
Power Supply | • An electrical adapter that converts voltage from 220V to or 3.3V or 12V or 5V
Voltage Regulator | • LM2596-5V Voltage Regulator XL4016DC –DC Buck converter
Voltag"4-20mA to e Converter Module XY-ITOV | CConverting the 4–20mA current signal coming out of the wind speed sensor into a voltage signal (e.g., 0–5V) that can be easily read by an Arduino or any other microcontroller.onverting the 4–20mA current signal coming out of the wind speed sensor into a voltage signal (0–5V) that can be ea sily read

## Slide 18
1.Arduino Mega 2560
• Function: Main control unit for sensors.
• Features: Large number of I/O pins and more memory than the Arduino Uno.
• Programming: Arduino IDE (C++) to collect data from sensors and transmit it wirelessly or over power lines.
• Operating voltage:
VIN input = 7–12V
Powered by a voltage regulator or 9V/12V source
First: A detailed explanation of the hardware components used.

## Slide 19
Key Features:
• Microcontroller: ATmega328P
• Operating Voltage: 5V
• Input Voltage (recommended): 7–12V
• Digital I/O Pins: 14 (6 PWM-capable)
•Analog Input Pins: 6 (A0–A5)
• Flash Memory: 32 KB
• SRAM: 2 KB
•Clock Speed: 16 MHz
• Communication: USB, UART (Serial), I2C, SPI
•Programming: via Arduino IDE through USB cable
________________________________________
Uses: • Transmitting wireless data nRF24L01 module
•Reading sensors
•Serial communication with other boards (like Mega, Raspberry Pi, or PLC)
•Displaying data on LCDs
)
Arduino Uno

## Slide 20
• Function: Central processing unit, used to display and analyze data on a graphical interface.
• Features: Wi-Fi support, small size, and Linux operating system.
• Programming: Python – used to display data on a website or graphical dashboard.
• Typical operating voltage: 5V via Micro-USB port
2.Raspberry Pi Zero W:

## Slide 21
Function:
• Measures atmospheric pressure and altitude.
• Measures temperature and humidity.
• Accuracy: More accurate than the DHT11.
• Programming: DHT library for Arduino.
• Operating voltage: 5V.
• Communication: I2C or SPI.
3.BMP280 Sensor (Pressure & Altitude)

## Slide 22
• Function: Rain sensor.
• Programming: Reading the analog value and converting it to a rain/no rain state.
• Operating voltage: 5V
4. MH-RD Rain drop Sensor Module

## Slide 23
• Function: Measuring wind speed and direction.
• Type: Typically analog or digital sensors based on magnetic pulses.
• Programming: Calculating the time between pulses or reading the voltage.
• Operating voltage: 24V
Wind Speed and Direction Sensors\ Anemometer and WindVane.5

## Slide 24
Voltage Converter XY-ITOV-4 "
Converting the 4–20mA current signal coming out of the wind speed sensor into a voltage signal (e.g., 0–5V) that can be easily read by an Arduino or any other microcontroller.
Purpose of Using the XY-ITOV Module
Main Function:
"To convert a 4–20mA current signal (from a wind speed sensor) into a "voltage signal (0–5V or 0–3.3V) that can be read by an analog input on a "microcontroller like Arduino, Raspberry Pi, ESP32

## Slide 25
• Function: Send data over long distances using low-power radio waves.
• Communication: SPI.
• Programming: Using the LoRa library in Arduino.
• Operating voltage: 3.3V
6.WIRELESS COMMUNICATION MODULE - 2.4GHz NRF24L01+PA+LNA SMA Wireless Transceiver Antenna

## Slide 26
• Function: Transfers data over power lines.
• Connectivity: Integrates with Arduino or Raspberry Pi and uses protocols such as HomePlug or X10.
• Programming: Depends on the type of PLC used, and data is often exchanged via UART or SPI.
• Operating voltage: 10V, To ensure safe and stable power delivery to the PLC Power Line "Communication module, a DC-DC Buck Converter (XL4016) is used in " the system. This module steps down the input voltage from 12V DC (from the main power source) to a regulated 10V DC, which matches the " "operating requirements of the PLC communication circuit.
7.Power Line Communication (PLC) Module

## Slide 27
Power Regulation Module Description "
To ensure safe and stable power delivery to the PLC Power Line "Communication module, a DC-DC Buck Converter (XL4016) is used in " the system. This module steps down the input voltage from 12V DC (from the main power source) to a regulated 10V DC, which matches the " "operating requirements of the PLC communication circuit.

## Slide 28
• Function: Displays data directly to the user.
• Programming: Using the Adafruit or LiquidCrystal libraries
• Operating voltage: 5V
.8 LCD screen

## Slide 29
Its primary function:
Detecting flammable and toxic gases, especially:
• Carbon monoxide (CO)
• Methane (CH₄)
• Butane and other flammable gases
9.MQ-9 – Gas Sensor Module

## Slide 30
How does it work?
The sensor contains an internal heating element and chemicals that react with gases.
When gas is present, the element's resistance changes, producing a voltage difference that is sent to the Arduino.
The programming language for the MQ-9 sensor when used with Arduino is:
C++ via the Arduino IDE
The sensor is programmed using the Arduino IDE, which is based on C++.
• Operating voltage: 5V
9.MQ-9 – Gas Sensor Module

## Slide 31
Light Meter Sensor
Main Function:
• Measures luminous intensity or ambient brightness.
• Provides a digital reading expressing the amount of light reaching the sensor, which can be correlated with solar radiation levels.
• Operating Voltage: 24V
10.Light Meter Sensor

## Slide 32
Voltage Regulation Module for Solar Radiation Sensor "
To provide a stable and safe power supply to the Solar Radiation Sensor, " a LM2596 Buck Converter was used in the system. This is a reliable and widely used DC-DC step-down converter, capable of efficiently reducing "voltage from 12V to the required 10V for the sensor.
14.voltage regulator

## Slide 33
We need it to reduce the voltage from 220V to 12V. "
1.AC to DC converter (Power Adapter / SMPS)
11.Power Supply
Component | Function
AC-DC Power Supply (Electrical Current Converter) | Takes 220V AC electricity from the wall and converts it to 3.3 v or 5V DC or 12V DC.

## Slide 34
Voltage Regulator Function
• Reduces and stabilizes voltage to a safe and stable level (5V or 3.3V).
• Protects components from damage caused by voltage spikes or fluctuations.
14.voltage regulator
Types of voltage regulators in the project:
Regulator | Output Voltage | Used for
LM2596 | 5V | 5V sensors, LCD screens, Arduino Mega

## Slide 35
Estimated Cost
"Smart Weather Station Components Cost (USD) ""
(Component)" | (Quantity) " | (USD) | " (USD)
Light Meter Sensor"" | 1 | 34.79 | 34.79
Raspberry Pi Zero | 1 | 43.21 | 43.21
Wind Speed & Direction Sensor" | 1 | 18.00 | 18.00
PLC Communication Module" | 2 | 26.48 | 52.96
LCD Display 400×1280" | 1 | 40.00 | 40.00
Arduino Mega" | 1 | 40.00 | 40.00
BME680 Sensor" | 1 | 21.33 | 21.33"
Rain Drop Sensor" | 1 | 5.13 | 5.13
GAS Sensor | 1 | 6.21 | 6.21
Wireless Communication Module" | 2 | 9.45 | 18.90
XL4016 DC-DC Buck Converte" | 1 | 10.00 | 10.00
SMPS Power Supply Unit (ATX) | 1 | 6 60.00 " | 60.00
" Arduino Uno | 4 | 10.00 | 40.00
Voltage Regulator /LM2596" | 1 | 10.00 | 10 .00
wires | 20 | 10.00 | 10.00
.Voltage Converter XY-ITOV-4 | 1 | 40.00 | 40.00
(Control Cabinet) | 1 | 80.00 | 80.00
" Total price: $508.75

## Slide 36
"Sensor" | "Function"
""Atmospheric Pressure Sensor" | "Measures atmospheric pressure in hPa units"
"Temperature Sensor" | Measures air temperature"
"Humidity Sensor" | Calculates the ratio of water vapor in the air"
"Wind Speed and Direction Sensor" | Monitors wind intensity and direction"
"Light/UV Radiation Sensor | Measures the intensity of sunlight or ultraviolet"
Data Analysis and Results"AA"
"5.1 Reading and analyzing climate data: "
"The smart station in this project was developed to collect and analyze multiple "climate data in real time, with a focus on providing accurate data to support ""the following areas: "
• Smart agriculture""
• Solar energy management""
• Weather forecasting"
• Environment and local climate""
• Components used in measurement and analysis:

## Slide 37
"Mechanism of action: "
• The Arduino Mega module collects sensor readings in real time.
• The data is processed internally and converted into a transmittable format
• The data is sent either via:
Wi-Fi to a Raspberry Pi or a cloud server. "
Or via the PLC via electrical wiring to the processing unit, without the "need for wireless networks.
*Results based on technical analysis of the system"
"1. Accuracy of atmospheric measurements: "
"The performance of the selected sensors was analyzed based on technical "data(Datasheet), and the results were summarized that the level of accuracy "ranges as follows: "

## Slide 38
Table:
Accuracy rate of climate variables:
Variable" | Accuracy Rate"
Temperature" | "±0.5 °C"
"Relative Humidity" | "±3% RH"
"Atmospheric Pressure" | ±1 hPa
"Wind Speed" | "±0.5 m/s
MQ-9 Gas Sensor Accuracy:
Detected Gas" | Typical Detection Range (ppm) " | "Approximate Accuracy
"Carbon Monoxide (CO) | "10 – 1000 ppm | ±10% – ±20%"
Methane (CH₄)" | 200 – 10000 ppm" | ±10% – ±20%"

## Slide 39
Sensor Results by Season – Yearly Analysis: "
"This section presents the results obtained from the smart weather station "sensors "in Palestine over a full year, categorized by the four seasons. Key "climate data "was recorded monthly and analyzed to extract average values "per season
"Parameter" | Average / Status"
"Temperature" | ""23.2 °C""
"Relative Humidity" | "55%"
Air Pressure" | "1012 hPa"
"Wind Speed" | "2.8 m/s"
"Solar Radiation" | "Moderate"
"Rainfall" | "Light Rain"

## Slide 40
Summer (June - August):
"Parameter"" | ""Average / Status"
Temperature" | "32.7 °C"
""Relative Humidity"" | "41%"
"Air Pressure" | 1005 hPa"
Wind Speed" | 2.0 m/s"
Solar Radiation" | High"
Rainfall" | "Rare"

## Slide 41
Autumn (September - November):
"Parameter"" | "Average / Status
Temperature" | 24.1 °C"
Relative Humidity" | 58%"
Air Pressure" | 1011 hPa"
Wind Speed" | 3.1 m/s"
Solar Radiation" | Moderate"
Rainfall" | Intermittent"

## Slide 42
Winter (December - February):
"Parameter" | "Average / Status
Temperature" | "11.2 °C
Relative Humidity" | 72%
Air Pressure" | "1019 hPa
Wind Speed" | "4.2 m/s
Solar Radiation" | Low
Rainfall | ""Heavy and Regular
"These values are highly suitable for environmental and agricultural "applications, and are considered highly accurate compared to the "requirements of non-industrial use." "

## Slide 43
The Future of Smart Weather Stations
Smart weather stations have witnessed remarkable development in the last two decades thanks to their integration with Fourth Industrial Revolution technologies, and this development is expected to accelerate in the coming years.
In this chapter, we review future trends in weather monitoring technologies, the role of artificial intelligence (AI), the use of advanced sensors, and the potential for integration with smart homes and other systems.

## Slide 44
Artificial Intelligence and Weather Forecasting
a) The Shift from Monitoring to Forecasting
Modern weather stations not only collect data, but also analyze it and issue real-time forecasts based on temporal and behavioral patterns.
Using AI algorithms such as neural networks and machine learning, it has become possible to:
• Analyze pressure and temperature changes to predict rain and storms.
• Link data from multiple regions to predict air mass movement.
• Classify periods of heat or frost hazard with unprecedented accuracy.
b) Applications of AI in Weather Stations
• Early warning systems based on historical data patterns.
• Improving the accuracy of short-term weather forecasts.
• Integrating weather data with crop management systems in smart agriculture.

## Slide 45
Using Advanced Sensors and Emerging Technologies
a) Advanced Environmental Sensors
• UV Sensors: To monitor radiation levels affecting humans and crops.
• Evapotranspiration Sensors: To calculate water loss from soil and plants.
• Harmful gas sensors (such as NOx and CO2): To support environmental studies and pollution monitoring.

## Slide 46
Integration with Smart Homes and Systems
a) Integration with smart assistants (Alexa, Google Assistant)
b) Smart control of heating and cooling
c) Connecting a weather station to smart irrigation systems.
d) Interaction with smart city systems

## Slide 47
الكلمة ختامية
في ختام هذا العمل، نقف لحظة تأمل وامتنان. لقد كانت هذه التجربة أكثر من مجرد مشروع أكاديمي، بل كانت رحلة معرفية وإنسانية خضناها بشغف، واجهنا خلالها تحديات فكرية وتقنية، وسعينا بكل ما أوتينا من جهد وإرادة لتقديم عمل يليق بثقة أساتذتنا، ودعم أهلنا، وتعاون زملائنا.
لقد تعلّمنا أن الإنجاز لا يولد من الفكرة وحدها، بل من الإيمان بها، والسعي المستمر نحو تحقيقها، والقدرة على تحويل النظرية إلى واقع، والخطط إلى خطوات ملموسة.
نشكر كل من كان له أثر في هذا الطريق، ولو بكلمة تشجيع أو دعاء صادق. ونعد أن يكون هذا المشروع خطوة أولى في مسيرة علمية ومهنية نطمح أن تكون مليئة بالعطاء، والابتكار، والمسؤولية.
وإلى كل من يقرأ هذه الصفحات… آمنوا بأفكاركم، واعملوا من أجلها، فربما تكون نواة لتغييرٍ حقيقي.