## Slide 1
An-Najah National University
  Faculty of Engineering and Information Technology
Civil Engineering Department
By
Hamed Arabasi
Malak Zakarneh
Ahmad Abed
Aya Hussien
Under supervision of: Prof. Khaled Al-Sahili
Design of the First Bike Network in Nablus City
Graduation Project II
Notes: لمزيد من عروض البوربوينت الاحترافية يرجى زيارتنا و الاشتراك بقناة اليوتيوب عن طريق الرابط التالي
https://www.youtube.com/c/%D8%B9%D8%A7%D9%84%D9%85%D8%A7%D9%84%D8%A8%D8%A7%D9%88%D8%B1%D8%A8%D9%88%D9%8A%D9%86%D8%AA

## Slide 2
The limited capacity of the city's infrastructure
the rapidly increasing number of vehicles
growing number of visitors
Traffic congestion
Importance of the Project

## Slide 3
Rafedia Street
Omar Ibn Al-Khattab St.
Palestine Street
Al-Shwetreh St.
Ghernatah St.
The City Center Area
Hettin Street
Faisal Street
Specifying the Study Area
Methodology

## Slide 4: Collection of Data
Using Available Data
Potential demand studies
Data Collection by Field Work
Roads inventory study
Traffic volume studies
Methodology

## Slide 5: Design Criteria
Bike Lane Design Guidelines
the Urban Bikeway Design Guide
AASHTO

## Slide 6
Data Calculation
(Road Inventory Study)
Table 3.9: At-Fatemiah School - Dimensions Of The Street Elements
Figure 3-17: At Al-Fatemiah School Section No.3 Existing Cross Section
Omar Ibn Al-Khattab Street

## Slide 7
Traffic Volume Study
The common peak hour for all intersections:

## Slide 8
Traffic Volume Analysis
Effect of Using the Bike Network in Reducing Traffic Volume
the classification of vehicles was collected during the traffic count study, as well as the questionnaire showing the number of students wishing to use the bike network. Thereafter, the reduction rate per hour was calculated.
912 students wishing to use a bike network
The reduction rate = 5-9 % at each intersection.

## Slide 9
Table: LOS And Delay For CBD Area Intersections, Before And After Adding A Bike Network.
Effect of Using the Bike Network in Improve the LOS

## Slide 10
Design Of The Bike Network
Notes: لمزيد من عروض البوربوينت الاحترافية يرجى زيارتنا و الاشتراك بقناة اليوتيوب عن طريق الرابط التالي
https://www.youtube.com/c/%D8%B9%D8%A7%D9%84%D9%85%D8%A7%D9%84%D8%A8%D8%A7%D9%88%D8%B1%D8%A8%D9%88%D9%8A%D9%86%D8%AA

## Slide 11
The Designed bike lanes At An- Najah New Campus

## Slide 12
Bike Box
Elephant Feet
Warning Signs and pavement markings
Design at intersection
Bike Lane Color
Median Refuge
Notes: لمزيد من عروض البوربوينت الاحترافية يرجى زيارتنا و الاشتراك بقناة اليوتيوب عن طريق الرابط التالي
https://www.youtube.com/c/%D8%B9%D8%A7%D9%84%D9%85%D8%A7%D9%84%D8%A8%D8%A7%D9%88%D8%B1%D8%A8%D9%88%D9%8A%D9%86%D8%AA

## Slide 13
Bike Box
Notes: لمزيد من عروض البوربوينت الاحترافية يرجى زيارتنا و الاشتراك بقناة اليوتيوب عن طريق الرابط التالي
https://www.youtube.com/c/%D8%B9%D8%A7%D9%84%D9%85%D8%A7%D9%84%D8%A8%D8%A7%D9%88%D8%B1%D8%A8%D9%88%D9%8A%D9%86%D8%AA

## Slide 14
Median Refuge
Notes: لمزيد من عروض البوربوينت الاحترافية يرجى زيارتنا و الاشتراك بقناة اليوتيوب عن طريق الرابط التالي
https://www.youtube.com/c/%D8%B9%D8%A7%D9%84%D9%85%D8%A7%D9%84%D8%A8%D8%A7%D9%88%D8%B1%D8%A8%D9%88%D9%8A%D9%86%D8%AA

## Slide 15
Elephant Feet
Notes: لمزيد من عروض البوربوينت الاحترافية يرجى زيارتنا و الاشتراك بقناة اليوتيوب عن طريق الرابط التالي
https://www.youtube.com/c/%D8%B9%D8%A7%D9%84%D9%85%D8%A7%D9%84%D8%A8%D8%A7%D9%88%D8%B1%D8%A8%D9%88%D9%8A%D9%86%D8%AA

## Slide 16
Typical Cross Sections
Section A-A: At An- Najah New Campus
Notes: لمزيد من عروض البوربوينت الاحترافية يرجى زيارتنا و الاشتراك بقناة اليوتيوب عن طريق الرابط التالي
https://www.youtube.com/c/%D8%B9%D8%A7%D9%84%D9%85%D8%A7%D9%84%D8%A8%D8%A7%D9%88%D8%B1%D8%A8%D9%88%D9%8A%D9%86%D8%AA

## Slide 17
Typical Cross Section C-C, Rafidia Street

## Slide 18
Typical Cross Sections
SECTION D-D: At An- Najah Old Campus
Notes: لمزيد من عروض البوربوينت الاحترافية يرجى زيارتنا و الاشتراك بقناة اليوتيوب عن طريق الرابط التالي
https://www.youtube.com/c/%D8%B9%D8%A7%D9%84%D9%85%D8%A7%D9%84%D8%A8%D8%A7%D9%88%D8%B1%D8%A8%D9%88%D9%8A%D9%86%D8%AA

## Slide 19
Grade of the Street
According to AASHTO
5% Max. Grades for any distance
8.3% Max. up to 61m distance
10% Max. up to 9m distance
12.5% up to 3m distance

## Slide 21
Proposed Parking Lot, An- Najah New Campus
Bikes Parking Lots
Proposed Parking Lot, An- Najah Old Campus
Designated Bikes Parking Lot
626 Bikes

## Slide 22
Proposed Parking Lot, An- Najah Old Campus
Bikes Parking Lots
Proposed Parking Lot, City Center
Designated Bike Parking Lot 214 Bikes

## Slide 23
Proposed Parking Lot, City Center
1512 m2.
Total Area
Bikes Parking Lots
Of the project
The

## Slide 24
CONCLUSIONS AND RECOMMENDATIONS
Total cost
Of the project
The
.
Term | Description | Unit | Quantity | Unit Cost ($) | Total Cost ($)
traffic Signs | - | No. | 405 | 150 | 60,750
U-Rack | Steel Rack | No. | 733 | 129 | 94,557
Painting of Bike Lanes | includes the Cost of painting materials and Labors | m^2 | 14480 | 8 | 115,840
asphalt | include asphalt, base course, and excavation | m^2 | 2490 | 25 | 62,250
Median Refuge Island | Excavation work, silt removal, reconstruction, and labor | m^2 | 53 | 50 | 2,650
Painting of dividing lines | Labor and painting materials | m | 15973 | 1 | 15,973
Total Cost |  |  |  |  | 352,020

## Slide 25
CONCLUSIONS AND RECOMMENDATIONS
The Bicycle is considered an Active mobility mode of transportation system all over the world.
This design is very important in the sense that it can reflect the sign of keeping up with international development at the university and in the city itself.
It is recommended that Nablus Municipality adopts the concept of providing bike network for the entire city, considering the outputs of this project. This will have a positive impact on the overall traffic operating conditions in the network, in addition to the health benefits of the users and the city’s residents and visitors as a whole.

## Slide 26
Thanks for your
listening.