## Slide 1: Design and implementation of an alternative heat source for wood presses.
Omar Baara Mohamed Hamadneh
Omar Abu Mady Fahmy AbdulQader

## Slide 2
The woodwork industry in Palestine has grown rapidly in the past few years and so did the demand of energy.

## Slide 3: Wood products
Composite and MDF

## Slide 4: Thermal wood press

## Slide 5: The problem
Heating is too expensive!

## Slide 6: Alternative solutions
Wood burner

## Slide 7
Fuel burner

## Slide 8: Parts
Controlled fuel injector
Air pressure regulator

## Slide 9
Air blower
Underground fuel tank

## Slide 10
Propane gas supply
Heat exchanger

## Slide 11
3”
1/2”

## Slide 13: Methodology
Two 3” pipes are welded together using a 90 degrees steel elbow

## Slide 14
Two holes are drilled into the horizontal pipe for the fuel and gas intake.

## Slide 15
Lastly, a cylindrical heat exchanger was fitted to the vertical 3” pipe

## Slide 16: Igniting the burner
The propane gas lighter is turned on until the burner is hot enough.
The fuel is the added in controlled volumes along with air from the blower
The propane gas is then turned off.

## Slide 17
Results and analysis

## Slide 18
Pout= 3 * 220 * 90 * 0.85
= 50490 W = 50.5 KW
Therefore the new heater should be able to supply 50.5 KW

## Slide 19: Fuel heater
Waste oil specifications2:
Density: 885 Kg/m3
Viscosity: 3.49
Flash point: 57oC
Calorific Value (CV): 42500 KJ/KG
Efficiency (η): 75%

## Slide 20
50.5 kW= 42500 * * 0.75
= 1.58*10-3 kg/s
Volumetric flow rate= (1.58*10-3)/885= 1.8*10-6 m3/s = 1.8*10-3 l/s

## Slide 21
Cost analysis:
Electric heater:
1kWh= 0.5 NIS
Total cost from the electrical heater for one day=
50.5*0.5*16= 404 NIS/day
Waste oil heater:
1m3 of waste oil= 1600 NIS
Total cost from the waste oil heater for one day=
(1600)*(1.8*10-6)*3600*16= 166 NIS/day

## Slide 22
Chart: 
| Electric | Waste oil
Cost/ day | 404 | 166
Column1
Column2

## Slide 23
Chart: 
| January | February | March | April | May | June | July | August | September | October | November | December
Electrical | 10504 | 9696 | 10908 | 10504 | 10706 | 10827.2 | 10948.4 | 11069.6 | 11190.8 | 11312 | 11433.2 | 11554.4
Waste oil | 4316 | 3984 | 4482 | 4316 | 4399 | 4448.8 | 4498.6 | 4548.4 | 4598.2 | 4648 | 4697.8 | 4747.6

## Slide 24: Controlling the heat
One of the main problems of such system is over heating.
It is not possible to repeatedly turn the burner on and off to control the temperature

## Slide 25
Using the results from the previous calculations, we find

## Slide 26: Safety and limitations

## Slide 27
Waste oil is hard to ignite
Harmful emissions

## Slide 28
Heat losses in the pipes
Fuel backflow into the tank

## Slide 29
Overheating and boiling of thermal oil.

## Slide 30: Why oil burners?

## Slide 31: Wood burners
Very big !
Fire hazard
Consumes storage space
Harmful emissions

## Slide 32: Oil burners
Relatively small
Easy to contain incase of a fire
No storage space required.
Very minimal

## Slide 33: Future business plans

## Slide 34
Thank you!