## Slide 1: Directorate Education Building Project
An- Najah National university
Faculty of Engineering
Building Engineering Department
Supervisor :
Luay Dweikat
Prepared by :
Majd Dweikat
Mahmoud Dweikat
Ameer Dweikat
Omar Abo Hadba

## Slide 2: OUTLINES
Introduction
Site description
Architectural design
Environmental design
Structural design
mechanical design
Electrical design
Quantity surveying

## Slide 3: Introduction

## Slide 4: Site description
Location : Nablus – Howara Town - (32.11" N , 35.27" E )
Area:
Total area 1570 m2
Surrounding
2 streets ( 8 m)
Residential building from south
height is (7 m )
Residential building
from west height is (11 m)

## Slide 5: Site Accessibility
Site Plan

## Slide 6: Architectural Design

## Slide 7: Project Description
5 floors, in addition to two basement as a parking .
Total area of the building equals to 5278 m2
Contains approximately 130 employee .
Second basement
First basement
Ground floor
First floor
Second floor
Third floor
Fourth floor
Stair Case
Total area
1148
591
1148
591
591
591
27
5278
m2
m2
m2
m2
m2
m2
m2
m
m2
m2
591
m2

## Slide 8: Bubble diagram

## Slide 9: Architectural Design
The Design for First Basement floor
The Design for Second Basement Floor

## Slide 10: Architectural Design
The Design for Ground floor

## Slide 11: Architectural Design
The Design for First Floor

## Slide 12: Architectural Design
The Old Design for Ground Floor
The New Design for Ground floor

## Slide 13: Architectural Design
The Old Design for First Floor
The New Design for First Floor

## Slide 14: Architectural Design
The New Design for Second Floor
The Old Design for Second Floor

## Slide 15: Architectural Design
The New Design for Third Floor
The Old Design for Third Floor

## Slide 16: Architectural Design
The New Design for Fourth Floor
The Old Design for Fourth Floor

## Slide 17: Elevations
East Elevation
West Elevation

## Slide 18: Elevations
South Elevation
North Elevation

## Slide 19: SECTIONS
SECTION 1-1
SECTION 2-2

## Slide 20: Environmental design
Energy Simulation and Thermal Comfort
Acoustical design
Daylighting
Environmental Adjustments
PV Design

## Slide 21: Environmental Adjustments
East Elevation
South Elevation

## Slide 22: Daylighting
Ground Floor Before
Ground Floor After

## Slide 23: Daylighting
First Floor Before
First Floor After

## Slide 24: Daylighting
Second Floor Before
Second Floor After

## Slide 25: Daylighting
Third Floor Before
Third Floor After

## Slide 26: Daylighting
Fourth Floor Before
Fourth Floor After

## Slide 27: Energy Simulation and thermal comfort
External Wall Without Insulation
External Wall With Insulation
Material Properties

## Slide 28: Energy Simulation and thermal comfort
Flat Roof Without Insulation
Flat Roof With Insulation
Material Properties

## Slide 29: Energy Simulation and thermal comfort
Internal Partitions
Under Ground Wall
Material Properties

## Slide 30: Energy Simulation and thermal comfort
Glazing Area
Material Properties

## Slide 31: Energy Simulation and thermal comfort
Material Properties
Section | Thickness (mm) | U-value (W/m2.K)
External Wall | 265 | 2.387
Below grade Wall | 49 | 2.701
Roof | 1250 | 0.948
Internal Partitions | 126 | 2.204
Glazing | 18 | 3.094
Section | Thickness (mm) | U-value (W/m2.K)
External Wall | 325 | 0.39
Below grade Wall | 49 | 2.701
Roof | 1330 | 0.256
Internal Partitions | 126 | 2.204
Glazing | 18 | 3.094

## Slide 32: Thermal analysis
Case | Description | Heating Load(kW) | Cooling Load(kW) | Load/Area(w/m2)
Case 1 | Without Insulation | 191.14 | 193.62 | 65.52
Case 2 | Manual Calculation | 197 |  | 66.67
Case 3 | With Insulation | 88.07 | 126.96 | 42.96
Case 4 | With Insulation and Environmental Adjustments | 88.07 | 114.34 | 38.69

## Slide 33
Heating load
Heating Load = 88.07 kW

## Slide 34
Cooling load
Cooling Load = 114.34 kW

## Slide 35
Thermal Comfort
Thermal Comfort for Building

## Slide 36
Thermal Comfort
Thermal Comfort for Ground Floor

## Slide 37
Thermal Comfort
Thermal Comfort for First Floor

## Slide 38
Thermal Comfort
Thermal Comfort for Second Floor

## Slide 39
Thermal Comfort
Thermal Comfort for Third Floor

## Slide 40
Thermal Comfort
Thermal Comfort for Fourth Floor

## Slide 41
Thermal Comfort
 | Facility [Hours]
Time Setpoint Not Met During Occupied Heating | 223.00
Time Setpoint Not Met During Occupied Cooling | 0.00
Time Not Comfortable Based on Simple ASHRAE 55-2004 | 2210.00

## Slide 42
Energy Consumption
Case | Description | Annually Energy Consumption(kWh) | Load/Area(kW/m2)
Case 1 | Without Insulation | 274605.94 | 92.93
Case 2 | Manual Calculation | 270105.22 | 91.41
Case 3 | With Insulation | 189144.96 | 64.01
Case 4 | With Insulation and Environmental Adjustments | 155236.73 | 52.53

## Slide 43
Energy Consumption

## Slide 44
PV-System

## Slide 45
PV-System
E | 181846.04 | kWh/Day
G | 5.50 | hr./Day
Efficiency | 0.5 | -
System Size | 82.657 | kWp
Wpv | 440 | Wp
No. of Module | 183.68 | Module
E | 181846.04 | kWh/Year
Yearly Total | 1750 | kWh/kWp
System Size | 103.91 | kWp
Wpv | 440 | Wp
No. of Module | 236.16 | Module
No. of Module = (184+237) / 2 = 211 Module.

## Slide 46
PV-System

## Slide 47
PV-System

## Slide 48
PV-System

## Slide 49: Acoustical analysis
Material:
Component | Finish Layer | Absorption Coefficient (α) |  |  |  |  | 
 |  | 63 Hz | 125 Hz | 250 Hz | 500 Hz | 1000 Hz | 4000 Hz
Ceiling | Acoustic Tile Suspended | 0.06 | 0.06 | 0.13 | 0.47 | 0.91 | 0.78
Wall | Plaster | 0.12 | 0.09 | 0.07 | 0.01 | 0.01 | 0.02
Floor | Tiles | 0.01 | 0.01 | 0.01 | 0.01 | 0.02 | 0.07
Window | Double Glass | 0.12 | 0.10 | 0.06 | 0.04 | 0.03 | 0.03
Door | Hollow Core Plywood | 0.44 | 0.41 | 0.35 | 0.25 | 0.2 | 0.14

## Slide 50: Acoustical analysis
Office Room

## Slide 51: Acoustical analysis
Reverberation Time

## Slide 52: Acoustical analysis
Reverberation Time
 | TOTAL | EMPTY | 50% | FULL
FREQ. | ABSPT. | RT (60) (sec) | RT (60) (sec) | RT (60) (sec)
63 Hz | 11.048 | 1.31 | 1.28 | 1.25
125 Hz | 8.920 | 1.46 | 1.43 | 1.40
250 Hz | 9.674 | 1.25 | 1.17 | 1.10
500 Hz | 17.468 | 0.78 | 0.75 | 0.72
1 kHz | 32.744 | 0.44 | 0.43 | 0.42
2 kHz | 34.040 | 0.40 | 0.39 | 0.39
4 kHz | 30.528 | 0.39 | 0.38 | 0.38
8 kHz | 28.685 | 0.31 | 0.31 | 0.31
16 kHz | 28.578 | 0.30 | 0.30 | 0.30

## Slide 53: Acoustical analysis
STC Calculations
STC for office room adjacent to office room and corridor

## Slide 54: Acoustical analysis
STC Calculations
STC for office room adjacent to outside

## Slide 55: Acoustical analysis
IIC Calculations

## Slide 56: Structural analysis
Codes
- ACI 318-14
- ACI 350 -97
- ASCE
UBC -97
Material
- Compressive strength for slab and beams ( fʹc ) = 24MPa
Compressive strength for columns, shear wall and footing
( fʹc ) = 28MPa
- Yielding strength of steel (fy) = 420 Mpa.
Bearing capacity =330 kN /m2

## Slide 57: Structural analysis
Designed load
SID for roof = 4.5 KN/m2
SID for slab = 4 KN/m2
Live load for slab = 3 KN/m2
Live load for parking = 5 KN/m2
EQ Loads (UBC97):
I= 1 Cv=0.32
R= 5.5 Ca=0.24
Z= 0.2 Ct= 0.0731

## Slide 58: Structural analysis
Checks
Compatibility check
All members moving together so
the check is OK.
ok

## Slide 59: Structural analysis
Checks
Equilibrium check .
All %errors less than %5 it’s ok.
ok

## Slide 60: Structural analysis
Checks
Stress σ & Strain ɛ check.
All %errors less than %10 it’s ok.
ok

## Slide 61: Structural analysis
Checks
Period check.
If TB ≤ 1.4 TA check is ok.
TB = 0.873 sec.
1.4 TA = 0.928 sec.
ok

## Slide 62: Structural analysis
Checks
Modal mass participation
ratio check.
sum UX= 0.906
sum UY= 0.907
If sum of UX and UY ≥ 0.9 check is ok.
ok

## Slide 63: Structural analysis
Checks
Base shear check.
ok
Manual calculation |  |  |  |  |  |  | 
weight of building (KN) | Ca | Cv | I | R | TB (sec) | V main (KN) | V secondary (KN)
70307.83 | 0.24 | 0.32 | 1 | 5.5 | 0.875 | 4675 | 1558.3
EQ ≥ V its ok.
EQX main = 4687.1 KN
EQY main = 4931.1 KN

## Slide 64: Structural analysis
Checks
Drift check.
ok
Story | R | H Floor (mm) | T Building (sec) | δx elastic (mm) | δx inelastic (mm) | max δx inelastic (mm) | Result
roof | 5.5 | 2900 | 0.873 | 47.708 | 33.5643 | 58 | Safe
FOF | 5.5 | 4100 | 0.873 | 38.99 | 31.339 | 82 | Safe
TF | 5.5 | 4100 | 0.873 | 30.85 | 35.28525 | 82 | Safe
SF | 5.5 | 4100 | 0.873 | 21.685 | 33.05225 | 82 | Safe
FF | 5.5 | 4100 | 0.873 | 13.1 | 27.99335 | 82 | Safe
GF | 5.5 | 4100 | 0.873 | 5.829 | 18.4723 | 82 | Safe
B1 | 5.5 | 2900 | 0.873 | 1.031 | 3.7807 | 58 | Safe
B2 | 5.5 | 2900 | 0.873 | 0.049 | 0.18865 | 58 | Safe
max δx inelastic ≥ δx inelastic

## Slide 65: Structural analysis
Checks
P−∆ Effects check.
ok
Story | R | H Floor (mm) | P Gravity load combination(Kn) | Ex (Kn) | Ux (mm) | ∆X (mm) | ƟX | Result
roof | 5.5 | 2900 | 319.6235 | 66.9414 | 37.772 | 7.678 | 0.06219 | No P_ Delta
FOF | 5.5 | 4100 | 10728.2019 | 1600.828 | 30.094 | 5.856 | 0.04919 | No P_ Delta
TF | 5.5 | 4100 | 20678.1807 | 2540.824 | 24.238 | 7.057 | 0.04811 | No P_ Delta
SF | 5.5 | 4100 | 30628.1596 | 3185.518 | 17.181 | 6.693 | 0.04029 | No P_ Delta
FF | 5.5 | 4100 | 40578.1448 | 3719.007 | 10.488 | 5.72 | 0.02791 | No P_ Delta
GF | 5.5 | 4100 | 52085.3153 | 4144.964 | 4.768 | 3.89 | 0.01461 | No P_ Delta
B1 | 5.5 | 2900 | 69888.1735 | 4445.14 | 0.878 | 0.687 | 0.00476 | No P_ Delta
B2 | 5.5 | 2900 | 84124.6089 | 4596.275 | 0.191 | 0.191 | 0.00121 | No P_ Delta
B3 | 5.5 | 3400 | 13054.6916 | 1286.024 | 0 | 0 | 0 | No P_ Delta
≥ 0.1

## Slide 66: Structural analysis
Detailing
Slab details.

## Slide 67: Structural analysis
Detailing
Beam details.

## Slide 68: Structural analysis
Detailing
Columns details.

## Slide 69: Structural analysis
Detailing
Columns details.

## Slide 70: Structural analysis
Detailing
Shear wall details.

## Slide 71: Structural analysis
Detailing
Single Footing details.

## Slide 72: Structural analysis
Detailing
Single Footing details.

## Slide 73: Structural analysis
Detailing
Wall Footing details.

## Slide 74: Structural analysis
Detailing
Matt Footing details.

## Slide 75: Structural analysis
Detailing
Septic Tank details.

## Slide 76: Water Tank details

## Slide 77: Water Tank details

## Slide 78: Basement wall details

## Slide 79: STAIRS details

## Slide 80: Sheet pile details

## Slide 81: Electrical design
Socket distribution
Artificial lighting
board distribution and low voltage

## Slide 82: Electrical design
Sockets design

## Slide 83: Electrical design
Sockets design

## Slide 84: Electrical design Lighting
Required Illuminance
Space | E (LUX)
Offices | 500
Corridors | 200-300
Kitchen | 200
WC | 150-300
Library | 500
Halls | 300-500
Electrical Room | 200-500
Parking | 150-300
type | Lm | efficacy(lm/w) | power(w)
luminaire 1 | 4900 | 143 | 29.5
luminaire 2 | 849 | 65 | 13
Luminaires

## Slide 85: Lighting and switches distribution

## Slide 86: Lighting and switches distribution

## Slide 87: Lighting and switches distribution

## Slide 88: Electrical design Artificial lighting
multipurpose hall

## Slide 89: low voltage

## Slide 90: Current Calculation
Floor | Socket Power (W) | Lighting Power (W) | Total
B2 | 20000 | 2015 | 22015
B1 | 20000 | 2108 | 22108
Ground | 29500 | 2197 | 31697
First | 31000 | 2140 | 33140
Second | 31250 | 2171 | 33421
Third | 30250 | 2202 | 32452
Fourth | 27000 | 2202 | 29202
Total | 189000 | 15035 | 204035
Socket and Lighting Power Calculations
Demand Factor for Socket = 0.65.
Demand Factor for Lighting = 0.80.
Floor | Load Current (A) | C.B Current (A) | Cable Current (A)
B2 | 31.69 | 39.62 | 49.52
B1 | 31.86 | 39.82 | 49.78
Ground | 37.60 | 47.00 | 58.75
First | 39.21 | 49.02 | 61.27
Second | 39.55 | 49.44 | 61.80
Third | 38.46 | 48.08 | 60.10
Fourth | 34.75 | 43.44 | 54.29
Current Calculations for Socket and Lighting
Equipment | Power (W) | Load Current (A) | C.B Current (A) | Cable Current (A)
Lifts | 32000 | 51.18 | 63.97 | 79.97
Pumps | 26851 | 42.94 | 53.68 | 67.10
AC System | 49000 | 78.37 | 97.96 | 122.45
Current Calculation for Other Electrical Equipment’s
Summary
Total Load Current Needed for Building = 312.54 A.
Circuit Breaker Current = 390.68 A.
Cable Current = 488.35 A.

## Slide 91: board distribution
Main Distribution Board for ground floor

## Slide 92: Risers Distribution

## Slide 93: Camera Riser

## Slide 94: Mechanical design

## Slide 95: Water System
Vertical | Horizontal | Branch
2 '' | 1.25'' | 0.75''
Diameter Of Pipes

## Slide 96: Water System
distribution fixture units for Ground Floor

## Slide 97: Drainage system
Pipe Diameter
Type | Diameter
WC | 4 inches.
Lavatory | 2 inches.
Kitchen Sink | 2 inches.
Vents | 2 inches.
Main Stack | 4 inches.
Between Manholes | 6 inches.

## Slide 98: Drainage system

## Slide 99: Drainage system

## Slide 100: Drainage system

## Slide 101: Drainage system
Storm water

## Slide 102: HVAC System
From the Design Builder program.
Total Heating Load = 110.16 kW.
Total Cooling Load = 131.49 kW.
Total Flowrate = 8000 L/s.

## Slide 103: HVAC System
Distribution of Indoor Unit and drainage for split

## Slide 104: HVAC System
Distribution of Indoor Unit and drainage for split

## Slide 105: HVAC System
Outdoor Unit on Roof

## Slide 106: Fire Fighting System

## Slide 107: Fire Fighting System

## Slide 108: Fire Fighting System

## Slide 109: Emergency Exit

## Slide 110: Elevators

## Slide 111: Project cost
The total cost of the project is 7019102 ₪ , And the unit cost is 1329.88 ₪/m2
111
Work | Budget Cost (₪) | Unit Cost (₪/m2) | Percentage %
Temporary Shoring | 438103 | 83.01 | 6.24%
Earth Work | 279375 | 52.93 | 3.98%
Sub-Structure | 296002 | 56.08 | 4.22%
Super Structure | 1690161 | 320.23 | 24.08%
Finishing | 2601325 | 492.86 | 37.06%
Mechanical Work | 351052 | 66.51 | 5.00%
Electrical Work | 1363084 | 258.26 | 19.42%
Total Budget Cost | 7019102 | 1329.88 | 100%

## Slide 112
Thank you for listening