## Slide 1
Nablus Municipality new building
An-Najah National University
Faculty of Engineering & Information Technology
Department of Building Engineering
Graduation Project (2)
Supervisor :Dr. Mutasim Babaa
June - 2021
Students:
Anas Melhim
Nedal Hantoli
Asim Hantoli

## Slide 2
Outline :
Introduction
Site analysis
Architectural Analysis and Environmental
Structural Analysis
Electro-Mechanical Design
Cost Estimation

## Slide 3
Through this project we redesigned the new building of Nablus Municipality, where redesign process included Architectural, structural, and environmental aspects.
The main objectives of this project were :
To comply with national and international codes and standards
To make this building energy efficient, comfortable and environmental friendly.
Introduction:

## Slide 4
Area and number of stories of building
The total area of the proposed municipality building is 3444 m ²
Distributed over 5 floors
Two car parks with an area of 2130 m²

## Slide 5
Site analysis
Location :
The project is located in Nablus - on Tulkarm Street – opposite to the Tamimi fuel station

## Slide 6
Site analysis
Wind direction
The winds in Palestine are west and southwesterly in the winter and westerly and northwesterly in the summer
summer
winter

## Slide 7
Site analysis
Noise
The building is affected by the disturbance from the surrounding streets on three sides, the noise level estimated to be equal 60-65 dB

## Slide 8
3D view

## Slide 9
3D view

## Slide 10
Architectural Analysis and Environmental

## Slide 11
Ground floor plan after redesign
Design modifications

## Slide 12
First floor plan after redesign
Design modifications

## Slide 13
Second floor plan after redesign
Design modifications

## Slide 14
Third floor plan after redesign
Design modifications
After

## Slide 15
Forth floor plan after redesign
Design modifications

## Slide 16
Design modifications
Parking

## Slide 17
Site plan
Design modifications

## Slide 18
Elevation after redesign
NW
SE

## Slide 19
NE
SW
Elevation after redesign

## Slide 20: Overshadowing :
In winter :
At 9:00 A.M.
In summer:
At 9:00 A.M.
Overshadowing :
In winter :
At 2:00 P.M.
In summer:
At 2:00 P.M.
In winter :
At 12:00 P.M.
In summer:
At 12:00 P.M.

## Slide 21
Environmental analysis and evaluated
Shading system
In general, in the eastern and western facades, the Louvre is used vertically, while in the south facade, the horizontal cantilever is used above the windows.

## Slide 22
we want to take advantages of daylight which come from glazing areas to the building.
and we used Revit software to estimate the daylight factor in all floors of the building before and after modification.
the acceptable levels prefer to be within 2-6% range.
The daylight factor
Environmental analysis and evaluated

## Slide 23
The daylight factor for stories
Environmental analysis and evaluated
For ground floor

## Slide 24
The daylight factor for stories
Environmental analysis and evaluated
For first floor

## Slide 25
The daylight factor for stories
Environmental analysis and evaluated
For second floor

## Slide 26
The daylight factor for stories
Environmental analysis and evaluated
For third floor

## Slide 27
The daylight factor for stories
Environmental analysis and evaluated
For fourth floor

## Slide 28
Environmental analysis and evaluated
Solar radiation on the elevation
Table the solar readings in the summer and winter seasons
Winter (wh/m²) | Summer (wh/m²) | Facade
177 | 380 | Roof
52 | 170 | NE
61 | 183 | NW
208 | 300 | SE
207 | 490 | SW
The average of the daylight factor for all floor in the building were within range 2-5 %

## Slide 29
Environmental analysis and evaluated
Energy consumption and baseline
We get the annual energy consumption rate of the building by using Design builder software and it was about 70 KWh/m2.
While, the baseline of the office building is 207KWh/m2.
Then we get that the annual saving of energy = 66 %

## Slide 30
Environmental analysis and evaluated
PMV of the building by using design builder software :

## Slide 31
Structural analysis

## Slide 32
General information
Structural analysis
Design code :
American Concrete Institute ACI 2014
American Society of Civil Engineers (ASCE) 7-98.
UBC-97
Materials :
Concrete.
f´c = 28 Mpa for shear walls, columns, beams, and slabs .
specific weight of Reinforced concrete (Ɣ) = 25 KN/m³
Yielding strength of steel (Fy = 420 Mpa)

## Slide 33
Loads
Live Load= 5 KN/m²
Superimposed dead load =4.5 KN/m² (assumed)
Weight of Masonry wall = 21 KN/m (assumed)
Weight of glass wall = 2.5 KN/m (assumed)
General information
General information
Structural analysis

## Slide 34
Structural element used
Structural analysis
- Slab:
Solid slab with 30 cm thickness
Two way ripped slab with 35 cm thickness
- Columns:
The columns C1 are dimensional (0.70* 0.50) m.
The columns C2 are dimensional (0.80* 0.50) m.
The columns C3 radius is (0.4) m.

## Slide 35
Structural element used
Structural analysis
Shear walls:
Thickness 30 cm for walls.
- Beams:
The drop beams dimensions are assumed to be
0.6m depth and 0.4m width .
The hidden beams dimensions are assumed to be
0.6m depth and 0.3m width .

## Slide 36
The building is one block
The structural layout of the building
Structural layout
Structural analysis

## Slide 37
Figure :3D model for the first part
Structural ETABS model
Structural analysis

## Slide 38
compatibility check
Equilibrium check
Deflection Check
All checks will be done to make sure that the work was done properly according to ACI
which is compatibility, equilibrium and Deflection Check
ETABS checks
Structural analysis

## Slide 39
compatibility check
Equilibrium check
Deflection Check
Compatibility check for the first part

## Slide 40
Table :Equilibrium check for the first part
Load | Etas(KN) | Parts | Manual(KN) | %Error
Live | 28099 | Slabs | 27875 | 0.79%
SID | 34208.6 | Slabs | 25087.5 | 2%
 |  | Walls | 9827 | 
 |  | Total (KN) | 34914.93 | 
Dead | 69099.3 | Slabs | 42451 | 2.3%
 |  | Columns | 166 | 
 |  | Walls | 12322.5 | 
 |  | Beams | 11195.15 | 
 |  | Total (KN) | 68934 | 
compatibility check
Equilibrium check
Deflection Check

## Slide 41
compatibility check
Equilibrium check
Deflection Check
Max deflection = 23 mm
23 – () = 14 mm
Critical span length =8.3 m
Deflection limit for slab (Δ) = = 34.5 mm

## Slide 42
The parameters seismic analysis :
Seismic zone : The Municipality is located in Nablus city therefore the seismic zone is (2B) and the Z value is 0.20 .
Soil profile : type of soil profile is SC .
Force Reduction Factor R = 5.5 (Building Frame System is used) (shear wall) .
Importance factor I = 1.
Acceleration-Dependent Seismic Coefficient Ca = 0.24
Velocity-Dependent Seismic Coefficient Cv = 0.32
Seismic Analysis

## Slide 43
Seismic checks
Drift check :
All drifts results shows in the
table for each floors is less
than limit .
Base shear check :
Ratio-x = manual value ETABS
value = 9088/2810.9 = 3.23.
New values of shear Old values of shear

## Slide 44
Structural elements design
Column design

## Slide 45
Structural elements design
Beams design

## Slide 46
Structural elements design
footing design

## Slide 47
Structural elements design
Retaining wall design

## Slide 48
Structural elements design
stair design

## Slide 49
Electro-Mechanical Design

## Slide 50
HVAC System : We selected VRF system for this building.
Block | Zone | Design Capacity (kW) | Floor Area (m2) | Volume (m3) | Flow/Floor Area (l/s-m2) | Design Cooling Load Per Floor Area(W/m2) | Air flow (L/s) | Flow rate of diffuser | # of diffuser
G.F | Zone1 | 4.37 | 114.9 | 448.3 | 2.66 | 38 | 305.634 | 75 | 4
G.F | Reception | 8.78 | 297.9 | 1114.8 | 2.22 | 29.5 | 661.338 | 125 | 6
G.F | Department Of Electricity | 0.64 | 17 | 66.2 | 2.6 | 37.5 | 44.2 | 50 | 1
G.F | Office | 0.64 | 18.4 | 71.7 | 2.37 | 34.7 | 43.608 | 50 | 1
G.F | Bathroom1 | 0.07 | 4.6 | 17.9 | 1.09 | 16.1 | 5.014 | 25 | 1
G.F | WC1 | 0.11 | 3.2 | 12.6 | 1.9 | 33.6 | 6.08 | 25 | 1
G.F | Bathroom | 0.13 | 6.5 | 25.2 | 1.33 | 19.6 | 8.645 | 25 | 1
G.F | WC2 | 0.19 | 4.8 | 18.7 | 2.24 | 38.9 | 10.752 | 25 | 1
G.F | WC | 0.18 | 8.2 | 32.1 | 1.44 | 22.5 | 11.808 | 25 | 1
G.F | Head Of The Tax Office | 0.73 | 22.3 | 86.9 | 2.35 | 32.7 | 52.405 | 75 | 1
G.F | Tax Office | 1.01 | 27.8 | 108.3 | 2.66 | 36.4 | 73.948 | 75 | 1
G.F | Secretary | 0.47 | 12.1 | 47.3 | 2.87 | 39.1 | 34.727 | 50 | 1
G.F | Security | 0.53 | 11 | 42.9 | 3.66 | 48.1 | 40.26 | 50 | 1
G.F | Head Of Water | 1.13 | 29.2 | 97.3 | 2.74 | 38.7 | 80.008 | 50 | 2
G.F | Department Of Water Office | 0.87 | 23.4 | 91.1 | 2.6 | 37.4 | 60.84 | 75 | 1
G.F | Head Of Electricity Department | 0.93 | 21.7 | 84.6 | 3.05 | 42.8 | 66.185 | 75 | 1
1ST Floor | WC1 | 0.21 | 4.7 | 16.5 | 2.61 | 44.5 | 12.267 | 25 | 1
1ST Floor | WC2 | 0.12 | 3.1 | 10.7 | 2.26 | 39.4 | 7.006 | 25 | 1
1ST Floor | Zone8 | 0.7 | 18.4 | 64 | 2.68 | 38.3 | 49.312 | 50 | 1
1ST Floor | Circulation | 2.79 | 108.6 | 433.8 | 2.05 | 25.7 | 222.63 | 75 | 3
1ST Floor | Reception | 6.22 | 175.6 | 610.9 | 2.74 | 35.4 | 481.144 | 100 | 5

## Slide 51
HVAC System
The picture shows the distribution of HVAC units on the first floor of the building

## Slide 52
Fire fighting
We selected the sprinkler system for this office building .

## Slide 53
Lighting
The following are the types of luminaires that were used in office lighting

## Slide 54
Lighting
The figure below shows an image taken from the DIALux-evo program.

## Slide 55
Lighting
The photo shows the lighting distribution on the second floor

## Slide 56
Acoustical
Plaster is one of the basic materials in the final finishing process in the building. Below are the values of plaster absorption at different frequencies
Flooring Office floors are designed from ceramics. Below are the absorption values of some frequencies

## Slide 57
Acoustical
Door
For the doors, oak doors are used. Below are the absorption values of some frequencies
Ceiling
In the offices in the municipality building, acoustic tiles have been used for the final finishing of the ceiling. Below are the values of absorption at different frequencies

## Slide 58
Acoustical
The figure below shows the RT60 values for an office on the first floor

## Slide 59
Drainage system
The picture shows the distribution of the drainage system on the third floor

## Slide 60
Water supply
The picture shows the distribution of the water supply on the forth floor

## Slide 61
Elevator
Required number = 3
Car capacity = 1250 kg
Car speed = 2 m/s
Car passenger capacity = 13 persons

## Slide 62
Cost Estimation
Chart: cost
| structre | finishing | Mechanical | electrical
المبيعات | 6875000 | 8567000 | 532000 | 625400
Group | Total cost (NIS) | Unit cost sikal
Structure | 6875000 | 1233
Finishing | 8567000 | 1540
Mechanical | 532000 | 117
Electrical | 625400 | 140
Total | 16599400 | 3000

## Slide 63
Thanks for your kind Attention