## Slide 2
Al -Najah National University
Faculty of Engineering and Information Technology
Civil Engineering Department
“ Analysis And Redesign Of A Commercial Building”
Prepared by:
Alaa Zabadi
Donia Salahat
Supervisor:
Dr . Imad Al-Qasem

## Slide 3
Outline :-
Introduction
Preliminary Design
3D model & Checks
Columns Design
Foundations Design

## Slide 4: PLAN

## Slide 5
Introduction
This project is a Commercial building which is one of the projects that built in Ramallah city.
Figure: Areas, height, and use of each floor in the project
Use of floor | Height (m) | Area (m2) | Floor
Garage | 2.60 | 690.95 | Basement 3
Garage | 3.30 | 690.57 | Basement 2
Shops | 4.18 | 690.75 | Basement 1
Shops | 3.64 | 788.4 | Ground
Shops | 3.64 | 791.01 | First
Shops | 3.38 | 730.45 | Second
Offices | 3.38 | 612.32 | Third
Offices | 3.38 | 605.14 | Fourth
Offices | 3.38 | 607.53 | Fifth
Offices | 3.38 | 607.53 | Sixth
Roof | 3.38 | 607.53 | Seventh

## Slide 6
Material
Structural material
Non-structural material
Value | Property
28 Mpa | Compressive strength of concrete (f́́c)
24.87*103 Mpa | Modulus of elasticity (Ec)
23 kN/m3 | Unit Weight of plain concrete (Ɣ)
25 kN/m3 | Unit Weight of plain concrete (Ɣ)
Value | Property
420 Mpa | Yield strength (fy)
2.04*103 Mpa | Modulus of elasticity (Ec)
Unit Weight kN/m3 | Material
12 or 16 | Block
26 | Tiles
23 | Plastering
26 | Masonry Stone
18 | Aggregate
23 | Concrete mortar

## Slide 7
Soil properties
In this project the bearing capacity of the soil based on the nature
of the soil in the site is 400KN/
Type equation here.Which mean that we have rocky soil characteristics.
Codes and Standards
ACI 318-19 (American Concrete Institute): building code requirements
of structural concrete and commentary.
IBC-97 (Uniform Building Code) .
Load
Live Load : ( 2 , 2.5 , 4 ) 𝑘𝑁/𝑚2
Dead Load : 5 𝑘𝑁/𝑚2
Super imposed Load : 4.54 𝑘𝑁/𝑚2

## Slide 8
Preliminary Design

## Slide 9
Slab design
After trying a different systems of slabs , the most suitable one for all the floors is a two way solid slab system with 200 mm thickness .
Flexure design
Figure :Cross-section
Figure :Frame max bending moment diagram (KN.m)

## Slide 10
Figure : The max moment values in Column strip (KN.m)

## Slide 11
Figure: The max bending moment values in Beam(KN.m)
Figure : The max bending moment values in column strip(KN.m)

## Slide 12
Figure: Middle strip moment diagram (KN.m)

## Slide 13
Slab middle strip | Slab column strip | Beam | 
187.4 | 57.30 | 324.717 | Max negative moment (KN.m²)
104.44 | 47 | 266.32 | Max positive moment (KN.m²)
0.0125 | 0.0018 | 0.0055 | 𝜌 Max negative moment
0.0038 | 0.0018 | 0.00447 | 𝜌 Max positive moment
3477.23 | 1251 | 1408 | As Max negative moment (mm2)
1055 | 1251 | 1144 | As Max negative moment (mm2)
5 Φ18 | 5 Φ18 | 5 Φ18 | Number of bars

## Slide 14
THREE - DIMENSIONAL MODEL (ANALYSIS AND DESIGN)

## Slide 16
Definition of material

## Slide 17: Slab
There is one thickness of slabs in both directions ( x & y ) equals 200 mm.
The definition of the 200mm slab

## Slide 18
Slab modifiers

## Slide 19: Beams
There is two types of beams with two different rectangular cross sections (750x550mm and 800x500mm)
Beam definition
Modifiers of beams

## Slide 20: columns
There are five column sections :
Rectangular(300x400mm)
Rectangular(400x500mm)
Circular with diameter 1300mm
Circular with diameter 1000mm
Circular with diameter 800mm

## Slide 21
modifies of Columns
Column Definition

## Slide 22: Shear walls
This building have a different thickness
of shear walls (300 mm, 200mm and 250 mm)
Shear wall definition
Shear wall modifiers

## Slide 23: Load Patterns
1.Live load 2.Dead load 3.Super imposed dead load 4.Response X & Y
Definition of Load patterns

## Slide 24: Live load
Live load on garages (basement3, and basement2) is 2 𝑘𝑁/𝑚2, but on shops (basement1 , ground , first and second floor ) is 4𝑘𝑁/𝑚2. And for offices (third , fourth , fifth and sixth floor) is 2.5 𝑘𝑁/𝑚2. Finally, Live load on the roof (seventh floor) is 5 𝑘𝑁/𝑚2
Live load on commercial floors

## Slide 25: Superimposed dead load
Superimposed dead load on the structure is
4.54 𝑘𝑁/𝑚2
load on commercial floors

## Slide 26: Seismic Loads
Response spectrum definition

## Slide 27
Load cases definition for response spectrum

## Slide 28: Seismic Loads calculations

## Slide 30
Using zones with 2% exceedance Ss = (0.25)*(0.2)*(1.5) = 0.075 S1 = (0.125)*(0.2)*(1.5) = 0.0375

## Slide 32
The maximum considered earthquake (MCER)
Spectral Response Acceleration Parameters:
SMS = Fa * Ss = 0.8 * 0.075 = 0.06
SM1 = Fv * S1 = 0.8 * 0.0375 = 0.03
The design spectral acceleration :
SDs = 2/3 * SMS = 2/3 * 0.06 = 0.04
SD1 = 2/3 * SM1 = 2/3 * 0.03 = 0.02

## Slide 33: Then , Cs = SDs∗Ie /R = (0.04*1.25)/5 = 0.25

## Slide 34: Determination of structure period
For all buildings, the value T may be approximated from the following formula:
T = CT * hnX
Where:
ℎ𝑛 = ℎ𝑒𝑖𝑔ℎ𝑡 𝑜𝑓 𝑡ℎ𝑒 𝑏𝑢𝑖𝑙𝑑𝑖𝑛𝑔
Ct = 0.047 for steel moment-resisting frames of reinforced concrete.
X = 0.9 for concrete resisting frames.
T = (0.047) * (40.84)0.9 = 1.324 Sec
From SAP :
T = 0.97 sec < 1.324 sec ⟶ OK

## Slide 35: Verifications of structural analysis & Checks
Compatibility
Equilibrium
Stress strain (Internal equilibrium)
Deflection

## Slide 36: Compatibility check
T from hand calculations
= 1.324 sec

## Slide 37
Equilibrium Check
Difference %L | SAP results kN | Hand result kN | Load type
3.039 | 82126.74 | 79704.39 | Dead
0.40 | 29117.21 | 29001.00 | SD
0.007 | 19080.39 | 19079.00 | Live

## Slide 38: Stress strain check
M11 value will be read at the frame . the allowable error between the hand calculation and sap should be less than 10%
Figure Choose load combination and moment M11

## Slide 39
FRAME
Section cut stresses & forces for frame – start of span
Section cut stresses &forces for frame – middle of span

## Slide 40
Section cut stresses &forces for frame – end of span

## Slide 41: BEAM
Section cut stresses &forces for beam – start , middle &end of span

## Slide 42
Deflection
ΔLt=Δ L +λ͚ ΔD +λt ΔLS
ΔD =Deflection due to dead load
ΔL =Deflection due to live load
ΔLS =Deflection due to sustained live load
ΔLt =Long term Deflection
λ=∈/(1+S ∆ρ ) , ρ=AS/bd
No compression steel (ρ=0) ,Assume 50% sustained live found
λ͚ =λt , AS live load assumed
for duration 5years or more ,∈=2
λ=2/(1+0)=2 → λ͚=λt=2
ΔLt=0.50ΔL +2ΔD + (2*0.50 ΔLS)
ΔLt= 2ΔD +1.50 ΔLS

## Slide 43
Definition of load combination for deflection

## Slide 44
high deflection panel

## Slide 45
Deflections in Deformed shape

## Slide 46
Deflection at the corner 1 of the panel
deflection at the middle of the panel

## Slide 47
deflection at the corner 2 of the panel
deflection at the corner 3 of the panel

## Slide 48
deflection at the corner 4 of the panel
deflection at the corner 5 of the panel

## Slide 49
Maximum deflection at the corner of the panel from combination load = 66.94 mm
Deflection =Δ middle of panel -
=58.0967 -
58.0967 - 35.568=22.529mm=
Allowable deflection =
―> clear distance = 8.22-0.8 =7.42 m = 7420mm
22.53mm <30.91mm ―> ok

## Slide 50: Drift check

## Slide 51
Drift Values in X and Y directions
Drift in x = δx
=
Drift in y = δy = = = 0.7452
Allowable Drift for floor 7 = 0.015 * h
= 0.015 * 3.38 * 1000
= 50.7 mm

## Slide 52
COLUMNS DESIGN

## Slide 53
Columns layout in Structure
Axial load on columns
Column Number | load (KN)
C1 | 3760.805
C2 | 4893.726
C3 | 3666.187
C4 | 901.621
C5 | 4961.046
C6 | 1135.412
C7 | 5261.51
C8 | 3177.875
C9 | 2105.598
C10 | 1713.18
C11 | 3240.809

## Slide 54: Columns grouping
Group number | Column number | Axial force range (KN)
1 | C4, C10 | 0-2000
2 | C1, C8, C9, C11 | 2000-4000
3 | C2, C5, C7 | 4000-6000
4 | C3, C6 | Special group

## Slide 55: Buckling Check
M1 = 48.93 KN.m
M2= 105.066 KN.m
r = (0.25)(0.8) = 0.2 ……….. (for circular column)
9.1 ≤ 28.41 ≤ 40 → → Short column

## Slide 56
Column 10, group 1 (300*400 mm)
Column 11 , group2
(400*500 mm)
COLUMNS SECTIONS

## Slide 57
Column 1 ,group 2
(D=800 mm)
Column 7 ,group 3 (D=800 mm)

## Slide 58
Column 3 ,special group
(D=1300 mm)
Column 6 ,special group
(D=1000 mm)

## Slide 59
COLUMNS DESIGN
Group | Critical column | Pu (KN) | Dimensions (mm) | As (mm2) | Reinforcement | Ties (mm)
1 | C10 | 1713.18 | 300*400 | 1107 | 6 ∅18 | 1∅ 10/ 250
2 | C11 | 3240.81 | 400*500 | 3716.12 | 8 ∅ 25 | 1∅ 10/ 250
2 | C1 | 3760.81 | D=800 | 5057.142 | 12 ∅ 25 | 1∅ 10/ 60
3 | C7 | 5261.5 | D=800 | 5057.142 | 12 ∅ 25 | 1∅ 10/ 60
Special group | C3 | 3666.19 | D=1300 | 13.266*103 | 18 ∅ 32 | 1∅ 10/ 60
Special group | C6 | 1135.41 | D=1000 | 7.85*103 | 16 ∅ 25 | 1∅ 10/ 60

## Slide 60: CHAPTER FIVE FOUNDATIONS DESIGN

## Slide 61: Footings design
Footing dimension
B = 26.34 m , L = 27.95 m
Area = B * L = 26.34 * 27.95 = 736.2 m2
  Calculate (d) depending on wide beam shear.
∑ Pu =160776.2 kN
qu = = = 218.4KN/m2
Vu = qu ( ) = 218.4 ( )
Vu = 658.5 - 327.6 d ----- (1)
∅𝑉𝑐 = ∅ √𝑓′𝑐 𝑏𝑤 𝑑 = (.75) ( ) ( √28) (1000) ( d*1000) / 1000 , ∅𝑉𝑐 = 661.44 𝑑 ----- (2)
Then Vu= ∅ 𝑉𝑐
658.8 - 327.6 d = 661.44 d , ∴ d = 0.70m

## Slide 62: Definitions
Material Definition

## Slide 63
Columns Sections Definition

## Slide 64
Slab Section Definition

## Slide 65
Load Pattern Definition

## Slide 66
Spring Definition

## Slide 67
punching shear Check
𝑉𝑢 𝑝𝑢𝑛𝑐ℎ𝑖𝑛𝑔 from SAP = 1024.5 KN
∅𝑉𝑐𝑝 = (0.75 ∗ ∗ √28 ∗ 1000 * 700)/1000 = 463 KN
∅𝑉𝑐𝑝 = 463 KN < 𝑉𝑢 𝑝𝑢𝑛𝑐ℎ𝑖𝑛𝑔
Try d = 1.3 m
𝑉𝑢 𝑝𝑢𝑛𝑐ℎ𝑖𝑛𝑔 from SAP = 787 KN
∅𝑉𝑐𝑝 = (0.75 ∗ ∗ √28 ∗ 1000 * 1300)/1000 = 860 KN
∅𝑉𝑐𝑝 = 860 KN > 𝑉𝑢𝑝𝑢𝑛𝑐ℎ𝑖𝑛𝑔 ⟶ OK .
∴ Use d = 1.3 m

## Slide 68
Deflection Check
Figure : Deflection of footing

## Slide 69
Figure :Maximum deflection of footing in (mm)
Note that The deflection should be less than 10 mm and it is 1.6mm

## Slide 70: Flexure distribution
Moment distribution in X direction (M11)

## Slide 71
Moment distribution in Y direction (M22)

## Slide 72
R
E
I
N
F
O
R
C
E
M
E
T

## Slide 73
Slab Reinforcement in x-direction for basement floor

## Slide 74
Slab Reinforcement in y-direction for
basement floor

## Slide 75
Beam Reinforcement

## Slide 76
Shear walls Reinforcement

## Slide 77
Reinforcement in x-direction for mat foundation

## Slide 78
Reinforcement in y-direction for mat foundation

## Slide 79
Stairs Reinforcement

## Slide 81
Thank you