## Slide 1: Strengthening of Al-Yasmeen Building against gravity and seismic loads using FRP technique and jacketing
Prepared by: Amro Nather Nassar
Huda Loai Yahya
Mohammad Hakam Assi
Mohammad Maher Jaradat
Raghad Abdel-Salam Owaidat
Supervised By: Dr. Munther Diab

## Slide 2: Content
Chapter One: Description of Project
Chapter Two : Seismic Analysis
Chapter Three: Redesign for gravity and seismic loads
Chapter Four: Strengthening of Weak elements

## Slide 3: Chapter one: Description of Project
About The Project:
"Al-Yasmeen building" is located in Nablus city. It's a building of 6 floors; used as residential and storage building of masonry walls and the floor area of 700 m2.

## Slide 4: Chapter one: Description of Project
Soil Bearing capacity = 250 KN/m^2
Compressive strength of concrete, f 'c = 28 MPa
Unit weight of reinforced concrete,ϓ=25KN/m3

## Slide 5: Chapter one: Description of Project
Loads
S.D=4.7
KN/m^2
Wall=21 KN/m
L.L=2.5
KN/m^2

## Slide 6: Chapter one: Description of Project
Structural System

## Slide 7: Chapter one: Description of Project
Sections used in reality:

## Slide 8: Chapter two: Seismic Analysis
After analysis of Structural behavior  Structural Constraint
Horizontal Irregularities
Vertical Irregularities

## Slide 9: Chapter two: Seismic Analysis
Types of Horizontal irregularities

## Slide 10: Chapter two: Seismic Analysis
Types of Vertical irregularities

## Slide 11: Chapter two: Seismic Analysis

## Slide 12: Chapter two: Seismic Analysis
Manually
Etabs
Limit
Period
0.6
0.64
Drift
70 mm
Period
1.72
99 mm
Drift

## Slide 13: Chapter two: Seismic Analysis

## Slide 14: Chapter two: Seismic Analysis
Difference between Center of Mass and Center OF Rigidity

## Slide 15: Chapter two: Seismic Analysis
Solve Structural Problem
Remove and add shear walls

## Slide 16: Chapter two: Seismic Analysis

## Slide 17: Chapter two: Seismic Analysis
Manually
Etabs
Limit
Period
0.71
0.64
Drift
70 mm
Period
0.862
7.75 mm
Drift

## Slide 18: Chapter two: Seismic Analysis
Start Seismic analysis
Equivalent lateral force method
Response Spectrum Analysis
Time History Analysis

## Slide 19: Chapter two: Seismic Analysis
Seismic Requirements:
  Zone II Seismic Activity ( Z=0.2)
  Occupancy Category:
  Risk Category II  I = 1.0

## Slide 20: Chapter two: Seismic Analysis
  Response Modification factor
  Moment Resisting Frame with shear
  walls, for ductility requirements
  Consider R=5

## Slide 21: Chapter two: Seismic Analysis
Determining suitable seismic analysis approach according to IBC2012 with ASCE7-10 that is related with this version of code.
1
SS and S1
2
Soil
3
SMS and SM1
4
SDS
5
SDC
SD1

## Slide 22: Chapter two: Seismic Analysis
Step 1 :
Ss = 2.5Z = 0.5
S1=1.25Z = 0.25
Step 2 : Site Soil Classification
bearing capacity of soil = 250KN/m2 Soft Rock

## Slide 23: Chapter two: Seismic Analysis
Step 3 : SMS = Fa*SS
SM1 = Fv*S1
SMS = 1.2*0.5 = 0.6
SM1 = 1.55*0.25 = 0.3875
Step 4 :
SDS = SMS = 0.6
SD1 = SM1 = 0.3875

## Slide 24: Chapter two: Seismic Analysis
Step 5: Seismic Design
Category D

## Slide 25: Chapter two: Seismic Analysis
Permitted analytical
Procedure

## Slide 26: Chapter two: Seismic Analysis
Equivalent Static Method
Manually:
V = Cs*W
In Y-Direction: T = 0.863 > 0.65, second equation is adopted
V = 5960 KN
In x-Direction: T = 0.441 < 0.65, first equation is adopted
V = 7946 KN

## Slide 27: Chapter two: Seismic Analysis
Analysis by Etabs
y

## Slide 28: Chapter two: Seismic Analysis
Response Spectrum Analysis
VEtabs = Mei*value from curve (a/g) *scale factor.
Vi = value from curve*Wi*(I/R)

## Slide 29: Chapter two: Seismic Analysis

## Slide 30: Chapter two: Seismic Analysis
Modification on Response scale factor

## Slide 31: Chapter Three: Redesign for gravity and seismic loads
Response spectrum is to be adopted to develop Ultimate load combinations
Load combinations according to ASCE 7-10:
1. 1.4D
2. 1.2D + 1.6L
3. 1.2D+ 1.0L + 1.0E
4. 0.9D + 1.0E
Sections to be used as real sections
In reality , 1% (percentage of rough) is used in most beam and columns

## Slide 32: Chapter Three: Redesign for gravity and seismic loads
Design of beams:
Three different beams is designed
manually to check design by Etabs
In three beams:
< min=0.0033
OK
Also, Shear design is OK

## Slide 33: Chapter Three: Redesign for gravity and seismic loads
Design of Columns
Manual design:
Check beam-column design
Check P-δ effect
From interaction diagram
  < 0.01
OK

## Slide 34: Chapter Three: Redesign for gravity and seismic loads
Design of Slab:
ɸMn for As,min is determined = 7.5 KN.m
Moment In all slab around 20KN.m
It needs 2 ɸ14 Top and Bottom Reinforcement

## Slide 35: Chapter Three: Redesign for gravity and seismic loads
Design of footings
Service loads
Grouping
Design
Single footing
Types used:
Wall footing

## Slide 36: Chapter Three: Redesign for gravity and seismic loads
Design of Single footing:
Steps:
Area of footing  Dimensions
Check one-way shear and punching shear  Thickness
Area of steel

## Slide 37: Chapter Three: Redesign for gravity and seismic loads
Compare with existing footings
One section used under all columns: 3.5 * 2.5 * 0.5

## Slide 38: Chapter Three: Redesign for gravity and seismic loads
Design of wall footings:
All values are nearly equal
One Type of wall footing is to be used:
Steps:
Area of footing  Width = 1 m
Check one-way shear  Thickness = 350 mm
Area of steel  5ɸ14/m
Compare with existing: 1.25 m width *0.5 m thickness
Design is SAFE

## Slide 39: Chapter Four: Strengthening of weak elements
Columns reinforcements exceeds maximum allowed
Column 1:  = 6.81 % BUT 3% is used
Column 2:  = 4.65 % BUT 3% is used

## Slide 40: Chapter Four: Strengthening of weak elements
Problems in beams
Beam 1:  = 2. 25% but exist reinforcement = 1%
Beam 2:  = 2. 42% and Av/s exceeds maximum allowed
Beam 3 : Av/s exceeds maximum allowed

## Slide 41: Chapter Four: Strengthening of weak elements
Different alternatives for Strengthening
Concrete Jacketing
Steel jacketing
FRP

## Slide 42: Chapter Four: Strengthening of weak elements
Concept of Concrete Jacketing
Increase section dimensions
Increase area of steel ( longitudinal rebar and stirrups)
Use Anchor bolts

## Slide 43: Chapter Four: Strengthening of weak elements
Column #1
1. New dimensions : 870 * 520 mm
2. As needed : 12Φ25
3. Anchor bolts : 12Φ40 with 150 mm development length
Column #2
1. New dimensions : 870 * 520 mm
2. As needed : 18Φ14
3. Anchor bolts : 12Φ40 with 150 mm development length
Concrete jacketing of columns

## Slide 44: Chapter Four: Strengthening of weak elements
Concrete jacketing of Beams
Beam #1
1. New dimensions : 1050*380 mm
2. As needed : 8Φ20
3. Anchor bolts : 12Φ16 with 150 mm development length

## Slide 45: Chapter Four: Strengthening of weak elements
Beam #2
1. New dimensions : 1050*380 mm
2. Reinforcement : 9Φ20 and 1Φ12/80mm
3. Anchor bolts : 12Φ16 with 150 mm development length
Beam #3
1. New dimensions : 800*380 mm
2. Reinforcement needed : 1Φ12/90mm
3. Anchor bolts : 12Φ16 with 150 mm development length
Concrete jacketing of beams

## Slide 46: Chapter Four: Strengthening of weak elements
FRP : Fiber Reinforced Polymer
Materials used
Functions
Concept of work

## Slide 47: Chapter Four: Strengthening of weak elements
FRP : Fiber Reinforced Polymer

## Slide 48
Thank You for your attention