## Slide 1: Self-Driven Car
Ammar Haj Hamad Izzat AL Kukhon
Supervisor : Dr. Luai Malhis
2011-2012

## Slide 2: Self-Driven Car
Outlines :
  Introduction
  Main Parts
  How it works
  Difficulties and solutions
  Future work
  Project Demo

## Slide 3: Introduction
The main idea of Self-Driven Car is to control the car while it is moving on the street and make it follows the instructions of the traffic signs
  To control the speed , direction of the car
  Avoiding the accidents by avoiding the obstacles in front of it
  The Project aims to help the drivers to securely reach their destination
We used Infra Red waves for communication between the car and the traffic signs

## Slide 4: Main Parts
Car Controller.
IR Data Communication .
Motor Driver.
Ultrasonic Obstacle Detector.
Line follower.
Street Module.

## Slide 5: Motor Driver
  LM293NE H Bridge Driver
    To control the speed and the direction of the car.
  Front and Back motors DC motors
  Each motor has three data pits to control it (enable , Input_1 and Input_2)

## Slide 6: Car Controller:
  PIC18f4620 Micro Controller
    Controls the motors directions and speed using the H bridge
      Speed Controlling :
        To control the motor there are three inputs in the H bridge (enable , Input_1 and Input_2
        Send motor enable to the H bridge
        PIC will generate a PWM signal with a specified duty and assign it to the Input_1 of the H Bridge
        Set or reset Input_2 ,to control the direction of the motor

## Slide 7: IR Data Communication
IR Data Communication :
The Most important part of the project
Consists of Two Parts :
  IR Senders :
    Central Unit used to send the data to each Traffic sign .
    Each Traffic sign represents a sender that sends specific data.
  IR Receiver
    Fixed on the car module.

## Slide 8: IR Data Communication
Why we Used IR technique
  Line of sigh ,similar to the real life
  Cheaper
  Available
  Short distance
IR difficulties
  Data loss
  Noise caused by the Light
  IR signals interference

## Slide 9: IR Sender
IR Sender :
  Consists of Five main components :
    PIC18f4620 : to assign each traffic sign unique data .
    MC14526 Decoder : to encode the data generated by the PIC.
    Signal Modulation :
      Using NE555 Timer to Modulate the signal with a 50KHZ carrier and forward it to the De-multiplexer.

## Slide 10: IR Sender
  IR Sender :
    74HCT 154 De-multiplexer :
      controlled by the PIC
      keep switching between All of the traffic signs and assign the serial data .
      The data will be sent twice to make sure that the data sent to be compared at the receiver side
    Traffic Signs :
      IR LEDs used to send the IR waves from the De-multiplexer

## Slide 11: IR Receiver
  IR Receiver Consists of three main components :
TSOP1738 :
  Used to Receive and demodulate the IR waves sent by the Traffic Signs
  Has a filter to reduce the noise from the lights and other noise sources

## Slide 12: IR Receiver
MC145027 decoder :
  Used to decode the Signals received by the TSOP
  Check if the address received match the address of the receiver
  Check if it received the same data twice with the same address

## Slide 13: IR Receiver
  On match put the decoded data to the Port D of the PIC and trigger an interrupt to the PIC on port B so that the PIC will start analyzing the data on Port D
  Finally The PIC will respond to the traffic sign data by sending the right command to the car

## Slide 14: Ultrasonic Obstacle Detector.
LV-Ez1 Ultra Sonic sensor used to detect the obstacles in front of the car .
  Once the sensor detects obstacles within it’s range it will give voltage level .
  The voltage sent to the ADC on the PIC to be compared to determine the distance of the obstacle .
  If the obstacle distance less than 30 cm the Car will stop.

## Slide 15: Line follower
The Line follower consists of two main components :
  IR sender and receiver :
      Two couples of sender and receiver (left and right)
      The sender will send the signals , if the surface under the sender is white , the receiver will receiver the reflected signals by the surface.
      Else if the surface is black the receiver will not receive any signal.

## Slide 16: Line follower
A couple of comparators :
  The comparator will compare the IR receiver voltage if it is less than 2.4 volt it will consider it as zero logic else it will be considered one logic.
  Once the car faces a white line either on left or right it will trigger a left or right interrupt on the PIC.
  The car will turn right for right line interrupt and vice versa.

## Slide 17: Street Module
We built the street with black color and white lines so that the car will follow the line .
The Street contains traffic signs represented by IR LEDs .
The IR LEDs are distributed with certain angels to be line of sight with the car receiver.

## Slide 18: Difficulties and solutions
First try was to decode IR signal from scratch using
Capture/compare feature of the PIC to analyze data generated on the other side using pwm ,this will be more sensitive to the noise, and it was solved using the current way of decoding.
Interference and signal attenuation .
Each traffic sign needs its own power to send its code and to reduce this huge power we use a de-mux with TDM to keep switching across all signs.

## Slide 19: Future work
Provide ultra sonic sensors in all sides of the car .
Enable to program the traffic signs using a keypad .
Using Image processing technique to recognize the signs .
Control the car using Wi-Fi technique .

## Slide 20
Thank You …