## Slide 1
An-Najah National University
Faculty of Engineering
Building Engineering Department
Graduation project II
“Modern secondary school design”
Prepared by
Esra’a Osama Braik
Saja Samir Abd Alsalam
Sarah Husam Jawhari
Supervisor
Arch. Moayad Salhab

## Slide 2
Outline
Design
Architectural
Structural
Environmental
Mechanical
Electrical
Cost
Introduction

## Slide 3
Introduction
The project includes an integrated detailed design for a modern secondary school for girls in Nablus city.
The school has a capacity of 480 students and consists of four floors in addition to the basement.

## Slide 4: ARCHITECTURAL DESIGN
1

## Slide 5
Site analysis
Location
The site is located in Al-Ma’ajeen in Nablus, Palestine
Area = 4150 m²
Slope, 10%
    Zone regulations
Streets surrounding the site

## Slide 6
Design
Floor | Area of the floor (m²) | Number of Classroom
Basement | 988 | -
Ground floor | 767 | 1
First floor | 875 | 5
Second floor | 875 | 5
Third floor | 711 | 5
Total Area | 4216 | 16
Summary of school floors

## Slide 7
School Site Plan

## Slide 8
Basement
Basement | 
Zone | Number
Electrical and mechanical room | 1
Storage | 1
Car Parking | 20 car

## Slide 9
Ground Floor
Ground floor | 
Zone | Number
Administration | 5
First Aid room | 1
Teacher’s room | 1
Classroom | 1
Canteen | 1
Students WC | 6

## Slide 10
First Floor
First Floor | 
Zone | Number
Multi-purpose | 1
Social worker room | 1
Teacher’s room | 1
Classroom | 5
Storage | 1
Students WC | 6

## Slide 11
Second Floor
Second Floor | 
Zone | Number
Computer Lab | 1
Laboratories | 2
Classroom | 5
Students WC | 6

## Slide 12
Third Floor
Third Floor | 
Zone | Number
Library | 1
Classroom | 5
Students WC | 6

## Slide 13
Elevations
Southern elevation
Northern elevation

## Slide 14
Sections
Section B-B
Section A-A

## Slide 15
Facilities for handicapped people
Handicapped Toilets
Ramp with 8% slope at each entrance
Elevators

## Slide 17: STRUCTURAL DESIGN
2

## Slide 18
Design data
The school building has five stories, its area is about 4261 m2
The basement’s height is 3 meters and the other stories has a height of 3.65 meters
Bearing capacity of soil is 250 kN/ m2

## Slide 19
Design data
Concrete Compressive Strength
B300 is used for slabs and beams
B350 is used for columns , shear walls and footings
Yielding Strength for Steel
Fy = 420 MPa

## Slide 20
Codes
ACI 318-08 (American Concrete Institute)
UBC-97 (Uniform Building Code)
ASCE (American Society of Civil Engineers)

## Slide 21
Loads
Gravity Loads
Live Load = 5 kN/m2
Super Imposed Dead Load = 4 kN/m2
Self own weight of structural elements of building
Lateral Loads
Seismic Loads

## Slide 22
Expansion joint

## Slide 23
Expansion joint
Block one
Block two

## Slide 24
Columns center lines
Block one
Block two

## Slide 25
Modeling (Etabs software)
Block one
Block two

## Slide 26
Modeling checks
Block one
Block two
Compatibility checks

## Slide 27
 | Block One |  |  | Block Two |  | 
Load | Manual | Etabs | Error % | Manual | Etabs | Error %
Live | 15448.4 | 15426.6 | 0.14 | 15448.4 | 15426.6 | 0.14
Dead | 19353.3 | 19135.6 | 1.12 | 10105.3 | 10614.6 | 5.04
SID | 29757.8 | 29466.1 | 0.95 | 29757.8 | 29466.1 | 0.95
Modeling checks
Equilibrium checks

## Slide 28
 | Manual | Etabs | Difference %
Corner | 1987.1 | 1952.6 | 1.76
Middle | 1974.9 | 2091.7 | 5.58
 | Manual | Etabs | Difference%
Beam2 | 443.3 | 410.04 | 8.11
Beam3 | 417.56 | 433.54 | 3.7
Manual | Etabs | Difference %
37.17 | 35.8 | 3.84
Modeling checks
Internal forces check

## Slide 29
Seismic design
Response Spectrum Parameters
Seismic zone is 2B (Z=0.2)
Importance factor, I=1.25
Force reduction factor, R=5.5
(Building Frame System)
Soil profiles in the project is (SD)
Acceleration-dependent seismic coefficients, Ca=0.28
Velocity-dependent seismic coefficients, Cv = 0.4

## Slide 30
Seismic checks
Modal Mass Participation Ratio
Period check
Base shear check
Drift check
P-delta check

## Slide 31
Seismic checks
Modal Mass Participation Ratio check
Block one
Block two

## Slide 32
Seismic checks
Period check
3/4
Ct = 0.0488 hn is the height of the building
 | Block one | Block two
T Etabs(sec) | 0.48 | 0.47
T limit (sec) | 0.55 | 0.55

## Slide 33
Seismic checks
Base shear check
Weight of the building = Own weight + SID + (0.25*Live load) For block one = 58070.53 kN For block two = 25366.72 kN
Block one |  |  |  | Block two |  |  | 
V calculated | V min | Vmax | V selected | V calculated | V min | Vmax | V selected
17252.1 | 2235.7 | 9238.5 | 9238.5 | 6823.79 | 837.1 | 3495.1 | 3495.1
Block one |  |  |  | Block two |  |  | 
T(sec) | V manual | Vx Etabs | Vy Etabs | T(sec) | V manual | Vx Etabs | Vy Etabs
0.48 | 9238.5 | 9245.6 | 9249.2 | 0.47 | 3495.1 | 3461.78 | 3467.65

## Slide 34
Seismic checks
Story drift check
Story | Height (mm) | Disp. X(mm) | Disp. Y(mm) | Drift x (mm) | Drift y (mm) | Delta x | Delta y | Delta limit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 
1 | 3000 | 0.29 | 0.90 | 0.29 | 0.90 | 1.11 | 3.45 | 75.00
2 | 3650 | 3.53 | 5.76 | 3.24 | 4.86 | 12.48 | 18.70 | 91.25
3 | 3650 | 8.61 | 12.98 | 5.08 | 7.23 | 19.57 | 27.82 | 91.25
4 | 3650 | 14.26 | 20.07 | 5.65 | 7.09 | 21.74 | 27.28 | 91.25
5 | 3650 | 22.09 | 24.19 | 7.83 | 4.12 | 30.13 | 15.86 | 91.25
Story | Height (mm) | Disp. X(mm) | Disp. Y(mm) | Drift x (mm) | Drift y (mm) | Delta x | Delta y | Delta limit
0 | 0 | 0.00 | 0 | 0 | 0 | 0 | 0 | 
1 | 3000 | 0.24 | 0.46 | 0.24 | 0.46 | 0.92 | 1.75 | 75
2 | 3650 | 2.95 | 1.86 | 2.71 | 1.40 | 10.45 | 5.39 | 91.25
3 | 3650 | 6.50 | 3.96 | 3.55 | 2.11 | 13.66 | 8.11 | 91.25
4 | 3650 | 10.48 | 6.46 | 3.97 | 2.50 | 15.30 | 9.63 | 91.25
5 | 3650 | 14.50 | 9.11 | 4.02 | 2.65 | 15.49 | 10.19 | 91.25
Block one
Block two

## Slide 35
Seismic checks
P-delta check
Block one
Block two
Story | D+L (kN) | Vx (kN) | Vy (kN) | Drift X(mm) | Drift Y(mm) | Height (mm) | Pdelta-x | P delta- y
Story 1 | 6960.33 | 5258.38 | 6692.02 | 0.288 | 0.897 | 3000 | 0.0001 | 0.00031
Story 2 | 6960.33 | 3103.42 | 6616.96 | 3.242 | 4.858 | 3650 | 0.002 | 0.00140
Story 3 | 6960.33 | 2260.90 | 5751.98 | 5.084 | 7.225 | 3650 | 0.0043 | 0.00240
Story 4 | 6960.33 | 1718.36 | 4273.48 | 5.648 | 7.087 | 3650 | 0.0063 | 0.00316
Story 5 | 6960.33 | 752.58 | 2227.70 | 7.827 | 4.12 | 3650 | 0.0198 | 0.00353
Story | D+L(kN) | Vx (kN) | Vy (kN) | Drift x (mm) | Drift y (mm) | Height (mm) | Pdelta-x | Pdelta- y
Story 1 | 3158.45 | 3415.95 | 3418.23 | 0.24 | 0.455 | 3000 | 7.4E-05 | 0.00014
Story 2 | 3158.45 | 3387.50 | 3341.25 | 2.714 | 1.401 | 3650 | 6.9E-04 | 0.00036
Story 3 | 3158.45 | 3073.74 | 3028.21 | 3.549 | 2.107 | 3650 | 1.0E-03 | 0.00060
Story 4 | 3158.45 | 2385.16 | 2342.51 | 6.464 | 2.501 | 3650 | 2.3E-03 | 0.00092
Story 5 | 3158.45 | 1292.04 | 1256.93 | 4.023 | 2.647 | 3650 | 2.7E-03 | 0.00182

## Slide 36
Design and Reinforcement
Slabs
Block one

## Slide 37
Design and Reinforcement
Typical section in ribbed slab

## Slide 38
Design and Reinforcement
Slab on grade and ramp detailing
Ramp
Slab on grade

## Slide 39
Design and Reinforcement
Beams
Beams layout

## Slide 40
Design and Reinforcement
Beams 17 and 18
Sample of detailing

## Slide 41
Design and Reinforcement
Sample of detailing
Beams 17 and 18

## Slide 42
Design and Reinforcement
Columns

## Slide 43
Design and Reinforcement
Sample of detailing for column (C1)
Column C1
Section 1-1

## Slide 44
Design and Reinforcement
Shear walls

## Slide 45
Design and Reinforcement
Sample of detailing for shear wall (SW2)

## Slide 46
Design and Reinforcement
Footings

## Slide 47
Design and Reinforcement
Footings
 | Dimensions(m) (With Blinding Concrete) |  |  | Bottom Reinforcement |  | Top Reinforcement
Footing | Length | Width | Thickness | Longitudinal Reinforcement | Transverse Reinforcement | Both directions
F1 | 2.8 | 2.6 | 0.55 | 12ɸ16 | 16ɸ16 | 5ɸ16/m
F2 | 2.6 | 2.4 | 0.5 | 13ɸ16 | 9ɸ16 | 6ɸ14/m
F3 | 2.7 | 1.5 | 0.5 | 10ɸ16 | 12ɸ16 | 5ɸ16/m
F4 | 3.7 | 2.7 | 0.6 | 11ɸ20 | 13ɸ20 | 6ɸ16/m
F5 | 3.0 | 2.7 | 0.55 | 12ɸ16 | 16ɸ16 | 5ɸ16/m
F6 | 3.8 | 2.8 | 0.6 | 13ɸ16/m | 6ɸ16/m | Long. 11ɸ16 Trans. 6ɸ16
F7 | Variable | 3.5 | 0.6 | 14ɸ18 | 6ɸ16/m | 6ɸ16/m
F8 | Variable | 2.5 | 0.6 | 10ɸ18 | 6ɸ16/m | 6ɸ16/m
F9 | 6.5 | 1.9 | 0.6 | 8ɸ18 | 22ɸ20 | 6ɸ16/m
F10 | 15.0 | 8.0 | 1.0 | 6ɸ20/m | 6ɸ20/m | 7ɸ20/m

## Slide 48
Design and Reinforcement
Sample of detailing for isolated footing (F2)
Footing F2
Section A-A
Section B-B

## Slide 49
Design and Reinforcement
Sample of detailing for combined footing (F6)
Footing F6
Section A-A

## Slide 50
Design and Reinforcement
Sample of detailing for wall footing (F8)
Footing F8

## Slide 51
Design and Reinforcement
Sample of detailing for mat footing (F10)
Footing F10
Section A-A

## Slide 52
Design and Reinforcement
Sample of detailing for mat footing (F10)
Stairs
Section A-A

## Slide 53: ENVIRONMENTAL DESIGN
3

## Slide 54
Envelope construction details
Floors
Floors
U-value = 0.663 W/m².K
Roofs
U-value = 0.383 W/m².K

## Slide 55
Envelope construction details
U-value = 0.463 W/m².K
Exterior Wall

## Slide 56
Solar analysis
21/1 – 10:00 AM
21/7 – 12:00 PM

## Slide 57
Thermal comfort
 | No HVAC system | HVAC system (heating)
PMV | -1.5 to 1 | -1 to 1
Number of non-comfortable hours | 1162 | 980
Summary
Site and source energy

## Slide 58
Lighting comfort
Daylighting
Ground floor
Good DF in different spaces. High DF for areas close to glazing

## Slide 59
Lighting comfort
Glare
Facility | Resulted glare | Maximum allowed limit
Headmaster office | <10 | 19
Classroom | 13 | 19
Multi-purpose room | 15 | 22
Library | <10 | 19
Classroom – GF

## Slide 60
Acoustic comfort
Reverberation time (RT60)
Facility | Resulted RT60 (ms) | Required RT60 (ms)
Headmaster office | 400-420 | 400-600
Classroom | 500-540 | 500-900
Multi-purpose room | 630-730 | 600-800
Library | 640-730 | 500-900

## Slide 61
Acoustic comfort
Sound Transmission class (STC)
42 dB
47 dB
Classroom - GF
STC for exterior wall
STC for classroom/corridor

## Slide 62
Acoustic comfort
Sound Transmission class (STC)
42 dB
41 dB
41 dB
47 dB
41 dB
41 dB
42 dB
47 dB
Multi-purpose room
Library

## Slide 63
Acoustic comfort
Sound Transmission class (STC)
42 dB
47 dB
41 dB
Headmaster office
 | IIC (dB)
Ceilings | 48
Roofs | 45
Impact Insulation Class (IIC)

## Slide 64: MECHANICAL DESIGN
4

## Slide 65
Water supply system
10 water tanks (1500L) are used
5 electric boilers (60L)
Boiler of solar evacuated tubes (200L)
Water source
Potable water is delivered from municipality
Rainwater will be harvested in a tank of a volume (130 m³) which will be reused for flushing system.

## Slide 66
Plumping
Diameters of pipes
Fixture units and demand
Demand and loss for each diameter

## Slide 67
Drainage system
Manholes

## Slide 68
Drainage system line diagram

## Slide 69
HVAC system
Radiators design
Used for southern and western spaces
Number of sections =
Using a product of 89.9 Watt/section
Natural ventilation is highly utilized in the school
No cooling system
Heating system : Radiators

## Slide 70
Radiators system
Radiators – Ground floor

## Slide 71
Radiators system
Fuel
The fuel used is LPG (Liquified Petroleum Gas)
Mass of fuel (Mf) = 6945.264 kg/season
Volume of fuel needed = 12.63 m³ (Density of LPG = 550 kg/m³)
Boiler chimney
Diameter of chimney = 0.13m
(130mm > 126mm the minimum recommended diameter)

## Slide 72
Mechanical site plan

## Slide 73
Fire fighting system
A and C fire classes are present
Fire extinguishers
(HCFC fire extinguishers) are used in administration spaces, laboratories, library and multi-purpose room
Hose reels
This system is used in corridors and parking with a height from floor of 1.2m

## Slide 74
Emergency evacuation
Ground floor

## Slide 75: ELECTRICAL DESIGN
5

## Slide 76
Electrical Equipment
Summary of number of switches, luminaires, sockets, distribution boards of each floor in the school
Floor | Number of switches | Number of luminaires | Number of normal sockets | Number of special sockets | Number of DB
Basement floor | 6 | 68 | - | - | 3
Ground floor | 19 | 118 | 31 | 2 | 1
First floor | 16 | 161 | 33 | 1 | 1
Second floor | 15 | 170 | 32 | 1 | 1
Third floor | 13 | 140 | 25 | 1 | 1

## Slide 77
Distribution board
There is one Main Distribution Board in the basement, and 7 sub-distribution boards in the upper floors
Main Distribution board
First floor Distribution board

## Slide 78
Electrical Estimations
 | DB-1 B1 | DB-2 GF | DB-3 FF | DB-4 SF | DB-5 SF (computer lab) | DB-6 TF
Lighting power(watt) | 1522 | 4447 | 9800 | 10115 | - | 9065
Lighting current (Amp) | 7 | 20.2 | 44.5 | 46 | - | 41.2
Sockets current (Amp) | - | 32 | 32 | 32 | 80 | 32
Special load current (Amp) | - | 48 | 16 | 16 | - | 16
Number of lighting branches | 20 | 23 | 20 | 20 | - | 23
Number of sockets branches | - | 10 | 7 | 6 | 15 | 6
Number of special load branches | - | 2 | 1 | 1 | - | 1
Circuit breaker current (Amp) | 6.4 | 34.2 | 31.6 | 34.9 | 24 | 33.5
Cable rated current (Amp) | 24 | 37 | 37 | 37 | 29 | 37
Cable cross sectional area (mm2) | 2.5 | 6 | 6 | 6 | 4 | 6

## Slide 79
Sockets
Sockets arrangement – Ground floor
Sockets arrangement – First floor

## Slide 80
Artificial lighting
Types of Luminaires used
Lamp name | Luminaire power (watt)
Artemide Lighting- 1xLED-35watt | 35
V-TAC - 4873 V-TAC 24W LED Premium Panel | 24
V-TAC 22W LED waterproof Tube T8 150cm | 22
Philips Lighting- 3xTL5-24watt | 80
Artificial lighting arrangement – Ground floor

## Slide 81
Artificial lighting
Summary of Illuminance for some zones in the school using Dialux-evo software
Zone | Illuminance | Recommended Illuminance
Head master | 439 | 300
Classroom | 491 | 300-500
Multi-purpose | 743 | 500
Library | 683 | 500-700

## Slide 82
Loudspeakers
The type which was used in the corridors was DS-160CDT loudspeaker in the ceiling with the specification shown.
Since the coverage angle is then the diameter of the coverage area is 8 m.
→ Six loudspeakers are needed in the corridor.

## Slide 83
Loudspeakers
Loudspeakers arrangement – Ground floor
DS-160CDT loudspeaker

## Slide 84
Photovoltaic system
Annual electricity consumption equals 39,781.51 kWh
Planned power of PV system =
= = 26.52 kWp
Tilt angle = 27°
Solar panels of 370 Wp for each one are used
The system will produce 45.57 MWh/year = 45,570 kWh/year. (Enough to cover 100% of the annual electricity of lighting and equipment only).

## Slide 85
Photovoltaic system
Project simple payback period
PV system cost = 26,520 $
Energy Tariff = 0.1665 $/kWh
Project production in the first year = 39,780 kWh
First year profit = 0.1665*39,780 = 6,623.37 $
Payback period = = 4 years

## Slide 86
Photovoltaic system
System of 72 PV cells

## Slide 87: COST OF PROJECT
6

## Slide 88
Cost
Cost includes material and labor costs
Total cost equals 1,776,125.00 $
Unit cost equals 421 $/m²
Item | Cost ($)
Site works | 86551.50
Finishing works | 590875.50
Structural works | 817402.00
Mechanical works | 162796.00
Electrical works | 118500.00
Total cost ($) | 1776125.00

## Slide 89: Thanks!