## Slide 1
An-Najah National University Engineering College Building Engineering Department
Preparad by: Danial Halabi
Muna Tuffaha
Tamara Samaro
Supervisor : Eng. Fadi Fatayer
Graduation Project II
Integrated Redesign of the Administrative and Economic Sciences Faculty

## Slide 2: Project Outline
Objectives
Architectural Aspect
Environmental Aspect
Structural Aspect
Electro-Mechanical Aspect
Site Analysis
Quantity survey

## Slide 3: Objectives and methodology

## Slide 4: Site analysis
Location:
The land on which the faculty is located at Ghassan al-shaka’a street, near Al-Ma’ajeen Neighborhood, in the north-west part of Nablus city.
The faculty is based on an area of 2000 m2

## Slide 5: Noise, Sun path and wind analysis:

## Slide 6: General Information
Faculty contains five stories (Ground, first , second , third and fourth floor) .
Each floor has an area of 546
Each floor has an area of 546 𝑚^2.
Faculty has three entrances, two of them have emergency stairs.
Faculty contains five stories (Ground, first , second , third and fourth floor) .
Faculty has three entrances, two of them have emergency stairs.

## Slide 7: Architectural Aspect

## Slide 8: Project’s Plans
Ground floor ( Before)

## Slide 9: Project’s Plans
Ground floor (After)

## Slide 10: Project’s Plans
First floor ( Before)

## Slide 11: Project’s Plans
First floor ( After)

## Slide 12: Project’s Plans
Second floor ( Before)

## Slide 13: Project’s Plans
Second floor ( After)

## Slide 14: Project’s Plans
Third floor ( Before)

## Slide 15: Project’s Plans
Third floor ( After)

## Slide 16: Project’s Plans
Fourth floor (Additional)

## Slide 17: South-west elevation

## Slide 18: North-east elevation

## Slide 19: Section A-A

## Slide 20: Section B-B

## Slide 21: Escape Plans
Escape plan through ground floor

## Slide 22: Escape Plans
Escape plan through other floors

## Slide 23: Structural Aspect

## Slide 24: Structural Design
This structural design is done by using the following codes:
ACI 318-11 for the design of reinforced concrete
ASCE 7 2010 for load combinations
UBC – 97 for earthquake design

## Slide 25: Structural Design
The structural design system used for this building is a two way ribbed slab system, single footings, combined footings, and mat footings.

## Slide 26: Structural Design
ETABS checks:
1- Compatibility check
Check is OK

## Slide 27: Structural Design
ETABS checks:
2- Equilibrium check
Check is OK
Load type | Manual | ETABS | Error | < 5%
Dead | 24494.79 | 24310.2 | 0.75 | OK
Live | 8377.3 | 8376.9 | 0.00 | OK
SID | 16265.89 | 16483.04 | 1.34 | OK

## Slide 28: Structural Design
ETABS checks:
3- Stress strain check
Check is OK
Load type | Manual | ETABS | Error | < 10%
Edge column | 1860.14 | 1838.03 | 1.19 | OK
Corner column | 1506.01 | 1573.89 | 4.51 | OK
Interior column | 1837.22 | 1829.35 | 0.43 | OK
Beam 1 | 146.86 | 139.24 | 5.46 | OK
Beam 2 | 130.35 | 128.45 | 1.46 | OK
Beam 3 | 98.38 | 92.17 | 6.32 | OK

## Slide 29: Structural Design
ETABS checks:
3- Stress strain check
Check is OK
Middle Strip |  |  |  |  |  | 
Manual Results |  |  | ETABS moment |  |  | 
Manual Moment | Frame length | Moment | ETABS moment | Length of Section Cut | Moment | Error %
4.05 | 1.29 | 3.14 | 4.04 | 1.29 | 3.13 | 0.25
36.08 | 1.51 | 23.89 | 31.7 | 1.51 | 20.99 | 12.14
44.34 | 1.73 | 25.63 | 46.35 | 1.73 | 26.79 | 4.53
Column Strip |  |  |  |  |  | 
Manual Results |  |  | ETABS moment |  |  | 
Manual Moment | Frame length | Moment | ETABS moment | Length of Section Cut | Moment | Error %
36.45 | 2.3 | 15.85 | 34.5 | 2.3 | 15.00 | 5.35
108.24 | 1.9 | 56.97 | 112.2 | 1.9 | 59.05 | 3.66
132.9 | 1.32 | 100.68 | 121.65 | 1.32 | 92.16 | 8.47
Frame |  |  |  |  |  | 
Manual Results |  |  | ETABS Results |  |  | 
Manual Moment | Frame length | Moment/m | ETABS moment | Length of Section Cut | Moment | Error %
40.5 | 4.9 | 8.27 | 38.54 | 4.9 | 7.87 | 4.84
144.32 | 4.9 | 29.45 | 143.9 | 4.9 | 29.37 | 0.29
177.24 | 4.9 | 36.17 | 168 | 4.9 | 34.29 | 5.21

## Slide 30: Structural Design
ETABS checks:
4- Time period check
From the 1st mode, Check is OK
T=0.541 seconds
T=0.0488(16) 3/4= 0.39 sec.
T from ETABS < 40% from method “A”
0.541 < 1.4*0.39=0.55 sec

## Slide 31: Structural Design
ETABS checks:
5- Base shear check
Check is OK
Load Case/Combo | FX | FY | FZ
 | kN | kN | kN
Dead | 0 | 0 | 24073.22
Live | 0 | 0 | 8377.159
SID | 0 | 0 | 16269.68
EQx 1 | -4608.88 | 0 | 0
EQx 2 | -4608.88 | 0 | 0
Direction | T | V manual | V ETABS | Error%
X | 0.498 | 4615.85 | 4608.875 | 0.15
Y | 0.33 | 4615.85 | 4608.875 | 0.15

## Slide 32: Structural Design
ETABS checks:
5- Drift check
Check is OK
Story | Height (mm) | Dis-x | Dis-y | Drift-x (ΔS) | Drift-y (ΔS) | Delta-x (Δm) | Delta-y (Δm) | Delta limit
0 | 4000 | 0 | 0 |  |  |  |  | 
1 | 4000 | 1.3 | 0.33 | 1.3 | 0.33 | 5.01 | 1.27 | 100
2 | 4000 | 3.4 | 0.89 | 4.7 | 1.22 | 18.10 | 4.70 | 100
3 | 4000 | 5.8 | 1.57 | 10.5 | 2.79 | 40.43 | 10.74 | 100
4 | 4000 | 8.2 | 2.3 | 18.7 | 5.09 | 72.00 | 19.60 | 100

## Slide 33: Structural Elements Design
Deflection check
The maximum deflection for span = 32.2mm
the critical deflection in the project which occur for cantilever and equal 8.9 mm. So, check is ok

## Slide 34: Structural Elements Design
Checking design members

## Slide 35: Structural Design
Slabs
The used system in structural design is two way ribbed slab
M11 max for all stories

## Slide 36: Structural Design
Slabs
The used system in structural design is two way ribbed slab
M22 max for all stories

## Slide 37: Structural Design
Slabs
For ground floor slab

## Slide 38: Structural Design
Slabs
For first floor slab

## Slide 39: Structural Design
Slabs
For second, third, and fourth slab

## Slide 40: Structural Design
Beams

## Slide 41: Structural Design
Slabs

## Slide 42: Structural Design
Beams
Cross section in B32, B33, B34

## Slide 43: Structural Design
Beams
Detailing of Beams

## Slide 44: Structural Design
Columns
Columns Centre lines plan

## Slide 45: Structural Design
Columns
Column | Width (cm) | Depth (cm) | Longitudinal steel | Stirrups L1 | Stirrups L2
C1 | 60 | 60 | 12Ø20 | Ø10 @144mm | Ø10 @288 mm

## Slide 46: Structural Design
Shear walls
Shear wall No. | B (mm) | H (mm) | As (boundary) ( | As (web) ( | As (boundary) |  | As (web) /m | 
 |  |  |  |  | Ø | #.of bars | Ø | #.of bars
SW1 | 200 | 5900 | 590 | 250 | 14 | 4 | 10 | 4
SW2 | 200 | 3500 | 350 | 250 | 14 | 3 | 10 | 4
SW3 | 200 | 750 | 75 | 250 | 10 | 2 | 10 | 4
SW4 | 200 | 1871 | 187.1 | 250 | 12 | 2 | 10 | 4
SW5 | 200 | 1470 | 147 | 250 | 14 | 2 | 10 | 4
SW6 | 200 | 2240 | 224 | 250 | 14 | 2 | 10 | 4
SW7 | 200 | 2560 | 256 | 250 | 14 | 2 | 10 | 4
SW8 | 200 | 2150 | 215 | 250 | 14 | 2 | 10 | 4
Shear wall No. | B (mm) | H (mm) |  |  | As (boundary) |  | As (web) /m | 
 |  |  |  |  | Ø | #.of bars | Ø | #.of bars
SW1 | 200 | 5900 | 590 | 250 | 14 | 4 | 10 | 4
SW2 | 200 | 3500 | 350 | 250 | 14 | 3 | 10 | 4
SW3 | 200 | 750 | 75 | 250 | 10 | 2 | 10 | 4
SW4 | 200 | 1871 | 187.1 | 250 | 12 | 2 | 10 | 4
SW5 | 200 | 1470 | 147 | 250 | 14 | 2 | 10 | 4
SW6 | 200 | 2240 | 224 | 250 | 14 | 2 | 10 | 4
SW7 | 200 | 2560 | 256 | 250 | 14 | 2 | 10 | 4
SW8 | 200 | 2150 | 215 | 250 | 14 | 2 | 10 | 4

## Slide 47: Structural Design
Stair

## Slide 48: Structural Design
Footings
Layout of footings

## Slide 49: Structural Design
Footings
Isolated footings
Footing NO. | Mu (KN.m) | 𝜌 | Asreq (/m) | Asmin (/m) | As (used) (/m) | Ø | #. Of Bars | Spacing (mm) | Available length(L) (m) | Development Length ( Ld ) (m)
F1 | 99 | 0.00231 | 786.19 | 720 | 786 | 12 | 7 | 167 | 0.69 | 0.6
F2 | 155 | 0.00277 | 1078.79 | 810 | 1079 | 12 | 10 | 112 | 0.91 | 0.57
F3 | 158 | 0.00282 | 1101.32 | 810 | 1101 | 12 | 10 | 112 | 0.93 | 0.58
F4 | 159 | 0.00284 | 1106.18 | 810 | 1106 | 12 | 10 | 112 | 0.93 | 0.59
F5 | 167 | 0.00234 | 1027.70 | 900 | 1028 | 12 | 10 | 112 | 0.94 | 0.55
F8 | 156 | 0.00280 | 1090.08 | 810 | 1090 | 12 | 10 | 112 | 0.91 | 0.58
F10 | 238 | 0.00220 | 1190.55 | 1080 | 1191 | 14 | 8 | 100 | 1.15 | 0.68
F11 | 186 | 0.00209 | 1023.41 | 990 | 1023 | 14 | 7 | 167 | 1.02 | 0.67
F12 | 111 | 0.00153 | 675.37 | 900 | 900 | 12 | 8 | 143 | 0.76 | 0.6
F13 | 129 | 0.00305 | 1037.82 | 720 | 1038 | 12 | 10 | 112 | 0.82 | 0.55
F14 | 129 | 0.00229 | 892.55 | 810 | 893 | 12 | 8 | 143 | 0.84 | 0.59
F15 | 125 | 0.00222 | 867.13 | 810 | 867 | 12 | 8 | 143 | 0.82 | 0.58
F16 | 101 | 0.00236 | 802.38 | 720 | 802 | 12 | 8 | 143 | 0.72 | 0.53
F17 | 119 | 0.00281 | 954.63 | 720 | 955 | 12 | 9 | 125 | 0.79 | 0.56
F18 | 156 | 0.00371 | 1261.91 | 720 | 1262 | 14 | 12 | 9 | 0.91 | 0.64
F19 | 75 | 0.00132 | 515.55 | 810 | 810 | 12 | 8 | 143 | 0.61 | 0.54
Footing NO. | Mu (KN.m) | 𝜌 |  |  |  | Ø | #. Of Bars | Spacing (mm) | Available length(L) (m) | Development Length ( Ld ) (m)
F1 | 99 | 0.00231 | 786.19 | 720 | 786 | 12 | 7 | 167 | 0.69 | 0.6
F2 | 155 | 0.00277 | 1078.79 | 810 | 1079 | 12 | 10 | 112 | 0.91 | 0.57
F3 | 158 | 0.00282 | 1101.32 | 810 | 1101 | 12 | 10 | 112 | 0.93 | 0.58
F4 | 159 | 0.00284 | 1106.18 | 810 | 1106 | 12 | 10 | 112 | 0.93 | 0.59
F5 | 167 | 0.00234 | 1027.70 | 900 | 1028 | 12 | 10 | 112 | 0.94 | 0.55
F8 | 156 | 0.00280 | 1090.08 | 810 | 1090 | 12 | 10 | 112 | 0.91 | 0.58
F10 | 238 | 0.00220 | 1190.55 | 1080 | 1191 | 14 | 8 | 100 | 1.15 | 0.68
F11 | 186 | 0.00209 | 1023.41 | 990 | 1023 | 14 | 7 | 167 | 1.02 | 0.67
F12 | 111 | 0.00153 | 675.37 | 900 | 900 | 12 | 8 | 143 | 0.76 | 0.6
F13 | 129 | 0.00305 | 1037.82 | 720 | 1038 | 12 | 10 | 112 | 0.82 | 0.55
F14 | 129 | 0.00229 | 892.55 | 810 | 893 | 12 | 8 | 143 | 0.84 | 0.59
F15 | 125 | 0.00222 | 867.13 | 810 | 867 | 12 | 8 | 143 | 0.82 | 0.58
F16 | 101 | 0.00236 | 802.38 | 720 | 802 | 12 | 8 | 143 | 0.72 | 0.53
F17 | 119 | 0.00281 | 954.63 | 720 | 955 | 12 | 9 | 125 | 0.79 | 0.56
F18 | 156 | 0.00371 | 1261.91 | 720 | 1262 | 14 | 12 | 9 | 0.91 | 0.64
F19 | 75 | 0.00132 | 515.55 | 810 | 810 | 12 | 8 | 143 | 0.61 | 0.54

## Slide 50: Structural Design
Footings
Combined footings
Footing NO. | Bottom Longitudinal steel |  |  |  |  | 
 | Mu (KN.m) | 𝜌 | As req (/m) | As min (/m) | Ø | #.of bars
F6 | 900.114 | 0.00690 | 6561.34 | 1976.08 | 20 | 21
F7 | 868.4 | 0.00694 | 6333.43 | 1894.64 | 20 | 21
F9 | 829.01 | 0.00583 | 5972.59 | 2127.08 | 20 | 20
Footing NO. | Bottom Longitudinal steel |  |  |  |  | 
 | Mu (KN.m) | 𝜌 |  |  | Ø | #.of bars
F6 | 900.114 | 0.00690 | 6561.34 | 1976.08 | 20 | 21
F7 | 868.4 | 0.00694 | 6333.43 | 1894.64 | 20 | 21
F9 | 829.01 | 0.00583 | 5972.59 | 2127.08 | 20 | 20
Footing NO. | Top Longitudinal steel |  |  |  | 
 | Mu (KN.m) | Asreq () | Asmin () | Ø | #.of bars
F6 | 329.6 | 2402.61 | 1976.08 | 14 | 16
F7 | 361.8 | 2638.69 | 1894.64 | 14 | 18
F9 | 213.89 | 1540.97 | 2127.08 | 14 | 14
Footing NO. | Top Longitudinal steel |  |  |  | 
 | Mu (KN.m) |  |  | Ø | #.of bars
F6 | 329.6 | 2402.61 | 1976.08 | 14 | 16
F7 | 361.8 | 2638.69 | 1894.64 | 14 | 18
F9 | 213.89 | 1540.97 | 2127.08 | 14 | 14
Footing NO. | Transverse steel |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Zone1 |  |  |  |  |  |  | Zone2 |  |  |  |  |  | 
 | qu (KN/) | Mu (KN.m) | 𝜌 | As | Asmin () | Ø | #.of bars | qu (KN/) | Mu (KN.m) | 𝜌 | As | Asmin () | Ø | #.of bars
F6 | 872.64 | 369.14 | 0.00690 | 2690.94 | 810.00 | 20 | 9 | 767.65 | 324.73 | 0.00601 | 2344.07 | 810.00 | 20 | 8
F7 | 849.30 | 321.07 | 0.00594 | 2315.85 | 810.00 | 20 | 8 | 790.61 | 298.89 | 0.00550 | 2145.55 | 810.00 | 20 | 7
F9 | 828.00 | 424.84 | 0.00804 | 3136.73 | 810.00 | 20 | 10 | 815.07 | 418.21 | 0.00791 | 3083.00 | 810.00 | 20 | 10
Footing NO. | Transverse steel |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Zone1 |  |  |  |  |  |  | Zone2 |  |  |  |  |  | 
 |  | Mu (KN.m) | 𝜌 |  |  | Ø | #.of bars |  | Mu (KN.m) | 𝜌 |  |  | Ø | #.of bars
F6 | 872.64 | 369.14 | 0.00690 | 2690.94 | 810.00 | 20 | 9 | 767.65 | 324.73 | 0.00601 | 2344.07 | 810.00 | 20 | 8
F7 | 849.30 | 321.07 | 0.00594 | 2315.85 | 810.00 | 20 | 8 | 790.61 | 298.89 | 0.00550 | 2145.55 | 810.00 | 20 | 7
F9 | 828.00 | 424.84 | 0.00804 | 3136.73 | 810.00 | 20 | 10 | 815.07 | 418.21 | 0.00791 | 3083.00 | 810.00 | 20 | 10

## Slide 51: Structural Design
Footings
Mat foundation
F21 Reinforcement
F20 Reinforcement

## Slide 52: Structural Design
Footings
Mat foundation
F23 Reinforcement
F22 Reinforcement

## Slide 53: Structural Design
Footings
Mat foundation
Section in F1-1

## Slide 54: Structural Design
Tie beams

## Slide 55: Water tank Design
Water tank volume is 240 m3 and its dimensions are 6m width, 10m depth and 4m height respectively.

## Slide 56: Water tank Design
SAP checks:
1- Compatibility check
Check is OK

## Slide 57: Water tank Design
SAP checks:
2- Deflection check
Maximum deflection is less than 10 mm so the check is OK
From water pressure
From soil pressure

## Slide 58: Structural Design
Detailing

## Slide 59: Structural Design
Section A-A

## Slide 60: Structural Design
Section B-B

## Slide 61: Environmental Aspect

## Slide 62: Environmental aspects include:
Thermal Analysis
Daylighting
Shading

## Slide 63: Thermal analysis
U-value for the external wall’s layers = 0.424 (W/m2-K).

## Slide 64
Internal walls: U-value = 1.188 (W/m2-K).
Roof: U-value = 0.343 (W/m2-K).
Inner ground’s cross section

## Slide 65: PMV graph from Design Builder
Site and source energy table using “Design Builder”

## Slide 66: Energy Conservation measure ( ECM)
Adjustable vertical louvers
Overhang ( Cantilever )
Shading Devices:

## Slide 67: Environmental Modifications on facades
South-west elevation (Before)
South-west elevation (After)

## Slide 68: Environmental Modifications on facades
North-east elevation (Before)
North-east elevation (After)

## Slide 69: Environmental Modifications on facades
South-east elevation (Before)
South-east elevation (After)

## Slide 70: Environmental Modifications on facades
North-west elevation (Before)
North-west elevation (After)

## Slide 71: Daylighting Analysis
Daylight factor analysis for First floor by Revit
Before modification
After modification
New Evaluation | old Evaluation | New design D.F | Old design D.F | Min D.F | Avg D.F | Space
Good | Fair | 2 | 1 | 1 | 2 | Staff office
Good | Poor | 2.5 | 1 | 2 | 5 | Classroom

## Slide 72: Electro-Mechanical Aspect

## Slide 73: Electro-Mechanical Design
Artificial Lighting Design.
Branches and Circuit Breakers Design.
Acoustical Design.
Water Supply Design.
Drainage System Design.
HVAC Design.
Firefighting and Fire safety Systems Design.

## Slide 74: Artificial Lighting Design

## Slide 75: Artificial Lighting Design by DIAlux.evo
Main Spaces | Minimum Recommended Illuminance Level (Lux) | Glare (UGR) | Uniformity
Classroom | 300 | 19 | 0.50
Meeting room | 500 | 19 | 0.40
Instructor’s office | 500 | 19 | 0.60
Canteen | 200 | 22 | 0.40
Computer room | 300 | 19 | 0.50
Main Spaces | Designed Illuminance Level (Lux) | Designed Glare (UGR) | Designed Uniformity
Classroom | 380 | 15.8 | 0.49
Meeting room | 512 | 17.9 | 0.47
Instructor’s office | 534 | 14.8 | 0.67
Canteen | 306 | 13.9 | 0.57
Computer room | 407 | 17.6 | 0.66
Design Results
Recommended Values

## Slide 76
Types of used luminaires in each space:
Space | Luminaire type | Manufacturer | Connected load (Watt)
Classroom | Recessed Directional light | Philips | 61 W 16 W
Meeting room | surface- mounted Recessed spot light | Schmitz-Leuchten Simon China | 47 W 7 W
Instructors office | Recessed | Philips | 23 W
Computer room | Recessed Directional light | Philips | 61 W 16 W
Canteen | Recessed | Philips | 33 W
Computer laboratory
Meeting room
Classroom room
Instructors office
Canteen

## Slide 77: Classroom Artificial Lighting Design
Classroom Simulation results from DIALux evo:
Luminaires layout

## Slide 78: Instructors Office Artificial Lighting Design
Instructors office Simulation results from DIALux evo:
Luminaires layout

## Slide 79
Canteen 3D View
Meeting room 3D View
Instructors office room 3D View

## Slide 80
Classroom 3D View
Computer room 3D View
Luminaires layout for Ground Floor

## Slide 81: Acoustical Design

## Slide 82: Acoustical Design
Spaces that were designed acoustically in the faculty:
Lecture room
2
Computer room
3
Instructors office
1
Meeting room
4

## Slide 83
Reverberation time ( RT60 )

## Slide 84: Classroom Acoustical Design
Optimum (RT60) for classroom ranges between (0.6-0.8) sec.
The absorption coefficients (α) for the finished materials at different frequencies:
Element |  | Finishing material | Frequency (Hz) |  |  |  |  |  |  | 
 |  |  | 63 | 125 | 250 | 500 | 1 K | 2 K | 4 K | 8 K
Walls | Plaster |  | 0.12 | 0.09 | 0.07 | 0.01 | 0.01 | 0.02 | 0.01 | 0.02
Floor | Terrazzo |  | 0.01 | 0.01 | 0.01 | 0.01 | 0.02 | 0.03 | 0.07 | 0.09
Ceiling | Acoustical tiles |  | 0.25 | 0.25 | 0.49 | 0.69 | 0.78 | 0.61 | 0.54 | 0.58
Window | Double glazing |  | 0.12 | 0.10 | 0.06 | 0.04 | 0.03 | 0.03 | 0.04 | 0.04
Seats | Wood |  | 0.08 | 0.08 | 0.14 | 0.12 | 0.19 | 0.18 | 0.17 | 0.20
Door | Plywood |  | 0.44 | 0.41 | 0.35 | 0.20 | 0.15 | 0.14 | 0.14 | 0.12
Lecture room RT60
Articulation loss

## Slide 85
Surface | Material
Ceiling | Acoustical Suspended Ceiling
Walls | Concrete Block Plaster
Floor | Thin carpet on concrete
Door | Hollow Core Plywood
Other wall | Fabric Acoustical Panel
Windows | Double glazed aluminum frame
Seats | Covered with leather
Finishing materials for the meeting room
Meeting room acoustical design
Meeting room RT60
Articulation loss

## Slide 86
RT60 for instructors office
RT60 optimum ranges (0.4-0.6 ) sec
RT60 results  OK
RT60 optimum ranges (0.6-0.8 ) sec
RT60 results  OK
RT60 optimum ranges (0.6-0.8 ) sec
RT60 results  OK
RT60 for meeting room
RT60 for computer room

## Slide 87
Sound Transmission Class (STC ) Design
Element | STC (dB)
Wall | STC 53 (dB)
Door | STC 44 (dB)
Composite STC | STC 50 (dB)
STC for classroom adjacent to corridor.

## Slide 88
Considered room | Adjacent space | STC Normal | STC Calculated
Meeting room | Corridor | STC 40 dB | 45
Meeting room | Classroom | STC 45 dB | 53
Meeting room | Outdoor | OITC 40 dB | 51
Considered room | Adjacent space | STC Normal | STC Calculated
Office | Corridor | STC 45 dB | 48
Office | Classroom | STC 45 dB | 50
Office | Outdoor | OITC 40 dB | 51
Office | Office | 50 STC dB | 53
Considered room | Adjacent space | STC Normal | STC Calculated
computer laboratory | Corridor | STC 45 dB | 50
computer laboratory | computer laboratory | STC 50 dB | 53
computer laboratory | Outdoor | OITC 50 dB | 53
Considered Room | Adjacent space | STC Normal | STC Calculated
Classroom | Corridor | STC 45 dB | 50
Classroom | Classroom | STC 50 dB | 53
Classroom | Outdoor | OITC 50 dB | 50
Classroom | Toilet and restroom areas | STC 53 dB | 53
Summary of designed STC for each designed space

## Slide 89
The OITC for the external walls = 65 dB more than the recommended = 50 dB, so the design of the external wall is ok
OITC of composite classroom’s external wall
Element | STC (dB)
Wall | STC 85 (dB)
Window | STC 55 (dB)
Composite STC | OITC 50(dB)

## Slide 90: Impact Insulation Class (IIC)
floor construction layers by using INSUL software.
The minimum IIC ratings for floor-ceiling assemblies above core learning spaces should be IIC-45. IIC value by using INSUL software is calculated to be 67 dB more than required value = 45 dB so, the design of the floor-ceiling layers is adequate.

## Slide 91: Electro-acoustics and Loud speakers design
Two types of loud speakers were used for designing the sound system of the faculty
Type | Space | Sensitivity dB | Coverage angle
PC-671R/RV | Corridor | 90 dB | 65▫
PL 8X | Lobby | 93 dB | 80▫
Loud speakers coverage area for the ground floor
Loud speakers distribution for the ground floor

## Slide 92: Heating, ventilation, and air conditions system design (HVAC)

## Slide 93
The system used for HVAC design is “ VRF system ” Variable refrigerant flow . Main components of VRF system are :
Out door unit (for cooling and heating).
Controller.
Fan coil unit.
Ducts.
Diffusers.

## Slide 94
results from Design Builder program:
Heating load capacity =155.52 KW
Cooling load capacity= 162.09 KW
Outdoor unit
From TOSHIBA
Fan coil Unit
From TOSHIBA

## Slide 95
Air distributing system (Diffuser)
From GRADA
From DAIKAIN
Cassette Unit
Controller

## Slide 96
HVAC system layout for fourth floor

## Slide 97: Branches and Circuit Breakers Design.

## Slide 98: Sockets Layout for Ground floor

## Slide 99: Sockets Layout for Fourth floor

## Slide 100: Main distribution board

## Slide 101: Water Supply System

## Slide 102
Water supply Plan for G.F

## Slide 103: Sewage and Drainage System

## Slide 104
Drainage system types:
Black water: which comes from urinals, W.C’s.
Gray water: which comes from kitchen sinks and lavatories.
Storm water: which comes from the rain.
Strom water drain layout for the faculty

## Slide 105
Drainage system layout for G.F
Storm water tank location

## Slide 106: Firefighting and Fire safety systems

## Slide 107: Firefighting and Protection systems used in the faculty
Fire extinguishers
Hose station
Sprinklers
Flame detector
Smoke sensors
Heat alarms
Fire break glass units

## Slide 108
distribution of used fire protection systems at the GF
Smoke and flame detectors distribution at the (GF) ground floor

## Slide 109
Fire break glass alarm distribution at the ground floor
    The Emergency Egress System (EES):
Emergency exist sign

## Slide 110
The locations of the emergency exits in the faculty

## Slide 111: Integration design

## Slide 112: Quantity Survey and Cost Estimation

## Slide 113: Summery of each work total cost
Type of work | Total cost of work (NIS)
Architectural work | 484,363.00
Structural work | 921,520.00
Finishing work | 1,845,939.00
Electro-Mechanical work | 1,016,768.00
Total project cost | 4,268,590
The estimated cost per unit area for the project is equal to 1,707.44 NIS/m2

## Slide 114: 3D Revit