## Slide 1
Prepared by
Ghada Salahat
Wejdan Hatim
Mena Omar

## Slide 2: Outline
Explain some technologies to improve 5G network.
Two-tier Architectures.
CRN Based Architectures.
D-D Communication Architectures.
Energy-Efficient Architectures.
5G is the combination between those Architectures.

## Slide 3: Motivations
The main motivation of going toward the fifth generation is to:
Support more than one hundred billion connections.
Increasing the capacity a thousand times.
Increasing the data rate up to 10Gbit/s speeds.
Make the latency less than 1ms.

## Slide 4: Review Of Project 1
Technology Evolution.
Challenges and Application Of 5G Network.
Communication Concepts.
MATLAB Simulation.

## Slide 5: 5G Enabling Technologies

## Slide 6: Why Millimeter Waves ?!
Frequency (30 GHz-300 GHz).
Wavelength (1-10 mm) .
f=c/λ
More bandwidth is available
Higher data rate
Security and privacy is better at mm waves.

## Slide 7: Why Small cells ?!
Small form factor (<6 ft3 )
“ Plug ’ n ‘ Play “
Operation
Low power output
( < 2 W )
Targeted coverage area
( < 10,000 ft2 )
Limited capacity
( < 128 users )
Low power consumption
( < 30 W )

## Slide 8: Why we need small cells ??
More mobile users, devices, data required, more capacity and coverage.
Increasing towers, allocate more spectrum, and use new technology are not enough.
Solutions is small cells
Adding more low power antennas in the field with lower footprint (coverage).
Similar to adding more towers idea
but with less power consumption, less users,
less interference.
Results : cheaper and more efficient network.

## Slide 9
Essentially multi user MIMO with lots of base station antennas.
A very large antenna array at each BS.
A large number of users are serves simultaneously.
Massive (very large).
Large transmitters/receivers.
High data rate, reduces latency, link reliability.
Equipment price increased, increases the capacity due to spatial multiplexing.
Why Massive MIMO ?!

## Slide 10: Why Beamforming ?!
Focusing the transmitted energy into a specific direction.
Increase energy to a specific user.
Reduce interference.
Beamforming in 5G

## Slide 11: Why Full duplex ?!
Single channel for transmitting and receiving signals at identical time and frequency
Increases link capacity, saves the spectrum, and cost.
Full duplex radio receives signals from another radio and receives interference signals by its own transmission, resulting in self-interference.
Full duplex radio has to implement techniques to cancel self-interference (SIC techniques).

## Slide 12: Architectures for the future 5G
Proposed Architectures for 5G:
Tow-tire Architecture .
Cognitive Radio Network based Architectures .
Device-to-Device Communication Architectures .
Energy-Efficient Architectures for 5G Networks .

## Slide 13: 5G network Architecture

## Slide 14: Tow-tier Architecture
The basic idea of two-tier architecture

## Slide 15: Cognitive Radio Network based Architectures
The basic idea of cognitive radio network

## Slide 16: Device-to-Device Communication Architectures
DR-OC
DC-OC
DC-DC
DR-DC
Four types to perform D2D communication

## Slide 17: Energy-Efficient Architectures
How to save energy ?
User centric 5G Network
Decoupling of signaling and data
UE connected to SBS
Energy harvesting device
Interference Management

## Slide 18: 5G network Architecture

## Slide 19: Matlab Simulation “MIMO 8X8”

## Slide 20: Matlab Simulation “MIMO 16X16”