## Slide 1
The Thermo Furnace:
Design, Build and Validation
An-Najah National University
Mechanical Engineering Department
Supervisor: Dr. Iyad Assaf
Graduation Project (2)
Prepared by:
Ali Jaber
Mahmoud Abu Alrob
Obaid Atieh
Sanad Obaid

## Slide 2: Objective:
To design and fabricate frame for the gas furnace .
Use the best insulating materials .
Use the best refractory materials .
Use burning system of the gas furnace to melt aluminum and copper .

## Slide 3: Component of furnace

## Slide 4
Basement of furnace
Steel [80*40*2.2]mm
Wheels [4 wheels with stopper ]
Body of furnace:
Consist of steel with thickness 3mm
Door of furnace:
Supportive
Bearing
Dampers
Jacks [for easily moving the door]
Handles for doors and casting process
Component of furnace

## Slide 5
Inner shell
Consist of cement fire , fire brick , rock wall and crucible
Gate channel for casting
Chimney
Burner gap
Insulation material between door and body

## Slide 6
Material required for insulation
Fire brick:
The dimension of a firebrick is (230*110*75) mm.
Thermal conductivity [K= 0.98 W/m.K ]
Brick type | Percentage SiO2 | Percentage Al2O3 | Percentage other constituents | melting point PCE oC
Super Duty | 49-53 | 40-44 | 5-7 | 1745-1760
High Duty | 50-80 | 35-40 | 5-9 | 1690-1745
Intermediate | 60-70 | 26-36 | 5-9 | 1640-1680
High Duty (Siliceous) | 65-80 | 18-30 | 3-8 | 1620-1680
Low Duty | 60-70 | 23-33 | 6-10 | 1520-1595

## Slide 7
Material required for insulation
Cement fire:
The Thermal conductivity [K= 0.98 W/m.K ] it is have the same properties of fire brick.
The type of it is [DURER, monolithics (GUNDUR 750)]
the thickness of cement fire is 15mm

## Slide 8
Material required for insulation
Rock wool :
The Thermal conductivity [K= 0.045 W/m.K ].
the thickness of Rock wool is 20mm

## Slide 9: Basic performance requirements of the furnace structure:
In its simplest form a furnace consists of a casing with a heat source, usually a flame to provide the process energy. Where flames are employed the heating may be direct using radiation from the flame.

## Slide 10: Design & calculation

## Slide 11
Cp for aluminum = 0.91kj/kg.k
Cp for copper = 0.39 kj/kg.k
The melting point for AL = 660 C`.
The melting point for Cu = 1084 C `.
The properties of melting metal and insulation material
Firebrick & Cement fire K =0.98 [W/m.K].
Rock wool K = 0.045 [w/m.K].
Steel K = 50 [W/m.K].
The specific latent heat of fusion of a substance is:
the amount of heat required to convert unit mass of the solid into the liquid without a change in temperature.
Aluminum | 321
Copper | 176
(kJ/kg)
(kJ/kg)

## Slide 12
Q=qs+ql
= 985 kJ for 1 kg Al.
= 0.7984 kw → 0.8 kw.
Ql=F*m
=321*(1)
=321 KJ
The total heat = sensible and latent heat:
Qs=m*cp*ΔT
=1*0.91*700
=637 kJ

## Slide 13
Using Fourier law for conduction heat transfer of cylinder, the equation is given by :
Rt = 0.875 k/w.

## Slide 14
the thicknesses of insulation material are:
ri = 0.205 m, r2 = 0.22, r3= 0.295 m, r5 =0.32m,
and r4 = 0.317m.
From this calculation the thickness of rock wool is 0.022m.

## Slide 15
It’s known the heating value for each:
Heat value for Liquefied Petroleum gas = 46044 KJ/Kg.
Heat value for diesel = 44800 KJ/Kg.
Why Petroleum gas used in the project

## Slide 16
[C + H (fuel)] + [O2 + N2 (Air)] -> (Combustion Process) -> [CO2 + H2O + N2 (Heat)]
CH4+ 2O2+ 7.52N2→CO2+ 2H2O + 7.52N2
Burning of methane mixture in air
CH4 + 1.25 x 2(O2 + 3.76 N2) -> CO2 + 2H2O + 0.5O2 + 9.4N2
chemical equation for methane burned with 25% excess air can be expressed as
Molar A/F = 2*4.76/1 = 9.52
Mass A/F = 2*4.76*28.97/16 = 17.24

## Slide 17
Thermocouple
The type of thermocouple used to measure the amount of temperature inside the furnace TYPE [J]
The thermo couple used with voltmeter to measure the temperature from relationship between temp. and mV.

## Slide 19
Procedure
First step:
During this step, the outer structure frames such as the furnace base, supports wheels and the refractory outside wall which are made of steel . The refractory outside wall is fixed with the frame supports by bearings so that it can be rotates form the vertical position to approximately 180o to allow pouring the melting metal in the tundish from the furnace door that located at the top of the refractory. The base and the supports are assembled by welding.

## Slide 20
Second step:
In this step a hole was made in the refractory outside wall of furnace opposite to the casting process for installing the burner, which will be the source of heat for melting the metal . In addition, the furnace door fixed at the top of the furnace so that the door can rotates 90o.

## Slide 21
Third Step:
After assembled the supports with the furnace base and open the hole burner hole the refractory outside wall was assembled with the frame using a rotator Sticky structure of furnace by adding bearing joint that mounted on the rack for allowing the furnace for rotation during the casting process .

## Slide 22
Fourth step:
After assembled the structure of furnace, the isolated stages such as the rock wool and the fiber brick are added inside the refractory inside room. The main objective of using these types of insulation to reduce heat losses as possible during casting process. During this step the rock wool is placed first on the floor of furnace and on the inside walls of furnace .

## Slide 23
Fifth step:
The firebricks was added in the bottom of furnace and on the inside wall in an appropriate manner, and it is installed to maintain the desired shape- circular shape-. After that the firebricks were cohesion together using fire cement. This type of fire cement (clay) is also used to fill the gaps between the firebricks. In addition, metal rods are used to keep the fire bricks in their positions during this processes and they are removed after the clay was dried . After that, a layer of clay was added to the firebrick inside surface as a plaster to form an extra layer of insulation and to maintain the of the firebrick in cohesion.

## Slide 24
Sixth step:
During this step, the furnace door was manufacturing. This include the door joints for allowing the door to open and close. In addition, the door handles were welded to the door cover for easy use . Moreover, supportive was welded to connect the cover door with the top surface of the furnace in order to open the door to approximately 90o. To keep the door cover closing during the melting metal (operation process), a stabilizers were added so that one end is fixed with the door cover and the other end was fixed with the furnace wall to keep the door cover closing

## Slide 25
Seventh step:
The gate channel was built up during this stage for pouring the melting metal from the crucible into the tundish. The gate channel be isolated by firebrick and clay . The gate was located at the top of the refractory structure.

## Slide 26
Conclusion and recommendation
The recommendation points is :
1-Add motor to facilitate rotation of the furnace structure to carry out the casting.
2-Production line can be designed for complete casting process, such as solidification
stage, cutting process metal working and shaping.
3-Automated control casting process can be design.
The conclusion points is:
1-Furnace capable of melting two types of metals
2- After we turn on the furnace the temperature inside is 1100 and did not heat up the outer surface of the furnace and this shows the effectiveness of the insulating material
3- Can melt large amounts inside the furnace up to 40 kg

## Slide 27: THANK YOU... .
Any Question ?