## Slide 1: Developing a Catalytic Pyrolysis Of Scrap Tires

## Slide 2: Introduction
Since, the early days of tire usage and the disposal of scrap tires has been a major problem worldwide.
In West bank, Palestine there are 390 thousand of scrap tires.
Therefore thousands of tires are at junkyard
One of the ways to disposal the waste tires is to burn them
land filling, grinding and reclaiming are another ways of disposal the waste tires

## Slide 3: Introduction
pyrolysis is chemically decomposing of organic materials in absence of oxygen at elevated temperature.
The products of pyrolysis of waste tires are gas, pyrolytic oil and char
Catalyst is a substance which is added to the reaction in order to increase the rate of the reaction and to enhance the products obtained from the reaction
very small amount of catalyst is required to alert the reaction because it is not consumed in the reaction and could act repeatedly.

## Slide 4: Literature review

## Slide 5: Non Catalytic Pyrolysis of Waste Tiers

## Slide 6: Wójtowicz, M.A. and M.A. Serio. (1996)

## Slide 7: Fernández, A. and C. Barriocanal, et al. (2012)
Chart: Presence of products
| Gas | Liquid | Char
Sales | 0.22 | 0.303 | 0.477
Pyrolysis for ﬁbres with Batch reactor, 350°c temperature and Atmospheric pressure.

## Slide 8: Catalytic Pyrolysis of Waste Tiers

## Slide 9: Shah, J. and M. Rasul, et al. (2008)
pyrolysis for waste tires with Catalysts MgO and CaCO3.With Batch reactor, 350°c temperature,2 hour duration and Atmospheric pressure.
Chart: 
| Gas presence | Liquid presence | Char presence
MgO | 0.244 | 0.398 | 0.358
Chart: CaCO3
| Gas presence | Liquid presence | Char presence
CaCO3 | 0.325 | 0.322 | 0.352

## Slide 10
Shah, J. and M. Jan, et al. (2009)
pyrolysis for waste tires with Catalysts Al2O3 , SiO2 and Al2O3 + SiO2 .With Batch reactor, 400°c and Atmospheric pressure.
Chart: Catalysts results
| Al2O3 | SiO2 | Al2O3 + SiO2
Gas presence | 0.2093 | 0.1546 | 0.05
oil presence | 0.232 | 0.282 | 0.148
solid presence | 0.5567 | 0.5626 | 0.8013

## Slide 11
Shameem Hossain, M., et al. (2017)
pyrolysis for waste CT(catalyst tiers ratio) with Catalysts ZSM-5 and zeolite.at 300°-600°c temperature.

## Slide 12
CT ratio 0.15
CT ratio 0.1
The results
The results

## Slide 13: Catalytic Processes

## Slide 14
Elbaba, I.F. and P.T. Williams. (2010)
A two-stage pyrolysis-gasification fixed bed reactor for waste tiers . With Catalysts Ni−Mg−Al. at a pyrolysis temperature of 500°C and gasification temperature of 800°C.
Increase in H2 and CO concentrations and decrease in CH4 and C2-C4 concentrations when the Ni-Mg-Al catalyst was added.

## Slide 15: Experimental Setup

## Slide 16: Front View of Setup

## Slide 17: Fixed-Bed Reactor

## Slide 18: Cooling System

## Slide 19: Methodology

## Slide 20: Study Methodology
Task #1 To conduct a comprehensive literatures reviews
Task #2 To synthesize the catalyst
Task #3 To examine the effect of catalysts’ holders
Task#4 To design an experimental setup

## Slide 21: Conclusion

## Slide 22: Conclusion
literature reviews published
Information about environmental problems
pyrolysis process was chosen to take place in the recycling process due to its big advantages
enhance and modify pyrolysis process
experimental setup was designed

## Slide 23: Thank You