## Slide 1
An-Najah National University
Engineering college
Building Engineering Department
Health Center
Prepared by:
Sobhi Ibrahim
Islam Ammar
Mohammad Odeh
Supervisor: Eng. Abdelhakim W. Al jawhari

## Slide 2
Structural Design
3
Mechanical Design And Safety system
Overview
Introduction
Architectural Design
Electrical Design
1-
2-
3-
4-
5-
6-
7-
Environmental Design
Quantity Surveying and Cost Estimation

## Slide 3
Introduction
1
There is an urgent need to improve the medical and health services provided to people and to make it as efficient and as near as possible to people’s living areas. Given the difficulties in the treatment especially in peak hours and the need to submit the treatment urgently, there is a need to establish health clinics or centers or even hospitals, with fair and correct distribution to cover almost all areas. A health center will help to solve this especially if it is designed to cover different medical services and if equipped by all required in addition to the human resource.

## Slide 4
Site Location
Area of building =2000 m2
area of site = 4350 m2

## Slide 5
Architectural Design
2

## Slide 6
Rating health clinics, according to the Palestinian Ministry of Health :-
The first level: to submit various health services for the agglomeration with a population of less than 2000 people
The second Level: to submit various health services for the agglomeration with a population from 2001-6000 people
The third Level: Level: to submit various health services for the agglomeration with a population from 6001-12000 people
The fourth level: Level: to submit various health services for the agglomeration with a population more than 12000 people
Architectural Design
2

## Slide 7
General description of the project
Reception area
Medical service (PHC)
laboratory
X-ray department
Support service
Medical service(MCH)
General management
Medical management
Environmental
Architectural Design
2
Notes: multipurpose hall it consists of several different elements and services cater to the public and the players, referees, supervisors and senior visitors and journalists.

## Slide 8
Spaces | Area(m2 )
Reception area | 60
Medical service (PHC) | 179
Laboratory | 44
X-ray department | 64
Support service | 44
Medial service(MCH) | 86
General management | 147
Medical management | 112
Environmental | 106
Recommendation Spaces :

## Slide 9
834m2 | Space total area
333m2 | Circulation and walls and stair 40%
83m2 | Contingency 10%
1250-1500 m2 | TOTAL AREA

## Slide 10
Ground Floor

## Slide 11
First Floor

## Slide 12
Second Floor

## Slide 13
North ELE.

## Slide 14
South ELE.

## Slide 15
West ELE.

## Slide 16
East ELE.

## Slide 19
Structural Design
3

## Slide 20
Structural Design
3

## Slide 21
Structural Design
3
One way ribbed slab with drop beams
Slab thickness =20cm
Loads Used:-
Dead load (superimposed) = 3.5 KN/𝑚2
Live load = 4 KN/𝑚2

## Slide 22
Main beam dimension (30*50)cm
Secondary beam dimension (50*20)cm

## Slide 23
Column dimension(30*60) (40*40)cm
Footing design
Single footing

## Slide 24
Shear Wall and Footing Reinforcement:

## Slide 25
3D Structural
3
block1
block2

## Slide 26
Deformed Shape For Block 2

## Slide 27
Equilibrium Check:
A ) Live load = are of floor *No. of floor *L.L
area of floors = 1240 m2
Live Load=4KN*1240=4960KN
B) Dead load
Slab (O.W)= (1240*.149*25)=4619KN
Beam weight=2340KN
(Columns +shear wall )weight = 3866KN
Total D.L=4619+2340+3866=10805KN
C) Super imposed= (3.5*1240)
= 4340KN

## Slide 28
D.L % error = (manual calculation – sap calculation / manual calculation)
= (10805 – 10235 / 10805)
= 5 % …. Ok
L.L % error = (manual calculation – sap calculation / manual calculation)
= (4960– 4717 / 4960)
= 4.1 % …. Ok
S.I.D % error= (manual calculation – sap calculation / manual calculation)
= (4340 – 4128 / 4340)
= 4.8 % …. Ok

## Slide 29
Internal Forces Checks:
Slab: We take the average moment from SAP and compare it with manual value.
Average moment (M) =4+4.5/2+14.5=18.75KN.M
Manual moment M = wu*L^2 / 8=14.9*3.3^2/8
=20KM.M
Moment % error = (manual calculation – sap calculation / manual calculation)
= (20 – 18.75) / 20 = 6.2% OK

## Slide 30
4
Environmental Design
44KW/m2
Heating and Cooling Load

## Slide 31
Daylight Factor
3.37%

## Slide 32
4.9%

## Slide 33
Acoustical Design:-
The range of the Reverberation time 0.6< RT60 < 1.4
RT60 = 1.18 second.
%Alcons = 10 is acceptable

## Slide 34
STC calculations :-
Room to adjacent room STC=52dB
Room to corridor STC=42.2 dB
Room to outside STC=41.1dB
ICC = 50dB

## Slide 35
Insulations Material
Materials like Foam, rubber and polystyrene, Fiberglass
.
Polystyrene layers
Lead sheet

## Slide 36
Medical waste management :-
Proper disposal of waste :-
All infectious waste and sharps containers :Incineration
All Domestic waste : Landfill
All hazardous waste : Chemical treatment before disposal

## Slide 37
5
Mechanical Design And Safety system :-
Heating and cooling systems:-
Split unit

## Slide 38
Water Supply System :-

## Slide 40
Drainage System:-

## Slide 41
Rain water Drainage :-

## Slide 42
Safety system:-
Fire extinguishers
Smoke Detectors
Fire House Cabinet

## Slide 45
Fire system alarm layout :-

## Slide 46
6
Electrical Design

## Slide 47
3 luminaries are need for offices
The uniformity > 50% it's ok

## Slide 48
In Office room used Philips lamp

## Slide 49
Quantity Surveying and Cost Estimation
7
The total price for the health center is 3.808422 million shekel.
The price for m2 for the concrete structure 1904.22NIS/m2

## Slide 50
Thank You