## Slide 1
Design of Directorate of Education In Nablus
Building Engineering Department
Graduation project II
Supervisor:
Dr. Moyad Salhab.
Students:
Mohamed Saqf Al-Heat Murad Mohamed Hasan Deaa Namrouti

## Slide 2: Contents:
Architectural Aspects
Structural Aspect
Environmental Aspect
Quantity surveying & Cost Estimate

## Slide 3: Contents:
Architectural Aspects
Structural Aspect
Environmental Aspect
Quantity surveying & Cost Estimate

## Slide 4: Architectural Aspects
Architectural Aspects
Architectural standards
Site analysis
Architectural modifications

## Slide 5: Architectural standards
Architectural Aspects
Architectural standards
Site analysis
Architectural modifications

## Slide 6: Architectural standards:
local requirements
based on the requirements of the Palestinian Directorate of Education
Ttypes of rooms required
number of people assigned to each room
International standards
taken from the-Metric-Handbook-Architecture.
Minimum requirement space

## Slide 7: Site analysis
Architectural Aspects
Architectural standards
Site analysis
Architectural modifications
Project Site
Entrances

## Slide 8: Site analysis
Architectural Aspects
Architectural standards
Site analysis
Architectural modifications
Project Site
Entrances

## Slide 9
Project Site:
The project is located in Nablus next to the old Directorate building on Faisal Street on the south side and Rawda Street on the east side

## Slide 10: Site analysis
Architectural Aspects
Architectural standards
Site analysis
Architectural modifications
Project Site
Entrances

## Slide 11
Entrances to the project:
The project site has three entrances and the building itself has three entrances and two emergency exits,

## Slide 12: Architectural modifications
Architectural Aspects
Architectural standards
Site analysis
Architectural modifications
Before and After
Substantial modifications

## Slide 13: Architectural modifications
Architectural Aspects
Architectural standards
Site analysis
Architectural modifications
Before and After
Substantial modifications

## Slide 14: Substantial modifications:
Selection of the project site:
The previous site for the project
The new site for the project

## Slide 15: Substantial modifications:
Add a new floor:
The previous proposal |  | 
Floor number | Floor name | Floor area (m2)
1 | ground floor | 932
2 | first floor | 1122
3 | second floor | 1145
4 | Third Floor | 590
5 | fourth floor | 302
 | total area | 4091
The new proposal |  | 
Floor number | Floor name | Floor area (m2)
1 | Basement | 1180
2 | ground floor | 964
3 | first floor | 1122
4 | second floor | 1145
5 | Third Floor | 590
6 | fourth floor | 352
 | total area | 5353

## Slide 16: Substantial modifications:
Add car parking:
Internal car parking
External car parking
consists of 36 cars
consists of 20 cars

## Slide 17: Substantial modifications:
Add environmental systems:
Sheading systems
Ventilation systems

## Slide 18: Substantial modifications:
Add emergency stairs:
Emergency stairs
Emergency stairs 2
Emergency stairs 1

## Slide 19: Architectural modifications
Architectural Aspects
Architectural standards
Site analysis
Architectural modifications
Before and After
Substantial modifications:

## Slide 20: Architectural modifications
Architectural Aspects
Architectural standards
Site analysis
Architectural modifications
Before and After
Outside
Inside
Substantial modifications:

## Slide 21: Architectural modifications
Architectural Aspects
Architectural standards
Site analysis
Architectural modifications
Before and After
Outside
Inside
Substantial modifications:

## Slide 22: The project before modification(Outside)

## Slide 23: The project after modification (Outside)

## Slide 24: The project after modification (Outside)

## Slide 25: Architectural modifications
Architectural Aspects
Architectural standards
Site analysis
Architectural modifications
Before and After
Outside
Inside
Substantial modifications:

## Slide 26: The project before modification (Inside)
The project after modification (Inside)
The project before modification (Inside)

## Slide 27
The project after modification (Inside)

## Slide 28
The project after modification (Inside)

## Slide 29: Contents:
Architectural Aspects
Structural Aspect
Environmental Aspect
Quantity surveying & Cost Estimate

## Slide 30: Contents:
Architectural Aspects
Structural Aspect
Environmental Aspect
Quantity surveying & Cost Estimate

## Slide 31: Structural Aspects
Materials
Concrete with compressive strength of 28 MPa (B350)
And Concrete with compressive strength of 40 MPa(B500)
Code
The parameters for seismic analysis
Loads
ACI 318-14
AISC360-10 for steel analysis
Seismic design UBC 97
ASCE for load design
Mass source: 100% for dead loads and SID , 25% for live loads
Seismic zone : The directorate is located in Nablus city Therefore, the seismic zone is 2B and the Z value is equal to 0.20.
Soil profile: The soil type is clay so the soil profile is SE .
Force Reduction Factor R = 5.5 (Building Frame System - shear wall)
Importance Factor I = 1
Acceleration-Dependent Seismic Coefficient Ca = 0.34
Velocity-Dependent Seismic Coefficient Cv = 0.64
Response spectrum scale factor = = = 1783
Response spectrum scale factor = (𝐼×𝑔)/𝑅 = (1∗9810)/5.5 = 1783
Live load = 3 kN/m2
SID load = 4 kN/m2
Materials
Concrete with compressive strength of 28 MPa (B350)
And Concrete with compressive strength of 40 MPa(B500)
Code
Loads
ACI 318-14
AISC360-10 for steel analysis
Seismic design UBC 97
ASCE for load design
Live load = 3 kN/m2
SID load = 4 kN/m2

## Slide 32: Ground and First floors
First Floor
Ground Floor

## Slide 33
Models for design
safe models for basement mat
safe models for Ground mat
sap model for dome steel
Etab model for concrete structure

## Slide 34
Seismic design checks
story | height | Dis X | Dis Y | Drift X(ΔS) | Drift Y(ΔS) | Delta x(ΔM) | Delta y(ΔM) | limit
 | mm | mm | mm | mm | mm | mm | mm | mm
0 |  | 0 | 0 | 0 | 0 | 0 | 0 | 80
1 | 4 | 8.8 | 9.5 | 8.8 | 9.5 | 6.16 | 6.65 | 80
2 | 4 | 18.5 | 19.3 | 9.7 | 9.8 | 6.79 | 6.86 | 80
3 | 4 | 29 | 31 | 10.5 | 11.7 | 7.35 | 8.19 | 80
4 | 4 | 42.8 | 42.7 | 13.8 | 11.7 | 9.66 | 8.19 | 80
5 | 4 | 62 | 49 | 19.2 | 6.3 | 13.44 | 4.41 | 80
Drift check
Load Case/Combo | Etab calculation |  | manual calclation | 
 | FX | FY | FX | FY
 | kN | kN | kN | kN
EQx Max | 15956.4 | 2630.21 | 16222.83 | 16222.83
EQy Max | 3221.01 | 15986 | 16222.83 | 16222.83
base shear check
Time period from mode 1 = 0.74 sec < 0.74 sec, the check is ok.
Time period from mode 2 = 0.688 sec < 0.74 sec, the check is ok.
Time period check
Model mass participating check
The sum of ux =0.92, uy=0.95 large then 0.9

## Slide 35
Beam section and mat section

## Slide 36
section using in design

## Slide 37: Contents:
Architectural Aspects
Structural Aspect
Environmental Aspect
Quantity surveying & Cost Estimate

## Slide 38: Contents:
Architectural Aspects
Structural Aspect
Environmental Aspect
Quantity surveying & Cost Estimate

## Slide 39
Environmental Aspect
Before
after
Main modifications using after editing
1-changing the window shape.
2-adding lovers
3-changing the Court center of building to court siphonage

## Slide 40: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 41: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 42
Checking and validation
Day lighting
Thermal
Ventilation analysis

## Slide 43
Checking and validation
Day lighting
Thermal
Ventilation analysis

## Slide 44
Day lighting
Day lighting for second floor

## Slide 45
Checking and validation
Day lighting
Thermal
Ventilation analysis

## Slide 46
Thermal design

## Slide 47
The comfort graph for the Directorate from Design Builder

## Slide 48
Temperature and heat loss
Total site and source energy

## Slide 49
Checking and validation
Day lighting
Thermal
Ventilation analysis

## Slide 50
Direction of wind
Section of Court siphonage
Ventilation analysis

## Slide 51
Checking the ventilation in Court

## Slide 52: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 53: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 54: Environmental Aspect
Inside
Outside
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 55
Inside the building :
The selected luminaires
Philips sqr- 1
Philips sqr- 2
Bright spot 1
Bright spot 2
Bright spot 3
Bright spot 4
Proled wall light
Cove light linear led
Zumtobel wall light
Bright ring 1
Bright ring 2
Philips ceiling rec.
Bright linear led

## Slide 56
Lighting with switches

## Slide 57
Illuminance result from DIALUXevo for the security room
Ground floor

## Slide 58
Result from DIALUX evo for dimming 80%.
Ground floor
Double volume
Room 3
Drivers room
Reception
WC corridor
Stair
Result from DIALUX evo form artificial only

## Slide 59
Outside the building :
The selected luminaires
bright side wall outside 2
bright side wall outside 3
bright side wall outside 1
bright floor outside
Philips outdoor roof

## Slide 60
Outside the building :
3D views

## Slide 61: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 62: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 63
Sockets plan for the Supply sections
Ground floor

## Slide 64
Ground floor
The electrical load of power and lighting system in the ground floor
Distribution of circuit breaker in DB1
Main distribution board of circuit breaker in the ground floor

## Slide 65
The electrical load of power and lighting in the MDB building
The electrical load of elevators and HVAC system in MDB HVAC and elevators

## Slide 66
Specification for Generator and UPS

## Slide 67: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 68: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 69
The spaces that were designed acoustically in the building
1- Director private room
2- Small offices
3- Large offices
4- Meeting room
The absorption coefficient for the finished material in offices
Acoustical design
The absorption coefficient for the finished material in meeting room

## Slide 70
Reverberation time(RT60):
The reverberation time for the director room according to Sabine
The reverberation time for the large offices according to Sabine

## Slide 71
Sound Transmission Loss (STC)
The sound transmission loss (STC) for the internal walls between different spaces
The sound transmission loss (STC) for the internal walls between different spaces in the faculty is more than the limit = 45 dB

## Slide 72
Sound Transmission Loss (STC)
The OITC for the external walls = 54dB more than the standard = 37 dB, so it is ok for the external walls
The OITC for the external

## Slide 73
Impact Insulation Class (IIC)
The IIC = 66 dB between 60dB and 70 dB , so it’s excellent.
The layers for the ceiling

## Slide 74
Loud speaker for meeting room
Sound pressure level (SPL) :
The direct SPL is between 75 dB and 85 dB , so it’s ok
Articulation loss % :
The maximum AL% in the room = 3.81% and the minimum value of AL% = 1.63 % , so its excellent .

## Slide 75
Noise Level
Loud speaker for meeting room
The recommended noise level for high conference meeting room = 35 dB
Speech transmission index (STI) :
The minimum STI = 0.7 and the maximum STI = 0.86 , so it’s excellent .

## Slide 76: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 77: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 78
The symbols of the suppression system in the plans
Fire alarm and Firefighting systems
The symbols for the detection and notification system.
The emergency lights and signs
Part of firefighting plan for the ground floor
Part of firefighting plan for the fourth floor

## Slide 79
The different types of sprinkler in the building
The different types of the extinguisher
manual alarm fire system
heat detector
Ultraviolet flame detector
smoke detector
extinguisher Shape
emergency lighting
exit sign
standpipe in site
hose station
Flood sprinkler

## Slide 80
Drop panel for the double volume
FM200 system
Wet chemical sprinkler

## Slide 81
The evacuation plan for the second floor

## Slide 82
Reflected false ceiling for second floor

## Slide 83: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 84: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 85
Vertical and horizontal transportation

## Slide 86: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical transportation
HVAC design
Water supply
Drainage

## Slide 87
Why VRF(Cassette unit):
1. Ultimate Flexibility, Multi-Port Change-Over Boxes Multiply the Options.
2. Precise Solutions, More Outdoor Units for Right-Sized Systems.
3. Efficient Performance, the Cost-Effective, Energy-Efficient Choice.
4. Absolute Control, Choose from Several Control Options.
HVAC system design for heating and cooling

## Slide 88
Selecting the system components:
Four machines, three of which are 16 tons, and one of which is 12 tons, are placed on the roof of the building, were selected to meet the project's need of 57 tons
HVAC system design for heating and cooling
Outdoor Units:
*system components selected from the YORK ® Company

## Slide 89
Selecting the system components:
HVAC system design for heating and cooling
Indoor Units:4-way Cassette unit
*system components selected from the YORK ® Company
Change-Over Boxes

## Slide 90
Second floor (HVAC system)

## Slide 91: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
HVAC design
Water supply
Drainage
Vertical and horizontal transportation

## Slide 92
The System used:
Water supply system:
*Roof tanks is a plastic tanks from ROYAL company.
** basement tank is a square RC tank.
The best system that can meet the requirements is basement tank and roof tank and pump.
Roof tanks*: Three tanks with a capacity of 5000 liters for each tank so the total capacity on roof will be 15 cubic meters.
basement tank**: The location of the tank in the basement floor and the size of this tank depends on the rate of water consumption is 100 cubic meters

## Slide 93
The System used:
Water supply system:
basement tank

## Slide 94: Environmental Aspect
Environmental Aspect
Checking and validation
Artificial lighting design
Power design
Acoustical design
Fire alarm and Firefighting systems
Vertical and horizontal transportation
HVAC design
Water supply
Drainage

## Slide 95
Group A:
Drainage system:

## Slide 96
Group B:
Drainage system:

## Slide 97: Contents:
Architectural Aspects
Structural Aspect
Environmental Aspect
Quantity surveying & Cost Estimate

## Slide 98: Contents:
Architectural Aspects
Structural Aspect
Environmental Aspect
Quantity surveying & Cost Estimate

## Slide 99
Quantity surveying & Cost Estimate
The total cost of the building is 8693828 NIS and the total area of the building is 5353m2 ,which means that the total unit cost per m2 is 1625 NIS/m2.
Earth work = 529000 NIS
Foundation Work = 758246 NIS
Retaining Wall = 164260 NIS
Super Structure = 2216368 NIS
Finishes Work = 2495552 NIS
Electrical work = 512065 NIS
Safety work = 139920 NIS
Mechanical work = 1511650 NIS
Site Work = 365267 NIS

## Slide 100
Chart: Percentage for each work from total cost of the building
| Earth work | Foundation Work | Retaining Wall | Super Structure | Finishes Work | Electrical work | Safety work | Mechanical work | Site Work
Sales | 529000 | 758246 | 164260 | 2216368 | 2495552 | 512065 | 139920 | 1511650 | 365267

## Slide 101
Thanks for listening