## Slide 1
An-Najah National University
Faculty of Engineering & Information Technology
Graduation Project - II
Nablus Public Library
Group Members
Ahmad Asfour
AlGhalee Shihab
Islam Bishawi
Yasmeen Najjar
Supervisor
Dr. Ahmad Haj Saleh

## Slide 2: TABLE OF CONTENTS 02 03 05 06 Enviromental Aspects 01 Quantity Survaying and Cost Estimation Introduction Structural Aspects 04 Architectural Aspects Eloctro-Mechanical Aspects

## Slide 3: Introduction
Project Description
Methodology
Project Location
Nablus Public Library

## Slide 4: Introduction – Project Description
In this graduation project, a public library consisting of Four floors with a total area of 1424 square meters was analyzed and re-designed.

## Slide 5: Introduction – Site Location
The proposed architectural site for the project has been changed from Al-Basateen Street to Al-Maajin area, so that it is farther from the Nablus Municipal Library with a total distance of 1.85 km distance from the city center.

## Slide 6: Introduction - Methodology

## Slide 7: Architectural Aspects
Site Analysis
Architectural Plans
Rendered Shots

## Slide 8: Site Analysis – Environmental Effect
Wind Direction
Noise Sources
Sun Path

## Slide 9: Architectural Aspects – Architectural Modifications
Adding Basement:
Mechanical Room.
Book Repairing Room.
Praying Room.
Cleaning Room.

## Slide 10: Architectural Aspects – Architectural Modifications (Cont’d)
2. Ground Floor Modifications
Before Modifications
After Modifications

## Slide 11: Architectural Aspects – Architectural Modifications (Cont’d)
2. First Floor Modifications
Before Modifications
After Modifications

## Slide 12: Architectural Aspects – Architectural Modifications (Cont’d)
Before Modifications
After Modifications
3. Second Floor Modifications

## Slide 13: Architectural Aspects – Architectural Modifications (Cont’d)
4. Site Plan

## Slide 14: Architectural Aspects – Elevations
North Elevation
South Elevation

## Slide 15: Architectural Aspects – Elevations
East Elevation
South Elevation
West Elevation

## Slide 16: Architectural Aspects – Sections

## Slide 17: Architectural Aspects – Rendered Views

## Slide 18: Environmental Aspects
Design Builder Simulation and Results
Daylight Factor Analysis
Shading System

## Slide 19: Environmental Aspects– Daylight Factor
Modifications
Opening was added to the stair case in the southern elevation.
Louvers were added each 50cm horizontally and vertically on the northern elevation because it has the largest area of glazing.
Stone frames acting as a cantilever to prevent glare.

## Slide 20: Environmental Aspects– Daylight Factor
Daylight Factor Analysis Ground Floor Plans
Before Modifications
After Modifications

## Slide 21: Environmental Aspects– Daylight Factor
Daylight Factor Analysis First Floor Plans
After Modifications
Before Modifications

## Slide 22: Environmental Aspects– Daylight Factor
Daylight Factor Analysis Second Floor Plans
Before Modifications
After Modifications

## Slide 23: Environmental Aspects – Shading Analysis
Shading in summer
At 8:00 am
At 2:00 pm
At 12:00 pm

## Slide 24: Environmental Aspects – Shading Analysis
Shading in Winter
At 8:00 am
At 3:00 pm
At 12:00 pm

## Slide 25: Environmental Aspects– Design Builder Analysis and Results
Wall Section
Wall U-Value
Design Builder Simulation Analysis

## Slide 26: Environmental Aspects– Design Builder Analysis and Results
Roof Section
Roof U-Value

## Slide 27: Environmental Aspects– Design Builder Analysis and Results
Window Definition
Glass U-Value
Window Section

## Slide 28: Environmental Aspects– Design Builder Analysis and Results
Design Builder Simulation Results

## Slide 29: Environmental Aspects– Design Builder Analysis and Results
Energy Baseline Comparison
Predicted Mean Value

## Slide 30: Structural Aspects
Preliminary Checks
Seismic Checks
Design Details

## Slide 31: Structural Aspects – Structural System
The following codes were used in the structural design:
ACI-318R-14 for reinforced concrete structural design
ASCE 7 2010 for load combinations
IBC – 2016 for seismic design.

## Slide 32: Structural Aspects – Design Data
Concrete - (fc) = 28 MPa.
Steel - (fy) = 420 Mpa
Soil Bearing Capacity=250kn/m2
Dead load (From ETABS)
Superimposed Loads = 2.5 KN/m2
Live Loads = 4 KN/m2
Design Data
Materials
Loads

## Slide 33: Structural Aspects – Structural Checks
Compatibility Check

## Slide 34: Structural Aspects – Structural Checks
Equilibrium Check
 | Etabs | Manual | Error(%) | < 5 %
Dead | 18096.79 | 17855.65 | 1.35 | 
Live | 6580 | 6593.36 | 0.203 | 
SID | 15916.26 | 16129.52 | 1.32 | 

## Slide 35: Structural Aspects – Structural Checks
Stress-Strain Check – Columns
C 30*40m | 
Structure elements | Manual
one way | 0
two way | 547.0164
main beams | 185.8442
column | 43.2
Total | 776.0606
ETABS | 715.6039
Difference | 8.4 %

## Slide 36: Structural Aspects – Structural Checks
Stress-Strain Check – Beams
Edge Beam (B45*30) |  |  |  |  | 
 | Manual (KN) |  | ETABS (KN) |  | Difference (%)
One way | 0 | 0 | M1- | -295.43 | 
Two way | 64.8 | 242.44 | M2- | -327.56 | 
Weight (kN/m) | 9.45 | 53.11 | M+ | 168.69 | 
Total(KN) | 518.098 |  | 480.189 |  | 7.89

## Slide 37: Structural Aspects – Structural Checks
Stress-Strain Check – Slab
Slab |  | 
ETABS | M1(-ve) | -14
 | M2 (-ve) | -30
 | M (+ve) | 28
 |  | 50
Manual | 48.30 | 
Difference | 3.3953 % | 
< 10 % |  | 

## Slide 38: Structural Aspects – Structural Checks
Deflection Checks

## Slide 39: Structural Aspects – Structural Checks
Seismic Checks
City of Structure | Nablus
Site Class | C- very dense soil and hard rock
Risk Category | II
Over strength factor | 2.5
Deflection Amplification factor | 4.5
Seismic Importance Factor | I=1
Structural Design Type | Building Frame System-Ordinary reinforced concrete shear walls
Response Modification factor ( R) | R=5

## Slide 40: Structural Aspects – Structural Checks
Seismic Checks

## Slide 41: Structural Aspects – Structural Checks
T Etabs (x direction) = 0.97 sec.
T Etabs (y direction) = 0.276 sec
Period Check

## Slide 42: Structural Aspects – Structural Checks
Base shear check
Axis | T | Tlimit | T final | Cs1 | Cs2 | Cs3 | Cs final | V | VETABS | Error %
X | 0.097 | 0.54656 | 0.097 | 0.103111 | 0.3592 | 0.0204 | 0.1031 | 2944.647 | 2898.1034 | 1.5806
Y | 0.276 | 0.54656 | 0.276 | 0.1031 | 0.1262 | 0.0204 | 0.1031 | 2944.647 | 2898.1034 | 1.5806

## Slide 43: Structural Aspects – Structural Checks
Drift Check
The allowable drift = 0.02
Where:
Cd: the floor height in meters.
Δmax: the story drift value from ETABS.
Ic: the importance factor which equals 1 in this project.
So =0.00028 < 0.02

## Slide 44: Structural Aspects – Structural Checks
P-Delta Check
Axis | P | S | h | theta
X | 38863.378 | 2.77*105 | 4 | 3.51*10-2
Y | 38863.378 | 5.35E*105 | 4 | 3.51*10-2
Θ < 0.1
If the previous equation is true, then the building is safe.
.
θ= PS*h
Where:
P: the story force in kN.
S: story stiffness.
h: story height in meters.

## Slide 45: Structural Aspects – Structural Elements Design
Slab Design
Basement Slab Design
Ground Floor Slab Design

## Slide 46: Structural Aspects – Structural Elements Design
Slab Design
First Floor Slab Design
Second Floor Slab Design

## Slide 47: Structural Aspects – Structural Elements Design
Slab Design
Two Way Ribbed Slab
One Way Ribbed Slab

## Slide 48: Structural Aspects – Structural Elements Design
Basement Column Distribution
Ground Floor Column Distribution
Columns Design

## Slide 49: Structural Aspects – Structural Elements Design
First Floor Column Distribution
Second Floor Column Distribution
Columns Design

## Slide 50: Structural Aspects – Structural Elements Design
Columns Design
Column | B (cm) | H (cm) | Rebar Percentage (%) | Longitudinal Reinforcement (cm2) | Bar diameter (mm) | Bar area (cm2) | # of Bars | Stirrups at the Middle | Stirrups at Supports
C1 (Corner Column) | 30 | 40 | 1% | 12 | 16 | 2.031 | 6 | 1 fi 10/150 mm | 1 fi 10/150 mm
C2 (Edge Column) | 40 | 60 | 1% | 24 | 20 | 2.54 | 10 | 1 fi 10/120 mm | 1 fi 10/120 mm
C3 (Middle Column) | 50 | 60 | 1% | 30 | 20 | 3.14 | 10 | 1 fi 10/120 mm | 1 fi 10/120 mm

## Slide 51: Structural Aspects – Columns Design
Columns Design

## Slide 52: Structural Aspects – Structural Elements Design
Basement Beams
Ground Floor Beams
Beams Design

## Slide 53: Structural Aspects – Structural Elements Design
First Floor Beams
Second Floor Beams
Beams Design

## Slide 54: Structural Aspects – Structural Elements Design
Beams Design
Beam Label | Width | Depth | Bottom | Top
B1 | 70 | 45 | 7 Ø 18 | 9 Ø 20
B2 | 70 | 45 | 4 Ø 14 | 5 Ø 16
B3 | 70 | 45 | 5 Ø 16 | 6 Ø 16
B4 | 70 | 45 | 3 Ø 12 | 4 Ø 16
B5 | 50 | 30 | 3 Ø 14 | 4 Ø 14
B6 | 70 | 45 | 10 Ø 18 | 7 Ø 25

## Slide 55: Structural Aspects – Structural Elements Design
Beams Design

## Slide 56: Structural Aspects – Structural Elements Design
Beams Design
Frame Section

## Slide 57: Structural Aspects – Structural Elements Design
Foundations Design
Mat Foundation
Single Footings
Wall Footings

## Slide 58: Structural Aspects – Structural Elements Design
Foundations Design – Mat Foundation

## Slide 59: Structural Aspects – Structural Elements Design
Foundations Design – Mat Foundation

## Slide 60: Structural Aspects – Structural Elements Design
Foundations Design – Single Footings
Type | Label | d (mm) | b (m) | L (m) | h (mm)
FT1 | 1,2,5 | 250 | 1.6 | 1.5 | 310
FT2 | 6,7 | 350 | 2 | 2.3 | 410
FT3 | 3,4 | 450 | 2.5 | 2.5 | 510
FT4 | 8,9 | 600 | 4 | 3.5 | 660

## Slide 61: Structural Aspects – Structural Elements Design
Foundations Design – Single Footings

## Slide 62: Structural Aspects – Structural Elements Design
Foundations Design – Single Footings

## Slide 63: Structural Aspects – Structural Elements Design
Foundations Design – Single Footings

## Slide 64: Structural Aspects – Structural Elements Design
Foundations Design – wall Footing
Footing Type 4 – 3D Detailing
Wall Footing Detailing

## Slide 65: Electro-Mechanical Aspects
Water Supply and Drainage
HVAC System
Power Design
Acoustical Design
Artificial Lighting

## Slide 66: Electro-Mechanical Aspects – Artificial Lighting
DIALux has been used for this Analysis and Design.
Designed Spaces:
Reading Area
Office
Children Room
Multiple Use Room
Achieve
Computer Lab

## Slide 67: Electro-Mechanical Aspects – Artificial Lighting
Reading Area

## Slide 68: Electro-Mechanical Aspects – Artificial Lighting
Reading Area

## Slide 69: Electro-Mechanical Aspects – Artificial Lighting
Computer Lab.

## Slide 70: Electro-Mechanical Aspects – Artificial Lighting
Lighting Plans
Ground Floor
First Floor

## Slide 71: Electro-Mechanical Aspects – Power Design
Socket and Distribution Boards Plans
Basement

## Slide 72: Electro-Mechanical Aspects – Power Design
Socket and Distribution Boards Plans
Ground Floor
First Floor

## Slide 73: Electro-Mechanical Aspects – Power Design
Summary Tables
Distribution Boards
switches, sockets, luminaires and Distribution Boards
 | DB-1 B | DB-2 GF | DB-3 GF (computer lab) | DB-4 FF | DB-5 SF
Lighting power (watt) | 554 | 1935.6 | - | 2154.2 | 2018.5
Lighting current (Amp) | 2.5 | 8.7 | - | 9.7 | 9.1
Number of lighting branches | 3 | 10 | - | 11 | 10
Number of sockets branches | 2 | 6 | 9 | 8 | 8
Number of special load branches | - | 1 | - | - | 1
Circuit breaker current (Amp) | 33.8 | 35.8 | 38.4 | 36.8 | 35.9
Cable rated current (Amp) | 37 | 37 | 50 | 37 | 37
Cable cross sectional area (mm2) | 6 | 6 | 10 | 6 | 6
Floor | Number of luminaires | Number of sockets | Number of switches | Number of DB
Basement | 26 | 6 | 8 | 3
Ground floor | 79 | 54 | 25 | 1
First floor | 89 | 26 | 22 | 1
Second floor | 82 | 29 | 26 | 1

## Slide 74: Electro-Mechanical Aspects – Water Supply and Drainage
Solar Boiler
 | Volume per Circulation (m3) | Tank Capacity (m3) | Number of Tanks
Cold Water | 12000 | 2 | 7
Hot Water | 2400 | 2.5 | 1
Water Tanks
Electrical Boiler
Number of Solar Boilers = 11
Two Electrical Boilers were needed for the Ground Floor and Second Floor

## Slide 75: Electro-Mechanical Aspects – Water Supply and Drainage
 | Ground floor |  | First floor |  | Second Floor | 
Feeder pipe | Diameter (Inch) | Pressure loss (Psi) | Diameter (Inch) | Pressure loss (Psi) | Diameter (Inch) | Pressure loss (Psi)
Vertical Feeder (1) | 2.5’’ | 1.29 | 2.5’’ | 1.29 | 2.5’’ | 1.29
Horizontal | 2’’ | 0.01 | 2’’ | 0.01 | 2’’ | 0.01
Main Branch | 1.5’’ | 0.39 | - | - | 1.5’’ | 0.39
Sub Branch | 1 | 0.59 | 1 | 0.59 | 1 | 0.59
Total losses | 2.28 |  | 1.89 |  | 2.28 | 
Max. losses | 9.19 |  | 3.5 |  | -2.1 | 
 | Ground floor |  | First floor |  | Second Floor | 
Feeder pipe | Diameter (Inch) | Pressure loss (Psi) | Diameter (Inch) | Pressure loss (Psi) | Diameter (Inch) | Pressure loss (Psi)
Vertical Feeder (2) | 2’’ | 0.36 | 2’’ | 0.36 | 2’’ | 0.36
Horizontal | 1.25’’ | 0.011 | 1.25’’ | 0.011 | 1.25’’ | 0.011
Main Branch | 0.75’’ | 1.5 | - | - | 0.75’’ | 1.5
Sub Branch | 0.5’’ | 0.73 | 0.5’’ | 0.73 | 0.5’’ | 0.73
Total losses | 2.6 |  | 1.1 |  | 2.6 | 
Max. losses | 9.19 |  | 3.5 |  | -2.1 | 
Cold Water Summary Table
Hot Water Summary Table

## Slide 76: Electro-Mechanical Aspects – Water Supply and Drainage
Water Supply Plans
First Floor
Ground Floor
Second Floor

## Slide 77: Electro-Mechanical Aspects – Water Supply and Drainage
Drainage System
Used Diameters
W.C Horizantal Pipe = 4″ at slope of 1%
Lavatory Horizantal Pipe = 2″ at slope of 2%
Kitchen Sink Horizantal Pipe = 2″ at slope of 2%
Main Manhole’s Pipe = 6″ at slope of 1%
Branch Manhole’s Pipe = 4″ at slope of 1%
Rainwater Vertical Pipe = 4″

## Slide 78: Electro-Mechanical Aspects – Water Supply and Drainage
Drainage System Sample Plans

## Slide 79: Electro-Mechanical Aspects – Water Supply and Drainage
Rainwater System and Manholes Plan

## Slide 80: Electro-Mechanical Aspects – Photovoltaic System Design
Module Specifications

## Slide 81: Electro-Mechanical Aspects – Photovoltaic System Design
Module Distribution Cases
Case 1
Case 2

## Slide 82: Electro-Mechanical Aspects – Photovoltaic System Design
Module Distribution Cases
Summary Table
Case No. | Number of Modules | Azimuth Angle | Tilt Angle | System Capacity (kWp) | Performance Ratio | Total yearly production (MWh/year)
Case 1 | 109 | 15 | 30 | 27.25 | 75.59% | 32.14
Case2 | 141 | 15 | 0 | 35.3 | 74.60% | 47.9
Performance Ratio
Payback Period

## Slide 83: Electro-Mechanical Aspects – HVAC Design
VRF System has been considered.
HVAC System Used Components:
Air handling Unit
Cassette Unit
Ducts
Diffusers

## Slide 84: Electro-Mechanical Aspects – HVAC Design
Design Capacity = 155.72 kW
Total Design Flowrate = 15.443 m3/sec.
Air Handling Unit Catalogue
Air Handling Unit Location

## Slide 85: Electro-Mechanical Aspects – HVAC Design
HVAC Plans
Ground Floor
Basement

## Slide 86: Electro-Mechanical Aspects – HVAC Design
HVAC Plans
Second Floor
First Floor

## Slide 87: Electro-Mechanical Aspects – Acoustical Design
Insul has been used for the STC values
Ease has been used for RT60 analysis
Designed Spaces:
Offices
Children Room
Computer Lab
Multiple Use Room

## Slide 88: Electro-Mechanical Aspects – Acoustical Design
Material | 125HZ | 250HZ | 500HZ | 1000HZ | 2000HZ | 4000HZ
Tiles | 0.01 | 0.01 | 0.01 | 0.02 | 0.02 | 0.02
Paint (Walls) | 0.01 | 0.02 | 0.03 | 0.03 | 0.04 | 0.05
Glass | 0.03 | 0.02 | 0.03 | 0.03 | 0.02 | 0.02
Gyptone Line (Ceiling) | 0.61 | 0.77 | 0.68 | 0.61 | 0.50 | 0.45
Plywood | 0.03 | 0.02 | 0.02 | 0.01 | 0.02 | 0.01
Parquet sur lambourdes (Floor) | 0.20 | 0.15 | 0.12 | 0.10 | 0.08 | 0.07
Seats | 0.25 | 0.27 | 0.30 | 0.30 | 0.30 | 0.30
Moquette sur thibaude | 0.10 | 0.20 | 0.50 | 0.60 | 0.80 | 0.80
Carpet | 0.20 | 0.25 | 0.30 | 0.30 | 0.30 | 0.30
Rubber | 0.02 | 0.03 | 0.03 | 0.03 | 0.03 | 0.02
Used Acoustical Materials

## Slide 89: Electro-Mechanical Aspects – Acoustical Design
Children Room Allowed RT60
0.4-0.80 Sec
Office Allowed RT60
0.4-0.70 Sec

## Slide 90: Electro-Mechanical Aspects – Acoustical Design
Partition Between Offices
Min. STC Required = 40DB
Partition Between W.Cs and adjacent
Min. STC Required = 50DB

## Slide 91: Electro-Mechanical Aspects – Acoustical Design
Ground Floor Fire-Fighting Plan
Allowed Articulation Loss = 7.1%
Maximum Articulation Loss ≈ 7%

## Slide 92: Electro-Mechanical Aspects – Fire Fighting System
Used Fire-fighting System
Dry Sprinkler System
Fire Hose Stations
Fire alarm System
Dry Stand Pipe
Fire-fighting Signs

## Slide 93: Electro-Mechanical Aspects – Fire Fighting System
Second Floor Fire-Fighting Plan
Fire-fighting Symbols

## Slide 94: Electro-Mechanical Aspects – Fire Fighting System
Ground Floor Fire-Fighting Plan
Fire-fighting Symbols

## Slide 95: Electro-Mechanical Aspects – Fire Fighting System
Ground Floor Excavation Plans
First Floor Excavation Plans

## Slide 96: Quantity Surveying & Cost Estimations
Preliminary Cost Estimation of the Library has been conducted based on the Unit base method.

## Slide 97: Cost Estimation
Chart: 
| Earthwork | Structural Work | Electrical Work | Mechanical Work | Finishing Work
 | 86305.02 | 813839.52 | 669980 | 177953 | 765360
Work Category | Cost (NIS)
Earthwork | 86,305
Structural Work | 813,839
Electrical Work | 669,980
Mechanical Work | 177953
Finishing Work | 765,360
Total Cost of the Project (NIS) | 
Unit Cost (NIS/m2) | 
Work Category | Cost (NIS)
Earthwork | 86,305
Structural Work | 813,839
Electrical Work | 669,980
Mechanical Work | 177953
Finishing Work | 765,360
Total Cost of the Project (NIS) | 
Unit Cost (NIS/m2) | 

## Slide 98: THANKS
Does anyone have any questions?