## Slide 1: Faculty of Engineering Building Engineering Department Design for office building (Sudah Center) (Graduation Project 2) Supervisor : Dr.Muhnnad Haj Hussein
Ahmad Younis Yazan Kalbouneh Yousef Omar

## Slide 2: Presentation outline :
1.Introduction
7.Electrical Design
2.Earlier Studies
5.Environmental Design
8.Quantity & Cost Estimation
4.Structural Design
3.Architectural Design
6.Mechanical Design

## Slide 4: 1. Introduction
Let’s start with the first set of slides

## Slide 5: Site And Location
It’s located in Main Street of Rafedea near to Al-Jnaid Prison Nablus-Palestine.

## Slide 6: Site And Location
-Site has a total area of 760 m2.
-Serviceable main street width equals 30m.

## Slide 7: Site Pros and Cons.
Pros.
-Good Southern view.
Good solar gain form the south.
Its located near to Al Najah University which is good to transportation.
Cons.
The main elevation of the building is facing south.
-The site is blocked from east & north.
Has a high surrounding noise

## Slide 8: 2. Earlier Studies: 2.1 Solar Analysis
In a Summer Day:
√ The Site is fully exposed to sun.
In a Winter Day:
√ in the morning hours the site is shaded,
√ in the midday, it is fully exposed to sun.

## Slide 9: 2.2 Noise Analysis
Highest value exceed 80 dB due to Rafedea street .

## Slide 10: 3. Architectural Re-design

## Slide 11
Usage of the building:
The building is an office building.
Normal Working hours for the offices from 8:00 am to 3:00 pm.
Used by 13 offices , 3 shops and a restaurant .

## Slide 12
Redesigned Site:
Existing Site:

## Slide 13
New Design:
Old Design Plans:
First Floor:

## Slide 14
Old Design West
Elevation
New Design West
Elevation

## Slide 15
Old Design East
Elevation
New Design East
Elevation

## Slide 16
Old Design main
Elevation
New Design main
Elevation

## Slide 17
Design Modifications:
1- Entrances :

## Slide 18
New Design:
Design Modifications:
2- Parking :
Old Parking Design:

## Slide 19
Larger space and facilities.
External terrace is provided.
Design Modifications:
Restaurant:

## Slide 20
Architectural plans (GF) :

## Slide 21
Architectural plans (First Floor):

## Slide 22
Table of Areas :
Floor | Total Area(m2)
Basement one | 755
Ground Floor | 313
First Floor | 346
Second Floor | 346
Third Floor | 346
Fourth Floor | 346
Fifth Floor | 346
Sixth Floor | 346
Sum | 3144

## Slide 23
Final Design Photos:

## Slide 24
Final Design Photos:

## Slide 25: 4. Structural Design

## Slide 26: Design Codes
ACI -318-08 (American Concrete Institution) for reinforced concrete structural design.
UBC-97 (Uniform Building Code) for earthquake load computations.
ASCE (American Society Of Civil Engineers) for design loads.

## Slide 27: Building Description
Consists of 8 Floors (Including Basement).

## Slide 28
Reinforced Concrete Compressive Strength (fc’)
Structural Item | Compressive Strength
Slab, Beams & cantilever walls | (B300)
Columns, walls & Foundations | (B300)
Blinding | (B250)

## Slide 29
Structural System
Beam Girder System.
The system of the slab is one way ribbed slab(30 cm thickness) with Drop beams.

## Slide 30
Building Modeling:

## Slide 31
Program Input:
Type of load | Load KN/m2
Live load | 4
Super imposed dead load | 4
Exterior walls | 25 KN/m
Structural Item | Modifier
Beams | 0.35
Slabs | 0.25
Walls | 0.70
Loads:
Modifiers:

## Slide 32
Model Validation Checks :
Compatibility Check :

## Slide 33
Model Validation Checks :
Deflection Check:
Deflection Doesn’t exceed the limitation.

## Slide 34
Model Validation Checks :
Base reaction (Equilibrium) Check :
Load | Manual | ETABS | Error
Dead load | 22250 KN | 22262 KN | 0.01 %
Live load | 10006 KN | 10012 KN | 0.01 %
Super imposed | 30954 KN | 30825 KN | 0.01 %

## Slide 35
Model Validation Checks :
Internal Forces Check :
Done for 2 samples of slab strip, beams and columns within difference less than 10%

## Slide 36
Period Check:
T(A) for building = 0.66 sec with 40% increase = 0.92 sec.
T(Bx) = 0.89 sec , T(By) = 0.52 sec
The period is OK.

## Slide 37
Base Shear Check:
Load Case/Combo | FX | FY
 | kN | kN
EQX Max | 2223 | 877
EQY Max | 1552 | 3909
Total weight of building = 55589 kN ‘D+0.25 L’

## Slide 38
Slab Design

## Slide 39
Beams Design

## Slide 40
Columns Design

## Slide 41
Columns Design

## Slide 42
Shear Wall Design

## Slide 43
Footing Layout:

## Slide 44
Footing Layout:

## Slide 45
Footing Layout:

## Slide 46
Basement Reinforcement

## Slide 47
Stairs Reinforcement

## Slide 48: 5. Environmental Design
College building Concrete Skeleton

## Slide 49
In a Summer day:
Solar Analysis
Building Shadow at 8:00 am on 21th July
Building Shadow at 12:00 pm on 21th July

## Slide 50
In A Winter day:
Solar Analysis
Building Shadow at 8:00 am on 21th January
Building Shadow at 12:00 pm on 21th January

## Slide 51
Daylight factor & Shading:
Solar Analysis
Daylight Factor exceeds limit
Louvers or steel covering

## Slide 52
Heating and cooling calculations:
Part | U value before (W/m².K) | U value after (W/m².K)
External walls | 1.16 | 0.52
Roof | 1.7 | 0.491
Window | 2.1 | 1.96
U-value Improvements:
Environmental design:
External wall section
Roof Section

## Slide 53
Heating and Cooling Load
Total Heating Capacity = 111 kW
Total Cooling Capacity = 125 kW

## Slide 54
Thermal Comfort
PMV Set

## Slide 55
Energy Consumption
Total site energy =150 Kwh/ m2

## Slide 56
Acoustical analysis (RT60):
- Classroom:
RT60 at 500 Hz=1.84 s
RT60 at 1000 Hz=1.90 s
- Before(empty space) :
RT60 at 500 Hz=0.70 s
RT60 at 1000 Hz=0.61 s
- After(empty space):
Acceptable range for Classrooms= (0.6-0.8) sec .
RT60 at 125 Hz=1.28 s
RT60 at 250 Hz=1.37 s
RT60 at 250 Hz=0.60 s
RT60 at 125 Hz=0.64 s

## Slide 57
Acoustical analysis (RT60):
- Library:
Acceptable range for Libraries = (0.55-0.95) sec .
RT60 at 250 Hz=0.59 s
RT60 at 500 Hz=0.69 s
RT60 at 1000 Hz=0.63 s
RT60 at 125 Hz=0.65 s
RT60 at 2000 Hz=0.60 s
- Case : (empty space)

## Slide 58
Acoustical analysis (RT60):
- Auditorium:
Acceptable range for Auditoriums= (0.80-1.20) sec .
RT60 at 250 Hz=0.89 s
RT60 at 500 Hz=0.93 s
RT60 at 1000 Hz=0.80 s
RT60 at 125 Hz=1.0 s
RT60 at 2000 Hz=0.68 s
- Case : (empty space)
RT60 at 4000 Hz=0.56 s
RT60 at 8000 Hz=0.57 s
Statistical Reverberation time curves

## Slide 59
Acoustical analysis (STC):
- Classrooms:
STC shall be >40 dB to avoid unwanted noise in space
STC =45 dB

## Slide 60
Acoustical analysis (STC):
- Library:
STC shall equal from45-55 dB or higher to avoid unwanted noise in space
STC =45 dB
Wall layers

## Slide 61
Acoustical analysis (STC):
- Auditorium:
STC shall equal 50 dB or higher to avoid noise traveling to adjacent spaces.
STC =51 dB

## Slide 62
Acoustical analysis (IIC):
IIC =34 dB
Concrete Slab

## Slide 63
Loudspeakers :
For Corridors
Speakers Distribution
PRO-180RPC In-ceiling speaker

## Slide 64
Loudspeakers :
For Auditorium
Ecotect Model for Auditorium
Ci3160RL-THX Ultra 2 certified in wall speakers.

## Slide 65
Loudspeakers :
For Auditorium
In wall Speakers Distribution

## Slide 66
Loudspeakers :
For Auditorium
Ceiling Small Speakers Distribution

## Slide 67: 6. Mechanical Design
College building Concrete Skeleton

## Slide 68
Mechanical Design Includes:
1.Water Supply Systems.
2. Drainage Water Systems Design.
3. HVAC system.

## Slide 69
Water Supply SYSTEM:
First Floors

## Slide 70
Water Supply SYSTEM:
Water Tanks:
Vertical = steel pipe
Horizontal = UPVC pipe
Branch = UPVC pipe

## Slide 71
Drainage Systems design:
First Floor Toilets

## Slide 72
HVAC System Design:
VRF System
Air flow (L/S) | Design capacity Cooling (Kw) | Design capacity Heating (Kw) | 
Varies from a space to another | 125 | 111 | All floors

## Slide 73
HVAC System Design:
VRF System
Outdoor selected from LG company and its capacity
Outdoor unit capacity
Cooling capacity = 112 kw
Heating capacity = 126 kw

## Slide 74
HVAC System Design:
VRF System
Fan coil selection ,which is depending on volumetric flow rate in each zone

## Slide 75
First floor HVAC (duct) system layout

## Slide 76
7.
Electrical Design

## Slide 77
Artificial Lighting:
- Manager office :
Lamp used: Philips Lighting (RC132V)
Power: 34 watt
Power Efficacy: 90lm/W, 110lm/W
CRI >80; CCT: 4000/6500K
Lighting level : 500 lux
Mounting height: 3.2 m
E.avg and U0 are accepted.

## Slide 78
- Manager office :
From the figures shown before the UGR is accepted (< 19)
Area of calculation for UGR

## Slide 79
Artificial Lighting:
Employee office:
Lamp used: Philips Lighting (RC132V)
Power: 34 watt
Power Efficacy: 90lm/W, 110lm/W
CRI >80; CCT: 4000/6500K
Lighting level : 500 lux
Mounting height: 3.2 m
E.avg and U0 are accepted.

## Slide 80
Employee office 3D:
Maneger office 3D:

## Slide 81
Artificial Lighting:
Lighting luminaries layout offices floor:

## Slide 82
Distribution of sockets:

## Slide 83: 8. Quantity and Cost Estimation
College building Concrete Skeleton

## Slide 84
B.O.Q :
Final BOQ |  | 
Item | Descriptions | Total (NIS)
Bill No.1 | Earth work | 291,036
Bill No.2 | Structural work | 2,298,876
Bill No.3 | Finishing work | 283,167
Bill No.4 | Mechanical | 1,138,578
Bill No.5 | Electrical | 307,395
Grand Total (NIS) |  | 4,319,050
The total area for building = 3145 m2
The total cost of the project is = 4,319,050 NIS
The unit cost for the project = 1374 NIS/m2

## Slide 85: 9. Safety Considerations
College building Concrete Skeleton

## Slide 86
-Emergency Stair Case:

## Slide 87
-Fire Detectors (Flame Detectors):

## Slide 88
-Fire Detectors (Smoke Detectors):

## Slide 89
Restaurant Smoke Detectors:

## Slide 90
-Evacuation Paths
Office Floor

## Slide 91
-Evacuation Paths
Restaurant Floor

## Slide 92: THANK YOU !