## Slide 1
An-Najah National University
Faculty of Engineering and Information Technology
Building Engineering Department
Graduation Project – II
Re-design of Nablus Municipality building.
Prepared By :
1. Ahmad Hamad.
2.Amr Turkman.
3. Mohammad Nathem.
4. Noor Jaber.
Supervisor:
Nirmeen Al-Barq.

## Slide 2
Introduction.
Site Analysis.
Architectural aspects.
Environmental aspects.
Structural aspects.
Electro mechanic aspects.
Cost Estimation.
Conclusion.
Contents:

## Slide 3
Introduction

## Slide 4
Objectives:
Redesigning and development the building, all aspects and engineering systems will be included where all weaknesses and problems of the building will be taken into account during the operation process.

## Slide 5
Site Analysis:
Location:
The land on which the Municipality will be built located in Yafa street near Jamal Abdul Nasser park.

## Slide 6
Architectural Design.

## Slide 7
General Information.
Floors.
Elevations.
Sections.
Architectural Design.

## Slide 8
General Information.
The land area is about 3000 m².
The municipality contains 7 floors, two of them are basement floors.
The main entrance in East elevation.

## Slide 10
N - elevation

## Slide 11
W - elevation

## Slide 12
N-W VIEW

## Slide 13
N-W elevation
N-E VIEW

## Slide 14
Site Plan.

## Slide 15
  Basement (1) floor.
  Floor height = 4.25 m.
Basement Floor after
Basement Floor before

## Slide 16
  Basement (2) floor.(new)
  Floor height = 4.25 m.

## Slide 17
Ground floor
  Floor height = 4.25 m.
Ground floor after
Ground floor before

## Slide 18
First floor.
Floor height = 4.25 m.
First Floor after
First Floor before

## Slide 19
Second floor.
Floor height = 4.25 m.
Second Floor after
Second Floor before

## Slide 20
Third floor.
Floor height = 4.25 m.
Third Floor before
Third Floor after

## Slide 21
Forth floor.
Floor height = 4.25 m.

## Slide 22
Environmental
aspects

## Slide 23
The orientation building.
Thermal Design.
Daylight factor.
Acoustic Design.
The important parameter of environmental assessment

## Slide 24
The Orientation and sun path of the building.

## Slide 25
Thermal Design

## Slide 27
Floor layers
External wall layers
plaster
PMV
Glazing Insulation

## Slide 28
Heating Design study state data

## Slide 29
Daylight analysis.

## Slide 34
Acoustical Design.
 Walls → perforated panel 2 sides + Plaster another side
 Floor → Carpet
 Ceiling → Gypsum wall
Material Choices:

## Slide 35
Ecotect program
the values of RT60 in this analysis its in the avg. in the a reverberation time in the range (1.2 to 1.7 )seconds
Multipurpose halls

## Slide 36
EASE program

## Slide 37
Direct SPL on Seats & Area

## Slide 38
Total SPL on Seats & Area

## Slide 39
INSIDE
OUTSIDE

## Slide 40
Structural Design.

## Slide 41
Structural Design
General Information
Design code :
ASCE-7 for loads and combinations.
American Concrete Institute ACI 2014 for design.
Materials:
1. Concrete.
Concrete used for slabs, columns and beams with (f'c=28 Mpa).
Cocrete (B350).
2. Steel rebar .
Steel yield strength Fy= 420 Mpa.
Loads:
Live Load for parking = 5 KN/m².
Live Load for floors = 3 KN/m².
Superimposed dead load = 4 KN/m².
Properties of Materials:
specific weight of Reinforced concrete = 25 KN/m³.
Specific weight of block = 12 KN/ m³.

## Slide 42
Block (1).
Slab Structural System:
One way ribbed slab.
The longest span (ln) = 6.30 m
two end continuous span
Thickness of slab = ln\21 = 6.30/21 = 30 cm.
Beams section:
Main beam (800*500)mm.
Secondary beam (600*300)mm.
columns section:(800*400)mm.

## Slide 43
Block (2).
Slab Structural System:
One way ribbed slab.
The longest span (ln) = 7.60 m
two end continuous span
Thickness of slab = ln\21 = 7.60/21 = 40 cm.
Beams section:
Main beam (800*500)mm.
Secondary beam (600*300)mm.
columns section:(800*400)mm.

## Slide 44
Block (3).
Slab Structural System:
One way ribbed slab.
The longest span (ln) = 7.40 m
one end continuous span
Thickness of slab = ln\21 = 7.40/18.5 = 40 cm.
Beams section:
Main beam (800*500)mm.
Secondary beam (600*300)mm.
columns section:(800*400)mm.

## Slide 45
Slab and Beams
GF Floor
(1 st) , (2 nd) and (3 rd) Floor

## Slide 46
(4 th Floor).

## Slide 47
Footing Design
Isolated footing.
wall footing.
Combined footing.

## Slide 50
3D model for block 1.
3D model for block 2.
3D model for block 3.

## Slide 51
Compatibility check.
Block 1
Block 2
Block 3

## Slide 52
% error | by manual (KN) | from ETAB(KN) | Load Case
4.3 % | 36483.5 | 34893 | Dead
1.26 % | 15709.6 | 15511.50 | Live
1.38 % | 16074.08 | 15852.15 | SID
Equilibrium check
% error | by manual (KN) | from ETAB(KN) | Load Case
2.6 % | 27509.94 | 26789.17 | Dead
0.0 % | 10723.66 | 10723.5 | Live
0.0 % | 10982.8 | 10982.99 | SID
% error | by manual (KN) | from ETAB(KN) | Load Case
4.6 % | 32885.44 | 31346.15 | Dead
0.5 % | 12356.05 | 12282.70 | Live
0.6 % | 11640.76 | 11563.53 | SID
BLOCK 1
BLOCK 2
BLOCK 3

## Slide 53
Internal force checks.
Element | from ETAB(KN) | manual (KN) | % of Diff.
Corner column | 2628.15 | 2372.4 | 9.7 %
Edge column | 3225 | 2980.2 | 7.6 %
int. column | 4330 | 4707.04 | 8.7 %
 | from ETAB(KN.m) | by manual (KN.m) | % of Diff.
Main Beam | 235.4 | 227.52 | 3.3 %
Sec Beam | 69.4 | 75.42 | 7.9 %
Slab | 55.83 | 52.02 | 6.8 %
Element | from ETAB(KN) | manual (KN) | % of Diff.
Corner column | 2932.72 | 2882.48 | 1.7 %
Edge column | 2695.15 | 2800.8 | 3.9 %
int. column | 3992.72 | 3731.4 | 6.5 %
 | from ETAB(KN.m) | by manual (KN.m) | % of Diff.
Main Beam | 99.72 | 123.77 | 9.4 %
Sec Beam | 69.95 | 64.75 | 7.4 %
Slab | 68.1 | 73.96 | 8.6 %
Element | from ETAB(KN) | manual (KN) | % of Diff.
Corner column | 2628.15 | 2372.4 | 4.6 %
Edge column | 3225 | 2980.2 | 5.8 %
int. column | 4330 | 4707.04 | 7.8 %
 | from ETAB(KN.m) | by manual (KN.m) | % of Diff.
Main Beam | 235.4 | 227.52 | 8.5 %
Sec Beam | 69.4 | 75.42 | 4.4 %
Slab | 55.83 | 52.02 | 5.3 %

## Slide 54
Design check

## Slide 55
Electro mechanic aspects

## Slide 56: Mechanical aspect

## Slide 57: 1st Floor

## Slide 58: 2nd Floor

## Slide 59: 3rd Floor

## Slide 60: 4th Floor

## Slide 61
1st Floor
G.F Floor
HVAC System

## Slide 62
2nd Floor
3rd Floor

## Slide 63
4th Floor

## Slide 64: Fire fighting system

## Slide 65
Detectors Types

## Slide 66
Electrical aspect

## Slide 67: Power Design
Ground Floor
First Floor

## Slide 68
second Floor
third Floor
Fourth Floor

## Slide 69: Lighting and Switch plan
Ground Floor
First Floor

## Slide 70
second Floor
third Floor
Fourth Floor

## Slide 71: Luminaire list
Artificial Lighting Design

## Slide 72: The recommended and standard for office manager space
Artificial lighting Render in office manager

## Slide 73
Artificial lighting Render in multi-purpose hall
The recommended and standard for multi-purpose hall

## Slide 74
Artificial lighting Render in corridor
The recommended and standard for corridor

## Slide 75: Summary of electrical loads consumed by the building
I = P / (V x P.F x).
I: Current. (A) P: Power. (W)
V: Voltage = 380 Volt. P.F: Power Factor = 0.95.
3-phase fuse were used due to the relatively large loads
Current Calculation for Other Electrical Equipment’s
Current Calculations for Socket and Lighting
Socket and Lighting Demand Power Calculations

## Slide 76
Quantity surveying & Cost Estimate