## Slide 2
CONTENTS
OBJECTIVES
STUDY AREA
QUESTIONNAIRE
WATER NETWORK ANALYSIS
ANALYSIS of EXISTING WATER NETWORK USING EPANET
EPANET USING DESIGN of FUTURE WATER NETWORK
COMARISON of The TWO NETWORK DESIGNS
CONCLUSIONS

## Slide 3
OBJECTIVES
Analysis an existing network .
Analyze the outcome of the questionnaire to draw some conclusions regarding the water supply services in the area .
Collect basic information about Attil Town .
Re-design of water supply network for Attil
Town .
Reach to final design. Two options with cost estimates and compare between them .

## Slide 4
STUDY AREA

## Slide 5
. Currently it is estimated at 11,000 capita : Population
Educational Situation : The education rate in the town is one of the highest compared to other towns . in Palestine
. Health Situation : Attil has a good healthy status
Agriculture is the main source of : Economic Situation
the economy of the town .
The climate of Attil is Meteorological Condition :
a Mediterranean type with moderate summers and
. warm winters

## Slide 6
QUESTIONNAIRE
Monthly income
Dependence on municipality as a source of water.
Existence of a garden in the house
Evaluation of the network

## Slide 7
Infusion of water
Satisfaction with the arrival of the service
Feeling any taste color/odor in water
Satisfaction of pressure level in the network

## Slide 10
WATER NETWORK ANALYSIS
Source of water: Attil Town is fed from Abu Sabha irrigation project . Water is pumped from the well by a booster pump and stored in the tank. The well rises
. 62 m above sea level
Tank : Water tank had been set up for Attil Town in 1976. It has a capacity of 200 m3 and rises 116 m above . sea level
Water is distributed in Length of the network :
a network of total length equals approximately 58 km ,and diameters ranging from 2 inch to 6 inch .

## Slide 11
Attil Water Network

## Slide 12
In Attil Network
Pipes : Pipes that transfer water has a different diameter 6, 4, 3 and 2 inches made from steel and steel pipes lined from inside with cement. The number of the pipes = 256 .
Nodes : Nodes are points join lines in the network with each other and where water enters or leaves the network. . The number of nodes = 232
. Area : Attil Town has a recent area equals 4572 dunums
Density : The average density almost equal to 4capita/dunum .

## Slide 13
Sample of Nodal Demand

## Slide 14
Summary of Nodal Demand Table
Total Pop / node = 10921 capita
Total Demand (L / day) = 1222938.73
14.1544= (Total Demand (L / S

## Slide 15
ANALYSIS of EXISTING WATER NETWORK USING EPANET
Network Model in EPANET
R
R : reservoir
P : pump
P
P
P

## Slide 16
Two Runs for Existing Water Network
At a Steady State Condition
1
2
At an Unsteady State Condition
By entering data on patterns icon and that is sourced from distribution of water consumption .during day and night in the West Bank

## Slide 17
Distribution of Water Consumption

## Slide 18
Network Table - Nodes at 6:00 Hrs for Existing
Network

## Slide 19
Network Table - Links at 6:00 Hrs for Existing
Network

## Slide 20
DESIGN OF FUTURE WATER NETWORK
USING EPANET
Attil water network will be designed for the next 25 years based on the year 2014 .
Population growth rate=1.6% according to Palestinian .Central Bureau of Statistics
The population in 2039 is estimated to be 16360 capita .
Per capita water consumption = 120 L/C/d according to Palestinian Water Authority .
Physical losses=15% and 90% of the municipal water .consumption is domestic consumption

## Slide 21
a per capita municipal water demand equals to 157 .L/C/d
The expansion in the urban areas in the future for a period of almost 25 years is within the area that is served from the existing water network . No horizontal expansion on the network .
The future water demand for each node in the network increases by a factor equals 2.42 .

## Slide 22
After Increasing Demand
Network Table - Nodes at 6:00 Hrs

## Slide 23
Network Table - Links at 6:00 Hrs

## Slide 24
Two options for modifying the network
Expansion on Existing Network:Model 1
R : reservoir
P : pump
R
P
P
P

## Slide 25
Network Table - Nodes at 6:00 Hrs for Model 1

## Slide 26
Network Table - Links at 6:00 Hrs for Model 1

## Slide 27
Model 2: Installation of a New Reservoir
R : reservoir
R

## Slide 28
Network Table - Nodes at 6:00 Hrs for Model 2

## Slide 29
Network Table - Links at 6:00 Hrs for Model 2

## Slide 30
COMPARISON BETWEEN The TWO MODELS

## Slide 31
CONCLUSIONS
Model 2 of design is better than model 1 to meet the requirements of future water demand for the next 25
years for many reasons:
Cost is cheaper than model 1 and equals around 2.26 Million NIS .
Has suitable pressure values and no need for pumps .in most of the buildings
The management of this model will be easier than .Model 1