## Slide 1
An-Najah National University
Faculty of Engineering and Information Technology
Industrial Engineering Department Graduation Project 2
Supervisor Name:
Dr.Ramiz Assaf
Eng.Raya Al-Shinnar
Group members:
Malak Saadeh
Ghusoon Salah

## Slide 2: Enabling Sustainable Futures and Economic Empowerment through PET Recycling in Nablus
RECYCLING

## Slide 3
Outline:
Background
Problem statement
Project Objectives
Introduction of PET
Previous work
Results and Discussions
Conclusion and Recommendation
Feasibility Study

## Slide 4: General Background
There are numerous environmental problems negatively affecting the environment.
Our project will focus on plastic waste, as studies have shown that plastic takes 1000 years to decompose.

## Slide 5
01
02
03
Accumulation of plastic waste in landfills.
Lack of recycling and absence of an integrated recycling facility.
There is no recycling of PET plastics in the West Bank.
PLASTIC PET
Problem Statement:

## Slide 6
Objectives:
Production of recycled PET plastic and high quality
Feasibility study for establishing a recycling plant
Encourage the cooperation of all stakeholders

## Slide 7
Introduction of PET
Polymer
Polyethylene terephthalate
Chemical Resistance
Strength to Weight Ratio
Transmissivity
Shatterproof
Potential for Recycling
properties

## Slide 8: Previous Work:
Through our research and data collection, we have learned that there are plastic recycling practices in the West Bank, but they are not specialized in PET plastic, such as Moatasem Khamis’ workshop.

## Slide 9: Our Work:
PET plastic waste
Processes
Recycled PET
PET quantities.
Suppliers.
Collecting and sorting.
Mechanical recycling plant
Machines
Equipment
Labor
Capacity
Plant layout
Location.
Area.
transportation
Valuable final product
Customers.
Price.
Feasibility study

## Slide 10: Assumptions :
A plastic sorting station in the city of Nablus, on Al-Sayrafi land
PET plastic is devoid of non-plastic impurities and unwanted plastic contaminants.
Impurities constituted 15% to 20% of PET plastic.
150 tons of recycled PET flakes requires approximately 180 tons of PET plastic waste.

## Slide 11: Feasibility Study:
A comprehensive analysis and evaluation of a proposed project.
Assess the potential risks and benefits.
Provide decision-makers with the necessary information to proceed with the project or not.
Feasibility study
Market study
Technical study
Financial
study
Feasibility study components:

## Slide 12: Market Study:
The goal is to use the Delphi method to determine whether the project is worth pursuing.
Academic advisors
Specialists from the Nablus Municipality
Plastic factory owners

## Slide 13
Examples of industries that rely on recycled PET plastic:
The finished product of our factory RPET flakes
Description of the product:
Market Study

## Slide 14
Market Study
The target customers:
Customer interest confirmed: plastic factories like Ithmar and National are keen to receive our output. One contacted owner expressed capacity for 150 tons recycled PET.

## Slide 15
Market Study
The target city:
Nablus City
Expansion plan outside the city limits of Nablus
Market Study
The competing market:
-Timely customer service/fulfillment -Minimize delays and ensure top quality with local production & direct inspection -Reducing shipping and transportation costs for the customer by providing local manufacturing.

## Slide 16
Market Study
Availability of raw material :
Market Study
Estimating current demand size:
After studying the market, it was found that the quantity of 150 tons would meet the needs of local factories.
If we provide PET plastic raw materials of appropriate quality, we will encourage the local market to manufacture products instead of importing them.
Based on statistics from the Municipality of Nablus, 220 tons of PET plastic are available per month, and according to the advice of experts and to ensure the arrival of full quantities, we will adopt an amount of 180 tons per month.

## Slide 17: Technical Study:
This stage ensures that the project can be developed and executed successfully from a technical perspective.
Technical study
Production Process
Equipment and machinery
Plant Location and Layout

## Slide 18
Production Process
Raw material inspection
Label Removing
Manual sorting
Non labeled PET
Separating
Remove Labeled PET
Crushing PET
Washing and separating
Hot washing and cleaning
Cleaning
by rubbing washing machine
Dewatering PET flakes
Packing PET into Bags
Final product RPET flakes
Flow process chart:
NO
YES

## Slide 19
Equipment and machinery
Production line Criteria:
specifications | amount
annual demand | 1800 ton/yr
working hours per year | 8hr* 5 days* 50 weeks
production rate | 900 kg/hr
line capacity | 1000 kg/hr
final product form | PET flakes
final product applications | non-food production
Shuliy Machinery Company furnished us with essential information, tailoring their recommendations to the specific polymer types, operating capacities, and desired final product shapes and qualities of our factory.

## Slide 20
Equipment and machinery
Production line layout:

## Slide 21
Equipment and machinery
Production line video:

## Slide 22
the establishment of the factory on Al-Sayrafi land, situated in the city of Nablus.
The required area is about 1 dunum, with a monthly rental cost amounting to 8,000 shekels.
Plant Location and Layout
Site selection and construction:
Department | Construction | Required Area | Cost NIS/ | Total Cost
Production | prefabricated building | 720 | 500 NIS | 360,000 NIS
Store | prefabricated building | 63 | 500 NIS | 31,500 NIS
Reception | Brickwork | 100 | 1,000 NIS | 100,000 NIS
Offices | Brickwork | 100 | 1,000 NIS | 100,000 NIS
Total construction cost |  |  |  | 591,500 NIS
The total required area for the construction equals 883 𝒎𝟐 .

## Slide 23
Plant Location and Layout
plant layout:

## Slide 24: Financial Study:
The financial study focuses on the project's financial feasibility. It involves estimating costs, revenue projections, and potential financial risks.
Financial study
Costs classification
Revenues
Financial
analysis

## Slide 25
Costs
classification
Capital investment:
# | Item name | Total cost (NIS)
1 | Building | 605,800
2 | Machines and equipment | 295,969
3 | Furniture | 17,500
4 | IT equipment | 7,700
5 | Vehicles | 22,000
Grand total |  | 948,969
Fixed assets:
2. Working Capital:
# | Item name/ description | cost/year | Cost/month | Cost for 4 months
1 | Total production cost | 2,472,305 | 206,025 | 824,102
2 | General and Admin. Expenses | 204,300 | 17025 | 68100
The working capital for 4 months |  |  |  | 892,202
The capital invested in our project amounts to 1,841,171 NIS.

## Slide 26
Costs Classification
Operational Costs:
# | Item name | Cost/year (NIS)
1 | HR Budget | 358,800
2 | Supplies | 1,635,360
3 | Utilities | 450,360
4 | Land rent | 96,000
5 | Licenses | 2,000
6 | Insurance | 15,000
7 | Maintenance | 63,946
8 | Hospitality | 1,500
9 | Stationery Expense & Ink | 3200
Grand total |  | 2,604,066

## Slide 27
Revenues
Selling Price:
# | Item name | Unit | Price NIS/ unit
1 | Recycled PET flakes | Ton | 2200 NIS/Ton
Expansion Plan:

## Slide 28
Financial Analysis
Income Statement :

## Slide 29
Financial Analysis
Cash Flow Statement :

## Slide 30
Financial Analysis
Net Cash Flow Diagram :

## Slide 31
Financial Analysis
Worse Scenario Analysis :

## Slide 32
Financial Analysis
Worse Scenario Analysis :
Income Statement:

## Slide 33
Financial Analysis
Worse Scenario Analysis :
Cash Flow Statement:

## Slide 34
Financial Analysis
Worse Scenario Analysis :
Net Cash Flow Diagram:

## Slide 35
Financial Analysis
# | Comparison | Scenario 1 | Scenario 2
1 | Rate of Return (ROR) | 64% | 37%
2 | MARR | 25% | 25%
3 | NPV without inflation | 2,745,664 NIS | 765,410 NIS
4 | Inflation | 2% | 5%
5 | NPV with inflation | 2,385,392 NIS | 317,025 NIS
6 | Payback Period (PbP) | 2 years & 4 months | 3 years & 6 months
7 | Break Even Point (BEP) |  | 
Stage 1 |  | 257 ton/year | 267 ton/year
Stage 2 |  | 270 ton /year | 297 ton /year
Stage 3 |  | 290 ton/year | 344 ton /year
Comparison between the two scenarios

## Slide 36: Results and Discussion:
-Our study, including an interview with Dr. Issam and gathering additional details, revealed that plastic waste makes up 10.1% of solid waste in Nablus. Despite the existence of recycling workshops in the West Bank, they do not focus on recycling PET plastic.
-After setting the factory's goal, we identified and considered all essential requirements, including location, land, machinery, and other fundamental aspects.
Market Results:
Technical Results

## Slide 37: Results and Discussion:
Financial Results:

## Slide 38: Conclusion :
Nablus wastes valuable PET plastic (recyclable!) by landfilling it. A dedicated PET recycling facility can fix this, creating jobs, industries, and eco-friendly products. Challenges exist, but potential is huge.

## Slide 39
Recommendations:
The success of the project hinges significantly on the active participation and collaboration of all relevant stakeholders, including the municipality, the establishment of a sorting station, and the engagement of community members.

## Slide 40
Thank you