## Slide 1
Sign Language
Glove
----------
Prepared By:
Aya Dwikat
Weam Obaid

## Slide 2
Outline
Introduction
Motivation
Objectives
Standards & Equipment
Methodology
Results & Analysis
Conclusion & Future Work

## Slide 3
Introduction
An electrical glove which could be worn by a deaf-mute person.
The glove will help the deaf-mute person translate his/her sign language into text and audio which could be visualized and heard by people without a disability.

## Slide 4
Introduction
The project with a sound recognition feature to help deaf-mute people visualize noise levels on the mobile application.

## Slide 5
Motivation
Miscommunication between people with and without disability.
Awareness of the surrounding environment

## Slide 6
Objectives
Help deaf-mute people integrate into society.
Warn deaf-mute people in the case of a very loud noise that could be an indication of something dangerous.

## Slide 7
Standards & Equipment
Tools and Applications:
Arduino 1.0.5
Android Studio
Equipment

## Slide 8
Equipment
LilyPad Arduino Main Board
Bluetooth HC-06
Accelerometer ADX335
Flex Sensor 4.5
LCD 16x2

## Slide 9
LilyPad Arduino Main Board
The LilyPad Arduino is designed
for e-textiles and wearables projects. It can be sewn to fabric and similarly mounted power supplies and sensors with conductive thread.

## Slide 10
LilyPad technical specs

## Slide 11
FT232R-FTDI
FTDI is used to program the Lilypad arduino

## Slide 12
Bluetooth HC-06
Bluetooth is used to receive messages and commands from the arduino and relay it to the mobile, and vice versa.

## Slide 13
Accelerometer ADX335
Accelerometer is used to sense simple orientation, it measures the acceleration and gives three readings for the x, y, and z axis

## Slide 14
Flex Sensor 4.5
The flex sensor changes its resistance when flexed so we can measure that change using one of the Arduino’s analog pins.

## Slide 15
LCD 16x2
We used a 16x2 LCD to display the letters sent by the arduino

## Slide 16
Methodology

## Slide 18
Sensors Inputs Calibration
take sensors readings of the two flex sensors and the accelerometer for five seconds, and track the highest and lowest values it gets.

## Slide 19
Voice System
Calm
Low Noise
Loud Noise
A Bell or a V. Loud Noise

## Slide 20
Conclusion
A project to enable deaf-mute people communicate well with others.
Translate eight letters: A, B, C, F, G, L, Q, and X into text and audio.
Voice detecting system.

## Slide 21
Future Work
Include more letters, words, and different languages.
Add the speaker and voice system to the glove.
Make a more appealing glove.

## Slide 22
Thank You 